ISUZU Specific Trouble Codes

P1106 MAP Circuit Intermittent Voltage High 
P1107 MAP Circuit Intermittent Voltage Low 
P1108 Barometric Pressure Circuit Input High 
P1111 IAT Sensor Circuit Intermittent Voltage High 
P1112 IAT Sensor Circuit Intermittent Voltage Low 
P1114 ECT Sensor Circuit Intermittent Voltage Low 
P1115 ECT Sensor Circuit Intermittent Voltage High 
P1121 TP Sensor Circuit Intermittent Voltage High 
P1122 TP Sensor Circuit Intermittent Voltage Low 
P1133 H02S Insufficient Switching Bank 1 Sensor 1 
P1134 H02S Transition Time Ratio Bank 1 Sensor 1 
P1153 H02S Insufficient Switching Bank 2 Sensor 1 
P1154 H02S Transition Time Ratio Bank 2 Sensor 1 
P1171 Fuel System Lean During Acceleration 
P1297 Electrical Load Detector Circuit Input Low 
P1298 Electrical Load Detector Circuit Input High 
P1300 Random Misfire 
P1336 CKP System Variation Not Learned 
P1359 CKP/TDC Sensor Disconnected 
P1361 TDC Sensor Intermittent Interruption 
P1362 TDC Sensor No Signal 
P1380 ABS Rough Road System Fault 
P1381 Cylinder Position Sensor Intermittent Interruption, Misfire Detected (Except 1998 Rodeo) 
P1381 ABS Rough Road Class 2 Serial Data Fault Or Link Error (1998 Rodeo) 
P1382 Cylinder Position Sensor No Signal 
P1390 G Sensor Circuit Intermittent Voltage Low 
P1391 G Sensor Performance 
P1392 G Sensor Voltage Low 
P1393 G Sensor Voltage High 
P1394 G Sensor Intermittent Voltage High 
P1404 EGR Valve Stuck Closed 
P1406 EGR Valve Pintle Position Circuit 
P1441 EVAP System Flow During Non-Purge 
P1442 EVAP Vacuum Switch Voltage High During Ignition On 
P1459 EVAP Emission Purge Flow Switch Malfunction 
P1491 EGR Valve Lift Insufficient Detected 
P1498 EGR Valve Lift Sensor Voltage High 
P1508 IAC System RPM Low 
P1509 IAC System RPM High 
P1546 A/C Compressor Clutch Output Circuit Malfunction 
P1548 A/C Compressor Clutch Output Circuit Malfunction 
P1607 PCM Internal Circuit Failure ‘‘A’’ 
P1618 SPI Communications Error 
P1625 PCM Unexpected Reset 
P1627 PCM A/D Conversion Malfunction 
P1635 5 Volt Reference Voltage Circuit Malfunction 
P1640 ODM 1 Input Voltage High (Except 1998 Rodeo) 
P1640 ODM Output ‘‘A’’ Circuit Fault (1998 Rodeo) 
P1650 Quad Driver Module ‘‘A’’ Fault 
P1790 Trans ROM Checksum Error 
P1792 Trans EEPROM Checksum Error 
P1835 Trans Kickdown Switch Malfunction 
P1850 Brake Band Apply Solenoid Malfunction 
P1860 TCC PWM Solenoid Circuit Failure 
P1870 Transmission Component Slipping