Коды ошибок CAN BUS(P0001-P2A11)

"P0001 SPEEDOMETER SENSOR OPEN/SHORT",
"P0002 NE SIGNAL - NO NE SIGNAL",
"P0003 G SIGNAL - NO G SIGNAL",
"P0004 SGT SIGNAL - NO SGT SIGNAL",
"P0005 REAR STEERING ANGLE SENSOR ",
"P0006 NO VSS SIGNAL",
"P0007 STOPLIGHT SW AND BRAKE SW DEFECT",
"P0008 MAF OPEN OR SHORT",
"P0009 P/S FULID LEVELSW LOW FULID SHORT",
"P000A SEPARATOR CODE",
"P000B WSS,SR(FR) OPEN OR SHORT ",
"P000C TP OPEN SHORT",
"P000D CRUISE (COAST) SIGNAL MAL",
"P000E CEHICLE SPEED SENSOR ",
"P000F H02S INACTIVATION",
"P0010 INTAKE CAMSHAFT POS ACTUATOR CIRCUIT(B1)",
"P0011 INTAKE CAMSHAFT TIMING OVER ADVANCED(B1)",
"P0012 INTAKE CAMSHAFT TIMING OVER RETARDED(B1)",
"P0013 EXHAUST CAMSHAFT POS ACTUATOR (B1)",
"P0014 EXHAUST CAMSHAFT POS TIMING OVER ADVANCED(B1)",
"P0015 EXHAUST CAMSHAFT POS TIMING OVER RETARDES(B1)",
"P0016 CRANKSHAFT POS CAMSHAFT POS CORRELATION (B1)",
"P0017 REAR STREEING GEAR DAMAGED",
"P0018 H02S(LH) INVERSION",
"P0019 SOLENOID (PRC) OPEN / SHORT",
"P001A SOLENOID (PURGE CONTROL) OPEN/SHORT",
"P001C SOLENOID (LH-REAR) OPEN/SHORT",
"P001D SOLENOID (EGR-VENT) OPEN/SHORT",
"P001F SOLENOID OPEN SHORT DEMAGED",
"P0020 INTAKE CAMSHAFT POS ACTUATOR CKT (B2)",
"P0021 INTAKE CAMSHAFT TIMING OVER ADVANCED(B2)",
"P0022 INTAKE CAMSHAFT TIMING OVER RETARDED(B2)",
"P0023 EXHAUST CAMSHAFT POS ACTUATOR (B2)",
"P0024 EXHAUST CAMSHAFT POS TIMING OVER ADVANCED(B2)",
"P0025 EXHAUST CAMSHAFT POS TIMING OVER RETARDES(B2)",
"P0026 INTAKE VALVE CONTROL SOL CKT (B1)",
"P0027 EXHAUST VALVE CONTROL SOL CKT (B1)",
"P0028 INTAKE VALVE CONTROL SOL CKT (B2)",
"P0029 SOLENOID VICS-OPEN / SHORT",
"P002E SOLENOID VRIS2 -OPEN",
"P0030 H02S HEATER (B1S1)",
"P0031 H02S HEATER CKT LOW VOLT (B1S1)",
"P0032 H02S HEATER CKT HIGH VOLT (B1S1)",
"P0033 TURBOCHARGE BYPASS VALVE CTRL OPEN",
"P0035 MOTOR RELAY OPEN SHORT DEFECT",
"P0036 H02S HEATER CKT (B1S2)",
"P0037 H02S -12 CIRCUIT LOW VOLT",
"P0038 H02S -12 CIRCUIT HIGH VOLT",
"P0039 RTS1 - OPEN SHORT",
"P003A RTS2 - OPEN SHORT",
"P003B TRS/ECTS OPEN OR SHORT",
"P003C SOLENOID (1-2 SHIFT) OPEN OR SHORT",
"P003D 4WS CONTROL UNIT - DAMAGED",
"P003E SOL (3-4 SHIFT ) OPEN/SHORT",
"P003F SOL (LOCKUP) OPEN/SHORT",
"P0040 POWERTRAIN CTRL MODULE",
"P0041 DOWNSTREAM HO2S SWAPED ",
"P0042 SOL (LINE PRESSURE) OPEN / SHORT",
"P0043 COOLANT FAN RELAY 1 OPEN/SHORT",
"P0044 COOLANT FAN RELAY SHORT",
"P0045 ECTS(FAN) OPEN SHORT",
"P0046 TURBO BOOST CTRL SOL CKT MAL",
"P0047 TURBO BOOST CTRL SOL CKT LOW",
"P0048 TURBO BOOST CTRL SOL CKT HIGH",
"P0049 TURBO TURBINE OVERSPEED",
"P004A TURBOCHARGER/SUPERCHARGER BOOST CONTROL SOLENOID B CIRCUIT / OPEN",
"P004B TURBOCHARGER/SUPERCHARGER BOOST CONTROL SOLENOID B CIRCUIT RANGE/PERFORMANCE",
"P004C TURBOCHARGER/SUPERCHARGER BOOST CONTROL SOLENOID B CIRCUIT LOW",
"P004D TURBOCHARGER/SUPERCHARGER BOOST CONTROL SOLENOID B CIRCUIT HIGH",
"P004E TURBO BOOST CTRL SOL A CKT",
"P004E TURBOCHARGER/SUPERCHARGER BOOST CONTROL SOLENOID A CIRCUIT INTERMITTENT/ERRATIC",
"P004F TURBO BOOST CTRL SOL B CKT",
"P004F TURBOCHARGER/SUPERCHARGER BOOST CONTROL SOLENOID B CIRCUIT INTERMITTENT/ERRATIC",
"P0050 HO2S HEATER CONTROL CKT(B2)",
"P0052 HO2S HEATER CONTROL CKT HIGH VOLT (B2S1)",
"P0053 H02S11 HEATER RESISTANCE OUT OF LIMIT",
"P0054 H02S12 HEATER RESISTANCE OUT OF LIMIT",
"P0055 HO2S HEATER RESISTANCE (B1S3)",
"P0056 HO2S HEATER RESISTANCE (B2S2)",
"P0057 HO2S HEATER CTRL CKT LOW VOLT (B2S2)",
"P0058 HOS2 HEATER CTRL CKT HIGH VOLT (B2S2)",
"P0059 HO2S HEATER RESISTANCE (B2S1)",
"P0060 HO2S HEATER RESISTANCE (B2S2)",
"P0061 HO2S HEATER RESISTANCE (B2S3)",
"P0062 HO2S HEATER CTRL CKT (B2S3)",
"P0063 HO2S HEATER CTRL CKT LOW VOLT (B2S3)",
"P0064 HO2S HEATER CTRL CKT HIGH VOLT (B2S3)",
"P0065 AIR ASSISTED INJ CTRL CKT MAL",
"P0066 AIR ASSISTED INJ CTRL CKT LOW",
"P0067 AIR ASSISTED INJ CTRL CKT HIGH",
"P0068 TP SENSOR INCONSISTENT WITH MAF SENSOR",
"P0069 MAO BAROMETRIC PRESSURE CORRELATION",
"P006F SYSTEM PASS",
"P0070 IAT CKT BELOW MIN VOLT",
"P0071 IAT CKT ABOVE MAX. VOLT",
"P0072 IAT > OR < EXPECTED",
"P0073 AMBIENT AIR TEMP CKT ABOVE MAX VOLT",
"P0074 ECT > OR < EXPECTED",
"P0075 ECT CKT BELOW MIN VOLT",
"P0076 ECT CKT ABOVE MAX VOLT",
"P0077 INTAKE VALVE CTRL HIGH (B1)",
"P0078 EXHAUST VALVE CTRL CKT (B1)",
"P0079 TP VOLT > OR < EXPECTED",
"P007A TP CKT BELOW MIN VOLT",
"P007B TP CKT ABOVE MAX VOLT",
"P0080 EXHAUST VALVE CTRL CKT HIGH (B1)",
"P0081 INSUFF MAP/MAF CHANGE DYNAMIC TEST",
"P0082 INTAKE VALVE CTRL CKT LOW (B2)",
"P0083 INTAKE VALVE CTRL CKT HIGH (B2)",
"P0084 EXHAUST VALVE CTRL CKT (B2)",
"P0085 EXHAUST VALVE CTRL CKT LOW (B2)",
"P0086 EXHAUST VALVE CTRL CKT HIGH (B2)",
"P0090 FUEL PRESSURE REGULATOR CTRL CKT",
"P0091 FUEL PRESSURE REGULATOR CTRL LOW",
"P0092 FUEL PRESSURE REGULATOR CTRL HIGH",
"P0093 FUEL SYSTEM LEAK DETECTED LARGE LEAK",
"P0094 FUEL SSYTEM LEAK DETECTED SMALL LEAK",
"P0095 INTAKE AIR TEMP SENSOR 2 CIRCUIT",
"P0096 IATS2 CKT RANGE/PERFORMANCE",
"P0097 IATS2 CIRCUIT LOW INPUT",
"P0098 IATS2 CIRCUIT HIGH INPUT",
"P0099 IATS2 CIRCUIT INTERMITTENT",
"P009D MAF CIRCUIT BELOW MIN VOLT",
"P009E MAF CIRCUIT ABOVE MAX VOLTAGE",
"P009F MAF > OR < EXPECTED",
"P010A MASS OR VOLUME AIR FLOW B CIRCUIT",
"P010B MASS OR VOLUME AIR FLOW B CIRCUIT RANGE/PERFORMANCE",
"P010C MASS OR VOLUME AIR FLOW B CIRCUIT LOW INPUT",
"P010D MASS OR VOLUME AIR FLOW B CIRCUIT HIGH INPUT",
"P010E MASS OR VOLUME AIR FLOW B CIRCUIT INTERMITTENT/ERRATIC",
"P010F MASS OR VOLUME AIR FLOW SENSOR A/B CORRELATION",
"P011A ENGINE COOLANT TEMPERATURE SENSOR 1/2 CORRELATION",
"P018A FUEL PRESSURE SENSOR B CIRCUIT",
"P018B FUEL PRESSURE SENSOR B CIRCUIT RANGE/PERFORMANCE",
"P018C FUEL PRESSURE SENSOR B CIRCUIT LOW",
"P018D FUEL PRESSURE SENSOR B CIRCUIT HIGH",
"P018E FUEL PRESSURE SENSOR B CIRCUIT INTERMITTENT/ERRATIC",
"P020A CYLINDER 1 INJECTION TIMING",
"P020B CYLINDER 2 INJECTION TIMING",
"P020C CYLINDER 3 INJECTION TIMING",
"P020D CYLINDER 4 INJECTION TIMING",
"P020E CYLINDER 5 INJECTION TIMING",
"P020F CYLINDER 6 INJECTION TIMING",
"P021A CYLINDER 7 INJECTION TIMING",
"P021B CYLINDER 8 INJECTION TIMING",
"P021C CYLINDER 9 INJECTION TIMING",
"P021D CYLINDER 10 INJECTION TIMING",
"P021E CYLINDER 11 INJECTION TIMING",
"P021F CYLINDER 12 INJECTION TIMING",
"P022A INTERCOOLER BYPASS CONTROL A CIRCUIT /OPEN",
"P022B INTERCOOLER BYPASS CONTROL A CIRCUIT LOW",
"P022C INTERCOOLER BYPASS CONTROL A CIRCUIT HIGH",
"P022D INTERCOOLER BYPASS CONTROL B CIRCUIT /OPEN",
"P022E INTERCOOLER BYPASS CONTROL B CIRCUIT LOW",
"P022F INTERCOOLER BYPASS CONTROL B CIRCUIT HIGH",
"P023A TURBOCHARGER/SUPERCHARGER INTERCOOLER COOLANT PUMP CONTROL CIRCUIT/OPEN",
"P023B TURBOCHARGER/SUPERCHARGER INTERCOOLER COOLANT PUMP CONTROL CIRCUIT LOW",
"P023C TURBOCHARGER/SUPERCHARGER INTERCOOLER COOLANT PUMP CONTROL CIRCUIT HIGH",
"P042A CATALYST TEMPERATURE SENSOR CIRCUIT (BANK 1, SENSOR CIRCUIT 2)",
"P042B CATALYST TEMPERATURE SENSOR CIRCUIT RANGE/PERFORMANCE (BANK1, SENSOR CIRCUIT 2)",
"P042C CATALYST TEMPERATURE SENSOR CIRCUIT LOW INPUT (BANK 1, SENSOR CIRCUIT 2)",
"P042D CATALYST TEMPERATURE SENSOR CIRCUIT HIGH INPUT (BANK 1, SENSOR CIRCUIT 2)",
"P043A CATALYST TEMPERATURE SENSOR CIRCUIT (BANK 2, SENSOR CIRCUIT 2)",
"P043B CATALYST TEMPERATURE SENSOR CIRCUIT RANGE/PERFORMANCE (BANK 2, SENSOR CIRCUIT 2)",
"P043C CATALYST TEMPERATURE SENSOR CIRCUIT LOW INPUT (BANK 2, SENSOR CIRCUIT 2)",
"P043D CATALYST TEMPERATURE SENSOR CIRCUIT HIGH INPUT (BANK 2, SENSOR CIRCUIT 2)",
"P043E EVAPORATIVE EMISSION SYSTEM LEAK DETECTION REFERENCE ORIFICE LOW FLOW",
"P043F EVAPORATIVE EMISSION SYSTEM LEAK DETECTION REFERENCE ORIFICE HIGH FLOW",
"P060A INTERNAL CONTROL MODULE MONITORING PROCESSOR PERFORMANCE",
"P060B INTERNAL CONTROL MODULE A/D PROCESSING PERFORMANCE",
"P060C INTERNAL CONTROL MODULE MAIN PROCESSOR PERFORMANCE",
"P060D INTERNAL CONTROL MODULE ACCELERATOR PEDAL POSITION PERFORMANCE",
"P060E INTERNAL CONTROL MODULE THROTTLE POSITION PERFORMANCE",
"P060F INTERNAL CONTROL MODULE ENGINE COOLANT TEMPERATURE PERFORMANCE",
"P061A INTERNAL CONTROL MODULE TORQUE PERFORMANCE",
"P061B INTERNAL CONTROL MODULE TORQUE CALCULATION PERFORMANCE",
"P061C INTERNAL CONTROL MODULE ENGINE RPM PERFORMANCE",
"P061D INTERNAL CONTROL MODULE ENGINE AIR MASS PERFORMANCE",
"P061E INTERNAL CONTROL MODULE BRAKE SIGNAL PERFORMANCE",
"P061F INTERNAL CONTROL MODULE THROTTLE ACTUATOR CONTROLLER PERFORMANCE",
"P062A FUEL PUMP A CONTROL CIRCUIT RANGE/PERFORMANCE",
"P062B INTERNAL CONTROL MODULE FUEL INJECTOR CONTROL PERFORMANCE",
"P062C INTERNAL CONTROL MODULE VEHICLE SPEED PERFORMANCE",
"P062D FUEL INJECTOR DRIVER CIRCUIT PERFORMANCE BANK 1",
"P062E FUEL INJECTOR DRIVER CIRCUIT PERFORMANCE BANK 2",
"P0A0A HIGH VOLTAGE SYSTEM INTER-LOCK CIRCUIT",
"P0A0B HIGH VOLTAGE SYSTEM INTER-LOCK CIRCUIT PERFORMANCE",
"P0A0C HIGH VOLTAGE SYSTEM INTER-LOCK CIRCUIT LOW",
"P0A0D HIGH VOLTAGE SYSTEM INTER-LOCK CIRCUIT HIGH",
"P0A0E HIGH VOLTAGE SYSTEM INTER-LOCK CIRCUIT INTERMITTENT",
"P0A0F ENGINE FAILED TO START",
"P0A1A GENERATOR CONTROL MODULE",
"P0A1B DRIVE MOTOR "A" CONTROL MODULE",
"P0A1C DRIVE MOTOR "B" CONTROL MODULE",
"P0A1D HYBRID POWERTRAIN CONTROL MODULE",
"P0A1E STARTER/GENERATOR CONTROL MODULE",
"P0A1F BATTERY ENERGY CONTROL MODULE",
"P0A2A DRIVE MOTOR "A" TEMPERATURE SENSOR CICRUIT",
"P0A2B DRIVE MOTOR "A" TEMPERATURE SENSOR CICRUIT RANGE/PERFORMANCE",
"P0A2C DRIVE MOTOR "A" TEMPERATURE SENSOR CICRUIT LOW",
"P0A2D DRIVE MOTOR "A" TEMPERATURE SENSOR CICRUIT HIGH",
"P0A2E DRIVE MOTOR "A" TEMPERATURE SENSOR CICRUIT INTERMITTENT",
"P0A2F DRIVE MOTOR "A" OVER TEMPERATURE",
"P0A30 DRIVE MOTOR "B" TEMPERATURE SENSOR CIRCUIT",
"P0A31 DRIVE MOTOR "B" TEMPERATURE SENSOR CICRUIT RANGE/PERFORMANCE",
"P0A32 DRIVE MOTOR "B" TEMPERATURE SENSOR CICRUIT LOW",
"P0A33 DRIVE MOTOR "B" TEMPERATURE SENSOR CICRUIT HIGH",
"P0A34 DRIVE MOTOR "B" TEMPERATURE SENSOR CICRUIT INTERMITTENT",
"P0A35 DRIVE MOTOR "B" OVER TEMPERATURE",
"P0A36 GENERATOR TEMPERATURE SENSOR CIRCUIT",
"P0A37 GENERATOR TEMPERATURE SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A38 GENERATOR TEMPERATURE SENSOR CIRCUIT LOW",
"P0A39 GENERATOR TEMPERATURE SENSOR CIRCUIT HIGH",
"P0A3A GENERATOR TEMPERATURE SENSOR CIRCUIT INTERMITTENT",
"P0A3B GENERATOR OVER TEMPERATURE",
"P0A3C DRIVE MOTOR "A" INVERTER OVER TEMPERATURE",
"P0A3D DRIVE MOTOR "B" INVERTER OVER TEMPERATURE",
"P0A3E GENERATOR INVERTER OVER TEMPERATURE",
"P0A3F DRIVE MOTOR "A" POSITION SENSOR CIRCUIT",
"P0A40 DRIVE MOTOR "A" POSITION SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A41 DRIVE MOTOR "A" POSITION SENSOR CIRCUIT LOW",
"P0A42 DRIVE MOTOR "A" POSITION SENSOR CIRCUIT HIGH",
"P0A43 DRIVE MOTOR "A" POSITION SENSOR CIRCUIT INTERMITTENT",
"P0A44 DRIVE MOTOR "A" POSITION SENSOR CIRCUIT OVERSPEED",
"P0A45 DRIVE MOTOR "B" POSITION SENSOR CIRCUIT",
"P0A46 DRIVE MOTOR "B" POSITION SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A47 DRIVE MOTOR "B" POSITION SENSOR CIRCUIT LOW",
"P0A48 DRIVE MOTOR "B" POSITION SENSOR CIRCUIT HIGH",
"P0A49 DRIVE MOTOR "B" POSITION SENSOR CIRCUIT INTERMITTENT",
"P0A4A DRIVE MOTOR "B" POSITION SENSOR CIRCUIT OVERSPEED",
"P0A4B GENERATOR POSITION SENSOR CIRCUIT",
"P0A4C GENERATOR POSITION SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A4D GENERATOR POSITION SENSOR CIRCUIT LOW",
"P0A4E GENERATOR POSITION SENSOR CIRCUIT HIGH",
"P0A4F GENERATOR POSITION SENSOR CIRCUIT INTERMITTENT",
"P0A50 GENERATOR POSITION SENSOR CIRCUIT OVERSPEED",
"P0A51 DRIVE MOTOR "A" CURRENT SENSOR CIRCUIT",
"P0A52 DRIVE MOTOR "A" CURRENT SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A53 DRIVE MOTOR "A" CURRENT SENSOR CIRCUIT LOW",
"P0A54 DRIVE MOTOR "A" CURRENT SENSOR CIRCUIT HIGH",
"P0A55 DRIVE MOTOR "B" CURRENT SENSOR CIRCUIT",
"P0A56 DRIVE MOTOR "B" CURRENT SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A57 DRIVE MOTOR "B" CURRENT SENSOR CIRCUIT LOW",
"P0A58 DRIVE MOTOR "B" CURRENT SENSOR CIRCUIT HIGH",
"P0A59 GENERATOR CURRENT SENSOR CIRCUIT",
"P0A5A GENERATOR CURRENT SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A5B GENERATOR CURRENT SENSOR CIRCUIT LOW",
"P0A5C GENERATOR CURRENT SENSOR CIRCUIT HIGH",
"P0A5D DRIVE MOTOR "A" PHASE U CURRENT",
"P0A5E DRIVE MOTOR "A" PHASE U CURRENT LOW",
"P0A5F DRIVE MOTOR "A" PHASE U CURRENT HIGH",
"P0A60 DRIVE MOTOR "A" PHASE V CURRENT",
"P0A61 DRIVE MOTOR "A" PHASE V CURRENT LOW",
"P0A62 DRIVE MOTOR "A" PHASE V CURRENT HIGH",
"P0A63 DRIVE MOTOR "A" PHASE W CURRENT",
"P0A64 DRIVE MOTOR "A" PHASE W CURRENT LOW",
"P0A65 DRIVE MOTOR "A" PHASE W CURRENT HIGH",
"P0A66 DRIVE MOTOR "B" PHASE U CURRENT",
"P0A67 DRIVE MOTOR "B" PHASE U CURRENT LOW",
"P0A68  DRIVE MOTOR "B" PHASE U CURRENT HIGH",
"P0A69 DRIVE MOTOR "B" PHASE V CURRENT",
"P0A6A DRIVE MOTOR "B" PHASE V CURRENT LOW",
"P0A6B DRIVE MOTOR "B" PHASE V CURRENT HIGH",
"P0A6C DRIVE MOTOR "B" PHASE W CURRENT",
"P0A6D DRIVE MOTOR "B" PHASE W CURRENT LOW",
"P0A6E DRIVE MOTOR "B" PHASE W CURRENT HIGH",
"P0A6F GENERATOR PHASE U CURRENT",
"P0A70 GENERATOR PHASE U CURRENT LOW",
"P0A71 GENERATOR PHASE U CURRENT HIGH",
"P0A72 GENERATOR PHASE V CURRENT",
"P0A73 GENERATOR PHASE V CURRENT LOW",
"P0A74 GENERATOR PHASE V CURRENT HIGH",
"P0A75 GENERATOR PHASE W CURRENT",
"P0A76 GENERATOR PHASE W CURRENT LOW",
"P0A77 GENERATOR PHASE W CURRENT HIGH",
"P0A78 DRIVE MOTOR "A" INVERTER PERFORMANCE",
"P0A79 DRIVE MOTOR "B" INVERTER PERFORMANCE",
"P0A7A GENERATOR INVERTER PERFORMANCE",
"P0A7B BATTERY ENERGY CONTROL MODULE REQUESTED MIL ILLUMINATION",
"P0A7C MOTOR ELECTRONIC OVER TEMPERATURE",
"P0A7D HYBRID BATTERY PACK STATE OF CHARGE LOW",
"P0A7E HYBRID BATTERY PACK OVER TEMPERATURE",
"P0A7F REPLACE HYBRID BATTERY PACK DETERIORATION",
"P0A80 REPLACE HYBRID BATTERY PACK",
"P0A81 HYBRID BATTERY PACK COOLING FAN 1 CONTROL CIRCUIT",
"P0A82 HYBRID BATTERY PACK COOLING FAN 1 PERFORMANCE OR STUCK OFF",
"P0A83 HYBRID BATTERY PACK COOLING FAN 1 STUCK ON",
"P0A84 HYBRID BATTERY PACK COOLING FAN 1 CONTROL CIRCUIT LOW",
"P0A85 HYBRID BATTERY PACK COOLING FAN 1 CONTROL CIRCUIT HIGH",
"P0A86 14 VOLT POWER MODULE CURRENT SENSOR CIRCUIT",
"P0A87 14 VOLT POWER MODULE CURRENT SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A88 14 VOLT POWER MODULE CURRENT SENSOR CIRCUIT LOW",
"P0A89 14 VOLT POWER MODULE CURRENT SENSOR CIRCUIT HIGH",
"P0A8A 14 VOLT POWER MODULE CURRENT SENSOR CIRCUIT INTERMITTENT",
"P0A8B 14 VOLT POWER MODULE SYSTEM VOLTAGE",
"P0A8C 14 VOLT POWER MODULE SYSTEM VOLTAGE UNSTABLE",
"P0A8D 14 VOLT POWER MODULE SYSTEM VOLTAGE LOW",
"P0A8E 14 VOLT POWER MODULE SYSTEM VOLTAGE HIGH",
"P0A8F 14 VOLT POWER MODULE SYSTEM VOLTAGE PERFORMANCE",
"P0A90 DRIVE MOTOR "A" PERFORMANCE",
"P0A91 DRIVE MOTOR "B" PERFORMANCE",
"P0A92 HYBRID GENERATOR PERFORMANCE",
"P0A93 INVERTER COOLING SYSTEM PERFORMANCE",
"P0A94 DC/DC CONVERTER PERFORMANCE",
"P0A95 HIGH VOLTAGE FUSE",
"P0A96 HYBRID BATTERY PACK COOLING FAN 2 CONTROL CIRCUIT",
"P0A97 HYBRID BATTERY PACK COOLING FAN 2 PERFORMANCE OR STUCK OFF",
"P0A98 HYBRID BATTERY PACK COOLING FAN 2 STUCK ON",
"P0A99 HYBRID BATTERY PACK COOLING FAN 2 CONTROL CIRCUIT ON",
"P0A9A HYBRID BATTERY PACK COOLING FAN 2 CONTROL CIRCUIT HIGH",
"P0A9B HYBRID BATTERY TEMPERATURE SENSOR CIRCUIT",
"P0A9C HYBRID BATTERY TEMPERATURE SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0A9D HYBRID BATTERY TEMPERATURE SENSOR CIRCUIT LOW",
"P0A9E HYBRID BATTERY TEMPERATURE SENSOR CIRCUIT HIGH",
"P0A9F HYBRID BATTERY TEMPERATURE SENSOR CIRCUIT INTERMITTENT/ERRATIC",
"P0AA0 HYBRID BATTERY POSITIVE CONTACTOR CIRCUIT",
"P0AA1 HYBRID BATTERY POSITIVE CONTACTOR CIRCUIT STUCK CLOSED",
"P0AA2 HYBRID BATTERY POSITIVE CONTACTOR CIRCUIT STUCK OPEN",
"P0AA3 HYBRID BATTERY NEGATIVE CONTACTOR CIRCUIT",
"P0AA4 HYBRID BATTERY NEGATIVE CONTACTOR CIRCUIT STUCK CLOSED",
"P0AA5 HYBRID BATTERY NEGATIVE CONTACTOR CIRCUIT STUCK OPEN",
"P0AA6 HYBRID BATTERY VOLTAGE SYSTEM ISOLATION FAULT",
"P0AA7 HYBRID BATTERY VOLTAGE ISOLATION SENSOR CIRCUIT",
"P0AA8 HYBRID BATTERY VOLTAGE ISOLATION SENSOR CIRCUIT RANGE/PERFORMANCE",
"P0AA9 HYBRID BATTERY VOLTAGE ISOLATION SENSOR CIRCUIT LOW",
"P0AAA HYBRID BATTERY VOLTAGE ISOLATION SENSOR CIRCUIT HIGH",
"P0AAB HYBRID BATTERY VOLTAGE ISOLATION SENSOR CIRCUIT INTERMITTENT/ERRATIC",
"P0AAC HYBRID BATTERY PACK AIR TEMPERATURE SENSOR A CIRCUIT",
"P0AAD HYBRID BATTERY PACK AIR TEMPERATURE SENSOR A CIRCUIT RANGE/PERFORMANCE",
"P0AAE HYBRID BATTERY PACK AIR TEMPERATURE SENSOR A CIRCUIT LOW",
"P0AAF HYBRID BATTERY PACK AIR TEMPERATURE SENSOR A CIRCUIT HIGH",
"P0AB0 HYBRID BATTERY PACK AIR TEMPERATURE SENSOR A CIRCUIT INTERMITTENT/ERRATIC",
"P0AB1 HYBRID BATTERY PACK AIR TEMPERATURE SENSOR B CIRCUIT",
"P0AB2 HYBRID BATTERY PACK AIR TEMPERATURE SENSOR B CIRCUIT RANGE/PERFORMANCE",
"P0AB3 HYBRID BATTERY PACK AIR TEMPERATURE SENSOR B CIRCUIT LOW",
"P0AB4 HYBRID BATTERY PACK AIR TEMPERATURE SENSOR B CIRCUIT HIGH",
"P0AB5 HYBRID BATTERY PACK AIR TEMPERATURE SENSOR B CIRCUIT INTERMITTENT/ERRATIC",
"P0AB6 ENGINE MOUNT CONTROL B CIRCUIT / OPEN",
"P0AB7 ENGINE MOUNT CONTROL B CIRCUIT LOW",
"P0AB8 ENGINE MOUNT CONTROL B CIRCUIT HIGH",
"P0AB9 HYBRID SYSTEM PERFORMANCE",
"P1000 OBD SYSTEMS READINESS TEST NOT COMPLETE",
"P1001 KOER NOT ABLE TO COMPLETE, KOER ABORTED",
"P1100 MASS AIR FLOW SENSOR CIRCUIT INTERMITTENT",
"P1101 MASS AIR FLOW SENSOR OUT OF SELF TEST RANGE",
"P1102 MASS AIR FLOW SENSOR IN RANGE BUT LOWER THAN EXPECTED",
"P1103 MASS AIR FLOW SENSOR IN RANGE BUT HIGHER THAN EXPECTED",
"P1104 MASS AIR FLOW SENSOR CIRCUIT GROUND",
"P1105 DUAL ALTERNATOR UPPER FAULT",
"P1106 DUAL ALTERNATOR LOWER FAULT",
"P1107 DUAL ALTERNATOR LOWER CIRCUIT",
"P1108 DUAL ALTERNATOR BATTERY LAMP CIRCUIT",
"P1109 INTAKE AIR TEMPERATURE 2 CIRCUIT INTERMITTENT",
"P1110 INTAKE AIR TEMPERATURE CIRCUIT (D/C) OPEN/SHORT",
"P1111 SYSTEM PASS",
"P1112 INTAKE AIR TEMPERATURE CIRCUIT INTERMITTENT",
"P1113 INTAKE AIR TEMPERATURE CIRCUIT (L/C) OPEN/SHORT",
"P1114 INTAKE AIR TEMPERATURE 2 CIRCUIT LOW INPUT (SUPER/TURBO CHARGED ENGINES)",
"P1115 INTAKE AIR TEMPERATURE 2 CIRCUIT HIGH INPUT (SUPER/TURBO CHARGED ENGINES)",
"P1116 ENGINE COOLANT TEMPERATURE SENSOR OUT OF SELF TEST RANGE",
"P1117 ENGINE COOLANT TEMPERATURE SENSOR CIRCUIT INTERMITTENT",
"P1118 MANIFOLD AIR TEMPERATURE CIRCUIT LOW INPUT",
"P1119 MANIFOLD AIR TEMPERATURE CIRCUIT HIGH INPUT",
"P1120 THROTTLE POSITION SENSOR A OUT OF RANGE LOW (RATCH TOO LOW)",
"P1121 THROTTLE POSITION SENSOR A INCONSISTENT WITH MAF/MAP SENSOR (SEE P0068)",
"P1122 PEDAL POSITION SENSOR A CIRCUIT LOW INPUT",
"P1123 PEDAL POSITION SENSOR A CIRCUIT HIGH INPUT",
"P1124 THROTTLE POSITION SENSOR A OUT OF SELF TEST RANGE",
"P1125 THROTTLE POSITION SENSOR A INTERMITTENT",
"P1126 THROTTLE POSITION (NARROW RANGE) SENSOR CIRCUIT",
"P1127 EXHAUST TEMPERATURE OUT OF RANGE, O2 SENSOR TESTS NOT COMPLETED",
"P1128 UPSTREAM HO2S SENSORS SWAPPED (SEE P0040)",
"P1129 DOWNSTREAM HO2S SENSORS SWAPPED (SEE P0041)",
"P1130 LACK OF HO2S11 SWITCHES - FUEL TRIM AT LIMIT",
"P1131 LACK OF HO2S11 SWITCHES - SENSOR INDICATES LEAN (SEE P2195)",
"P1132 LACK OF HO2S11 SWITCHES - SENSOR INDICATES RICH (SEE P2196)",
"P1133 BANK 1 FUEL CONTROL SHIFTED LEAN (FAOSC) (SEE P2096)",
"P1134 BANK 1 FUEL CONTROL SHIFTED RICH (FAOSC) (SEE P2097)",
"P1135 PEDAL POSITION SENSOR A CIRCUIT INTERMITTENT",
"P1136 CONTROL BOX FAN CIRCUIT",
"P1137 LACK OF HO2S12 SWITCHES - SENSOR INDICATES LEAN (SEE P2270)",
"P1138 LACK OF HO2S12 SWITCHES - SENSOR INDICATES RICH (SEE P2271)",
"P1139 WATER IN FUEL INDICATOR CIRCUIT",
"P1140 WATER IN FUEL CONDITION",
"P1141 FUEL RESTRICTION INDICATOR CIRCUIT",
"P1142 FUEL RESTRICTION CONDITION",
"P1143 AIR ASSISTED INJECTOR CONTROL VALVE RANGE/PERFORMANCE",
"P1144 AIR ASSISTED INJECTOR CONTROL VALVE CIRCUIT",
"P1145 CALCULATED TORQUE ERROR",
"P1146 ALTERNATOR LOAD LOW INPUT (SAME AS P1245, ADDED FOR JAG)",
"P1147 MANIFOLD AIR TEMPERATURE / INTAKE AIR TEMPERATURE CORRELATION",
"P1148 GENERATOR 2 CONTROL CIRCUIT",
"P1149 GENERATOR 2 MONITOR CIRCUIT HIGH",
"P1150 LACK OF HO2S21 SWITCHES - FUEL TRIM AT LIMIT",
"P1151 LACK OF HO2S21 SWITCHES - SENSOR INDICATES LEAN (SEE P2197)",
"P1152 LACK OF HO2S21 SWITCHES - SENSOR INDICATES RICH (SEE P2198)",
"P1153 BANK 2 FUEL CONTROL SHIFTED LEAN (FAOSC) (SEE P2098)",
"P1154 BANK 2 FUEL CONTROL SHIFTED RICH (FAOSC) (SEE P2099)",
"P1155 ALTERNATIVE FUEL CONTROL MODULE HAS ACTIVATED THE MIL",
"P1156 FUEL SELECT SWITCH CIRCUIT",
"P1157 LACK OF HO2S22 SWITCHES - SENSOR INDICATES LEAN (SEE P2272)",
"P1158 LACK OF HO2S22 SWITCHES - SENSOR INDICATES RICH (SEE P2273)",
"P1159 FUEL STEPPER MOTOR",
"P1167 INVALID TEST, OPERATOR DID NOT ACTUATE THROTTLE",
"P1168 FUEL RAIL PRESSURE SENSOR IN RANGE BUT LOW",
"P1169 FUEL RAIL PRESSURE SENSOR IN RANGE BUT HIGH",
"P1170 ENGINE SHUT OFF SOLENOID",
"P1171 ROTOR SENSOR",
"P1172 ROTOR CONTROL",
"P1173 ROTOR CALIBRATION",
"P1174 CAM SENSOR",
"P1175 CAM CONTROL",
"P1176 CAM CALIBRATION",
"P1177 SYNCHRONIZATION",
"P1178 BOLTUP LIMITS",
"P1179 LONG TERM FUEL TRIM TOO RICH - BANKS 1 AND 2 (AMFR)",
"P1180 FUEL DELIVERY SYSTEM - LOW",
"P1181 FUEL DELIVERY SYSTEM - HIGH",
"P1182 FUEL SHUT OFF SOLENOID CIRCUIT",
"P1183 ENGINE OIL TEMPERATURE SENSOR CIRCUIT",
"P1184 ENGINE OIL TEMPERATURE SENSOR OUT OF SELF TEST RANGE",
"P1185 FUEL PUMP TEMPERATURE SENSOR HIGH",
"P1186 FUEL PUMP TEMPERATURE SENSOR LOW",
"P1187 VARIANT SELECTION",
"P1188 CALIBRATION MEMORY",
"P1189 PUMP SPEED SIGNAL",
"P1190 CALIBRATION RESISTOR OUT OF RANGE",
"P1191 KEY LINE VOLTAGE",
"P1192 V EXTERNAL",
"P1193 EGR DRIVER OVER CURRENT",
"P1194 ECM/PCM A/D CONVERTER",
"P1195 SCP HBCC CHIP FAILED TO INITIALIZE",
"P1196 KEY OFF VOLTAGE HIGH",
"P1197 KEY OFF VOLTAGE LOW",
"P1198 PUMP ROTOR CONTROL UNDERFUELING",
"P1199 FUEL LEVEL INPUT CIRCUIT LOW",
"P1200 INJECTOR RANGE/PERFORMANCE",
"P1201 CYLINDER #1 INJECTOR CIRCUIT OPEN/SHORTED",
"P1202 CYLINDER #2 INJECTOR CIRCUIT OPEN/SHORTED",
"P1203 CYLINDER #3 INJECTOR CIRCUIT OPEN/SHORTED",
"P1204 CYLINDER #4 INJECTOR CIRCUIT OPEN/SHORTED",
"P1205 CYLINDER #5 INJECTOR CIRCUIT OPEN/SHORTED",
"P1206 CYLINDER #6 INJECTOR CIRCUIT OPEN/SHORTED",
"P1207 CYLINDER #7 INJECTOR CIRCUIT OPEN/SHORTED",
"P1208 CYLINDER #8 INJECTOR CIRCUIT OPEN/SHORTED",
"P1209 INJECTOR CONTROL PRESSURE PEAK DELTA TEST FAULT",
"P1210 INJECTOR CONTROL PRESSURE HIGHER THAN DESIRED (ENGINE OFF)",
"P1211 INJECTOR CONTROL PRESSURE HIGHER/LOWER THAN DESIRED (ENGINE RUNNING)",
"P1212 INJECTOR CONTROL PRESSURE LOWER THAN DESIRED (ENGINE CRANK OR RUN)",
"P1213 START INJECTOR CIRCUIT",
"P1214 PEDAL POSITION SENSOR B CIRCUIT INTERMITTENT",
"P1215 PEDAL POSITION SENSOR C CIRCUIT LOW INPUT",
"P1216 PEDAL POSITION SENSOR C CIRCUIT HIGH INPUT",
"P1217 PEDAL POSITION SENSOR C CIRCUIT INTERMITTENT",
"P1218 CID HIGH",
"P1219 CID LOW",
"P1220 SERIES THROTTLE CONTROL SYSTEM",
"P1221 TRACTION CONTROL SYSTEM",
"P1222 TRACTION CONTROL OUTPUT CIRCUIT",
"P1223 PEDAL POSITION SENSOR B CIRCUIT HIGH INPUT",
"P1224 THROTTLE POSITION SENSOR B OUT OF SELF TEST RANGE",
"P1225 NEEDLE LIFT SENSOR",
"P1226 CONTROL SLEEVE SENSOR CIRCUIT",
"P1227 WASTEGATE FAILED CLOSED (OVER PRESSURE)",
"P1228 WASTEGATE FAILED OPEN (UNDER PRESSURE)",
"P1229 CHARGE AIR COOLER PUMP DRIVER",
"P1230 FUEL PUMP LOW SPEED MALFUNCTION (VLCM)",
"P1231 FUEL PUMP SECONDARY CIRCUIT LOW, HIGH SPEED (VLCM)",
"P1232 FUEL PUMP SPEED PRIMARY CIRCUIT (TWO SPEED FUEL PUMP)",
"P1233 FUEL PUMP DRIVER MODULE DISABLED OR OFF LINE (FUEL PUMP DRIVER MODULE)",
"P1234 FUEL PUMP DRIVER MODULE DISABLED OR OFF LINE (FUEL PUMP DRIVER MODULE)",
"P1235 FUEL PUMP CONTROL OUT OF RANGE (FUEL PUMP DRIVER MODULE/VLCM)",
"P1236 FUEL PUMP CONTROL OUT OF RANGE (FUEL PUMP DRIVER MODULE)",
"P1237 FUEL PUMP SECONDARY CIRCUIT (FUEL PUMP DRIVER MODULE)",
"P1238 FUEL PUMP SECONDARY CIRCUIT (FUEL PUMP DRIVER MODULE)",
"P1239 SPEED FUEL PUMP POSITIVE FEED",
"P1240 SENSOR POWER SUPPLY",
"P1241 SENSOR POWER SUPPLY LOW INPUT",
"P1242 SENSOR POWER SUPPLY HIGH INPUT",
"P1243 SECOND FUEL PUMP FAULT OR GROUND FAULT",
"P1244 ALTERNATOR LOAD HIGH INPUT (SEE P0626)",
"P1245 ALTERNATOR LOAD LOW INPUT (SEE P0625)",
"P1246 ALTERNATOR LOAD INPUT (SEE P0622)",
"P1247 TURBO BOOST PRESSURE LOW",
"P1248 TURBO BOOST PRESSURE NOT DETECTED",
"P1249 WASTEGATE CONTROL VALVE PERFORMANCE",
"P1250 THROTTLE VALVE SPRING",
"P1251 AIR MIXTURE SOLENOID CIRCUIT",
"P1252 PEDAL CORRELATION PDS1 AND LPDS HIGH",
"P1253 PEDAL CORRELATION PDS1 AND LPDS LOW",
"P1254 PEDAL CORRELATION PDS2 AND LPDS HIGH",
"P1255 PEDAL CORRELATION PDS2 AND LPDS LOW",
"P1256 PEDAL CORRELATION PDS1 AND HPDS",
"P1257 PEDAL CORRELATION PDS2 AND HPDS",
"P1258 PEDAL CORRELATION PDS1 AND PDS2",
"P1259 IMMOBILIZER TO PCM SIGNAL ERROR",
"P1260 THEFT DETECTED, VEHICLE IMMOBILIZED",
"P1261 CYLINDER #1 HIGH TO LOW SIDE SHORT",
"P1262 CYLINDER #2 HIGH TO LOW SIDE SHORT",
"P1263 CYLINDER #3 HIGH TO LOW SIDE SHORT",
"P1264 CYLINDER #4 HIGH TO LOW SIDE SHORT",
"P1265 CYLINDER #5 HIGH TO LOW SIDE SHORT",
"P1266 CYLINDER #6 HIGH TO LOW SIDE SHORT",
"P1267 CYLINDER #7 HIGH TO LOW SIDE SHORT",
"P1268 CYLINDER #8 HIGH TO LOW SIDE SHORT",
"P1269 IMMOBILIZER CODE NOT PROGRAMMED",
"P1270 ENGINE RPM OR VEHICLE SPEED LIMITER REACHED",
"P1271 CYLINDER #1 HIGH TO LOW SIDE OPEN",
"P1272 CYLINDER #2 HIGH TO LOW SIDE OPEN",
"P1273 CYLINDER #3 HIGH TO LOW SIDE OPEN",
"P1274 CYLINDER #4 HIGH TO LOW SIDE OPEN",
"P1275 CYLINDER #5 HIGH TO LOW SIDE OPEN",
"P1276 CYLINDER #6 HIGH TO LOW SIDE OPEN",
"P1277 CYLINDER #7 HIGH TO LOW SIDE OPEN",
"P1278 CYLINDER #8 HIGH TO LOW SIDE OPEN",
"P1279 CONTROL SLEEVE SENSOR CIRCUIT RANGE/PERFORMANCE",
"P1280 INJECTOR CONTROL PRESSURE SENSOR CIRCUIT LOW",
"P1281 INJECTOR CONTROL PRESSURE SENSOR CIRCUIT HIGH",
"P1282 INJECTOR CONTROL PRESSURE HIGHER THAN DESIRED (ENGINE RUNNING)",
"P1283 INJECTOR PRESSURE REGULATOR CONTROL CIRCUIT",
"P1284 ABORTED KOER - INJECTOR CONTROL PRESSURE FAILURE",
"P1285 CYLINDER HEAD OVERTEMPERATURE CONDITION",
"P1286 FUEL PULSEWIDTH IN RANGE BUT LOWER THAN EXPECTED",
"P1287 FUEL PULSEWIDTH IN RANGE BUT HIGHER THAN EXPECTED",
"P1288 CYLINDER HEAD TEMPERATURE SENSOR OUT OF SELF TEST RANGE",
"P1289 CYLINDER HEAD TEMPERATURE SENSOR CIRCUIT HIGH INPUT",
"P1290 CYLINDER HEAD TEMPERATURE SENSOR CIRCUIT LOW INPUT",
"P1291 INJECTOR HIGH SIDE SHORT TO GND OR VBATT - BANK 1",
"P1292 INJECTOR HIGH SIDE SHORT TO GND OR VBATT - BANK 2",
"P1293 INJECTOR HIGH SIDE OPEN - BANK 1",
"P1294 INJECTOR HIGH SIDE OPEN - BANK 2",
"P1295 INJECTOR MULTIPLE FAULTS - BANK 1",
"P1296 INJECTOR MULTIPLE FAULTS - BANK 2",
"P1297 INJECTOR HIGH SIDE SWITCHES SHORTED TOGETHER",
"P1298 INJECTOR DRIVER MODULE FAILURE",
"P1299 CYLINDER HEAD OVERTEMPERATURE PROTECTION ACTIVE",
"P1300 BOOST CALIBRATION FAULT",
"P1301 BOOST CALIBRATION HIGH",
"P1302 BOOST CALIBRATION LOW",
"P1303 EXHAUST GAS RECIRCULATION CALIBRATION FAULT",
"P1304 EXHAUST GAS RECIRCULATION CALIBRATION HIGH",
"P1305 EXHAUST GAS RECIRCULATION CALIBRATION LOW",
"P1306 KICKDOWN RELAY PULL-IN CIRCUIT",
"P1307 KICKDOWN RELAY HOLD CIRCUIT",
"P1308 A/C CLUTCH CIRCUIT",
"P1309 MISFIRE MONITOR HARDWARE - CMP MISALIGNED, CKP/CMP NOISE, PCM AICE CHIP",
"P1310 IONIZATION MISFIRE DETECTION MODULE FAULT",
"P1311 IONIZATION MISFIRE DETECTION MODULE COMMUNICATION FAULT",
"P1312 INJECTION PUMP TIMING ACTUATOR CIRCUIT",
"P1313 MISFIRE RATE CATALYST DAMAGE FAULT - BANK 1",
"P1314 MISFIRE RATE CATALYST DAMAGE FAULT - BANK 2",
"P1315 PERSISTENT MISFIRE",
"P1316 INJECTOR DRIVER MODULE CODES DETECTED",
"P1317 INJECTOR CIRCUIT/INJECTOR DRIVER MODULE CODES NOT RETRIEVED",
"P1318 INJECTION TIMING PISTON POSITION SENSOR CIRCUIT",
"P1319 INJECTION TIMING PISTON POSITION SENSOR CIRCUIT RANGE/PERFORMANCE",
"P1320 DISTRIBUTOR SIGNAL INTERRUPT",
"P1321 CYLINDER #9 HIGH TO LOW SIDE SHORT",
"P1322 CYLINDER #10 HIGH TO LOW SIDE SHORT",
"P1323 CYLINDER #11 HIGH TO LOW SIDE SHORT",
"P1324 CYLINDER #12 HIGH TO LOW SIDE SHORT",
"P1325 CYLINDER #9 HIGH TO LOW SIDE OPEN",
"P1326 CYLINDER #10 HIGH TO LOW SIDE OPEN",
"P1327 CYLINDER #11 HIGH TO LOW SIDE OPEN",
"P1328 CYLINDER #12 HIGH TO LOW SIDE OPEN",
"P1329 INJECTOR CONTROL PRESSURE HIGHER THAN DESIRED (ENGINE RUNNING)",
"P1330 INJECTOR CONTROL PRESSURE LOWER THAN DESIRED (ENGINE RUNNING)",
"P1331 TURBO/SUPER CHARGER BOOST HIGH SIDE CONTROL CIRCUIT / OPEN",
"P1332 TURBO/SUPER CHARGER BOOST HIGH SIDE CONTROL CIRCUIT LOW",
"P1333 TURBO/SUPER CHARGER BOOST HIGH SIDE CONTROL CIRCUIT HIGH",
"P1334 EGR THROTTLE POSITION SENSOR MINUMUM/MAXIMUM STOP PERFORMANCE",
"P1335 EGR POSITION SENSOR MINIMUM/MAXIMUM STOP PERFORMANCE",
"P1336 CRANKSHAFT/CAMSHAFT SENSOR RANGE/PERFORMANCE",
"P1337 THROTTLE POSITION OUTPUT CIRCUIT",
"P1338 FUEL PUMP DRIVER MODULE COMMUNICATION CIRCUIT (FUEL PUMP DRIVER MODULE)",
"P1339 FUEL PUMP DRIVER MODULE COMMUNICATION CIRCUIT (FUEL PUMP DRIVER MODULE)",
"P1340 CAMSHAFT POSITION SENSOR B CIRCUIT",
"P1341 CAMSHAFT POSITION SENSOR B CIRCUIT RANGE/PERFORMANCE",
"P1342 PEDAL DEMAND SENSOR A CIRCUIT RANGE/PERFORMANCE",
"P1343 PEDAL DEMAND SENSOR B CIRCUIT RANGE/PERFORMANCE",
"P1344 PEDAL DEMAND SENSOR C CIRCUIT RANGE/PERFORMANCE",
"P1345 CYLINDER DISCRIMINATION SIGNAL (FROM CMP SENSOR)",
"P1346 FUEL LEVEL SENSOR B CIRCUIT",
"P1347 FUEL LEVEL SENSOR B CIRCUIT RANGE/PERFORMANCE",
"P1348 FUEL LEVEL SENSOR B CIRCUIT LOW INPUT",
"P1349 FUEL LEVEL SENSOR B CIRCUIT HIGH INPUT",
"P1350 FUEL LEVEL SENSOR B CIRCUIT INTERMITTENT",
"P1351 IGNITION DIAGNOSTIC MONITOR INPUT CIRCUIT",
"P1352 IGNITION COIL A PRIMARY CIRCUIT",
"P1353 IGNITION COIL B PRIMARY CIRCUIT",
"P1354 IGNITION COIL C PRIMARY CIRCUIT",
"P1355 IGNITION COIL D PRIMARY CIRCUIT",
"P1356 IGNITION DIAGNOSTIC MONITOR INDICATES ENGINE NOT TURNING",
"P1357 IGNITION DIAGNOSTIC MONITOR PULSEWIDTH NOT DEFINED",
"P1358 IGNITION DIAGNOSTIC MONITOR SIGNAL OUT OF SELF TEST RANGE (NO CPU OK)",
"P1359 SPARK OUTPUT CIRCUIT",
"P1360 IGNITION COIL A SECONDARY CIRCUIT",
"P1361 IGNITION COIL B SECONDARY CIRCUIT",
"P1362 IGNITION COIL C SECONDARY CIRCUIT",
"P1363 IGNITION COIL D SECONDARY CIRCUIT",
"P1364 IGNITION COIL PRIMARY CIRCUIT",
"P1365 IGNITION COIL SECONDARY CIRCUIT",
"P1366 IGNITION SPARE",
"P1367 IGNITION SPARE",
"P1368 IGNITION SPARE",
"P1369 ENGINE TEMPERATURE LIGHT CIRCUIT",
"P1370 INSUFFICIENT RPM INCREASE DURING SPARK TEST",
"P1371 IGNITION COIL - CYLINDER 1 - EARLY ACTIVATION FAULT",
"P1372 IGNITION COIL - CYLINDER 2 - EARLY ACTIVATION FAULT",
"P1373 IGNITION COIL - CYLINDER 3 - EARLY ACTIVATION FAULT",
"P1374 IGNITION COIL - CYLINDER 4 - EARLY ACTIVATION FAULT",
"P1375 IGNITION COIL - CYLINDER 5 - EARLY ACTIVATION FAULT",
"P1376 IGNITION COIL - CYLINDER 6 - EARLY ACTIVATION FAULT",
"P1377 INJECTOR OVERVOLTAGE SHUT-DOWN",
"P1378 FUEL INJECTOR CONTROL MODULE SYSTEM VOLTAGE LOW",
"P1379 FUEL INJECTOR CONTROL MODULE SYSTEM VOLTAGE HIGH",
"P1380 CAMSHAFT POSITION ACTUATOR CIRCUIT (BANK 1) (SEE P0010)",
"P1381 CAMSHAFT POSITION TIMING OVER ADVANCED (BANK 1) (SEE P0011)",
"P1382 CAMSHAFT POSITION TIMING SOLENOID #1 CIRCUIT",
"P1383 CAMSHAFT POSITION TIMING OVER RETARDED (BANK 1) (SEE P0012)",
"P1384 VARIABLE VALVE TIMING SOLENOID A CIRCUIT",
"P1385 CAMSHAFT POSITION ACTUATOR CIRCUIT (BANK 2) (SEE P0013)",
"P1386 CAMSHAFT POSITION TIMING OVER ADVANCED (BANK 2) (SEE P0014)",
"P1387 CAMSHAFT POSITION TIMING SOLENOID #2 CIRCUIT (SEE P0015)",
"P1388 CAMSHAFT POSITION TIMING OVER RETARDED (BANK 2) (SEE P0022)",
"P1389 GLOW PLUG CIRCUIT HIGH SIDE, LOW INPUT",
"P1390 OCTANE ADJUST SERVICE PIN IN USE/CIRCUIT OPEN",
"P1391 GLOW PLUG CIRCUIT LOW INPUT (BANK 1)",
"P1392 GLOW PLUG CIRCUIT HIGH INPUT (BANK 1)",
"P1393 GLOW PLUG CIRCUIT LOW INPUT (BANK 2)",
"P1394 GLOW PLUG CIRCUIT HIGH INPUT (BANK 2)",
"P1395 GLOW PLUG MONITOR FAULT (BANK 1)",
"P1396 GLOW PLUG MONITOR FAULT (BANK 2)",
"P1397 SYSTEM VOLTAGE OUT OF SELF TEST RANGE",
"P1398 VARIABLE VALVE TIMING SOLENOID B CIRCUIT HIGH INPUT",
"P1399 GLOW PLUG CIRCUIT HIGH SIDE, HIGH INPUT",
"P1400 DIFFERENTIAL PRESSURE FEEDBACK EGR CIRCUIT LOW INPUT",
"P1401 DIFFERENTIAL PRESSURE FEEDBACK EGR CIRCUIT HIGH INPUT",
"P1402 EXHAUST GAS RECIRCULATION METERING ORIFICE RESTRICTED",
"P1403 DIFFERENTIAL PRESSURE FEEDBACK SENSOR HOSES REVERSED",
"P1404 EGR TEMPERATURE SENSOR CIRCUIT",
"P1405 DIFFERENTIAL PRESSURE FEEDBACK SENSOR UPSTREAM HOSE OFF OR PLUGGED",
"P1406 DIFFERENTIAL PRESSURE FEEDBACK SENSOR DOWNSTREAM HOSE OFF OR PLUGGED",
"P1407 EXHAUST GAS RECIRCULATION NO FLOW DETECTED",
"P1408 EXHAUST GAS RECIRCULATION FLOW OUT OF SELF TEST RANGE",
"P1409 EGR VACUUM REGULATOR SOLENOID CIRCUIT",
"P1410 AIR CLEANER INLET CONTROL CIRCUIT",
"P1411 SECONDARY AIR INJECTION INCORRECT DOWNSTREAM FLOW DETECTED",
"P1412 EXHAUST GAS RECIRCULATION VALVE FROZEN",
"P1413 SECONDARY AIR INJECTION MONITOR CIRCUIT LOW INPUT (SEE P2257)",
"P1414 SECONDARY AIR INJECTION MONITOR CIRCUIT HIGH INPUT (SEE P2258)",
"P1415 AIR PUMP CIRCUIT",
"P1416 PORT AIR CIRCUIT",
"P1417 PORT AIR RELIEF CIRCUIT",
"P1418 SPLIT AIR #1 CIRCUIT",
"P1419 SPLIT AIR #2 CIRCUIT",
"P1420 CATALYST TEMPERATURE SENSOR",
"P1421 CATALYST DAMAGE",
"P1422 EXHAUST GAS IGNITION TEMPERATURE SENSOR",
"P1423 EXHAUST GAS IGNITION FUNCTIONAL TEST",
"P1424 EXHAUST GAS IGNITION PLUG PRIMARY",
"P1425 EXHAUST GAS IGNITION PLUG SECONDARY",
"P1426 EXHAUST GAS IGNITION MINI-MAF SENSOR OUT OF RANGE",
"P1427 EXHAUST GAS IGNITION MINI-MAF SENSOR CIRCUIT SHORTED",
"P1428 EXHAUST GAS IGNITION MINI-MAF SENSOR CIRCUIT OPEN",
"P1429 ELECTRIC AIR PUMP PRIMARY",
"P1430 ELECTRIC AIR PUMP SECONDARY",
"P1431 MISFIRE MONITOR DISABLED, UNABLE TO LEARN WHEEL PROFILE (TO BE DELETED, SEE P0315)",
"P1432 THERMOSTAT HEATER CONTROL CIRCUIT",
"P1433 A/C REFRIGERANT TEMPERATURE CIRCUIT LOW",
"P1434 A/C REFRIGERANT TEMPERATURE CIRCUIT HIGH",
"P1435 A/C REFRIGERANT TEMPERATURE CIRCUIT RANGE/PERFORMANCE",
"P1436 A/C EVAPORATOR AIR TEMPERATURE CIRCUIT LOW (SEE P0537)",
"P1437 A/C EVAPORATOR AIR TEMPERATURE CIRCUIT HIGH (SEE P0538)",
"P1438 A/C EVAPORATOR AIR TEMPERATURE CIRCUIT RANGE/PERFORMANCE",
"P1439 FLOOR TEMP SWITCH CIRCUIT",
"P1440 PURGE VALVE STUCK OPEN",
"P1441 ELC SYSTEM 1",
"P1442 EVAPORATIVE EMISSION SYSTEM CONTROL LEAK DETECTED",
"P1443 EVAPORATIVE EMISSION SYSTEM CONTROL VALVE  (LOW/NO FLOW)",
"P1444 EVAPORATIVE EMISSION SYSTEM PURGE FLOW SENSOR CIRCUIT LOW INPUT",
"P1445 EVAPORATIVE EMISSION SYSTEM PURGE FLOW SENSOR CIRCUIT HIGH INPUT",
"P1446 EVAPORATIVE VACUUM SOLENOID CIRCUIT",
"P1447 ELC SYSTEM CLOSURE VALVE FLOW",
"P1448 ELC SYSTEM 2",
"P1449 EVAPORATIVE CHECK SOLENOID CIRCUIT",
"P1450 UNABLE TO BLEED UP FUEL TANK VACUUM",
"P1451 EVAPORATIVE EMISSION SYSTEM VENT CONTROL CIRCUIT",
"P1452 UNABLE TO BLEED UP FUEL TANK VACUUM",
"P1453 FUEL TANK PRESSURE RELIEF VALVE MALFUNCTION",
"P1454 EVAPORATIVE EMISSION SYSTEM VACUUM TEST",
"P1455 EVAPORATIVE EMISSION SYSTEM CONTROL LEAK DETECTED (GROSS LEAK/NO FLOW)",
"P1456 FUEL TANK TEMPERATURE SENSOR CIRCUIT",
"P1457 UNABLE TO PULL FUEL TANK VACUUM",
"P1458 IGNITION TIMING CONTROL SOLENOID",
"P1459 A/C RECIRCULATION SWITCH OUT OF SELF TEST RANGE",
"P1460 WIDE OPEN THROTTLE A/C CUTOUT CIRCUIT (SEE P0645)",
"P1461 A/C PRESSURE SENSOR CIRCUIT HIGH INPUT",
"P1462 A/C PRESSURE SENSOR CIRCUIT LOW INPUT",
"P1463 A/C PRESSURE SENSOR INSUFFICIENT PRESSURE CHANGE",
"P1464 A/C DEMAND OUT OF SELF TEST RANGE",
"P1465 A/C RELAY CIRCUIT",
"P1466 A/C REFRIGERANT TEMPERATURE SENSOR CIRCUIT",
"P1467 A/C COMPRESSOR TEMPERATURE SENSOR",
"P1468 SSPOD OPEN CIRCUIT OR CLOSED CIRCUIT",
"P1469 RAPID A/C CYCLING (SEE P0534)",
"P1470 A/C CYCLING PERIOD TOO SHORT",
"P1471 ELECTRODRIVE FAN 1 OPERATIONAL FAILURE (DRIVER SIDE)",
"P1472 ELECTRODRIVE FAN 2 OPERATIONAL FAILURE (PASSENGER SIDE)",
"P1473 FAN CIRCUIT OPEN (VLCM)",
"P1474 FAN CONTROL PRIMARY CIRCUIT",
"P1475 FAN RELAY (LOW) CIRCUIT",
"P1476 FAN RELAY (HIGH) CIRCUIT",
"P1477 ADDITIONAL FAN RELAY CIRCUIT (SEE P0482)",
"P1478 COOLING FAN DRIVER",
"P1479 HIGH FAN CONTROL PRIMARY CIRCUIT",
"P1480 FAN SECONDARY LOW WITH LOW FAN ON",
"P1481 FAN SECONDARY LOW WITH HIGH FAN ON",
"P1482 SCP",
"P1483 FAN CIRCUIT SHORTED TO GROUND (VLCM)",
"P1484 FAN DRIVER CIRCUIT OPEN TO POWER GROUND (VLCM)",
"P1485 EGRV CIRCUIT",
"P1486 EGRA CIRCUIT",
"P1487 EXHAUST GAS RECIRCULATION CHECK SOLENOID CIRCUIT",
"P1488 EXHAUST (MUFFLER) BYPASS CONTROL CIRCUIT",
"P1490 SECONDARY AIR RELIEF SOLENOID CIRCUIT",
"P1491 SECONDARY SWITCH SOLENOID CIRCUIT",
"P1492 APLSOL SOLENOID CIRCUIT",
"P1493 RCNT SOLENOID CIRCUIT",
"P1494 SPCUT SOLENOID CIRCUIT",
"P1495 TCSPL SOLENOID CIRCUIT",
"P1496 EGR STEPPER MOTOR 1 CONTROL CIRCUIT LOW/HIGH",
"P1497 EGR STEPPER MOTOR 2 CONTROL CIRCUIT LOW/HIGH",
"P1498 EGR STEPPER MOTOR 3 CONTROL CIRCUIT LOW/HIGH",
"P1499 EGR STEPPER MOTOR 4 CONTROL CIRCUIT LOW/HIGH",
"P1500 VEHICLE SPEED SENSOR",
"P1501 VEHICLE SPEED SENSOR OUT OF SELF TEST RANGE",
"P1502 VEHICLE SPEED SENSOR INTERMITTENT",
"P1503 AUXILIARY SPEED SENSOR",
"P1504 IDLE AIR CONTROL CIRCUIT (SEE P0511)",
"P1505 IDLE AIR CONTROL SYSTEM AT ADAPTIVE CLIP",
"P1506 IDLE AIR CONTROL OVERSPEED ERROR (SEE P0507)",
"P1507 IDLE AIR CONTROL UNDERSPEED ERROR (SEE P0506)",
"P1508 IDLE UP SOLENOID 1 CIRCUIT",
"P1509 IDLE UP SOLENOID 2 CIRCUIT",
"P1510 IDLE SIGNAL CIRCUIT",
"P1511 IDLE SWITCH (ELECTRIC CONTROL THROTTLE) CIRCUIT",
"P1512 INTAKE MANIFOLD RUNNER CONTROL STUCK CLOSED (BANK 1) (SEE P2006)",
"P1513 INTAKE MANIFOLD RUNNER CONTROL STUCK CLOSED (BANK 2) (SEE P2007)",
"P1514 HIGH LOAD NEUTRAL/DRIVE FAULT",
"P1515 ELECTRIC CURRENT CIRCUIT",
"P1516 INTAKE MANIFOLD RUNNER CONTROL INPUT ERROR (BANK 1) (SEE P2014)",
"P1517 INTAKE MANIFOLD RUNNER CONTROL INPUT ERROR (BANK 2) (SEE P2019)",
"P1518 INTAKE MANIFOLD RUNNER CONTROL STUCK OPEN (BANK 1) (SEE P2004)",
"P1519 INTAKE MANIFOLD RUNNER CONTROL STUCK CLOSED (BANK 1) (SEE P2006)",
"P1520 INTAKE MANIFOLD RUNNER CONTROL  CIRCUIT (SEE P2008)",
"P1521 VARIABLE RESONANCE INDUCTION SYSTEM SOLENOID #1 CIRCUIT",
"P1522 VARIABLE RESONANCE INDUCTION SYSTEM SOLENOID #2 CIRCUIT",
"P1523 IVC SOLENOID CIRCUIT",
"P1524 VARIABLE INTAKE SOLENOID CIRCUIT",
"P1525 AIR BYPASS VALVE",
"P1526 AIR BYPASS SYSTEM",
"P1527 BYPASS AIR SOLENOID (ACCELERATE WARM-UP) CIRCUIT",
"P1528 SUBSIDIARY THROTTLE VALVE SOLENOID CIRCUIT",
"P1529 SCAIR SOLENOID CIRCUIT",
"P1530 A/C CLUTCH CIRCUIT OPEN (VLCM)",
"P1531 INVALID TEST - ACCELERATOR PEDAL MOVEMENT",
"P1532 INTAKE MANIFOLD COMMUNICATION CONTROL  CIRCUIT (BANK 2) (SEE P0663)",
"P1533 AIR ASSISTED INJECTOR CIRCUIT",
"P1534 RESTRAINT DEPLOYMENT INDICATOR CIRCUIT",
"P1535 BLOWER FAN SPEED CIRCUIT RANGE/PERFORMANCE",
"P1536 PARKING BRAKE SWITCH CIRCUIT",
"P1537 INTAKE MANIFOLD RUNNER CONTROL STUCK OPEN (BANK 1) (SEE P2004)",
"P1538 INTAKE MANIFOLD RUNNER CONTROL STUCK OPEN (BANK 2) (SEE P2005)",
"P1539 A/C CLUTCH CIRCUIT OVERCURRENT/SHORT (VLCM)",
"P1540 AIR BYPASS VALVE CIRCUIT",
"P1541 INTAKE MANIFOLD RUNNER CONTROL  CIRCUIT RANGE/PERFORMANCE",
"P1542 PRIMARY PCM ID CIRCUIT (DUAL PCM APPLICATION)",
"P1543 ENGINE COOLANT HEATER A CONTROL CIRCUIT",
"P1544 ENGINE COOLANT HEATER B CONTROL CIRCUIT",
"P1545 EXHAUST GAS RECIRCULATION HIGH SIDE CONTROL CIRCUIT / OPEN",
"P1546 EXHAUST GAS RECIRCULATION HIGH SIDE CONTROL CIRCUIT LOW",
"P1547 EXHAUST GAS RECIRCULATION HIGH SIDE CONTROL CIRCUIT HIGH",
"P1549 INTAKE MANIFOLD COMMUNICATION CONTROL  CIRCUIT (BANK 1) (SEE P0660)",
"P1550 POWER STEERING PRESSURE SENSOR OUT OF SELF TEST RANGE",
"P1551 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 1",
"P1552 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 2",
"P1553 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 3",
"P1554 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 4",
"P1555 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 5",
"P1556 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 6",
"P1557 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 7",
"P1558 INJECTOR CIRCUIT RANGE/PERFORMANCE - CYLINDER 8",
"P1562 PCM B+ VOLTAGE LOW (KAM POWER)",
"P1563 INJECTION PUMP CONTROL MODULE REQUESTING ENGINE STOP",
"P1564 INJECTION PUMP CONTROL MODULE REQUESTING REDUCED FUELING",
"P1565 SPEED CONTROL COMMAND SWITCH OUT OF RANGE HIGH",
"P1566 SPEED CONTROL COMMAND SWITCH OUT OF RANGE LOW",
"P1567 SPEED CONTROL OUTPUT CIRCUIT",
"P1568 SPEED CONTROL UNABLE TO HOLD SPEED",
"P1569 INTAKE MANIFOLD RUNNER CONTROL  CIRCUIT LOW (SEE P0661)",
"P1570 INTAKE MANIFOLD RUNNER CONTROL  CIRCUIT HIGH (SEE P0662)",
"P1571 BRAKE SWITCH",
"P1572 BRAKE PEDAL SWITCH CIRCUIT",
"P1573 THROTTLE POSITION NOT AVAILABLE",
"P1574 THROTTLE POSITION SENSOR OUTPUTS DISAGREE",
"P1575 PEDAL POSITION OUT OF SELF TEST RANGE",
"P1576 PEDAL POSITION NOT AVAILABLE",
"P1577 PEDAL POSITION SENSOR OUTPUTS DISAGREE",
"P1578 ETC POWER LESS THAN DEMAND",
"P1579 ETC IN POWER LIMITING MODE",
"P1580 ELECTRONIC THROTTLE MONITOR PCM OVERRIDE",
"P1581 ELECTRONIC THROTTLE MONITOR MALFUNCTION",
"P1582 ELECTRONIC THROTTLE MONITOR DATA AVAILABLE",
"P1583 ELECTRONIC THROTTLE MONITOR CRUISE DISABLEMENT",
"P1584 THROTTLE CONTROL DETECTED ETB MALFUNCTION",
"P1585 THROTTLE CONTROL MALFUNCTION",
"P1586 ELECTRONIC THROTTLE TO PCM COMMUNICATION ERROR",
"P1587 THROTTLE CONTROL MODULATED COMMAND MALFUNCTION",
"P1588 THROTTLE CONTROL DETECTED LOSS OF RETURN SPRING",
"P1589 THROTTLE CONTROL UNABLE TO CONTROL TO DESIRED THROTTLE ANGLE",
"P1600 LOSS OF KAM POWER, CIRCUIT OPEN",
"P1601 ECM/TCM SERIAL COMMUNICATION ERROR",
"P1602 IMMOBILIZER/ECM COMMUNICATION ERROR",
"P1603 ID NUMBER UNREGISTERED",
"P1604 CODE WORD UNREGISTERED",
"P1605 KEEP ALIVE MEMORY TEST FAILURE",
"P1606 ECM CONTROL RELAY OUTPUT CIRCUIT",
"P1607 MIL OUTPUT CIRCUIT",
"P1608 WATCHDOG MALFUNCTION",
"P1609 DIAGNOSTIC LAMP DRIVER",
"P1610 INTERACTIVE REPROGRAMMING CODE - REPLACE MODULE (USD WITH P1615/17/19/20)",
"P1611 INTERACTIVE REPROGRAMMING CODE - DIAGNOSE FURTHER (USED WITH P1616/18)",
"P1612 INTERACTIVE REPROGRAMMING CODE - REPEAT TEST - ENGINE IS CRANKING",
"P1613 INTERACTIVE REPROGRAMMING CODE - TBD",
"P1614 INTERACTIVE REPROGRAMMING CODE - TBD",
"P1615 INTERACTIVE REPROGRAMMING CODE - ERASE ERROR",
"P1616 INTERACTIVE REPROGRAMMING CODE - ERASE ERROR, LOW VOLTAGE",
"P1617 INTERACTIVE REPROGRAMMING CODE - BLOCK PROGRAM ERROR",
"P1618 INTERACTIVE REPROGRAMMING CODE - BLOCK PROGRAM ERROR, LOW VOLTAGE",
"P1619 INTERACTIVE REPROGRAMMING CODE - TOTAL CHECKSUM ERROR",
"P1620 INTERACTIVE REPROGRAMMING CODE - OVERLAY CHECKSUM ERROR",
"P1621 IMMOBILIZER CODE WORDS DO NOT MATCH",
"P1622 IMMOBILIZER ID DOES NOT MATCH",
"P1623 IMMOBILIZER CODE WORD/ID NUMBER WRITE FAILURE",
"P1624 ANTI-THEFT SYSTEM",
"P1625 FAN DRIVER CIRCUIT OPEN TO POWER B+ (VLCM)",
"P1626 A/C CIRCUIT OPEN TO POWER B+ (VLCM)",
"P1627 MODULE SUPPLY VOLTAGE OUT OF RANGE",
"P1628 MODULE IGNITION SUPPLY INPUT",
"P1629 INTERNAL VOLTAGE REGULATOR",
"P1630 INTERNAL VREF",
"P1631 MAIN RELAY (POWER HOLD)",
"P1632 SMART ALTERNATOR FAULTS SENSOR / CIRCUIT",
"P1633 KEEP ALIVE POWER VOLTAGE TOO LOW",
"P1634 DATA OUTPUT LINK CIRCUIT",
"P1635 TIRE/AXLE OUT OF ACCEPTABLE RANGE",
"P1636 INDUCTIVE SIGNATURE CHIP COMMUNICATION ERROR",
"P1637 CAN LINK ECM/ABS CONTROL MODULE CIRCUIT/NETWORK",
"P1638 CAN LINK ECM/INSTM CIRCUIT/NETWORK",
"P1639 VEHICLE ID BLOCK CORRUPTED, NOT PROGRAMMED",
"P1640 POWERTRAIN DTCS AVAILABLE IN ANOTHER CONTROL MODULE (REF. PID 0946)",
"P1641 FUEL PUMP PRIMARY CIRCUIT",
"P1642 CAN LINK CIRCUIT",
"P1643 CAN LINK ENGINE CONTROL MODULE/TRANSMISSION CONTROL MODULE CIRCUIT/NETWORK",
"P1644 FUEL PUMP SPEED CONTROL CIRCUIT",
"P1645 FUEL PUMP RESISTOR SWITCH CIRCUIT",
"P1646 LINEAR O2 SENSOR CONTROL CHIP (BANK 1)",
"P1647 LINEAR O2 SENSOR CONTROL CHIP (BANK 2)",
"P1648 KNOCK SENSOR INPUT CHIP",
"P1649 FUEL INJECTION PUMP MODULE",
"P1650 POWER STEERING PRESSURE SWITCH OUT OF SELF TEST RANGE",
"P1651 POWER STEERING PRESSURE SWITCH INPUT",
"P1652 IDLE AIR CONTROL MONITOR DISABLED BY PSPS FAILED ON",
"P1653 POWER STEERING OUTPUT CIRCUIT",
"P1654 RECIRCULATION OVERRIDE CIRCUIT",
"P1655 STARTER DISABLE CIRCUIT",
"P1656 CAN LINK PCM/PCM CIRCUIT/NETWORK",
"P1657 CAN LINK CHIP MALFUNCTION",
"P1658 INJECTION PUMP CONTROL MODULE SYSTEM VOLTAGE",
"P1659 INJECTION PUMP CONTROL MODULE POWER CIRCUIT",
"P1660 OUTPUT CIRCUIT CHECK CIRCUIT HIGH INPUT",
"P1661 OUTPUT CIRCUIT CHECK CIRCUIT LOW INPUT",
"P1662 EDU_EN OUTPUT CIRCUIT",
"P1663 FUEL DEMAND COMMAND SIGNAL OUTPUT CIRCUIT",
"P1664 INJECTION PUMP CONTROL MODULE MALFUNCTION",
"P1665 INJECTION PUMP CONTROL MODULE COMMUNICATIONS",
"P1666 INJECTION PUMP CONTROL MODULE/ECM CRANK REFERENCE SYNCHRONIZATION",
"P1667 CYLINDER ID CIRCUIT",
"P1668 PCM/IDM COMMUNICATIONS ERROR",
"P1669 INJECTION PUMP CONTROL MODULE MONITORING ECM FAULT",
"P1670 ELECTRONIC FEEDBACK SIGNAL NOT DETECTED",
"P1671 SECONDARY FUEL PUMP RELAY",
"P1672 CAN LINK ECM / SUSPENSION CONTROL MODULE CIRCUIT/NETWORK",
"P1673 ABS LAMP CONTROL CIRCUIT",
"P1674 CONTROL MODULE SOFTWARE CORRUPTED",
"P1680 METERING OIL PUMP FAILURE",
"P1681 METERING OIL PUMP FAILURE",
"P1682 METERING OIL PUMP FAILURE",
"P1683 METERING OIL PUMP TEMPERATURE SENSOR CIRCUIT",
"P1684 METERING OIL PUMP POSITION SENSOR CIRCUIT",
"P1685 METERING OIL PUMP STEPPING MOTOR CONT. CIRCUIT",
"P1686 METERING OIL PUMP STEPPING MOTOR CONT. CIRCUIT",
"P1687 METERING OIL PUMP STEPPING MOTOR CONT. CIRCUIT",
"P1688 METERING OIL PUMP STEPPING MOTOR CONT. CIRCUIT",
"P1689 OIL PRESSURE CONTROL SOLENOID CIRCUIT",
"P1690 WASTEGATE SOLENOID CIRCUIT",
"P1691 TURBO PRESSURE CONTROL SOLENOID CIRCUIT",
"P1692 TURBO CONTROL SOLENOID CIRCUIT",
"P1693 TURBO CHARGE CONTROL CIRCUIT",
"P1694 TURBO CHARGE RELIEF CIRCUIT",
"P1695 CAN LINK INJECTION PUMP CONTROL MODULE/ENGINE CONTROL MODULE",
"P1696 CAN LINK ENGINE CONTROL MODULE/CRUISE CONTROL MODULE CIRCUIT/NETWORK",
"P1697 CRUISE CONTROL DISTANCE-CONTROL INPUT CIRCUIT",
"P1698 COLD START FUEL PUMP PRIMARY CIRCUIT     (BRAZIL ETHANOL VEHICLES ONLY)",
"P1699 CAN LINK ECM / CLIMATE CONTROL MODULE",
"P1700 TRANSMISSION INDETERMINATE FAILURE (FAILED TO NEUTRAL)",
"P1701 REVERSE ENGAGEMENT ERROR",
"P1702 TRANSMISSION RANGE SENSOR CIRCUIT INTERMITTENT",
"P1703 BRAKE SWITCH OUT OF SELF TEST RANGE",
"P1704 TRANSMISSION RANGE CIRCUIT NOT INDICATING PARK/NEUTRAL DURING SELF TEST",
"P1705 TRANSMISSION RANGE CIRCUIT NOT INDICATING PARK/NEUTRAL DURING SELF TEST",
"P1706 HIGH VEHICLE SPEED OBSERVED IN PARK",
"P1707 TRANSFER CASE NEUTRAL INDICATOR HARD FAULT PRESENT",
"P1708 CLUTCH SWITCH CIRCUIT",
"P1709 PARK NEUTRAL POSITION SWITCH OUT OF SELF TEST RANGE",
"P1710 TRANSMISSION CONTROL MODULE SOLENOID/INTERNAL GROUND CIRCUIT",
"P1711 TRANSMISSION FLUID TEMPERATURE SENSOR OUT OF SELF TEST RANGE",
"P1712 TRANSMISSION TORQUE REDUCTION REQUEST SIGNAL",
"P1713 TRANSMISSION FLUID TEMPERATURE SENSOR IN RANGE FAILURE (< 50 DEG F)",
"P1714 SHIFT SOLENOID A INDUCTIVE SIGNATURE",
"P1715 SHIFT SOLENOID B INDUCTIVE SIGNATURE",
"P1716 SHIFT SOLENOID C INDUCTIVE SIGNATURE",
"P1717 SHIFT SOLENOID D INDUCTIVE SIGNATURE",
"P1718 TRANSMISSION FLUID TEMPERATURE SENSOR IN RANGE FAILURE (> 250 DEG F)",
"P1719 ENGINE TORQUE SIGNAL",
"P1720 VEHICLE SPEED (METER) CIRCUIT",
"P1721 GEAR 1 INCORRECT RATIO",
"P1722 STALL SPEED",
"P1723 GEAR 3 INCORRECT RATIO",
"P1724 GEAR 4 INCORRECT RATIO",
"P1725 INSUFFICIENT ENGINE SPEED INCREASE DURING SELF TEST",
"P1726 INSUFFICIENT ENGINE SPEED DECREASE DURING SELF TEST",
"P1727 COAST CLUTCH SOLENOID INDUCTIVE SIGNATURE",
"P1728 TRANSMISSION SLIP",
"P1729 4X4L SWITCH",
"P1730 GEAR CONTROL MALFUNCTION 2,3,5",
"P1731 1-2 SHIFT MALFUNCTION",
"P1732 2-3 SHIFT MALFUNCTION",
"P1733 3-4 SHIFT MALFUNCTION",
"P1734 GEAR CONTROL MALFUNCTION",
"P1735 FIRST GEAR SWITCH CIRCUIT FAILURE",
"P1736 SECOND GEAR SWITCH CIRCUIT FAILURE",
"P1737 LOCKUP SOLENOID",
"P1738 SHIFT TIME ERROR",
"P1739 SLIP SOLENOID",
"P1740 TORQUE CONVERTER CLUTCH SOLENOID INDUCTIVE SIGNATURE",
"P1741 TORQUE CONVERTER CLUTCH SOLENOID CONTROL ERROR",
"P1742 TORQUE CONVERTER CLUTCH SOLENOID CIRCUIT FAILED ON",
"P1743 TORQUE CONVERTER CLUTCH SOLENOID CIRCUIT FAILED ON",
"P1744 TORQUE CONVERTER CLUTCH SOLENOID CIRCUIT PERFORMANCE",
"P1745 LINE PRESSURE SOLENOID",
"P1746 PRESSURE CONTROL SOLENOID A OPEN CIRCUIT (SEE P0960)",
"P1747 PRESSURE CONTROL SOLENOID A SHORT CIRCUIT (SEE P0962)",
"P1748 PRESSURE CONTROL SOLENOID A",
"P1749 PRESSURE CONTROL SOLENOID A FAILED LOW",
"P1750 CLUTCH ADAPTIVE LEARNING NOT DONE",
"P1751 SHIFT SOLENOID A PERFORMANCE",
"P1752 SHIFT SOLENOID A CIRCUIT SHORT",
"P1753 MAX ADAPTED EPC PRES(2ND GEAR)",
"P1754 COAST CLUTCH SOLENOID CIRCUIT",
"P1755 MAX ADAPTED EPC PRES(3RD GEAR)",
"P1756 SHIFT SOLENOID B PERFORMANCE",
"P1757 SHIFT SOLENOID B CIRCUIT SHORT",
"P1758 PRESSURE SOLENOID CONTROL SYSTEM INCORRECT CURRENT",
"P1759 2-4 BRAKE FAILSAFE VALVE MALFUNCTION",
"P1760 PRESSURE CONTROL SOLENOID A SHORT CIRCUIT INTERMITTENT (SEE P0963)",
"P1761 SHIFT SOLENOID C PERFORMANCE",
"P1762 OVERDRIVE BAND FAILED OFF",
"P1763 LOW AND REVERSE BRAKE PRESSURE SWITCH CIRCUIT",
"P1764 LOW AND REVERSE BRAKE FAILSAFE VALVE MALFUNCTION",
"P1765 TIMING SOLENOID CIRCUIT",
"P1766 SHIFT SOLENOID D PERFORMANCE",
"P1767 TORQUE CONVERTER CLUTCH CIRCUIT",
"P1768 PERFORMANCE/NORMAL/WINTER MODE INPUT",
"P1769 AG4 TRANSMISSION TORQUE MODULATION FAULT (VW TRANS)",
"P1770 CLUTCH SOLENOID CIRCUIT",
"P1771 SHIFT SOLENOID E PERFORMANCE",
"P1772 THROTTLE POSITION SENSOR CIRCUIT LOW INPUT",
"P1773 CAN LINK PCM/FUEL FIRED HEATER MALFUNCTION",
"P1774 CAN LINK GEAR SHIFT MODULE / TCM",
"P1775 TORQUE DOWN SIGNAL #1 CIRCUIT",
"P1776 TORQUE DOWN SIGNAL #2 CIRCUIT",
"P1777 TORQUE DOWN RESPONSE SIGNAL CIRCUIT",
"P1778 TRANSMISSION REVERSE I/P CIRCUIT",
"P1779 TRANSMISSION CONTROL INDICATOR LIGHT CIRCUIT",
"P1780 TRANSMISSION CONTROL SWITCH (O/D CANCEL) CIRCUIT OUT OF SELF TEST RANGE",
"P1781 4X4L CIRCUIT OUT OF SELF TEST RANGE",
"P1782 PERFORMANCE/ECONOMY SWITCH CIRCUIT OUT OF SELF TEST RANGE",
"P1783 TRANSMISSION OVERTEMPERATURE CONDITION",
"P1784 TRANSMISSION MECHANICAL FAILURE - FIRST AND REVERSE",
"P1785 TRANSMISSION MECHANICAL FAILURE - FIRST AND SECOND",
"P1786 3-2 DOWNSHIFT ERROR",
"P1787 2-1 DOWNSHIFT ERROR",
"P1788 PRESSURE CONTROL SOLENOID B OPEN CIRCUIT (SEE P0964)",
"P1789 PRESSURE CONTROL SOLENOID B SHORT CIRCUIT (SEE P0966)",
"P1790 TP (MECHANICAL) CIRCUIT",
"P1791 TP (ELECTRIC) CIRCUIT",
"P1792 BAROMETER PRESSURE CIRCUIT",
"P1793 INTAKE AIR VOLUME CIRCUIT",
"P1794 BATTERY VOLTAGE CIRCUIT",
"P1795 INCONSISTENT CAN LEVEL",
"P1796 CAN CONTROLLER CIRCUIT (BUS OFF)",
"P1797 CAN TCM/ECM CIRCUIT MALFUNCTION",
"P1798 CAN TCM/INST CIRCUIT MALFUNCTION",
"P1799 CAN TCM/ABS CIRCUIT MALFUNCTION",
"P1800 TRANSMISSION CLUTCH INTERLOCK SAFETY SWITCH CIRCUIT FAILURE",
"P1801 TRANSMISSION CLUTCH INTERLOCK SAFETY SWITCH OPEN CIRCUIT",
"P1802 TRANSMISSION CLUTCH INTERLOCK SAFETY SWITCH SHORT CIRCUIT TO BATTERY",
"P1803 TRANSMISSION CLUTCH INTERLOCK SAFETY SWITCH SHORT CIRCUIT TO GROUND",
"P1804 4-WHEEL DRIVE HIGH INDICATOR CIRCUIT FAILURE",
"P1805 4-WHEEL DRIVE HIGH INDICATOR OPEN CIRCUIT",
"P1806 4-WHEEL DRIVE HIGH INDICATOR SHORT CIRCUIT TO BATTERY",
"P1807 4-WHEEL DRIVE HIGH INDICATOR SHORT CIRCUIT TO GROUND",
"P1808 4-WHEEL DRIVE LOW INDICATOR CIRCUIT FAILURE",
"P1809 4-WHEEL DRIVE LOW INDICATOR OPEN CIRCUIT",
"P1810 4-WHEEL DRIVE LOW INDICATOR SHORT CIRCUIT TO BATTERY",
"P1811 4-WHEEL DRIVE LOW INDICATOR SHORT CIRCUIT TO GROUND",
"P1812 4-WHEEL DRIVE MODE SELECT CIRCUIT FAILURE",
"P1813 4-WHEEL DRIVE MODE SELECT OPEN CIRCUIT",
"P1814 4-WHEEL DRIVE MODE SELECT SHORT CIRCUIT TO BATTERY",
"P1815 4-WHEEL DRIVE MODE SELECT SHORT CIRCUIT TO GROUND",
"P1816 TRANSMISSION NEUTRAL SAFETY SWITCH CIRCUIT FAILURE",
"P1817 TRANSMISSION NEUTRAL SAFETY SWITCH OPEN CIRCUIT",
"P1818 TRANSMISSION NEUTRAL SAFETY SWITCH SHORT CIRCUIT TO BATTERY",
"P1819 TRANSMISSION NEUTRAL SAFETY SWITCH SHORT CIRCUIT TO GROUND",
"P1820 TRANSFER CASE CLOCKWISE SHIFT RELAY COIL CIRCUIT FAILURE",
"P1821 TRANSFER CASE CLOCKWISE SHIFT RELAY COIL OPEN CIRCUIT",
"P1822 TRANSFER CASE CLOCKWISE SHIFT RELAY COIL SHORT CIRCUIT TO BATTERY",
"P1823 TRANSFER CASE CLOCKWISE SHIFT RELAY COIL SHORT CIRCUIT TO GROUND",
"P1824 4-WHEEL DRIVE CLUTCH RELAY CIRCUIT FAILURE",
"P1825 4-WHEEL DRIVE CLUTCH RELAY OPEN CIRCUIT",
"P1826 4-WHEEL DRIVE LOW CLUTCH RELAY CIRCUIT TO BATTERY",
"P1827 4-WHEEL DRIVE LOW CLUTCH RELAY CIRCUIT TO GROUND",
"P1828 TRANSFER CASE COUNTER CLOCKWISE SHIFT RELAY COIL CIRCUIT FAILURE",
"P1829 TRANSFER CASE COUNTER CLOCKWISE SHIFT RELAY COIL OPEN CIRCUIT",
"P1830 TRANSFER CASE COUNTER CLOCKWISE SHIFT RELAY COIL SHORT CIRCUIT TO BATTERY",
"P1831 TRANSFER CASE COUNTER CLOCKWISE SHIFT RELAY COIL SHORT CIRCUIT TO GROUND",
"P1832 TRANSFER CASE DIFFERENTIAL LOCK-UP SOLENOID CIRCUIT FAILURE",
"P1833 TRANSFER CASE DIFFERENTIAL LOCK-UP SOLENOID OPEN CIRCUIT",
"P1834 TRANSFER CASE DIFFERENTIAL LOCK-UP SOLENOID SHORT CIRCUIT TO BATTERY",
"P1835 TRANSFER CASE DIFFERENTIAL LOCK-UP SOLENOID SHORT CIRCUIT TO GROUND",
"P1836 TRANSFER CASE FRONT SHAFT SPEED SENSOR CIRCUIT FAILURE",
"P1837 TRANSFER CASE REAR SHAFT SPEED SENSOR CIRCUIT FAILURE",
"P1838 TRANSFER CASE SHIFT MOTOR CIRCUIT FAILURE",
"P1839 TRANSFER CASE SHIFT MOTOR OPEN CIRCUIT",
"P1840 TRANSFER CASE SHIFT MOTOR SHORT CIRCUIT TO BATTERY",
"P1841 TRANSFER CASE SHIFT MOTOR SHORT CIRCUIT TO GROUND",
"P1842 TRANSFER CASE DIFFERENTIAL LOCK-UP FEEDBACK SWITCH CIRCUIT FAILURE",
"P1843 TRANSFER CASE DIFFERENTIAL LOCK-UP FEEDBACK SWITCH OPEN CIRCUIT",
"P1844 TRANSFER CASE DIFFERENTIAL LOCK-UP FEEDBACK SWITCH SHORT CIRCUIT TO BATTERY",
"P1845 TRANSFER CASE DIFFERENTIAL LOCK-UP FEEDBACK SWITCH SHORT CIRCUIT TO GROUND",
"P1846 TRANSFER CASE CONTACT PLATE 'A' CIRCUIT FAILURE",
"P1847 TRANSFER CASE CONTACT PLATE 'A' OPEN CIRCUIT",
"P1848 TRANSFER CASE CONTACT PLATE 'A' SHORT CIRCUIT TO BATTERY",
"P1849 TRANSFER CASE CONTACT PLATE 'A' SHORT CIRCUIT TO GROUND",
"P1850 TRANSFER CASE CONTACT PLATE 'B' CIRCUIT FAILURE",
"P1851 TRANSFER CASE CONTACT PLATE 'B' OPEN CIRCUIT",
"P1852 TRANSFER CASE CONTACT PLATE 'B' SHORT CIRCUIT TO BATTERY",
"P1853 TRANSFER CASE CONTACT PLATE 'B' SHORT CIRCUIT TO GROUND",
"P1854 TRANSFER CASE CONTACT PLATE 'C' CIRCUIT FAILURE",
"P1855 TRANSFER CASE CONTACT PLATE 'C' OPEN CIRCUIT",
"P1856 TRANSFER CASE CONTACT PLATE 'C' SHORT CIRCUIT TO BATTERY",
"P1857 TRANSFER CASE CONTACT PLATE 'C' SHORT CIRCUIT TO GROUND",
"P1858 TRANSFER CASE CONTACT PLATE 'D' CIRCUIT FAILURE",
"P1859 TRANSFER CASE CONTACT PLATE 'D' OPEN CIRCUIT",
"P1860 TRANSFER CASE CONTACT PLATE 'D' SHORT CIRCUIT TO BATTERY",
"P1861 TRANSFER CASE CONTACT PLATE 'D' SHORT CIRCUIT TO GROUND",
"P1862 TRANSFER CASE CONTACT PLATE POWER CIRCUIT FAILURE",
"P1863 TRANSFER CASE CONTACT PLATE POWER OPEN CIRCUIT",
"P1864 TRANSFER CASE CONTACT PLATE POWER SHORT TO BATTERY",
"P1865 TRANSFER CASE CONTACT PLATE POWER SHORT TO GROUND",
"P1866 TRANSFER CASE SYSTEM CONCERN - SERVICING REQUIRED",
"P1867 TRANSFER CASE CONTACT PLATE GENERAL CIRCUIT FAILURE",
"P1868 4-WHEEL DRIVE INDICATOR (LAMP) CIRCUIT FAILURE",
"P1869 4-WHEEL DRIVE INDICATOR (LAMP) CIRCUIT SHORT TO BATTERY",
"P1870 MECHANICAL TRANSFER CASE 4X4 SWITCH CIRCUIT FAILURE",
"P1871 MECHANICAL TRANSFER CASE 4X4 SWITCH CIRCUIT SHORT TO BATTERY",
"P1872 MECHANICAL 4-WHEEL DRIVE AXLE LOCK LAMP CIRCUIT FAILURE",
"P1873 MECHANICAL 4-WHEEL DRIVE AXLE LOCK LAMP CIRCUIT SHORT TO BATTERY",
"P1874 TRANSFER CASE HALL EFFECT SENSOR POWER CIRCUIT FAILURE",
"P1875 TRANSFER CASE HALL EFFECT SENSOR POWER CIRCUIT SHORT TO BATTERY",
"P1876 TRANSFER CASE 2-WHEEL DRIVE SOLENOID CIRCUIT FAILURE",
"P1877 TRANSFER CASE 2-WHEEL DRIVE SOLENOID CIRCUIT SHORT TO BATTERY",
"P1878 TRANSFER CASE DISENGAGED SOLENOID CIRCUIT FAILURE",
"P1879 TRANSFER CASE DISENGAGED SOLENOID OPEN CIRCUIT",
"P1880 TRANSFER CASE DISENGAGED SOLENOID SHORT TO BATTERY",
"P1881 ENGINE COOLANT LEVEL SWITCH CIRCUIT",
"P1882 ENGINE COOLANT LEVEL SWITCH CIRCUIT SHORT TO GROUND",
"P1883 ENGINE COOLANT LEVEL SWITCH CIRCUIT",
"P1884 ENGINE COOLANT LEVEL LAMP  CIRCUIT SHORT TO GROUND",
"P1885 TRANSFER CASE DISENGAGED SOLENOID SHORT TO GROUND",
"P1886 4X4 INITIALIZATION FAILURE",
"P1887 4-WHEEL DRIVE CONTROL SOLENOID CIRCUIT FAILURE",
"P1888 DIFFERENTIAL OIL TEMPERATURE SENSOR CIRCUIT FAILURE",
"P1889 OIL PRESSURE PUMP PERFORMANCE",
"P1890 4-WHEEL DRIVE MODE SELECT RETURN INPUT CIRCUIT FAILURE",
"P1891 TRANSFER CASE CONTACT PLATE GROUND RETURN OPEN CIRCUIT",
"P1892 AXLE DISCONNECT ENGAGEMENT SOLENOID CIRCUIT HIGH",
"P1893 AXLE DISCONNECT ENGAGEMENT SOLENOID CIRCUIT LOW",
"P1894 AXLE DISCONNECT DISENGAGEMENT SOLENOID CIRCUIT HIGH",
"P1895 AXLE DISCONNECT DISENGAGEMENT SOLENOID CIRCUIT LOW",
"P1896 AXLE DISCONNECT ENGAGEMENT POSITION SENSOR CIRCUIT HIGH",
"P1897 AXLE DISCONNECT ENGAGEMENT POSITION SENSOR CIRCUIT LOW",
"P1898 AXLE DISCONNECT INDICATOR CIRCUIT HIGH",
"P1899 AXLE DISCONNECT INDICATOR CIRCUIT LOW",
"P1900 OUTPUT SHAFT SPEED SENSOR CIRCUIT INTERMITTENT",
"P1901 TURBINE SHAFT SPEED SENSOR CIRCUIT INTERMITTENT",
"P1902 KICKDOWN SOLENOID RELAY CONTROL CIRCUIT (ALLISON",
"P1903 KICKDOWN SOLENOID CIRCUIT LOW VOLTAGE",
"P1904 KICKDOWN SOLENOID CIRCUIT HIGH VOLTAGE",
"P1905 CONTROL MODULE CONFIGURED FOR END-OF-LINE TEST MODE",
"P1906 KICKDOWN PULL RELAY OPEN OR SHORT CIRCUIT TO GROUND (A4LD)",
"P1907 KICKDOWN HOLD RELAY OPEN OR SHORT CIRCUIT TO GROUND (A4LD)",
"P1908 TRANSMISSION PRESSURE CONTROL SOLENOID OPEN OR SHORT (A4LD)",
"P1909 TRANSMISSION FLUID TEMPERATURE SENSOR CIRCUIT OPEN OR SHORT (A4LD)",
"P1910 REVERSE LAMP CONTROL CIRCUIT / OPEN",
"P1911 REVERSE LAMP CONTROL CIRCUIT LOW",
"P1912 REVERSE LAMP CONTROL CIRCUIT HIGH",
"P1913 SENSOR GROUND REFERENCE A CIRCUIT/OPEN",
"P1914 SENSOR GROUND REFERENCE A CIRCUIT LOW",
"P1915 SENSOR GROUND REFERENCE A CIRCUIT HIGH",
"P1916 SENSOR GROUND REFERENCE B CIRCUIT/OPEN",
"P1917 SENSOR GROUND REFERENCE B CIRCUIT LOW",
"P1918 SENSOR GROUND REFERENCE B CIRCUIT HIGH",
"P1919 ENGINE COOLANT TEMPERATURE SIGNAL",
"P1920 ENGINE SPEED SIGNAL",
"P1921 TRANSMISSION RANGE SIGNAL",
"P1922 FUEL ADDITIVE LEVEL CIRCUIT",
"P1923 FUEL ADDITIVE LEVEL CIRCUIT RANGE/PERFORMANCE",
"P1924 FUEL ADDITIVE LEVEL CIRCUIT LOW",
"P1925 FUEL ADDITIVE LEVEL CIRCUIT HIGH",
"P1926 FUEL ADDITIVE LEVEL CIRCUIT INTERMITTENT/ERRATIC",
"P1927 FUEL ADDITIVE LEVEL TOO LOW/EMPTY",
"P1928 FUEL ADDITIVE PUMP CONTROL CIRCUIT / OPEN",
"P1929 FUEL ADDITIVE PUMP CONTROL CIRCUIT PERFORMANCE",
"P1930 FUEL ADDITIVE PUMP CONTROL CIRCUIT LOW",
"P1931 FUEL ADDITIVE PUMP CONTROL CIRCUIT HIGH",
"P1932 FUEL ADDITIVE LEVEL LOW",
"P1933 FUEL LEVEL SIGNAL",
"P1934 VEHICLE SPEED SIGNAL",
"P1935 BRAKE SWITCH/SENSOR SIGNAL",
"P1936 CLUTCH SWITCH/SENSOR SIGNAL",
"P1937 FUEL FIRED HEATER CONTROL CIRCUIT / OPEN",
"P1938 FUEL FIRED HEATER CONTROL CIRCUIT LOW",
"P1939 FUEL FIRED HEATER CONTROL CIRCUIT HIGH",
"P1A01 GENERATOR BRAKE PERFORMANCE",
"P1A02 TRANSMISSION ONE WAY CLUTCH PERFORMANCE",
"P1A03 DRIVE MOTOR A SHUTDOWN CIRCUIT",
"P1A04 GENERATOR SHUTDOWN CIRCUIT",
"P1A05 DESIRED ENGINE SPEED SIGNAL",
"P1A06 VEHICLE MODE SIGNAL",
"P1A07 INVERTER HIGH VOLTAGE PERFORMANCE",
"P1A08 GENERATOR MODE SIGNAL",
"P1A09 HYBRID BATTERY POWER OFF SIGNAL",
"P1A0A IMMEDIATE SHUTDOWN SIGNAL",
"P1A0B HYBRID BATTERY POWER LIMIT EXCEEDED",
"P1A0C HYBRID POWERTRAIN CONTROL MODULE - ENGINE DISABLED",
"P1A0D HYBRID POWERTRAIN CONTROL MODULE - GENERATOR DISABLED",
"P1A0E HYBRID POWERTRAIN CONTROL MODULE - MOTOR DISABLED",
"P1A0F HYBRID POWERTRAIN CONTROL MODULE - VEHICLE DISABLED",
"P1A10 HYBRID POWERTRAIN CONTROL MODULE - BATTERY DISABLED",
"P1A11 HYBRID POWERTRAIN CONTROL MODULE - ONE WAY CLUTCH DISABLED",
"P1A12 HYBRID POWERTRAIN CONTROL MODULE - GENERATOR BRAKE DISABLED",
"P2072 THROTTLE ACTUATOR CONTROL SYSTEM - ICE BREAKAGE",
"P2073 MANIFOLD ABSOLUTE PRESSURE/MASS AIR FLOW - THROTTLE POSITION CORRELATION AT IDLE",
"P2074 MANIFOLD ABSOLUTE PRESSURE/MASS AIR FLOW - THROTTLE POSITION CORRELATION AT HIGHER LOAD",
"P2448 SECONDARY AIR INJECTION SYSTEM HIGH AIRFLOW BANK 1",
"P2449 SECONDARY AIR INJECTION SYSTEM HIGH AIRFLOW BANK 2",
"P2450 EVAPORATIVE EMISSION CONTROL SYSTEM SWITCHING VALVE PERFORMANCE OR STUCK OPEN",
"P2451 EVAPORATIVE EMISSION CONTROL SYSTEM SWITCHING VALVE STUCK CLOSED",
"P2452 PARTICULATE MATTER TRAP DIFFERENTIAL PRESSURE SENSOR CIRCUIT",
"P2453 PARTICULATE MATTER TRAP DIFFERENTIAL PRESSURE SENSOR CIRCUIT RANGE/PERFORMANCE",
"P2454 PARTICULATE MATTER TRAP DIFFERENTIAL PRESSURE SENSOR CIRCUIT LOW",
"P2455 PARTICULATE MATTER TRAP DIFFERENTIAL PRESSURE SENSOR CIRCUIT HIGH",
"P2456 PARTICULATE MATTER TRAP DIFFERENTIAL PRESSURE SENSOR CIRCUIT INTERMITTENT/ERRATIC",
"P2457 EXHAUST GAS RECIRCULATION COOLER SYSTEM PERFORMANCE",
"P250A ENGINE OIL LEVEL SENSOR CIRCUIT",
"P250B ENGINE OIL LEVEL SENSOR CIRCUIT RANGE/PERFORMANCE",
"P250C ENGINE OIL LEVEL SENSOR CIRCUIT LOW",
"P250D ENGINE OIL LEVEL SENSOR CIRCUIT HIGH",
"P250E ENGINE OIL LEVEL SENSOR CIRCUIT INTERMITTENT/ERRATIC",
"P250F ENGINE OIL LEVEL TOO LOW",
"P251A PTO ENABLE SWITCH CIRCUIT / OPEN",
"P251B PTO ENABLE SWITCH CIRCUIT LOW",
"P251C PTO ENABLE SWITCH CIRCUIT HIGH",
"P251D PTO ENGINE SHUTDOWN CIRCUIT / OPEN",
"P251E PTO ENGINE SHUTDOWN CIRCUIT LOW",
"P251F PTO ENGINE SHUTDOWN CIRCUIT HIGH",
"P252A ENGINE OIL QUALITY SENSOR CIRCUIT",
"P252B ENGINE OIL QUALITY SENSOR CIRCUIT RANGE/PERFORMANCE",
"P252C ENGINE OIL QUALITY SENSOR CIRCUIT LOW",
"P252D ENGINE OIL QUALITY SENSOR CIRCUIT HIGH",
"P252E ENGINE OIL QUALITY CIRCUIT INTERMITTENT/ERRATIC",
"P252F ENGINE OIL LEVEL TOO HIGH",
"P253A PTO SENSE CIRCUIT / OPEN",
"P253B PTO SENSE CIRCUIT RANGE/PERFORMANCE",
"P253C PTO SENSE CIRCUIT LOW",
"P253D PTO SENSE CIRCUIT HIGH",
"P253E PTO SENSE CIRCUIT INTERMITTENT/ERRATIC",
"P254A PTO SPEED SELECTOR SENSOR/SWITCH 1 CIRCUIT / OPEN",
"P254B PTO SPEED SELECTOR SENSOR/SWITCH 1 CIRCUIT RANGE/PERFORMANCE",
"P254C PTO SPEED SELECTOR SENSOR/SWITCH 1 CIRCUIT LOW",
"P254D PTO SPEED SELECTOR SENSOR/SWITCH 1 CIRCUIT HIGH",
"P254E PTO SPEED SELECTOR SENSOR/SWITCH 1 CIRCUIT INTERMITTENT/ERRATIC",
"P255A PTO SPEED SELECTOR SENSOR/SWITCH 2 CIRCUIT / OPEN",
"P255B PTO SPEED SELECTOR SENSOR/SWITCH 2 CIRCUIT RANGE/PERFORMANCE",
"P255C PTO SPEED SELECTOR SENSOR/SWITCH 2 CIRCUIT LOW",
"P255D PTO SPEED SELECTOR SENSOR/SWITCH 2 CIRCUIT HIGH",
"P255E PTO SPEED SELECTOR SENSOR/SWITCH 2 CIRCUIT INTERMITTENT/ERRATIC",
"P256A ENGINE IDLE SPEED SELECTOR SENSOR/SWITCH CIRCUIT / OPEN",
"P256B ENGINE IDLE SPEED SELECTOR SENSOR/SWITCH CIRCUIT RANGE/PERFORMANCE",
"P256C ENGINE IDLE SPEED SELECTOR SENSOR/SWITCH CIRCUIT LOW",
"P256D ENGINE IDLE SPEED SELECTOR SENSOR/SWITCH CIRCUIT HIGH",
"P256E ENGINE IDLE SPEED SELECTOR SENSOR/SWITCH CIRCUIT INTERMITTENT/ERRATIC",
"P2578 TURBOCHARGER SPEED SENSOR CIRCUIT",
"P2

Коды ошибок OBD-II(P0100-P0485)

P0100   Mass or Volume Air Flow Circuit Malfunction  
 P0101  Mass or Volume Air Flow Circuit Range/Performance Problem  
 P0102  Mass or Volume Air Flow Circuit Low Input  
 P0103  Mass or Volume Air Flow Circuit High Input  
 P0104  Mass or Volume Air Flow Circuit Intermittent  
 P0105  Manifold Absolute Pressure/Barometric Pressure Circuit Malfunction  
 P0106  Manifold Absolute Pressure/Barometric Pressure Circuit Range/Performance Problem  
 P0107  Manifold Absolute Pressure/Barometric Pressure Circuit Low Input  
 P0108  Manifold Absolute Pressure/Barometric Pressure Circuit High Input  
 P0109  Manifold Absolute Pressure/Barometric Pressure Circuit Intermittent  
 P0110  Intake Air Temperature Circuit Malfunction  
 P0111  Intake Air Temperature Circuit Range/Performance Problem  
 P0112  Intake Air Temperature Circuit Low Input  
 P0113  Intake Air Temperature Circuit High Input  
 P0114  Intake Air Temperature Circuit Intermittent  
 P0115  Engine Coolant Temperature Circuit Malfunction  
 P0116  Engine Coolant Temperature Circuit Range/Performance Problem  
 P0117  Engine Coolant Temperature Circuit Low Input  
 P0118  Engine Coolant Temperature Circuit High Input  
 P0119  Engine Coolant Temperature Circuit Intermittent  
 P0120  Throttle/Pedal Position Sensor/Switch A Circuit Malfunction  
 P0120  ETS MainThrottle Position Sensor Malfunction (Hyundai)  
 P0121  Throttle/Pedal Position Sensor/Switch A Circuit Range/Performance Problem  
 P0122  Throttle/Pedal Position Sensor/Switch A Circuit Low Input  
 P0123  Throttle/Pedal Position Sensor/Switch A Circuit High Input  
 P0124  Throttle/Pedal Position Sensor/Switch A Circuit Intermittent  
 P0125  Insufficient Coolant Temperature for Closed Loop Fuel Control  
 P0126  Insufficient Coolant Temperature for Stable Operation  
 P0128  Range/Performance Problem In Thermostat(Acura)  
 P0128  ECT Below Thermostat Regulating Temperature(GM)  
 P0130  O2 Sensor Circuit Malfunction (Bank 1 Sensor 1)  
 P0131  O2 Sensor Circuit Low Voltage (Bank 1 Sensor 1)  
 P0132  O2 Sensor Circuit High Voltage (Bank 1 Sensor 1)  
 P0133  O2 Sensor Circuit Slow Response (Bank 1 Sensor 1)  
 P0134  O2 Sensor Circuit No Activity Detected (Bank 1 Sensor 1)  
 P0135  O2 Sensor Heater Circuit Malfunction (Bank 1 Sensor 1)  
 P0136  O2 Sensor Circuit Malfunction (Bank 1 Sensor 2)  
 P0137  O2 Sensor Circuit Low Voltage (Bank 1 Sensor 2)  
 P0138  O2 Sensor Circuit High Voltage (Bank 1 Sensor 2)  
 P0139  O2 Sensor Circuit Slow Response (Bank 1 Sensor 2)  
 P0140  O2 Sensor Circuit No Activity Detected (Bank 1 Sensor 2)  
 P0141  O2 Sensor Heater Circuit Malfunction (Bank 1 Sensor 2)  
 P0142  O2 Sensor Circuit Malfunction (Bank 1 Sensor 3)  
 P0143  O2 Sensor Circuit Low Voltage (Bank 1 Sensor 3)  
 P0144  O2 Sensor Circuit High Voltage (Bank 1 Sensor 3)  
 P0145  O2 Sensor Circuit Slow Response (Bank 1 Sensor 3)  
 P0146  O2 Sensor Circuit No Activity Detected (Bank 1 Sensor 3)  
 P0147  O2 Sensor Heater Circuit Malfunction (Bank 1 Sensor 3)  
 P0150  O2 Sensor Circuit Malfunction (Bank 2 Sensor 1)  
 P0151  O2 Sensor Circuit Low Voltage (Bank 2 Sensor 1)  
 P0152  O2 Sensor Circuit High Voltage (Bank 2 Sensor 1)  
 P0153  O2 Sensor Circuit Slow Response (Bank 2 Sensor 1)  
 P0154  O2 Sensor Circuit No Activity Detected (Bank 2 Sensor 1)  
 P0155  O2 Sensor Heater Circuit Malfunction (Bank 2 Sensor 1)  
 P0156  O2 Sensor Circuit Malfunction (Bank 2 Sensor 2)  
 P0157  O2 Sensor Circuit Low Voltage (Bank 2 Sensor 2)  
 P0158  O2 Sensor Circuit High Voltage (Bank 2 Sensor 2)  
 P0159  O2 Sensor Circuit Slow Response (Bank 2 Sensor 2)  
 P0160  O2 Sensor Circuit No Activity Detected (Bank 2 Sensor 2)  
 P0161  O2 Sensor Heater Circuit Malfunction (Bank 2 Sensor 2)  
 P0162  O2 Sensor Circuit Malfunction (Bank 2 Sensor 3)  
 P0163  O2 Sensor Circuit Low Voltage (Bank 2 Sensor 3)  
 P0164  O2 Sensor Circuit High Voltage (Bank 2 Sensor 3)  
 P0165  O2 Sensor Circuit Slow Response (Bank 2 Sensor 3)  
 P0166  O2 Sensor Circuit No Activity Detected (Bank 2 Sensor 3  
 P0167  O2 Sensor Heater Circuit Malfunction (Bank 2 Sensor 3)  
 P0170  Fuel Trim Malfunction (Bank 1)  
 P0171  System too Lean (Bank 1)  
 P0172  System too Rich (Bank 1)  
 P0173  Fuel Trim Malfunction (Bank 2)  
 P0174  System too Lean (Bank 2)  
 P0175  System too Rich (Bank 2)  
 P0176  Fuel Composition Sensor Circuit Malfunction  
 P0177  Fuel Composition Sensor Circuit Range/Performance  
 P0178  Fuel Composition Sensor Circuit Low Input  
 P0179  Fuel Composition Sensor Circuit High Input  
 P0180  Fuel Temperature Sensor A Circuit Malfunction  
 P0181  Fuel Temperature Sensor A Circuit Range/Performance  
 P0182  Fuel Temperature Sensor A Circuit Low Input  
 P0183  Fuel Temperature Sensor A Circuit High Input  
 P0184  Fuel Temperature Sensor A Circuit Intermittent  
 P0185  Fuel Temperature Sensor B Circuit Malfunction  
 P0186  Fuel Temperature Sensor B Circuit Range/Performance  
 P0187  Fuel Temperature Sensor B Circuit Low Input  
 P0188  Fuel Temperature Sensor B Circuit High Input  
 P0189  Fuel Temperature Sensor B Circuit Intermittent  
 P0190  Fuel Rail Pressure Sensor Circuit Malfunction  
 P0191  Fuel Rail Pressure Sensor Circuit Range/Performance  
 P0192  Fuel Rail Pressure Sensor Circuit Low Input  
 P0193  Fuel Rail Pressure Sensor Circuit High Input  
 P0194  Fuel Rail Pressure Sensor Circuit Intermittent  
 P0195  Engine Oil Temperature Sensor Malfunction  
 P0196  Engine Oil Temperature Sensor Range/Performance  
 P0197  Engine Oil Temperature Sensor Low  
 P0198  Engine Oil Temperature Sensor High  
 P0199  Engine Oil Temperature Sensor Intermittent  
 P0200  Injector Circuit Malfunction  
 P0201  Injector Circuit Malfunction - Cylinder 1  
 P0202  Injector Circuit Malfunction - Cylinder 2  
 P0203  Injector Circuit Malfunction - Cylinder 3  
 P0204  Injector Circuit Malfunction - Cylinder 4  
 P0205  Injector Circuit Malfunction - Cylinder 5  
 P0206  Injector Circuit Malfunction - Cylinder 6  
 P0207  Injector Circuit Malfunction - Cylinder 7  
 P0208  Injector Circuit Malfunction - Cylinder 8  
 P0209  Injector Circuit Malfunction - Cylinder 9  
 P0210  Injector Circuit Malfunction - Cylinder 10  
 P0211  Injector Circuit Malfunction - Cylinder 11  
 P0212  Injector Circuit Malfunction - Cylinder 12  
 P0213  Cold Start Injector 1 Malfunction  
 P0214  Cold Start Injector 2 Malfunction  
 P0215  Engine Shutoff Solenoid Malfunction  
 P0216  Injection Timing Control Circuit Malfunction  
 P0217  Engine Overtemp Condition  
 P0218  Transmission Over Temperature Condition  
 P0219  Engine Overspeed Condition  
 P0220  Throttle/Pedal Position Sensor/Switch B Circuit Malfunction  
 P0220  ETS Throttle Position Sensor Property Malfunction (Hyundai)  
 P0221  Throttle/Pedal Position Sensor/Switch B Circuit Range/Performance Problem  
 P0222  Throttle/Pedal Position Sensor/Switch B Circuit Low Input  
 P0223  Throttle/Pedal Position Sensor/Switch B Circuit High Input  
 P0224  Throttle/Pedal Position Sensor/Switch B Circuit Intermittent  
 P0225  Throttle/Pedal Position Sensor/Switch C Circuit Malfunction  
 P0226  Throttle/Pedal Position Sensor/Switch C Circuit Range/Performance Problem  
 P0227  Throttle/Pedal Position Sensor/Switch C Circuit Low Input  
 P0228  Throttle/Pedal Position Sensor/Switch C Circuit High Input  
 P0229  Throttle/Pedal Position Sensor/Switch C Circuit Intermittent  
 P0230  Fuel Pump Primary Circuit Malfunction  
 P0231  Fuel Pump Secondary Circuit Low  
 P0232  Fuel Pump Secondary Circuit High  
 P0233  Fuel Pump Secondary Circuit Intermittent  
 P0234  Engine Overboost Condition  
 P0235  Turbocharger Boost Sensor A Circuit Malfunction  
 P0236  Turbocharger Boost Sensor A Circuit Range/Performance  
 P0237  Turbocharger Boost Sensor A Circuit Low  
 P0238  Turbocharger Boost Sensor A Circuit High  
 P0239  Turbocharger Boost Sensor B Malfunction  
 P0240  Turbocharger Boost Sensor B Circuit Range/Performance  
 P0241  Turbocharger Boost Sensor B Circuit Low  
 P0242  Turbocharger Boost Sensor B Circuit High  
 P0243  Turbocharger Wastegate Solenoid A Malfunction  
 P0244  Turbocharger Wastegate Solenoid A Range/Performance  
 P0245  Turbocharger Wastegate Solenoid A Low  
 P0246  Turbocharger Wastegate Solenoid A High  
 P0247  Turbocharger Wastegate Solenoid B Malfunction  
 P0248  Turbocharger Wastegate Solenoid B Range/Performance  
 P0249  Turbocharger Wastegate Solenoid B Low  
 P0250  Turbocharger Wastegate Solenoid B High  
 P0251  Injection Pump Fuel Metering Control "A" Malfunction (Cam/Rotor/Injector)  
 P0252  Injection Pump Fuel Metering Control "A" Range/Performance (Cam/Rotor/Injector)  
 P0253  Injection Pump Fuel Metering Control "A" Low (Cam/Rotor/Injector)  
 P0254  Injection Pump Fuel Metering Control "A" High (Cam/Rotor/Injector)  
 P0255  Injection Pump Fuel Metering Control "A" Intermittent (Cam/Rotor/Injector)  
 P0256  Injection Pump Fuel Metering Control "B" Malfunction (Cam/Rotor/Injector)  
 P0257  Injection Pump Fuel Metering Control "B" Range/Performance (Cam/Rotor/Injector)  
 P0258  Injection Pump Fuel Metering Control "B" Low (Cam/Rotor/Injector)  
 P0259  Injection Pump Fuel Metering Control "B" High (Cam/Rotor/Injector)  
 P0260  Injection Pump Fuel Metering Control "B" Intermittent (Cam/Rotor/Injector)  
 P0261  Cylinder 1 Injector Circuit Low  
 P0262  Cylinder 1 Injector Circuit High  
 P0263  Cylinder 1 Contribution/Balance Fault  
 P0264  Cylinder 2 Injector Circuit Low  
 P0265  Cylinder 2 Injector Circuit High  
 P0266  Cylinder 2 Contribution/Balance Fault  
 P0267  Cylinder 3 Injector Circuit Low  
 P0268  Cylinder 3 Injector Circuit High  
 P0269  Cylinder 3 Contribution/Balance Fault  
 P0270  Cylinder 4 Injector Circuit Low  
 P0271  Cylinder 4 Injector Circuit High  
 P0272  Cylinder 4 Contribution/Balance Fault  
 P0273  Cylinder 5 Injector Circuit Low  
 P0274  Cylinder 5 Injector Circuit High  
 P0275  Cylinder 5 Contribution/Balance Fault  
 P0276  Cylinder 6 Injector Circuit Low  
 P0277  Cylinder 6 Injector Circuit High  
 P0278  Cylinder 6 Contribution/Balance Fault  
 P0279  Cylinder 7 Injector Circuit Low  
 P0280  Cylinder 7 Injector Circuit High  
 P0281  Cylinder 7 Contribution/Balance Fault  
 P0282  Cylinder 8 Injector Circuit Low  
 P0283  Cylinder 8 Injector Circuit High  
 P0284  Cylinder 8 Contribution/Balance Fault  
 P0285  Cylinder 9 Injector Circuit Low  
 P0286  Cylinder 9 Injector Circuit High  
 P0287  Cylinder 9 Contribution/Balance Fault  
 P0288  Cylinder 10 Injector Circuit Low  
 P0289  Cylinder 10 Injector Circuit High  
 P0290  Cylinder 10 Contribution/Balance Fault  
 P0291  Cylinder 11 Injector Circuit Low  
 P0292  Cylinder 11 Injector Circuit High  
 P0293  Cylinder 11 Contribution/Balance Fault  
 P0294  Cylinder 12 Injector Circuit Low  
 P0295  Cylinder 12 Injector Circuit High  
 P0296  Cylinder 12 Contribution/Range Fault  
 P0300  Random/Multiple Cylinder Misfire Detected  
 P0301  Cylinder 1 Misfire Detected  
 P0302  Cylinder 2 Misfire Detected  
 P0303  Cylinder 3 Misfire Detected  
 P0304  Cylinder 4 Misfire Detected  
 P0305  Cylinder 5 Misfire Detected  
 P0306  Cylinder 6 Misfire Detected  
 P0307  Cylinder 7 Misfire Detected  
 P0308  Cylinder 8 Misfire Detected  
 P0309  Cylinder 9 Misfire Detected  
 P0310  Cylinder 10 Misfire Detected  
 P0311  Cylinder 11 Misfire Detected  
 P0312  Cylinder 12 Misfire Detected  
 P0320  Ignition/Distributor Engine Speed Input Circuit Malfunction  
 P0321  Ignition/Distributor Engine Speed Input Circuit Range/Performance  
 P0322  Ignition/Distributor Engine Speed Input Circuit No Signal  
 P0323  Ignition/Distributor Engine Speed Input Circuit Intermittent  
 P0325  Knock Sensor 1 Circuit Malfunction (Bank 1 or Single Sensor)  
 P0326  Knock Sensor 1 Circuit Range/Performance (Bank 1 or Single Sensor)  
 P0327  Knock Sensor 1 Circuit Low Input (Bank 1 or Single Sensor)  
 P0328  Knock Sensor 1 Circuit High Input (Bank 1 or Single Sensor)  
 P0329  Knock Sensor 1 Circuit Intermittent (Bank 1 or Single Sensor)  
 P0330  Knock Sensor 2 Circuit Malfunction (Bank 2)  
 P0331  Knock Sensor 2 Circuit Range/Performance (Bank 2)  
 P0332  Knock Sensor 2 Circuit Low Input (Bank 2)  
 P0333  Knock Sensor 2 Circuit High Input (Bank 2)  
 P0334  Knock Sensor 2 Circuit Intermittent (Bank 2)  
 P0335  Crankshaft Position Sensor A Circuit Malfunction  
 P0336  Crankshaft Position Sensor A Circuit Range/Performance  
 P0337  Crankshaft Position Sensor A Circuit Low Input  
 P0338  Crankshaft Position Sensor A Circuit High Input  
 P0339  Crankshaft Position Sensor A Circuit Intermittent  
 P0340  Camshaft Position Sensor Circuit Malfunction  
 P0341  Camshaft Position Sensor Circuit Range/Performance  
 P0342  Camshaft Position Sensor Circuit Low Input  
 P0343  Camshaft Position Sensor Circuit High Input  
 P0344  Camshaft Position Sensor Circuit Intermittent  
 P0350  Ignition Coil Primary/Secondary Circuit Malfunction  
 P0351  Ignition Coil A Primary/Secondary Circuit Malfunction  
 P0352  Ignition Coil B Primary/Secondary Circuit Malfunction  
 P0353  Ignition Coil C Primary/Secondary Circuit Malfunction  
 P0354  Ignition Coil D Primary/Secondary Circuit Malfunction  
 P0355  Ignition Coil E Primary/Secondary Circuit Malfunction  
 P0356  Ignition Coil F Primary/Secondary Circuit Malfunction  
 P0357  Ignition Coil G Primary/Secondary Circuit Malfunction  
 P0358  Ignition Coil H Primary/Secondary Circuit Malfunction  
 P0359  Ignition Coil I Primary/Secondary Circuit Malfunction  
 P0360  Ignition Coil J Primary/Secondary Circuit Malfunction  
 P0361  Ignition Coil K Primary/Secondary Circuit Malfunction  
 P0362  Ignition Coil L Primary/Secondary Circuit Malfunction  
 P0370  Timing Reference High Resolution Signal A Malfunction  
 P0371  Timing Reference High Resolution Signal A Too Many Pulses  
 P0372  Timing Reference High Resolution Signal A Too Few Pulses  
 P0373  Timing Reference High Resolution Signal A Intermittent/Erratic Pulses  
 P0374  Timing Reference High Resolution Signal A No Pulses  
 P0375  Timing Reference High Resolution Signal B Malfunction  
 P0376  Timing Reference High Resolution Signal B Too Many Pulses  
 P0377  Timing Reference High Resolution Signal B Too Few Pulses  
 P0378  Timing Reference High Resolution Signal B Intermittent/Erratic Pulses  
 P0379  Timing Reference High Resolution Signal B No Pulses  
 P0380  Glow Plug/Heater Circuit "A" Malfunction  
 P0381  Glow Plug/Heater Indicator Circuit Malfunction  
 P0382  Glow Plug/Heater Circuit "B" Malfunction  
 P0385  Crankshaft Position Sensor B Circuit Malfunction  
 P0386  Crankshaft Position Sensor B Circuit Range/Performance  
 P0387  Crankshaft Position Sensor B Circuit Low Input  
 P0388  Crankshaft Position Sensor B Circuit High Input  
 P0389  Crankshaft Position Sensor B Circuit Intermittent

P0400   Exhaust Gas Recirculation Flow Malfunction  
 P0401  Exhaust Gas Recirculation Flow Insufficient Detected  
 P0402  Exhaust Gas Recirculation Flow Excessive Detected  
 P0403  Exhaust Gas Recirculation Circuit Malfunction  
 P0404  Exhaust Gas Recirculation Circuit Range/Performance  
 P0405  Exhaust Gas Recirculation Sensor A Circuit Low  
 P0406  Exhaust Gas Recirculation Sensor A Circuit High  
 P0407  Exhaust Gas Recirculation Sensor B Circuit Low  
 P0408  Exhaust Gas Recirculation Sensor B Circuit High  
 P0410  Secondary Air Injection System Malfunction  
 P0411  Secondary Air Injection System Incorrect Flow Detected  
 P0412  Secondary Air Injection System Switching Valve A Circuit Malfunction  
 P0413  Secondary Air Injection System Switching Valve A Circuit Open  
 P0414  Secondary Air Injection System Switching Valve A Circuit Shorted  
 P0415  Secondary Air Injection System Switching Valve B Circuit Malfunction  
 P0416  Secondary Air Injection System Switching Valve B Circuit Open  
 P0417  Secondary Air Injection System Switching Valve B Circuit Shorted  
 P0418  Secondary Air Injection System Relay "A" Circuit Malfunction  
 P0419  Secondary Air Injection System Relay "B" Circuit Malfunction  
 P0420  Catalyst System Efficiency Below Threshold (Bank 1)  
 P0421  Warm Up Catalyst Efficiency Below Threshold (Bank 1)  
 P0422  Main Catalyst Efficiency Below Threshold (Bank 1)  
 P0423  Heated Catalyst Efficiency Below Threshold (Bank 1)  
 P0424  Heated Catalyst Temperature Below Threshold (Bank 1)  
 P0430  Catalyst System Efficiency Below Threshold (Bank 2)  
 P0431  Warm Up Catalyst Efficiency Below Threshold (Bank 2)  
 P0432  Main Catalyst Efficiency Below Threshold (Bank 2)  
 P0433  Heated Catalyst Efficiency Below Threshold (Bank 2)  
 P0434  Heated Catalyst Temperature Below Threshold (Bank 2)  
 P0440  Evaporative Emission Control System Malfunction  
 P0441  Evaporative Emission Control System Incorrect Purge Flow  
 P0442  Evaporative Emission Control System Leak Detected (small leak)  
 P0443  Evaporative Emission Control System Purge Control Valve Circuit Malfunction  
 P0444  Evaporative Emission Control System Purge Control Valve Circuit Open  
 P0445  Evaporative Emission Control System Purge Control Valve Circuit Shorted  
 P0446  Evaporative Emission Control System Vent Control Circuit Malfunction  
 P0447  Evaporative Emission Control System Vent Control Circuit Open  
 P0448  Evaporative Emission Control System Vent Control Circuit Shorted  
 P0449  Evaporative Emission Control System Vent Valve/Solenoid Circuit Malfunction  
 P0450  Evaporative Emission Control System Pressure Sensor Malfunction  
 P0451  Evaporative Emission Control System Pressure Sensor Range/Performance  
 P0452  Evaporative Emission Control System Pressure Sensor Low Input  
 P0453  Evaporative Emission Control System Pressure Sensor High Input  
 P0454  Evaporative Emission Control System Pressure Sensor Intermittent  
 P0455  Evaporative Emission Control System Leak Detected (gross leak)  
 P0456  EVAP Leak Monitor Small Leak Detected (CHRYSLER)  
 P0460  Fuel Level Sensor Circuit Malfunction  
 P0461  Fuel Level Sensor Circuit Range/Performance  
 P0462  Fuel Level Sensor Circuit Low Input  
 P0463  Fuel Level Sensor Circuit High Input  
 P0464  Fuel Level Sensor Circuit Intermittent  
 P0465  Purge Flow Sensor Circuit Malfunction  
 P0466  Purge Flow Sensor Circuit Range/Performance  
 P0467  Purge Flow Sensor Circuit Low Input  
 P0468  Purge Flow Sensor Circuit High Input  
 P0469  Purge Flow Sensor Circuit Intermittent  
 P0470  Exhaust Pressure Sensor Malfunction  
 P0471  Exhaust Pressure Sensor Range/Performance  
 P0472  Exhaust Pressure Sensor Low  
 P0473  Exhaust Pressure Sensor High  
 P0474  Exhaust Pressure Sensor Intermittent  
 P0475  Exhaust Pressure Control Valve Malfunction  
 P0476  Exhaust Pressure Control Valve Range/Performance  
 P0477  Exhaust Pressure Control Valve Low  
 P0478  Exhaust Pressure Control Valve High  
 P0479  Exhaust Pressure Control Valve Intermittent  
 P0480  Cooling Fan 1 Control Circuit Malfunction  
 P0481  Cooling Fan 2 Control Circuit Malfunction  
 P0482  Cooling Fan 3 Control Circuit Malfunction  
 P0483  Cooling Fan Rationality Check Malfunction  
 P0484  Cooling Fan Circuit Over Current  
 P0485  Cooling Fan Power/Ground Circuit Malfunction

Коды ошибок OBD-II(P0600-P1719)

P0500   Vehicle Speed Sensor Malfunction  
 P0501  Vehicle Speed Sensor Range/Performance  
 P0502  Vehicle Speed Sensor Low Input  
 P0503  Vehicle Speed Sensor Intermittent/Erratic/High  
 P0505  Idle Control System Malfunction  
 P0506  Idle Control System RPM Lower Than Expected  
 P0507  Idle Control System RPM Higher Than Expected  
 P0510  Closed Throttle Position Switch Malfunction  
 P0520  Engine Oil Pressure Sensor/Switch Circuit Malfunction  
 P0521  Engine Oil Pressure Sensor/Switch Circuit Range/Performance  
 P0522  Engine Oil Pressure Sensor/Switch Circuit Low Voltage  
 P0523  Engine Oil Pressure Sensor/Switch Circuit High Voltage  
 P0530  A/C Refrigerant Pressure Sensor Circuit Malfunction  
 P0531  A/C Refrigerant Pressure Sensor Circuit Range/Performance  
 P0532  A/C Refrigerant Pressure Sensor Circuit Low Input  
 P0533  A/C Refrigerant Pressure Sensor Circuit High Input  
 P0534  Air Conditioner Refrigerant Charge Loss  
 P0550  Power Steering Pressure Sensor Circuit Malfunction  
 P0551  Power Steering Pressure Sensor Circuit Range/Performance  
 P0552  Power Steering Pressure Sensor Circuit Low Input  
 P0553  Power Steering Pressure Sensor Circuit High Input  
 P0554  Power Steering Pressure Sensor Circuit Intermittent  
 P0560  System Voltage Malfunction  
 P0561  System Voltage Unstable  
 P0562  System Voltage Low  
 P0563  System Voltage High  
 P0565  CRUISE CONTROL ON SIGNAL MALFUNCTION  
 P0566  Cruise Control Off Signal Malfunction  
 P0567  Cruise Control Resume Signal Malfunction  
 P0568  Cruise Control Set Signal Malfunction  
 P0569  Cruise Control Coast Signal Malfunction  
 P0570  Cruise Control Accel Signal Malfunction  
 P0571  Cruise Control/Brake Switch A Circuit Malfunction  
 P0572  Cruise Control/Brake Switch A Circuit Low  
 P0573  Cruise Control/Brake Switch A Circuit High  
 P0574  Cruise Control Related Malfunction  
 P0575  Cruise Control Related Malfunction  
 P0576  Cruise Control Related Malfunction  
 P0577  Cruise Control Related Malfunction  
 P0578  Cruise Control Related Malfunction  
 P0579  Cruise Control Related Malfunction  
 P0580  Cruise Control Related Malfunction

P0600   Serial Communication Link Malfunction  
 P0601  Internal Control Module Memory Check Sum Error  
 P0602  Control Module Programming Error  
 P0603  Internal Control Module Keep Alive Memory (KAM) Error  
 P0604  Internal Control Module Random Access Memory (RAM) Error  
 P0605  Internal Control Module Read Only Memory (ROM) ErroR  
 P0606  PCM Processor Fault  
 P0607  Control Module VSS Output "A" Malfunction  
 P0609  Control Module VSS Output "B" Malfunction  
 P0620  Generator Control Circuit Malfunction  
 P0621  Generator Lamp "L" Control Circuit Malfunction  
 P0622  Generator Field "F" Control Circuit Malfunction  
 P0645  A/C Clutch Relay Circuit (CHRYSLER)  
 P0650  Malfunction Indicator Lamp (MIL) Control Circuit Malfunction  
 P0654  Engine RPM Output Circuit Malfunction  
 P0655  Engine Hot Lamp Output Control Circuit Malfucntion  
 P0656  Fuel Level Output Circuit Malfunction

P0700   Transmission Control System Malfunction  
 P0701  Transmission Control System Range/Performance  
 P0702  Transmission Control System Electrical  
 P0703  Torque Converter/Brake Switch B Circuit Malfunction  
 P0704  Clutch Switch Input Circuit Malfunction  
 P0705  Transmission Range Sensor Circuit malfunction (PRNDL Input)  
 P0706  Transmission Range Sensor Circuit Range/Performance  
 P0707  Transmission Range Sensor Circuit Low Input  
 P0708  Transmission Range Sensor Circuit High Input  
 P0709  Transmission Range Sensor Circuit Intermittent  
 P0710  Transmission Fluid Temperature Sensor Circuit Malfunction  
 P0711  Transmission Fluid Temperature Sensor Circuit Range/Performance  
 P0712  Transmission Fluid Temperature Sensor Circuit Low Input  
 P0713  Transmission Fluid Temperature Sensor Circuit High Input  
 P0714  Transmission Fluid Temperature Sensor Circuit Intermittent  
 P0715  Input/Turbine Speed Sensor Circuit Malfunction  
 P0716  Input/Turbine Speed Sensor Circuit Range/Performance  
 P0717  Input/Turbine Speed Sensor Circuit No Signal  
 P0718  Input/Turbine Speed Sensor Circuit Intermittent  
 P0719  Torque Converter/Brake Switch B Circuit Low  
 P0720  Output Speed Sensor Circuit Malfunction  
 P0721  Output Speed Sensor Range/Performance  
 P0722  Output Speed Sensor No Signal  
 P0723  Output Speed Sensor Intermittent  
 P0724  Torque Converter/Brake Switch B Circuit High  
 P0725  Engine Speed input Circuit Malfunction  
 P0726  Engine Speed Input Circuit Range/Performance  
 P0727  Engine Speed Input Circuit No Signal  
 P0728  Engine Speed Input Circuit Intermittent  
 P0730  Incorrect Gear Ratio  
 P0731  Gear 1 Incorrect ratio  
 P0732  Gear 2 Incorrect ratio  
 P0733  Gear 3 Incorrect ratio  
 P0734  Gear 4 Incorrect ratio  
 P0735  Gear 5 Incorrect ratio  
 P0736  Reverse incorrect gear ratio  
 P0740  Torque Converter Clutch Circuit Malfuction  
 P0741  Torque Converter Clutch Circuit Performance or Stuck Off  
 P0742  Torque Converter Clutch Circuit Stuck On  
 P0743  Torque Converter Clutch Circuit Electrical  
 P0744  Torque Converter Clutch Circuit Intermittent  
 P0745  Pressure Control Solenoid Malfunction  
 P0746  Pressure Control Solenoid Performance or Stuck Off  
 P0747  Pressure Control Solenoid Stuck On  
 P0748  Pressure Control Solenoid Electrical  
 P0749  Pressure Control Solenoid Intermittent  
 P0750  Shift Solenoid A Malfunction  
 P0751  Shift Solenoid A Performance or Stuck Off  
 P0752  Shift Solenoid A Stuck On  
 P0753  Shift Solenoid A Electrical  
 P0754  Shift Solenoid A Intermittent  
 P0755  Shift Solenoid B Malfunction  
 P0756  Shift Solenoid B Performance or Stuck Off  
 P0757  Shift Solenoid B Stuck On  
 P0758  Shift Solenoid B Electrical  
 P0759  Shift Solenoid B Intermittent  
 P0760  Shift Solenoid C Malfunction  
 P0761  Shift Solenoid C Performance or Stuck Off  
 P0762  Shift Solenoid C Stuck On  
 P0763  Shift Solenoid C Electrical  
 P0764  Shift Solenoid C Intermittent  
 P0765  Shift Solenoid D Malfunction  
 P0766  Shift Solenoid D Performance or Stuck Off  
 P0767  Shift Solenoid D Stuck On  
 P0768  Shift Solenoid D Electrical  
 P0769  Shift Solenoid D Intermittent  
 P0770  Shift Solenoid E Malfunction  
 P0771  Shift Solenoid E Performance or Stuck Off  
 P0772  Shift Solenoid E Stuck On  
 P0773  Shift Solenoid E Electrical  
 P0774  Shift Solenoid E Intermittent  
 P0780  Shift Malfunction  
 P0781  1-2 Shift Malfunction  
 P0782  2-3 Shift Malfunction  
 P0783  3-4 Shift Malfunction  
 P0784  4-5 Shift Malfunction  
 P0785  Shift/Timing Solenoid Malfunction  
 P0786  Shift/Timing Solenoid Range/Performance  
 P0787  Shift/Timing Solenoid Low  
 P0788  Shift/Timing Solenoid High  
 P0789  Shift/Timing Solenoid Intermittent  
 P0790  Normal/Performance Switch Circuit Malfunction  
 P0801   Reverse Inhibit Control Circuit Malfunction  
 P0803  1-4 Upshift (Skip Shift) Solenoid Control Circuit Malfunction  
 P0804  1-4 Upshift (Skip Shift) Lamp Control Circuit Malfunction  
 P0812   Reverse Switch Input Malfunction (Ford)  
 P1000   Transmission Solenoid Malfunction - OBD II Test Incomplete (Mazda)  
 P1000   Monitor Testing Not Complete (Ford)  
 P1001  KOER Not Able To Complete, KOER Aborted (Ford)  
 P1083  Fuel Control Mixture Lean (Bank 1 Sensor 1) (BMW)  
 P1084  Fuel Control Mixture Rich (Bank 1 Sensor 1) (BMW)  
 P1085  Fuel Control Mixture Lean (Bank 2 Sensor 1)  
 P1086  Fuel Control Mixture Rich (Bank 2 Sensor 1) (BMW)  
 P1087  O2 Sensor Circuit Slow Response in Lean Control Range (Bank 1 Sensor 1) (BMW)  
 P1088  O2 Sensor Circuit Slow Response in Rich Control Range (Bank 1 Sensor 1) (BMW)  
 P1089  O2 Sensor Circuit Slow Response in Lean Control Range (Bank 1 Sensor 2) (BMW)  
 P1090  Pre-Catalyst Fuel Trim Too Lean Bank 1 (BMW)  
 P1091  Pre-Catalyst Fuel Trim Too Rich Bank 1 (BMW)  
 P1092  Pre-Catalyst Fuel Trim Too Lean Bank 2 (BMW)  
 P1093  Pre-Catalyst Fuel Trim Too Rich Bank 2 (BMW)  
 P1094  O2 Sensor Circuit Slow Response in Rich Control Range (Bank 2 Sensor 1) (BMW)  
 P1095  O2 Sensor Circuit Slow Switching From Lean to Rich (Bank 1 Sensor 1) (BMW)  
 P1096  O2 Sensor Circuit Slow Switching From Lean to Rich (Bank 2 Sensor 1) (BMW)  
 P1097  O2 Sensor Circuit Slow Response after Coast Down Fuel Cutoff (Bank 1 Sensor 1) (BMW)  
 P1098  O2 Sensor Circuit Slow Response after Coast Down Fuel Cutoff (Bank 2 Sensor 2) (BMW)  
P1100   MAF Intermittant (Mazda)  
 P1100  Manifold Absolute Pressure (MAP) Sensor Malfunction (Open/Short) (Hyundai)  
 P1101  MAF Out Of Range (Mazda)  
 P1102  Manifold Absolute Pressure (MAP) Sensor Malfunction - Low Voltage (Hyundai)  
 P1103  Manifold Absolute Pressure (MAP) Sensor Malfunction - High Voltage (Hyundai)  
 P1105  MAP/BARO Switch Solenoid Valve (Infiniti)  
 P1106  Manifold Absolute Pressure (MAP) sensor circuit intermittent high voltage  
 P1106  Barometric pressure circuit problem (Acura, Honda)  
 P1107  Manifold Absolute Pressure (MAP) sensor circuit intermittent low voltage  
 P1107  Barometric pressure circuit low input (Acura, Honda)  
 P1108  BARO to MAP signal circuit comparison too high  
 P1108  Barometric pressure circuit high input (Acura, Honda)  
 P1110  Intake Valve Timing Control (Left Bank) (Infiniti)  
 P1110  Atmospheric Pressure Sensor Low Input (Subaru)  
 P1111  Intake Air Temperature (IAT) sensor intermittent high voltage  
 P1111  Engine Coolant Temperature Radiator Outlet Sensor Low Input (BMW)  
 P1111  Atmospheric Pressure Sensor High Input (Subaru)  
 P1112  Intake Air Temperature (IAT) sensor intermittent low voltage  
 P1112  Engine Coolant Temperature Radiator Outlet Sensor High Input (BMW)  
 P1112  Atmospheric Pressure Sensor Range/Performance Problem (Subaru)  
 P1114  Engine Coolant Temperature (ECT) sensor circuit intermittent low voltage  
 P1114  Intake Air Temperature 2 Circuit Low Input (Ford)  
 P1115  Engine Coolant Temperature (ECT) sensor circuit intermittent high voltage  
 P1115  Coolant Temperature Sensor Plausibility (BMW)  
 P1115  Intake Air Temperature 2 Circuit High Input (Ford)  
 P1116  Mass Or Volume Air Flow Circuit Range/Performance Problem (Bank 2) (BMW)  
 P1116  ECT Sensor Out Of Range (Ford, Mazda)  
 P1117  Mass Or Volume Air Flow Circuit Low Input (Bank 2) (BMW)  
 P1117  ECT Intermittent (Ford)  
 P1117  ECT Intermittent (Mazda)  
 P1118  Mass Or Volume Air Flow Circuit High Input (Bank 2) (BMW)  
 P1120  Pedal Position Sensor Circuit (BMW)  
 P1120  TPS Out Of Range Low (Ford, Mazda)  
 P1120  Secondary Throttle Position Sensor (Stps) (Infiniti)  
 P1121  Throttle Position (TP) Sensor Inconsistent With MAF Sensor High Voltage  
 P1121  Pedal Position 1 Range/Performance Problem (BMW)  
 P1122  Throttle Position (TP) Sensor Inconsistent With MAF Sensor Low Voltage  
 P1122  Pedal Position 1 Low Input (BMW)  
 P1123  Pedal Position 1 High Input (BMW)  
 P1124  TPS Out Of Self Test Range (Ford)  
 P1124  TPS Out Of Self Test Range (Mazda)  
 P1125  TPS Intermittant (Ford)  
 P1125  TPS Intermittant (Infiniti)  
 P1125  Tandem Throttle Position Sensor(Mazda)  
 P1126  Thermostat Function (Nissan)  
 P1127  Exhaust Not Warm Enough, Downstream Sensor Not Tested (Ford)  
 P1128  MAP Lower Than Expected (Acura, Honda)  
 P1129  MAP Higher Than Expected (Acura, Honda)  
 P1129  Upstream O2 Sensors Swapped Bank To Bank (HO2S-11-21) (Ford)  
 P1129  Downstream O2 Sensors Swapped Bank To Bank (HO2S-12-22) (Mazda)  
 P1130  Lack Of HO2S-11, Fuel Trim At Limit (Ford)  
 P1130  Heated O2 Sensor (HO2S) 11 At Adaptive Limit (Mazda)  
 P1130  Swirl Control SOL/V (Nissan)  
 P1130  Front Right Oxygen Sensor Circuit Open (Subaru)  
 P1130  A/F Sensor Circuit Range/Performance (Bank 1 Sensor 1) (Toyota)  
 P1131  HO2S 11 Indicates Lean (Ford, Mazda)  
 P1131  Front Right Oxygen Sensor Circuit Shorted (Subaru)  
 P1132  O2 Sensor Heater Control Circuit (Bank 1 Sensor 1) (BMW)  
 P1132  HO2S 11 Indicates Rich (Ford, Mazda)  
 P1133  Heated Oxygen Sensor (HO2S) insufficient switching bank 1 sensor 1 (Rear Bank)  
 P1133  O2 Sensor Heater Control Circuit (Bank 2 Sensor 1) (BMW)  
 P1133  A/F Sensor Circuit Response (Bank 1 Sensor 1) (Toyota)  
 P1134  Heated Oxygen Sensor (HO2S) transition time ratio bank 1 sensor 1 (Rear Bank)  
 P1134  O2 Sensor Heater Circuit Signal Intermittent (Bank 1 Sensor 2) (BMW)  
 P1134  Front Oxygen (A/F) Sensor Micro-Computer Problem (Subaru)  
 P1135  O2 Sensor Heater Circuit Low Voltage (Bank 1 Sensor 1) (BMW)  
 P1135  Intake Valve Timing Control (Right Bank) (Infiniti)  
 P1135  Front Left Oxygen Sensor Circuit Open (Subaru)  
 P1135  A/F Sensor Heater Circuit Malfunction (Bank 1 Sensor 1) (Toyota)  
 P1136  O2 Sensor Heater Circuit High Voltage (Bank 1 Sensor 1) (BMW)  
 P1136  Front Left Oxygen Sensor Curcuit Shorted (Subaru)  
 P1137  O2 Sensor Heater Circuit Signal Intermittant (Bank 1 Sensor 2) (BMW)  
 P1137  Lack Of HO2S-12 Switch Indicates Lean (Ford)  
 P1138  O2 Sensor Heater Circuit Low Voltage (Bank 1 Sensor 2) (BMW)  
 P1138  Lack Of HO2S-12 Switch Indicates Rich (Ford)  
 P1139  O2 Sensor Heater Circuit High Voltage (Bank 1 Sensor 2) (BMW)  
 P1139  Front Right Oxygen Sensor Heater Circuit Range (Subaru)  
 P1140  Mass or Volume Air Flow Circuit Range/Performance Problem (BMW)  
 P1140  Intake Valve Timing Control Position Sensor (Left Bank) (Infiniti)  
 P1140  Front Left Oxygen Sensor Heater Circuit Range (Subaru)  
 P1142  TPS Circuit Range/Perf. Problem (Low Input) (Subaru)  
 P1144  Mass Air Flow Sensor Open/Short To Ground. (Volkswagen)  
 P1145  Solenoid Valve Running Losses Control Circuit Electrical (BMW)  
 P1145  Intake Valve Timing Control Position Sensor (Right Bank) (Infiniti)  
 P1145  Mass Air Flow Sensor Short To Positive. (Volkswagen)  
 P1146  Pressure Sensor Circuit Range/Perf. (High Input) (Subaru)  
 P1146  Mass Air Flow Sensor Supply Voltage. (Volkswagen)  
 P1147  ETS Sub Accel Position Sensor 1 Malfunction (Hyundai)  
 P1148  Closed Loop Control (Bank 1) (Nissan, Infiniti)  
 P1150  Lack Of HO2S-21 Switch Fuel Trim At Limit (Ford)  
 P1150  A/F Sensor Circuit Range/Performance (Bank 2 Sensor 2) (Toyota)  
 P1151  O2 Sensor Heater Circuit Signal Intermittant (Bank 2 Sensor 1) (BMW)  
 P1151  Lack Of HO2S-21 Switch Indicates Lean (Ford)  
 P1151  ETS Main Accel Position Sensor 2 Malfunction (Hyundai)  
 P1152  O2 Sensor Heater Circuit Low Voltage (Bank 2 Sensor 1) (BMW)  
 P1152  Lack Of HO2S-21 Switch Indicates Rich (Ford)  
 P1153  O2 Sensor Heater Circuit High Voltage (Bank 2 Sensor 1) (BMW)  
 P1153  Heated Oxygen Sensor (HO2S) insufficient switching bank 2 sensor 1 (Front Bank)  
 P1153  A/F Sensor Circuit Response (Bank 2 Sensor 1) (Toyota)  
 P1154  Heated Oxygen Sensor (HO2S) transition time ratio bank 2 sensor 1 (Front Bank)  
 P1155  O2 Sensor Heater Circuit Intermittant (Bank 2 Sensor 2) (BMW)  
 P1155  ETS Limp Home Valve (Hyundai)  
 P1155  A/F Sensor Heater Circuit (Bank 2 Sensor 1) (Toyota)  
 P1155  Manifold Absolute Pressure Sensor Short To Positive. (Volkswagen)  
 P1156  O2 Sensor Heater Circuit Low Voltage (Bank 2 Sensor 2) (BMW)  
 P1156  Manifold Absolute Pressure Sensor Open/Short To Ground. (Volkswagen)  
 P1157  O2 Sensor Heater Circuit High Voltage (Bank 2 Sensor 2) (BMW)  
 P1157  Lack Of HO2S-22 Switch Indicates Lean (Ford)  
 P1157  Manifold Absolute Pressure Sensor Supply Voltage. (Volkswagen)  
 P1158  Fuel Trim Additve Bank 1 Low (BMW)  
 P1158  Lack Of HO2S-22 Switch Indicates Rich (Ford)  
 P1159  Fuel Trim Additve Bank 1 High (BMW)  
 P1159  Variable Intake Motor Malfunction (Hyundai)  
 P1160  Fuel Trim Additve Bank 2 Low (BMW)  
 P1160  Intake Air Temperature Sensor Short To Ground. (Volkswagen)  
 P1161  Fuel Trim Additve Bank 2 High (BMW)  
 P1161  Intake Air Temperature Sensor Open/Short To Positive. (Volkswagen)  
 P1162  Fuel Trim Additve Per Ignition Bank 1 Low (BMW)  
 P1162  Intake Air Temperature Sensor Short To Ground. (Volkswagen)  
 P1163  Fuel Trim Additve Per Ignition Bank 1 High (BMW)  
 P1163  Fuel Temperature Sensor Open/Short To Positive. (Volkswagen)  
 P1164  Fuel Trim Additve Per Ignition Bank 2 Low (BMW)  
 P1164  Fuel Temperature Sensor Implausible Signal. (Volkswagen)  
 P1165  Fuel Trim Additve Per Ignition Bank 2 High (BMW)  
 P1165  Swirl Control Valve Control Vacuum Check Switch (Nissan)  
 P1168  FRP Sensor In Range But Low (Ford)  
 P1168  Closed Loop Control (Bank 2) (Nissan, Infiniti)  
 P1169  FRP Sensor In Range But High (Ford)  
 P1171  Electronic Throttle System Open (Hyundai)  
 P1172  Electronic Throttle System Motor Current (Hyundai)  
 P1173  Electronic Throttle System Rationality Malfunction (Hyundai)  
 P1174  Fuel Trim Adaptation Additve Bank 1 Malfunction (BMW)  
 P1174  Electronic Throttle System #1 Close Malfunction (Hyundai)  
 P1175  Fuel Trim Adaptation Additve Bank 2 Malfunction (BMW)  
 P1175  Electronic Throttle System #2 Close Malfunction (Hyundai)  
 P1176  O2 Sensor Slow Response Bank 1 (BMW)  
 P1176  ETS Motor Open/Short #1 (Hyundai)  
 P1177  O2 Sensor Slow Response Bank 2 (BMW)  
 P1176  ETS Motor Open/Short #2 (Hyundai)  
 P1178  O2 Sensor Signal Circuit Slow Switching From Rich to Lean (Bank 1 Sensor 1) (BMW)  
 P1178  ETS Motor Battery Voltage Open (Hyundai)  
 P1179  O2 Sensor Signal Circuit Slow Switching From Rich to Lean (Bank 2 Sensor 1) (BMW)  
 P1180  O2 Sensor Signal Circuit Slow Switching From Rich to Lean (Bank 1 Sensor 2) (BMW)  
 P1180  Fuel Delivery System Low (Ford)  
 P1181  O2 Sensor Signal Circuit Slow Switching From Rich to Lean (Bank 2 Sensor 2) (BMW)  
 P1181  Fuel Delivery System High (Ford)  
 P1182  O2 Sensor (Bank 1 Sensor 2) Open Circuit During Coast Down Fuel Cut-off (BMW)  
 P1183  EOT Sensor Circuit Malfunction (Ford)  
 P1183  O2 Sensor (Bank 2 Sensor 2) Open Circuit During Coast Down Fuel Cut-off (BMW)  
 P1184  EOT Sensor Out Of Range (Ford)  
 P1186  O2 Sensor Heater Control Circuit (Bank 1 Sensor 2) (BMW)  
 P1187  O2 Sensor Heater Control Circuit (Bank 2 Sensor 2) (BMW)  
 P1188  Fuel Control (Bank 1 Sensor 1) (BMW)  
 P1189  Fuel Control (Bank 2 Sensor 1) (BMW)  
 P1189  Engine Oil Pressure Switch Circuit  
 P1190  Pre-catalyst Fuel Trim System Bank 1 (BMW)  
 P1191  Pre-catalyst Fuel Trim System Bank 2 (BMW)  
 P1192  Post-catalyst Fuel Trim System Bank 1 (BMW)  
 P1192  Inlet Air Temp. Circuit Low (Chrysler, Jeep)  
 P1193  Post-catalyst Fuel Trim System Bank 2 (BMW)  
 P1193  Inlet Air Temp. Circuit High (Chrysler, Jeep)  
 P1195  1/1 O2 Sensor Slow During Catalyst Monitor (Chrysler, Jeep)  
 P1196  2/1 O2 Sensor Slow During Catalyst Monitor (Chrysler, Jeep)  
 P1197  1/2 O2 Sensor Slow During Catalyst Monitor (Chrysler, Jeep)  
 P1198  Radiator Temperature Sensor Volts Too High (Chrysler, Jeep)  
 P1199  Radiator Temperature Sensor Volts Too Low (Chrysler, Jeep)  
 P1210   Traction Control System (TCS) Signal Circuit (Infiniti)  
 P1211   ABS/TCS Control Unit (Nissan)  
 P1212   ABS/TCS Communication Line (Nissan)  
 P1217   Engine Over Temperature (Overheat) (Nissan)  
 P1220   Fuel Pump Control Module (FPCM) (Infiniti)  
 P1221   Pedal Position Sensor 2 Range/Performance Problem (BMW)  
 P1222  Pedal Position Sensor 2 Low Input (BMW)  
 P1223  Pedal Position Sensor 2 High Input (BMW)  
 P1229  Supercharger Intercooler Pump Not Working (Ford)  
 P1232  Low Speed Fuel Pump Primary Circuit Malfunction (Ford)  
 P1233  Fuel System Disabled Or Offline (Ford)  
 P1234  Fuel System Disabled Or Offline (Ford)  
 P1235  Fuel Pump Control Out Of Range (Ford)  
 P1236  Fuel Pump Control Out Of Range (Ford)  
 P1237  Fuel Pump Secondary Circuit Malfunction (Ford)  
 P1238  Fuel Pump Secondary Circuit Malfunction (Ford)  
 P1244  Generator Load Input Low (Ford)  
 P1245  Generator Load Input High (Ford)  
 P1245  Needle Lift Sensor Short To Ground (Volkswagen)  
 P1246  Generator Load Input Failed (Ford)  
 P1246  Needle Lift Implausible Signal (Volkswagen)  
 P1247  Needle Lift Sensor Open/Short To Positive (Volkswagen)  
 P1248  Start Of Cold Start Injector Control Difference (Volkswagen)  
 P1251  Start Of Cold Start Injector Short To Positive (Volkswagen)  
 P1252  Start Of Cold Start Injector Open/Short To Ground (Volkswagen)  
 P1255  Engine Coolant Temperature Sensor Short To Ground (Volkswagen)  
 P1256  Engine Coolant Temperature Sensor Open/Short To Positive (Volkswagen)  
 P1258  Engine Metal Over Temperature Protection  
 P1259  VTEC System Malfunction (Acura, Honda)  
 P1260  Fuel Pump Speed Relay Control Circuit (GM)  
 P1260  Theft Detected - Engine Disabled (Ford, Mazda)  
 P1270  Control Module Self-Test, Torque Monitoring (BMW)  
 P1270  Vehicle Speed Limiter Reached (Ford, Mazda)  
 P1271  Ambient Air Pressure Sensor Electrical (BMW)  
 P1281  Engine Is Cold Too Long (Chrysler, Jeep)  
 P1282  Fuel Pump Relay Control Circuit(Chrysler, Jeep)  
 P1283  Switching Solenoid for Air Assisted Injection Valves Bank 1 Control Circuit Electrical (BMW)  
 P1284  Switching Solenoid for Air Assisted Injection Valves Bank 1 Control Circuit Signal Low (BMW)  
 P1285  Switching Solenoid for Air Assisted Injection Valves Bank 1 Control Circuit Signal High (BMW)  
 P1285  Cylinder Head Over Temperature Sensed (Ford)  
 P1287  Switching Solenoid for Air Assisted Injection Valves Bank 2 Control Circuit Electrical (BMW)  
 P1288  Switching Solenoid for Air Assisted Injection Valves Bank 2 Control Circuit Signal Low (BMW)  
 P1288  Intake Manifold Short Runner Solenoid Circuit (Chrysler, Jeep)  
 P1288  CHT Sensor Out of Self-Test Range (Ford)  
 P1289  Switching Solenoid for Air Assisted Injection Valves Bank 2 Control Circuit Signal High (BMW)  
 P1289  Manifold Tune Valve Solenoid Circuit (Chrysler, Jeep)  
 P1289  CHT Sensor High Input (Ford)  
 P1290  CNG Fuel Pressure Too High (Chrysler, Jeep)  
 P1290  CHT Sensor Low Input (Ford)  
 P1291  No Temp Rise Seen From Fuel Heaters (Chrysler, Jeep)  
 P1292  CNG Pressure Sensor Voltage Too High (Chrysler, Jeep)  
 P1293  CNG Pressure Sensor Voltage Too Low (Chrysler, Jeep)  
 P1294  Target Idle Not Reached (Chrysler, Jeep)  
 P1295  No 5 Volts To TP Sensor (Chrysler, Jeep)  
 P1296  No 5 Volts To MAP Sensor (Chrysler, Jeep)  
 P1297  Low Voltage ELD Circuit (Acura, Honda)  
 P1297  No Change in MAP From Start To Run (Chrysler, Jeep)  
 P1298  High Voltage In ELD Circuit (Acura, Honda)  
 P1298  Lean Operation At wide Open Throttle (Chrysler, Jeep)  
 P1299  Vacuum Leak Found (IAC Fully Seated)(Chrysler, Jeep)  
 P1299  Cylinder Head Over Temperature Protection Active (Ford)  
 P1300   Random Misfire (Acura)  
 P1300  Igniter Circuit Malfunction (Toyota)  
 P1309  Misfire Monitor Disabled (Ford)  
 P1313  "A" Camshaft Position Plausibility (BMW)  
 P1317  "B" Camshaft Position Plausibility (BMW)  
 P1320  Ignition Control (IC) Module 4x Reference Circuit Intermittent No Pulses  
 P1320  Ignition Signal (Nissan, Infiniti)  
 P1323  Ignition Control (IC) Module 24x Reference Circuit low frequency  
 P1327  Knock Sensor 2 (Bank 1) Low Input (BMW)  
 P1328  Knock Sensor 2 (Bank 1) High Input (BMW)  
 P1330  Spark Timing Adjust Malfunction (Hyundai)  
 P1332  Knock Sensor 4 Low Input (BMW)  
 P1333  Knock Sensor 4 High Input (BMW)  
 P1335  Crankshaft Position Sensor (REF) (Nissan)  
 P1335  Crankshaft Position Sensor Circuit Malfunction (Toyota)  
 P1336  Crankshaft Speed Fluctuation Sensor Intermittant Interruption (Acura)  
 P1336  CKP and/or CMP Input Signal to PCM Concerns (Ford)  
 P1336  Crankshaft Position System Variation Not Learned (GM)  
 P1336  Crankshaft Position Sensor (CKPS) (Nissan, Infiniti)  
 P1337  Crankshaft Speed Fluctuation Sensor No Signal (Acura)  
 P1340  Multiple Cylinder Misfire During Start (BMW)  
 P1341  Multiple Cylinder Misfire With Fuel Cut-off (BMW)  
 P1342  Misfire During Start Cylinder 1 (BMW)  
 P1343  Misfire Cylinder 1 With Fuel Cut-off (BMW)  
 P1344  Misfire During Start Cylinder 2 (BMW)  
 P1345  Misfire Cylinder 2 With Fuel Cut-off (BMW)  
 P1346  Misfire During Start Cylinder 3 (BMW)  
 P1347  Misfire Cylinder 3 With Fuel Cut-off (BMW)  
 P1348  Misfire During Start Cylinder 4 (BMW)  
 P1349  Misfire Cylinder 4 With Fuel Cut-off (BMW)  
 P1350  Misfire During Start Cylinder 5 (BMW)  
 P1350  Ignition Control System  
 P1351  Misfire Cylinder 5 With Fuel Cut-off (BMW)  
 P1351  Ignition Coil Control Circuit High Voltage (GM)  
 P1352  Misfire During Start Cylinder 6 (BMW)  
 P1352  Ignition Bypass Circuit High Voltage (GM)  
 P1353  Misfire Cylinder 6 With Fuel Cut-off (BMW)  
 P1354  Misfire During Start Cylinder 7 (BMW)  
 P1354  Modulating Piston Displacement Sensor Electrial Circuit Malfunction (Volkswagen)  
 P1355  Misfire Cylinder 7 With Fuel Cut-off (BMW)  
 P1356  Misfire During Start Cylinder 8 (BMW)  
 P1357  Misfire Cylinder 8 With Fuel Cut-off (BMW)  
 P1358  Misfire During Start Cylinder 9 (BMW)  
 P1359  Crankshaft Position/TDC/Cylinder Position Sensor Connector Disconnection (Acura)  
 P1359  Misfire Cylinder 9 With Fuel Cut-off (BMW)  
 P1360  Misfire During Start Cylinder 10 (BMW)  
 P1361  Intermittent Interruption In TDC1 Sensor Circuit (Acura, Honda)  
 P1361  Misfire Cylinder 10 With Fuel Cut-off (BMW)  
 P1361  Ignition Control (IC) Circuit Low Voltage (GM)  
 P1362  No Signal In TDC 1 Sensor Circuit (Acura, Honda)  
 P1362  Misfire During Start Cylinder 11 (BMW)  
 P1362  Ignition Bypass Circuit Low Voltage (GM)  
 P1363  Misfire Cylinder 11 With Fuel Cut-off (BMW)  
 P1364  Misfire During Start Cylinder 12 (BMW)  
 P1365  Misfire Cylinder 12 With Fuel Cut-off (BMW)  
 P1366  Intermittent Interruption In TDC 2 Sensor Circuit (Acura, Honda)  
 P1367  No Signal In TDC 2 Sensor Circuit (Acura, Honda)  
 P1370  Ignition Control (IC) Module 4x Reference too many pulses  
 P1371  Ignition Control (IC) Module 4x Reference too few pulses  
 P1374  CKP High to Low Resolution Frequency Correlation (GM)  
 P1375  Ignition Control (IC) Module 24x Reference High Voltage  
 P1376  Ignition Ground Circuit  
 P1377  Ignition Control (IC) Module Cam Pulse to 4x Reference Pulse Comparison  
 P1380  EBTCM DTC Detected-Rough Data Unusable  
 P1380  Misfire Detected - Rough Road Data Not Available (GM)  
 P1380  Variable Cam Timing Solenoid A Circuit Malfunction (Ford)  
 P1381  Misfire Detected-No EBTCM/PCM Serial Data  
 P1381  Cylinder Position Sensor Intermittant Inturruption (Acura)  
 P1381  Variable Cam Timing Over-advanced (Bank 1) (Ford)  
 P1381  Misfire Detected - No Commun. W/ Brake Control Mod (GM)  
 P1382  Cylinder Position Sensor No Signal (Acura)  
 P1383  Variable Cam Timing Over-retarded (Bank 1) (Ford)  
 P1384  Knock Sensor 3 Circuit (BMW)  
 P1385  Knock Sensor 4 Circuit (BMW)  
 P1386  Control Module Self-test, Knock Control Baseline Test Bank 1 (BMW)  
 P1387  Engine Control Module Inoperative (Volkswagen)  
 P1388  Auto Shutdown Relay Circuit (Chrysler, Jeep)  
 P1389  No ASD Relay Output Voltage At PCM (Chrysler, Jeep)  
 P1390  Timing Belt Skipped One Tooth or More (Chrysler, Jeep, Mitsubishi)  
 P1390  Octane Adjust Out Of Range (Mazda)  
 P1391  Intermittent Loss of CMP or CKP (Chrysler, Jeep)  
 P1396  Crankshaft Position Sensor Segment Timing Plausibility (BMW)  
 P1397  Camshaft Position Sensor "B" Circuit (Bank 1) (BMW)  
 P1398  Mis-Fire Adapter Numerator at Limit (Chrysler, Jeep)  
 P1399  Wait To Start Lamp Circuit (Chrysler, Jeep)  
 P1400   Heated Catalyst Battery Voltage or Current too Low During Heating (Bank 1) (BMW)  
 P1400  DPFE Sensor Low Voltage (Ford, Mazda)  
 P1400  EGRC-Solenoid Valve (Infiniti)  
 P1400  Manifold Differential Pressure Sensor Circuit Malfunction (Mitsubishi)  
 P1400  Fuel Tank Pressure Control Solenoid Circuit Low Input (Subaru)  
 P1401  Heated Catalyst Current too High During Heating (Bank 1) (BMW)  
 P1401  DPFE Sensor High Voltage (Ford, Mazda)  
 P1401  EGR Temperature Sensor (Infiniti)  
 P1402  Heated Catalyst Power Switch Overtemperature Condition (Bank 1) (BMW)  
 P1402  EGR Function (Open) (Infiniti)  
 P1402  EGR Vacuum Regulator Solenoid Valve Short To Positive (Volkswagen)  
 P1403  Carbon Canister Shut Off valve Control Circuit Electrical (BMW)  
 P1403  No 5 Volts To EGR Sensor (Chrysler, Jeep)  
 P1403  DPFE Hoses Reversed (Mazda)  
 P1403  EGR System Control Difference (Volkswagen)  
 P1404  Exhaust Gas Recirculation (EGR) Valve Pintle Stuck Open  
 P1404  Heated Catalyst Current too High During Heating (Bank 2) (BMW)  
 P1404  EGR Closed Position Performance (GM)  
 P1405  Heated Catalyst Power Switch Overtemperature Condition (Bank 2) (BMW)  
 P1405  DPFE Upstream Hose Off Or Plugged (Ford, Mazda)  
 P1406  Heated Catalyst Internal Control Module Checksum/ROM Error (BMW)  
 P1406  DPFE Downstream Hose Off Or Plugged (Ford, Mazda)  
 P1407  EGR No Flow Detected (Mazda)  
 P1408  EGR Out Of Self Test Range (Ford, Mazda)  
 P1409  EGR Vacuum Regulator Solenoid Circuit Malfunction (Ford, Mazda)  
 P1410  EGR Valve Position Sensor Circuit Malfunction (Toyota)  
 P1411  Secondary Air Injection System Downstream Flow (Ford)  
 P1413  Secondary Air Injection Pump Relay Control Circuit Signal Low (BMW)  
 P1413  Secondary Air Injection System Monitor Circuit Low (Ford)  
 P1414  Secondary Air Injection System Monitor Circuit High (BMW)  
 P1414  Secondary Air Injection System Monitor Circuit High (Ford)  
 P1415  Secondary Air Injection (AIR) System Bank 1 (GM)  
 P1416  Secondary Air Injection (AIR) System Bank 2 (GM)  
 P1420  Secondary Air Valve Control Circuit Electrical(BMW)  
 P1420  Fuel Tank Pressure Control Solenoid Circuit High Input (Subaru)  
 P1421  Secondary Air System Bank 1 (BMW)  
 P1422  Secondary Air System Bank 2 (BMW)  
 P1432  Secondary Air Injection System Incorrect Flow Detected (BMW)  
 P1432  THTRC Circuit Failure (Ford)  
 P1436  A/C Evaporator Temperature Circuit Low Input (Ford)  
 P1437  A/C Evaporator Temperature Circuit High Input (Ford)  
 P1438  Purge Control Valve Control Open Circuit (BMW)  
 P1439  Purge Control Valve Control Circuit Signal Low(BMW)  
 P1440  Purge Control Valve Control Circuit Signal High(BMW)  
 P1440  EVAP Control System (Small Leak) (Positive Pressure) (Nissan, Infiniti)  
 P1441  Evaporative System Flow During Non-Purge  
 P1441  Leakage Diagnostic Pump Control Open Circuit(BMW)  
 P1441  Evaporative Emission System Flow During Non-Purge (GM)  
 P1441  EGR Vacuum Regulator Solenoid Valve Open/Short To Ground (Volkswagen)  
 P1442  Leakage Diagnostic Pump Control Circuit Signal Low (BMW)  
 P1443  Leakage Diagnostic Pump Control Circuit Signal High (BMW)  
 P1443  Small Or No Purge Flow Condition (Ford)  
 P1443  Evaporative Emission Control System (Mazda)  
 P1443  EVAP System Vent Control Function Problem (Subaru)  
 P1444  Diagnostic Module Tank Leakage (DM-TL) Pump Control Open Circuit (BMW)  
 P1444  Purge Flow Sensor Low Input (Mazda)  
 P1444  Canister Purge Volume Control Solenoid Valve (Nissan, Infiniti)  
 P1445  Diagnostic Module Tank Leakage (DM-TL) Pump Control Circuit Signal Low (BMW)  
 P1445  Purge Flow Sensor High Input (Mazda)  
 P1446  Diagnostic Module Tank Leakage (DM-TL) Pump Control Circuit Signal High (BMW)  
 P1446  EVAP Canister Vent Control Valve (Close) (Nissan, Infiniti)  
 P1447  Diagnostic Module Tank Leakage (DM-TL) Pump Too High During Switching (BMW)  
 P1447  EVAP Control System Purge Flow Monitoring (Nissan, Infiniti)  
 P1448  Diagnostic Module Tank Leakage (DM-TL) Pump Too Low During Switching (BMW)  
 P1448  EVAP Canister Vent Control Valve (Open) (Nissan, Infiniti)  
 P1449  Diagnostic Module Tank Leakage (DM-TL) Pump Too High (BMW)  
 P1450  Diagnostic Module Tank Leakage (DM-TL) Switching Solenoid Open Circuit (BMW)  
 P1450  Unable To Bleed Up Fuel Tank Vacuum (Ford)  
 P1451  Diagnostic Module Tank Leakage (DM-TL) Switching Solenoid Control Circuit Signal Low (BMW)  
 P1451  EVAP Control System Canister Vent Solenoid Circuit Malfunction (Ford)  
 P1452  Diagnostic Module Tank Leakage (DM-TL) Switching Solenoid Control Circuit Signal High (BMW)  
 P1453  Secondary Air Injection Pump Relay Control Circuit Electrical (BMW)  
 P1454  Secondary Air Injection Pump With Series Resistor Control Circuit Electrical (BMW)  
 P1456  Leak Detected In EVAP Control System (Acura, Honda)  
 P1456  Heated Catalyst Heater Power Supply Open Circuit (Bank 1) (BMW)  
 P1457  Leak Detected In EVAP Control System (Acura, Honda)  
 P1457  Heated Catalyst Heater Power Switch Temperature Sensor Electrical (Bank 1) (BMW)  
 P1459  Heated Catalyst Heater Power Supply Open Circuit (Bank 2) (BMW)  
 P1460  Heated Catalyst Heater Power Switch Temperature Sensor Electrical (Bank 2) (BMW)  
 P1460  WOT A/C Cutoff Circuit Malfunction (Ford, Mazda)  
 P1461  Heated Catalyst Gate Voltage Signal Low (BMW)  
 P1461  ACP Sensor High Voltage (Ford)  
 P1462  Heated Catalyst Internal Control Module Checksum/ROM Error (BMW)  
 P1462  ACP Sensor Low Voltage (Ford)  
 P1463  Heated Catalyst Battery Temperature Sensor 1 Electrical (BMW)  
 P1463  ACP Sensor Insufficent Pressure Change (Ford)  
 P1464  Heated Catalyst Battery Temperature Sensor 2 Electrical (BMW)  
 P1464  A/C Demand Out Of Range (Ford)  
 P1464  Fuel Level Sensor Circuit (Ground Signal) (Nissan)  
 P1465  Heated Catalyst Battery Temperature Sensor 1 or 2 Plausibility (BMW)  
 P1466  Heated Catalyst Power Switch Temperature Sensor Plausibility (BMW)  
 P1467  Heated Catalyst Comparison Battery Voltages of Power Switches Plausibility (BMW)  
 P1468  Heated Catalyst Battery Disconnecting Switch Plausibility (BMW)  
 P1469  Low A/C Cycling Period (Ford)  
 P1470  Leakage Diagnostic Pump Control Circuit Electrical (BMW)  
 P1472  Diagnostic Module Tank leakage (DM-TL) Switching Solenoid Control Circuit Electrical (BMW)  
 P1473  Diagnostic Module Tank leakage (DM-TL) Pump Current Plausibility (BMW)  
 P1474  HCF Primary Circuit Failure (Ford)  
 P1474  LFC Primary Circuit Failure (Ford)  
 P1475  Leakage Diagnostic Pump Reed Switch Did Not Close (BMW)  
 P1476  Leakage Diagnostic Pump Clamped Tube (BMW)  
 P1476  Too Little Secondary Air (Chrysler, Jeep)  
 P1477  Leakage Diagnostic Pump Reed Switch Did Not Open (BMW)  
 P1477  Too Much Secondary Air (Chrysler, Jeep)  
 P1477  MFC Primary Circuit Failure (Ford)  
 P1478  Battery Temp Sensor Volts Out of Limit (Chrysler, Jeep)  
 P1479  Transmission Fan Relay Circuit (Chrysler, Jeep)  
 P1479  HFC Primary Circuit Failure (Ford)  
 P1480  PCV Solenoid Valve (Chrysler, Jeep)  
 P1480  Cooling Fan Relay 1 Circuit High Input (Subaru)  
 P1482  Catalyst Temperature Sensor Circuit Shorted Low (Chrysler, Jeep)  
 P1483  Engine Cooling System Performance  
 P1483  Catalyst Temperature Sensor Circuit Shorted High (Chrysler, Jeep)  
 P1484  Catalytic Converter Overheat Detected (Chrysler, Jeep)  
 P1485  Air Injection Solenoid Circuit (Chrysler, Jeep)  
 P1486  Evap Leak Monitor Pinched Hose (Chrysler, Jeep)  
 P1487  Hi Speed Rad Fan CTRL Relay Circuit (Chrysler, Jeep)  
 P1488  Auxiliary 5 Volt Supply Output Too Low (Chrysler, Jeep)  
 P1489  High Speed Fan CTRL Relay Circuit (Chrysler, Jeep)  
 P1490  Low Speed Fan CTRL Relay Circuit (Chrysler, Jeep)  
 P1490  Vacuum Cut Valve Bypass Valve (Circuit) (Nissan, Infiniti)  
 P1491  Malfunction In EGR System (Acura, Honda)  
 P1491  Rad Fan Control Relay Circuit (Chrysler, Jeep)  
 P1491  Vacuum Cut Valve Bypass Valve (Nissan, Infiniti)  
 P1492  EVAP Canister Purge Control/Solenoid Valve (Circuit) (Nissan, Infiniti)  
 P1492  Ambient/Batt Temp Sen Volts Too High (Chrysler, Jeep)  
 P1493  Ambient/Batt Temp Sen Volts Too Low (Chrysler, Jeep)  
 P1493  EVAP Canister Purge Control Valve/Solenoid Valve (Infiniti)  
 P1494  Leak Detection Pump Switch or Mechanical Fault (Chrysler, Jeep)  
 P1495  Leak Detection Pump Solenoid Circuit (Chrysler, Jeep)  
 P1496  5 Volt Supply Output Too Low (Chrysler, Jeep)  
 P1498  Voltage Problem In EGR Valve Position Sensor Circuit (Acura, Honda)  
 P1498  High speed Rad Fan Ground CTRL Rly Circuit (Chrysler, Jeep)  
 P1500   Idle Speed Control Valve Stuck Open (BMW)  
 P1500  Vehicle Speed Sensor (VSS) Intermittant (Ford, Mazda)  
 P1500  Generator FR Terminal Circuit Malfunction (Mitsubishi)  
 P1501  Idle Speed Control Valve Stuck Closed (BMW)  
 P1501  Vehicle Speed Sensor (VSS) Out Of Range (Ford)  
 P1502  Idle Speed Control Valve Closing Solenoid Control Circuit Signal High (BMW)  
 P1502  Vehicle Speed Sensor (VSS) Intermittant (Ford)  
 P1502  Idle Speed Control Valve Closing Solenoid Control Circuit Signal Low (BMW)  
 P1503  Idle Speed Control Valve Closing Solenoid Control Circuit Signal Low (BMW)  
 P1504  Idle Speed Control Valve Closing Solenoid Control Open Circuit (BMW)  
 P1504  Idle Air Control (IAC) Circuit Malfunction (Ford)  
 P1505  Idle Speed Control Valve Closing Solenoid Control Circuit Electrial (BMW)  
 P1505  Idle Air Control At Adaptive Clip (Mazda)  
 P1506  Idle Speed Control Valve Open Solenoid Control Circuit Signal High (BMW)  
 P1506  Idle Air Control System Overspeed Error (Ford, Mazda)  
 P1507  Idle Speed Control Valve Open Solenoid Control Circuit Signal Low (BMW)  
 P1507  Idle Air Control System Underspeed Error (Ford, Mazda)  
 P1507  Idle Control System Malfunction (Fail-Safe) (Subaru)  
 P1508  Idle Air Control (IAC) System - Low RPM  
 P1508  Idle Air Control Valve Circuit Failure (Acura)  
 P1508  Idle Speed Control Valve Opening Solenoid Control Open Circuit (BMW)  
 P1509  Idle Speed Control Valve Opening Solenoid Control Circuit Electrial (BMW)  
 P1510  Idle Speed Control Valve Stuck (BMW)  
 P1511  DISA Control Circuit Electrical (BMW)  
 P1512  DISA Control Circuit Signal Low (BMW)  
 P1513  DISA Control Circuit Signal High (BMW)  
 P1516  Inlet Manifold Runner Control Input Error (Bank 1) (Ford)  
 P1517  Inlet Manifold Runner Control Input Error (Bank 2) (Ford)  
 P1518  Inlet Manifold Runner Control Stuck Open (Ford)  
 P1518  Starter Switch Circuit Low Input (Subaru)  
 P1519  Malfunction In IAC Valve Circuit (Acura, Honda)  
 P1519  "A" Camshaft Position Actuator Bank 1 (BMW)  
 P1519  Inlet Manifold Runner Control Stuck Closed (Ford)  
 P1520  Intake Manifold Runner Control (IMRC) circuit malfunction  
 P1520  "B" Camshaft Position Actuator Bank 1 (BMW)  
 P1520  Stop Light Switch Signal Malfunction (Toyota)  
 P1521   Power Steering Switch Malfunction (Hyundai)  
 P1522  "A" Camshaft Position Actuator Bank 2 (BMW)  
 P1523  "A" Camshaft Position Actuator Signal Low Bank 1 (BMW)  
 P1524  Throttle Position (TP) Sensor Learned Closed Throttle Angle Degrees Out-Of-Range  
 P1524  "A" Camshaft Position Actuator Signal High Bank 1 (BMW)  
 P1525  Throttle Position (TP) Sensor Learned Closed Throttle Angle Degrees Out-Of-Range  
 P1525  "A" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1526  "A" Camshaft Position Actuator Control Open Circuit Bank 2 (BMW)  
 P1527  Trans Range / Pressure Switch Comparison  
 P1527  "A" Camshaft Position Actuator Control Circuit Signal Low Bank 1 (BMW)  
 P1528  "A" Camshaft Position Actuator Control Circuit Signal High Bank 1 (BMW)  
 P1529  "B" Camshaft Position Actuator Control Circuit Signal Low Bank 1 (BMW)  
 P1530  "B" Camshaft Position Actuator Control Circuit Signal High Bank 1 (BMW)  
 P1531  "B" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1532  "B" Camshaft Position Actuator Control Open Circuit Bank 2 (BMW)  
 P1533  "B" Camshaft Position Actuator Control Circuit Signal Low Bank 2 (BMW)  
 P1534  "B" Camshaft Position Actuator Control Circuit Signal High Bank 2 (BMW)  
 P1537  Fuel Cut-off Valve Incorrect Function (Volkswagen)  
 P1538  Fuel Cut-off Valve Open/Short To Ground (Volkswagen)  
 P1540   Pedal Position Sensor (BMW)  
 P1540  VSS Signal Too High (Volkswagen)  
 P1541  Pedal Position Sensor Double Error (BMW)  
 P1542  Pedal Position Sensor Electrical (BMW)  
 P1543  Pedal Position Sensor (BMW)  
 P1544  Pedal Position Sensor (BMW)  
 P1545  Pedal Position Sensor (BMW)  
 P1546  Pedal Position Sensor (BMW)  
 P1546  Air Conditioning (A/C) Clutch Relay Control Circuit (GM)  
 P1546  Wastegate Bypass Regulator Valve Short To Positive (Volkswagen)  
 P1549  Intake Manifold Control Circuit Malfunction (Ford)  
 P1549  Wastegate Bypass Regulator Valve Open/Short To Ground (Volkswagen)  
 P1550  Idle Speed Control valve Closing Solenoid Control Circuit Electrical (BMW)  
 P1550   PSP Sensor Malfunction (Ford)  
 P1550  Charge Pressure Control Difference (Volkswagen)  
 P1551  "A" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1552  "A" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1554  Cruise Engaged Circuit High Voltage  
 P1556  "A" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1560  Cruise Control System-Transaxle Not in Drive  
 P1560  "B" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1560  Back-Up Voltage Circuit Malfunction (Subaru)  
 P1561  Quantity Adjuster Control Difference (Volkswagen)  
 P1562  Quantity Adjuster Upper Stop Value (Volkswagen)  
 P1563  Quantity Adjuster Lower Stop Value (Volkswagen)  
 P1564  Cruise Control System-Vehicle Acceleration too high  
 P1564  Control Module Selection (BMW)  
 P1565  "B" Camshaft Position Actuator Control Open Circuit Bank 1 (BMW)  
 P1566  Cruise Control System-Engine RPM Too High  
 P1567  Cruise Control- ABCS Active  
 P1569  "A" Camshaft Position Actuator Control Open Circuit Bank 2 (BMW)  
 P1570  Cruise Control System - Traction Control Active  
 P1571  Traction Control System PWM Circuit No Frequency  
 P1572  Brake Pedal Switch Circuit (Ford)  
 P1574  EBTCM System- Stop Lamp Switch Circuit High Voltage  
 P1575  Extended Travel Brake Switch Circuit High Voltage  
 P1579  Park/Neutral to Drive/Reverse At high Throttle Angle  
 P1580  Throttle Valve Mechanically Stuck (BMW)  
 P1581  "B" Camshaft Position Actuator Control Open Circuit Bank 2 (BMW)  
 P1585  Cruise Control Inhibit Output Circuit (GM)  
 P1589  Control Module Self Test, Knock Control Test Pulse Bank 1 (BMW)  
 P1590  Neutral Position Switch Circuit High Input (Subaru)  
 P1591  Neutral Position Switch Circuit Low Input (Subaru)  
 P1593  DISA Control Circuit Electrical (BMW)  
 P1594  "B" Camshaft Position Actuator Control Open Circuit Bank 2 (BMW)  
 P1594  Charging System Voltage Too High (Chrysler, Jeep)  
 P1594  AT Diagnosis Input Signal Circuit Malfunction (Subaru)  
 P1595  Speed Control Solenoid Circuits (Chrysler, Jeep)  
 P1595  AT Diagnosis Input Signal Circuit Low Input (Subaru)  
 P1596  Speed Control Switch always High (Chrysler, Jeep)  
 P1596  AT Diagnosis Input Signal Circuit High Input (Subaru)  
 P1597  Speed Control Switch always Low (Chrysler, Jeep)  
 P1598  A/C Pressure Sensor Volts Too High (Chrysler, Jeep)  
 P1599  A/C Pressure Sensor Volts Too Low (Chrysler, Jeep)  
 P1599  Engine Stall or Near Stall Detected  
 P1600   Battery Voltage SRC High Exceeded (Jeep)  
 P1600  ECM BATT Malfunction (Toyota)  
 P1600  Supply Voltage Too Low (Volkswagen)  
 P1602   Loss of EBTCM Serial Data  
 P1602  Control Module Self Test, Control Module Defective (BMW)  
 P1602  PCM Not Programmed (Chrysler, Jeep)  
 P1603 Loss of SDM Serial Data 
 P1603  Control Module Self Test, Torque Monitoring (BMW)  
 P1603  Battery Backup Circuit Malfunction (Mitsubishi)  
 P1604  Loss of IPC Serial Data  
 P1604  Control Module Self Test, Speed Monitoring (BMW)  
 P1605  Loss of HVACC Serial Data  
 P1605  Keep Alive Memory Failure (Ford)  
 P1605  Powertrain Control Module (Mazda)  
 P1605  A/T Diagnosis Communication Line (Nissan, Infiniti)  
 P1607  Malfunction In PCM Internal Circuit (Acura, Honda)  
 P1607  CAN Version (BMW)  
 P1607  Electronic Throttle System Communication Error (Hyundai)  
 P1608  Serial Communicating Link Control Module (BMW)  
 P1609  Serial Communicating Link EML (BMW)  
 P1610  Loss of PZM Serial Data  
 P1610  Immobilizer Function (Mitsubishi)  
 P1611  Loss of CVRTD Serial Data  
 P1611  Serial Communicating Link Transmission Control Module (BMW)  
 P1612  Engine Control Module Incorrectly Coded (Volkswagen)  
 P1614  Electronic Throttle System Module Malfunction (Hyundai)  
 P1616  Glow Plug Indicator Lamp Short To Positive (Volkswagen)  
 P1617  Engine Oil Level Switch Circuit  
 P1617  Glow Plug Indicator Lamp Open/Short To Ground (Volkswagen)  
 P1618  Glow Plug Relay Short To Positive (Volkswagen)  
 P1619  MAP Cooling Control Circuit Signal Low (BMW)  
 P1619  Glow Plug Relay Open/Short To Ground (Volkswagen)  
 P1620  MAP Cooling Control Circuit Signal High (BMW)  
 P1621  PCM Memory Performance  
 P1622  MAP Cooling Control Circuit Electrical (BMW)  
 P1623  Pedal Position Sensor Potentiometer Supply (BMW)  
 P1624  Pedal Position Sensor Potentiometer Supply Channel 1 Electrical (BMW)  
 P1624  Customer Snapshot Requested - Data Available (GM)  
 P1625  Pedal Position Sensor Potentiometer Supply Channel 2 Electrical (BMW)  
 P1626  Theft Deterrent System - Fuel Enable Circuit  
 P1626  Implausible Signal From Transmission Control Module (Volkswagen)  
 P1630  Theft Deterrent - PCM in Learn Mode  
 P1631  Theft Deterrent - Password Incorrect  
 P1631  Throttle Position Sensor Signal Too High (Volkswagen)  
 P1632  Theft Deterrent - Fuel Disabled  
 P1632  Throttle Valve Adaptation; Adaptation Condition Not Met (BMW)  
 P1632  Traction Control System Malfunction (Hyundai)  
 P1632  Throttle Position Sensor Supply Voltage (Volkswagen)  
 P1633  Ignition Supplement Power Circuit Low Voltage  
 P1633  Throttle Valve Adaptation; Limp Home Position (BMW)  
 P1633  Keep Alive Power Voltage Too Low (Ford)  
 P1634  Ignition 1 Power Circuit Low Voltage  
 P1634  Throttle Valve Adaptation; Spring Test Failed (BMW)  
 P1635  Throttle Valve Adaptation; Lower Mechanical Stop Not Adapted (BMW)  
 P1635  5 Volt Reference Circuit (GM)  
 P1635  Tire/Axle Out Of Acceptable Range (Ford)  
 P1636  Throttle Valve Control Circuit (BMW)  
 P1636  Inductive Signiture Chip Communication Error (Ford)  
 P1637  Throttle Valve Position Control; Control Deviation (BMW)  
 P1638  Throttle Valve Position Control; Throttle Stuck Temporarily (BMW)  
 P1639  Throttle Valve Position Control; Throttle Stuck Permanently (BMW)  
 P1639  5 Volt Reference 2 Circuit (GM)  
 P1639  Vehicle ID Block Not Programmed Or Corrupt (Ford)  
 P1639  Throttle Position Sensor Implausible Signal (Volkswagen)  
 P1640  Internal Control Module (ROM/RAM) Error (BMW)  
 P1640  DTC's Available In Another Module (Ford)  
 P1640  Driver 1 - Input High Voltage  
 P1640  Engine Control Module Inoperative (Volkswagen)  
 P1641  Malfunction Indicator Lamp (MIL) Control Circuit  
 P1642  Vehicle Speed Output Circuit  
 P1644  Delivered Torque Output Circuit  
 P1645  EVAP Solenoid Output Circuit  
 P1646  EVAP Vent Valve Output Circuit  
 P1648  CAN-Bus System Component Failure (Volkswagen)  
 P1649  Implausible Signal From ABS Control Module (Volkswagen)  
 P1650  Driver 2 - Input High Voltage  
 P1650  Power Steering Pressure Switch Malfunction (Ford)  
 P1650  Power Steering Pressure Switch Out Of Range (Mazda)  
 P1651  Power Steering Pressure Switch Input Malfunction (Mazda)  
 P1651  Power Steering Pressure Switch Signal Malfunction (Ford)  
 P1652  Lift/Dive Circuit  
 P1654  Cruise Disable Output Circuit  
 P1656  Automatic Transaxle (Acura, Honda)  
 P1660  Cooling Fan Control Circuits  
 P1660  A/T FI Data Line Failure (Acura, Honda)  
 P1670  ODM has Detected a Voltage greater than 33 volts (GM)  
 P1676  FPTDR Signal Failure (Acura, Honda)  
 P1678  FPTDR Signal Line Failure (Acura, Honda)  
 P1680  Clutch Released Switch Circuit (Chrysler, Jeep)  
 P1681  No I/P Cluster CCD/J1850 Messages Received (Chrysler, Jeep)  
 P1681  A/T FI Signal A Low Input (Acura, Honda)  
 P1682  A/T FI Signal A High Input (Acura, Honda)  
 P1682  Charging System Voltage Too Low (Chrysler, Jeep)  
 P1683  Speed Control Power Relay or S/C 12V Driver Circuit (Chrysler, Jeep)  
 P1684  Battery Disconnected Within Last 50 Starts (Chrysler, Jeep)  
 P1685  Skim Invalid Key (Chrysler, Jeep)  
 P1686  No SKIM Bus Message Received (Chrysler, Jeep)  
 P1686  A/T FI Signal B Low Input (Acura, Honda)  
 P1687  A/T FI Signal B High Input (Acura, Honda)  
 P1687  No Cluster Bus Message (Chrysler, Jeep)  
 P1689  Traction Control Delivered Torque Output Circuit (GM)  
 P1690  Malfunction Indicator Lamp (MIL) Electrical (BMW)  
 P1693  DTC Detected In Companion Mode (Chrysler, Jeep)  
 P1694  Fault In Companion Mode (Chrysler, Jeep)  
 P1695  No CCD/J185O Message From BCM (Chrysler, Jeep)  
 P1696  PCM Failure EEPROM Write Denied (Chrysler, Jeep)  
 P1697  PCM Failure SRI Mile Not Stored (Chrysler, Jeep)  
 P1698  No Bus Message From TCM (Chrysler, Jeep)  
 P1698  Engine Torque Control Cut Signal Circuit Low Input (Subaru)  
 P1699  Engine Torque Control Cut Signal Circuit High Input (Subaru)  
 P1700   TPS Circuit Malfunction For AT (Subaru)  
 P1701   Transmission Solenoid Malfunction (Mazda)  
 P1701   Cruise Control Set Signal Circuit Malfunction For AT (Subaru)  
 P1703  Brake On/Off Switch (Mazda)  
 P1703  Brake On/Off Switch Out Of Range (Ford)  
 P1703   Low Clutch Timing Control Solenoid Circuit Malfunction (Subaru)  
 P1705  Automatic Transaxle (Acura, Honda)  
 P1705  Transmisson Range Sensor Out Of Range (Ford)  
 P1705  Transmisson Range Sensor (Mazda)  
 P1705  Throttle Position Sensor ((Nissan, Infiniti))  
 P1706  Automatic Transaxle (Acura, Honda)  
 P1706  Park/Neutral Position (PNP) Switch (Nissan)  
 P1709  Automatic Transaxle (Acura, Honda)  
 P1709  Park/Neutral Position Switch Out Of Range (Ford, Mazda)  
 P1710  Automatic Transaxle (Acura, Honda)  
 P1711  Transmission Fluid Temperature Sensor (Mazda)  
 P1711   Engine Torque Control Signal 1 Circuit Malfunction (Subaru)  
 P1712   Engine Torque Control Signal 2 Circuit Malfunction (Subaru)  
 P1713  Automatic Transaxle (Acura, Honda)  
 P1719  Skip Shift Sole

Коды ошибок OBD-II(P1720-P1900)

P1729  4x4 Low Switch Malfunction (Ford, Mazda)  
 P1734  Pressure Control Solenoid "B" Electrical (BMW)  
 P1738  Automatic Transaxle (Acura, Honda)  
 P1738  Pressure Control Solenoid "C" Electrical (BMW)  
 P1739  Automatic Transaxle (Acura, Honda)  
 P1740  Automatic Transaxle (Acura, Honda)  
 P1743  Pressure Control Solenoid "E" Electrical (BMW)  
 P1744  Pressure Control Solenoid "A" Electrical (BMW)  
 P1746  EPC Solenoid Failed Low (Mazda)  
 P1746  Transmission Control Module Output Stage (BMW)  
 P1747  CAN Bus Monitoring (BMW)  
 P1747  EPC Solenoid Short Circuit (Mazda)  
 P1748  Transmission Control Module Self Test (BMW)  
 P1749  Secondary Pressure Solenoid Communication Error (BMW)  
 P1749  EPC Solenoid Open Circuit (Mazda)  
 P1750  Secondary Pressure Solenoid Circuit Range/Performance (BMW)  
 P1751  Secondary Pressure Solenoid Open Circuit (BMW)  
 P1751  Shift Solenoid #1 (SS1) (Mazda)  
 P1751  A/T Control Relay Malfunction (Mitsubishi)  
 P1753  Automatic Transaxle (Acura, Honda)  
 P1754  Coast Clutch Solenoid (Mazda)  
 P1756  GOV Press Not Equal To Target @ 15-20 PSI (Chrysler, Jeep)  
 P1756  Shift Solenoid #2 (SS2) (Mazda)  
 P1757  GOV Press Not Equal To Target @ 15-20 PSI (Chrysler, Jeep)  
 P1758  Automatic Transaxle (Acura, Honda)  
 P1760  Overrun Clutch Solenoid Valve (Nissan, Infiniti)  
 P1761  Shift Solenoid Malfunction (BMW)  
 P1761  Shift Solenoid #3 (SS3) (Mazda)  
 P1762  Gov Press Sen Offset Volts Too Low or high(Chrysler, Jeep)  
 P1763  Governor Pressure Sensor Volts Too High (Chrysler, Jeep)  
 P1764  Governor Pressure Sensor Volts Too Low (Chrysler, Jeep)  
 P1765  CAN Throttle Valve (BMW)  
 P1765  Trans 12 Volt Supply Relay CTRL Circuit (Chrysler, Jeep)  
 P1768  Automatic Transaxle (Acura, Honda)  
 P1770  CAN Torque Interface (BMW)  
 P1773  Automatic Transaxle (Acura, Honda)  
 P1778  Automatic Transaxle (Acura, Honda)  
 P1780  CAN Torque Reduction (BMW)  
 P1780  Transmission Control Switch (Mazda)  
 P1780  Transmission Control Switch Out Of Range(Ford)  
 P1780  Park/Neutral Position Switch Malfunction (Only For A/T) (Toyota)  
 P1781  4x4 Switch Out Of Range (Ford, Mazda)  
 P1783  Transmission Over Temperature Condition (Mazda)  
 P1786  Automatic Transaxle (Acura, Honda)  
 P1790  Automatic Transaxle (Acura, Honda)  
 P1791  Automatic Transaxle (Acura, Honda)  
 P1792  Automatic Transaxle (Acura, Honda)  
 P1794  Automatic Transaxle (Acura, Honda)  
 P1810   TFP Valve Position Switch Circuit (GM)  
 P1811  Maximum Adapt and Long Shift (GM)  
 P1819  Internal Mode Switch - No Start/Wrong Range (GM)  
 P1820  Internal Mode Switch Circuit A Low (GM)  
 P1822  Internal Mode Switch Circuit B High (GM)  
 P1823  Internal Mode Switch Circuit P Low (GM)  
 P1825  Internal Mode Switch - Invalid Range (GM)  
 P1826  Internal Mode Switch Circuit C High (GM)  
 P1851  Implausible Signal From ABS Control Module (Volkswagen)  
 P1854  Drive Train CAN-Bus Inoperative (Volkswagen)  
 P1860  TCC PWM Solenoid Circuit Electrical (GM)  
 P1887  TCC Release Switch Circuit (GM)  
 P1899  Park/Neutral Position Switch Stuck In Park or In Gear (Chrysler, Jeep)  
P1900  Output Shaft Speed Sensor Circuit Failure (Ford)

Коды ошибок CAN BUS(B1001-B2263)

"B1001 HEADLAMP LEVELING RELAY COIL SHORT TO BATTERY",
"B1002 HEADLAMP LEVELING RELAY COIL FAILURE",
"B1003 MODE DOOR CIRCUIT FAILURE",
"B1004 GLOW PLUG SHORT TO BATTERY OR TRANSISTOR FAILURE",
"B1005 FUEL PUMP SHORT TO BATTERY OR TRANSISTOR FAILURE",
"B1006 LOW FUEL LEVEL TO START HEATER",
"B1007 COOLANT PUMP SHORT TO BATTERY OR TRANSISTOR FAILURE",
"B1008 BLOWER FAN SHORT TO BATTERY OR TRANSISTOR FAILURE",
"B1009 HEAT SWITCH SHORT TO GROUND",
"B1010 PARKING AID MODULE SWITCH NOT CONNECTED",
"B1011 REAR WIPER PARK SENSE STUCK",
"B1012 REAR WIPER PARK SENSE FAILURE",
"B1013 OCCUPANT CLASSIFICATION SYSTEM CALIBRATION FAULT",
"B1014 RAIN SENSOR INTERNAL FAULT",
"B1015 CEI UNCONFIGURED",
"B1016 JUMP START CONTROL MODULE FAULT",
"B1017 AIRBAG DEPLOYMENT DISABLED FOR MANUFACTURING",
"B1018 (HEV) POWER CHECK FAILURE",
"B1020 DOOR MOTOR DRIVER CIRCUIT FAILURE",
"B1021 END BUTTON CIRCUIT SHORT TO BATTERY",
"B1022 END BUTTON CIRCUIT FAILURE",
"B1023 TALK BUTTON CIRCUIT SHORT TO BATTERY",
"B1024 TALK BUTTON CIRCUIT FAILURE",
"B1025 SEND BUTTON CIRCUIT SHORT TO BATTERY",
"B1026 SEND BUTTON CIRCUIT FAILURE",
"B1027 AIR DISCHARGE TEMPERATURE SENSOR (RIGHT) FLOOR SHORT TO GROUND",
"B1028 AIR DISCHARGE TEMPERATURE SENSOR (RIGHT) FLOOR OPEN CIRCUIT",
"B1029 AIR DISCHARGE TEMPERATURE SENSOR (RIGHT) PANEL SHORT TO GROUND",
"B1030 AIR DISCHARGE TEMPERATURE SENSOR (RIGHT) PANEL OPEN CIRCUIT",
"B1031 SDARS SATELLITE ANTENNA OPEN",
"B1032 SDARS SATELLITE ANTENNA SHORT",
"B1033 SDARS SERVICE DEACTIVATED",
"B1034 RADIO START SIGNAL CIRCUIT FAILURE",
"B1035 CD-READ-TEST READ ERROR",
"B1038 MICROPHONE INPUT CIRCUIT FAILURE",
"B1039 MICROPHONE INPUT CIRCUIT SHORT TO BATTERY",
"B1040 LED ARRAY CIRCUIT SHORT TO BATTERY",
"B1041 DIRECTION INDICATOR POWER FEED BLOWN FUSE",
"B1042 FRONT CRASH SENSOR #2 INTERNAL FAULT",
"B1043 FRONT CRASH SENSOR #2 DRIVER COMMUNICATIONS FAULT",
"B1044 FRONT CRASH SENSOR #2 SHORT TO GROUND/VBATT",
"B1045 FRONT CRASH SENSOR #2 CROSS LINK TO ANOTHER SENSOR",
"B1046 DRIVER SIDE AIRBAG CURTAIN CROSS LINK TO ANOTHER FIRING LOOP",
"B1047 DRIVER SIDE, SIDE MOUNT AIRBAG CROSS LINK TO ANOTHER FIRING LOOP",
"B1048 PASSENGER SIDE AIRBAG CROSS LINK TO ANOTHER FIRING LOOP",
"B1049 PASSENGER SEATBELT PRETENSIONER CROSS LINK TO ANOTHER FIRING LOOP",
"B104A FRONT CRASH SENSOR #2 ID FAULT",
"B104B DRIVER SIDE CRASH SENSOR CROSS LINK TO ANOTHER SENSOR",
"B104C PASSENGER SIDE CRASH SENSOR CROSS LINK TO ANOTHER SENSOR",
"B104D FRONT CRASH SENSOR CROSS LINK TO ANOTHER SENSOR",
"B104E DRIVER SIDE CRASH SENSOR CIRCUIT SHORT TO GND/VBATT",
"B104F PASSENGER SIDE CRASH SENSOR INTERNAL FAULT",
"B1050 PASSENGER SIDE CRASH SENSOR CIRCUIT SHORT TO GND/VBATT",
"B1051 DRIVER SIDE CRASH SENSOR INTERNAL FAULT",
"B1052 PASSENGER SEATBELT BUCKLE SWITCH CROSS LINK TO ANOTHER SENSOR",
"B1053 DRIVER SEATBELT BUCKLE SWITCH CROSS LINK TO ANOTHER SENSOR",
"B1054 DRIVER SEATBELT PRETENSIONER CROSS LINK TO ANOTHER FIRING LOOP",
"B1055 PASSENGER SIDE, SIDE MOUNT AIRBAG CROSS LINK TO ANOTHER FIRING LOOP",
"B1056 PASSENGER SIDE AIRBAG CURTAIN CROSS LINK TO ANOTHER FIRING LOOP",
"B1057 DRIVER AIRBAG CROSS LINK TO ANOTHER FIRING LOOP",
"B1058 DRIVER AIRBAG CROSS LINK TO ANOTHER FIRING LOOP - LOOP #2",
"B1059 PASSENGER AIRBAG CROSS LINK TO ANOTHER FIRING LOOP - LOOP #2",
"B105A CRASH COUNTER - REACHED MAXIMUM",
"B1060 TIRE PRESSURE MONITOR SYSTEM (TPMS) TELLTALE CIRCUIT SHORT TO GROUND",
"B1061 TIRE PRESSURE MONITOR SYSTEM (TPMS) TELLTALE CIRCUIT SHORT TO BATTERY/OPEN",
"B1062 TIRE PRESSURE MONITOR SYSTEM (TPMS) TELLTALE CIRCUIT INCORRECT PWM FREQUENCY",
"B1063 INNER LEFT REAR (ILR) TIRE PRESSURE SENSOR FAULT",
"B1064 INNER RIGHT REAR (IRR) TIRE PRESSURE SENSOR FAULT",
"B1065 RADIO VOLUME CUTBACK CIRCUIT SHORT TO BATTERY",
"B1066 RADIO VOLUME CUTBACK CIRCUIT FAILURE",
"B1067 CLIMATE CONTROL / AUDIO ILLUMINATION OUTPUT FAILURE",
"B1068 SWITCH ILLUMINATION OUTPUT FAILURE",
"B1069 KEYLESS VEHICLE SECURE ID NOT TRANSFERRED",
"B1070 INTERIOR ANTENNA GROUP CIRCUIT SHORT TO GROUND",
"B1071 INTERIOR TRUNK ANTENNA CIRCUIT SHORT TO GROUND",
"B1072 DRIVER DOOR HANDLE ANTENNA NOT CONNECTED",
"B1073 PASSENGER DOOR HANDLE ANTENNA NOT CONNECTED",
"B1074 EXTERIOR TRUNK (BUMPER) ANTENNA NOT CONNECTED",
"B1075 PASSSENGER INTERIOR ANTENNA GROUP NOT CONNECTED",
"B1076 INTERIOR TRUNK ANTENNA NOT CONNECTED",
"B1077 DRIVER DOOR HANDLE ANTENNA CIRCUIT SHORT TO GROUND",
"B1078 DRIVER DOOR HANDLE ANTENNA CIRCUIT SHORT TO BATTERY",
"B1079 PASSENGER DOOR HANDLE ANTENNA CIRCUIT SHORT TO BATTERY",
"B1080 EXTERIOR TRUNK (BUMPER) ANTENNA CIRCUIT SHORT TO BATTERY",
"B1081 PASSENGER INTERIOR ANTENNA GROUP CIRCUIT SHORT TO BATTERY",
"B1082 INTERIOR TRUNK ANTENNA CIRCUIT SHORT TO BATTERY",
"B1083 PASSENGER DOOR HANDLE ANTENNA CIRCUIT SHORT TO GROUND",
"B1084 TRUNK LAMP CIRCUIT FAILURE",
"B1085 RESTRAINT SYSTEM - SEATBELT LOAD LIMITER STATUS",
"B1086 EXTERIOR TRUNK (BUMPER) ANTENNA CIRCUIT SHORT TO GROUND",
"B1087 PASSENGER REAR(PR) LATCH CLUTCH SWITCH ACTIVE WITHOUT PR UNLOCK PULL SWITCH",
"B1088 DRIVER REAR(DR) LATCH CLUTCH SWITCH ACTIVE WITHOUT DR UNLOCK PULL SWITCH",
"B1089 PASSENGER FRONT(PF) LATCH CLUTCH SWITCH ACTIVE WITHOUT PF UNLOCK PULL SWITCH",
"B1090 DRIVER FRONT(DF) LATCH CLUTCH SWITCH ACTIVE WITHOUT DF UNLOCK PULL SWITCH",
"B1091 PASSIVE KEY (PK) PROGRAMMING ERROR",
"B1092 SERIAL LINE TO SMART STEERING COLUMN DEVICE (SSCD) SHORT TO BATTERY OR GROUND",
"B1093 SMART STEERING COLUMN DEVICE (SSCD) - ID MISMATCH",
"B1094 SMART STEERING COLUMN DEVICE (SSCD) ID NOT STORED",
"B1095 SMART STEERING COLUMN DEVICE (SSCD) HARDWARE ERROR",
"B1096 SMART STEERING COLUMN DEVICE (SSCD) COMMUNICATION TIMEOUT",
"B1097 AUDIO SYSTEM TWEETER CIRCUIT FAULT",
"B1197 FUEL OPERATED HEATER (FOH) FUEL PRESSURE SWITCH STUCK OPEN",
"B1198 FUEL OPERATED HEATER (FOH) FUEL CHECK VALVE SHORT TO GROUND",
"B1199 FUEL OPERATED HEATER (FOH) FUEL CHECK VALVE OPEN/SHORT TO BATTERY",
"B1200 CLIMATE CONTROL PUSHBUTTON CIRCUIT FAILURE",
"B1201 FUEL SENDER CIRCUIT FAILURE",
"B1202 FUEL SENDER CIRCUIT OPEN",
"B1203 FUEL SENDER CIRCUIT SHORT TO BATTERY",
"B1204 FUEL SENDER CIRCUIT SHORT TO GROUND",
"B1205 EIC SWITCH-1 ASSEMBLY CIRCUIT FAILURE",
"B1206 EIC SWITCH-1 ASSEMBLY CIRCUIT OPEN",
"B1207 EIC SWITCH-1 ASSEMBLY CIRCUIT SHORT TO BATTERY",
"B1208 EIC SWITCH-1 ASSEMBLY CIRCUIT SHORT TO GROUND",
"B1209 EIC SWITCH-2 ASSEMBLY CIRCUIT FAILURE",
"B1210 EIC SWITCH-2 ASSEMBLY CIRCUIT OPEN",
"B1211 EIC SWITCH-2 ASSEMBLY CIRCUIT SHORT TO BATTERY",
"B1212 EIC SWITCH-2 ASSEMBLY CIRCUIT SHORT TO GROUND",
"B1213 ANTI-THEFT NUMBER OF PROGRAMMED KEYS IS BELOW MINIMUM",
"B1214 RUNNING BOARD LAMP CIRCUIT FAILURE",
"B1215 RUNNING BOARD LAMP CIRCUIT SHORT TO BATTERY",
"B1216 EMERGENCY & ROAD SIDE ASSISTANCE SWITCH CIRCUIT SHORT TO GROUND",
"B1217 HORN RELAY COIL CIRCUIT FAILURE",
"B1218 HORN RELAY COIL CIRCUIT SHORT TO VBATT",
"B1219 FUEL TANK PRESSURE SENSOR CIRCUIT FAILURE",
"B1220 FUEL TANK PRESSURE SENSOR CIRCUIT OPEN",
"B1221 DRIVER SEAT HEATER OUTPUT FAULT",
"B1222 FUEL TEMPERATURE SENSOR #1 CIRCUIT FAILURE",
"B1223 FUEL TEMPERATURE SENSOR #1 CIRCUIT OPEN",
"B1224 FUEL TEMPERATURE SENSOR #1 CIRCUIT SHORT TO BATTERY",
"B1225 FUEL TEMPERATURE SENSOR #1 CIRCUIT SHORT TO GROUND",
"B1226 FUEL TEMPERATURE SENSOR #2 CIRCUIT FAILURE",
"B1227 FUEL TEMPERATURE SENSOR #2 CIRCUIT OPEN",
"B1228 FUEL TEMPERATURE SENSOR #2 CIRCUIT SHORT TO BATTERY",
"B1229 FUEL TEMPERATURE SENSOR #2 CIRCUIT SHORT TO GROUND",
"B1230 DRIVER SEAT SWITCH FAULT",
"B1231 LONGITUDINAL ACCELERATION THRESHOLD EXCEEDED",
"B1232 DO NOT USE  (SEE SHOP MANUAL FOR DESCRIPTION)",
"B1233 GLASS BREAK SENSOR FAILURE",
"B1234 MIRROR SWITCH INVALID CODE",
"B1235 WINDOW FEEDBACK FAILURE",
"B1236 WINDOW FEEDBACK LOSS OF SIGNAL",
"B1237 WINDOW FEEDBACK OUT OF RANGE",
"B1238 OVER TEMPERATURE FAULT",
"B1239 AIR FLOW BLEND DOOR DRIVER CIRCUIT FAILURE",
"B1240 WIPER WASHER REAR PUMP RELAY CIRCUIT FAILURE",
"B1241 WIPER WASHER REAR PUMP RELAY CIRCUIT SHORT TO BATTERY",
"B1242 AIR FLOW RECIRCULATION DOOR DRIVER CIRCUIT FAILURE",
"B1243 EXPRESS WINDOW DOWN SWITCH CIRCUIT SHORT TO BATTERY",
"B1244 WIPER REAR MOTOR RUN RELAY CIRCUIT FAILURE",
"B1245 WIPER REAR MOTOR RUN RELAY CIRCUIT SHORT TO BATTERY",
"B1246 DIM PANEL POTENTIOMETER SWITCH CIRCUIT FAILURE",
"B1247 PANEL DIM SWITCH CIRCUIT OPEN",
"B1248 PASSENGER'S SEATBACK AUTOGLIDE REARWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1249 BLEND DOOR FAILURE",
"B1250 AIR TEMPERATURE INTERNAL SENSOR CIRCUIT FAILURE",
"B1251 AIR TEMPERATURE INTERNAL SENSOR CIRCUIT OPEN",
"B1252 AIR TEMPERATURE INTERNAL SENSOR CIRCUIT SHORT TO BATTERY",
"B1253 AIR TEMPERATURE INTERNAL SENSOR CIRCUIT SHORT TO GROUND",
"B1254 AIR TEMPERATURE EXTERNAL SENSOR CIRCUIT FAILURE",
"B1255 AIR TEMPERATURE EXTERNAL SENSOR CIRCUIT OPEN",
"B1256 AIR TEMPERATURE EXTERNAL SENSOR CIRCUIT SHORT TO BATTERY",
"B1257 AIR TEMPERATURE EXTERNAL SENSOR CIRCUIT SHORT TO GROUND",
"B1258 SOLAR RADIATION SENSOR CIRCUIT FAILURE",
"B1259 SOLAR RADIATION SENSOR CIRCUIT OPEN",
"B1260 SOLAR RADIATION SENSOR CIRCUIT SHORT TO BATTERY",
"B1261 SOLAR RADIATION SENSOR CIRCUIT SHORT TO GROUND",
"B1262 SERVO MOTOR DEFROST CIRCUIT FAILURE",
"B1263 SERVO MOTOR VENT CIRCUIT FAILURE",
"B1264 SERVO MOTOR FOOT CIRCUIT FAILURE",
"B1265 SERVO MOTOR COOLAIR BYPASS CIRCUIT  FAILURE",
"B1266 SERVO MOTOR AIRINTAKE LEFT CIRCUIT FAILURE",
"B1267 SERVO MOTOR AIRINTAKE RIGHT CIRCUIT FAILURE",
"B1268 SERVO MOTOR POTENTIOMETER DEFROST CIRCUIT FAILURE",
"B1269 SERVO MOTOR POTENTIOMETER DEFROST CIRCUIT OPEN",
"B1270 SERVO MOTOR POTENTIOMETER DEFROST CIRCUIT SHORT TO BATTERY",
"B1271 SERVO MOTOR POTENTIOMETER DEFROST CIRCUIT SHORT TO GROUND",
"B1272 SERVO MOTOR POTENTIOMETER VENT CIRCUIT FAILURE",
"B1273 SERVO MOTOR POTENTIOMETER VENT CIRCUIT OPEN",
"B1274 SERVO MOTOR POTENTIOMETER VENT CIRCUIT SHORT TO BATTERY",
"B1275 SERVO MOTOR POTENTIOMETER VENT CIRCUIT SHORT TO GROUND",
"B1276 SERVO MOTOR POTENTIOMETER FOOT CIRCUIT FAILURE",
"B1277 SERVO MOTOR POTENTIOMETER FOOT CIRCUIT OPEN",
"B1278 SERVO MOTOR POTENTIOMETER FOOT CIRCUIT SHORT TO BATTERY",
"B1279 SERVO MOTOR POTENTIOMETER FOOT CIRCUIT SHORT TO GROUND",
"B1280 SERVO MOTOR POTENTIOMETER COOLAIR CIRCUIT FAILURE",
"B1281 SERVO MOTOR POTENTIOMETER COOLAIR CIRCUIT OPEN",
"B1282 SERVO MOTOR POTENTIOMETER COOLAIR CIRCUIT SHORT TO BATTERY",
"B1283 SERVO MOTOR POTENTIOMETER COOLAIR CIRCUIT SHORT TO GROUND",
"B1284 SERVO MOTOR POTENTIOMETER AIRINTAKE LEFT CIRCUIT FAILURE",
"B1285 SERVO MOTOR POTENTIOMETER AIRINTAKE LEFT CIRCUIT OPEN",
"B1286 SERVO MOTOR POTENTIOMETER AIRINTAKE LEFT CIRCUIT SHORT TO BATTERY",
"B1287 SERVO MOTOR POTENTIOMETER AIRINTAKE LEFT CIRCUIT SHORT TO GROUND",
"B1288 SERVO MOTOR POTENTIOMETER AIRINTAKE RIGHT CIRCUIT FAILURE",
"B1289 SERVO MOTOR POTENTIOMETER AIRINTAKE RIGHT CIRCUIT OPEN",
"B1290 SERVO MOTOR POTENTIOMETER AIRINTAKE RIGHT CIRCUIT SHORT TO BATTERY",
"B1291 SERVO MOTOR POTENTIOMETER AIRINTAKE RIGHT CIRCUIT SHORT TO GROUND",
"B1292 BATTERY POWER RELAY CIRCUIT FAILURE",
"B1293 BATTERY POWER RELAY CIRCUIT OPEN",
"B1294 BATTERY POWER RELAY CIRCUIT SHORT TO BATTERY",
"B1295 BATTERY POWER RELAY CIRCUIT SHORT TO GROUND",
"B1296 POWER SUPPLY SENSOR CIRCUIT FAILURE",
"B1297 POWER SUPPLY SENSOR CIRCUIT OPEN",
"B1298 POWER SUPPLY SENSOR CIRCUIT SHORT TO BATTERY",
"B1299 POWER SUPPLY SENSOR CIRCUIT SHORT TO GROUND",
"B1300 POWER DOOR LOCK CIRCUIT FAILURE",
"B1301 POWER DOOR LOCK CIRCUIT OPEN",
"B1302 ACCESSORY DELAY RELAY COIL CIRCUIT FAILURE",
"B1303 ACCESSORY DELAY RELAY COIL CIRCUIT OPEN",
"B1304 ACCESSORY DELAY RELAY COIL CIRCUIT SHORT TO BATTERY",
"B1305 ACCESSORY DELAY RELAY COIL CIRCUIT SHORT TO GROUND",
"B1306 OIL LEVEL SWITCH CIRCUIT OPEN",
"B1307 OIL LEVEL SWITCH CIRCUIT SHORT TO BATTERY",
"B1308 OIL LEVEL SWITCH CIRCUIT SHORT TO GROUND",
"B1309 POWER DOOR LOCK CIRCUIT SHORT TO GROUND",
"B1310 POWER DOOR UNLOCK CIRCUIT FAILURE",
"B1311 POWER DOOR UNLOCK CIRCUIT OPEN",
"B1312 LAMP HEADLAMP INPUT CIRCUIT SHORT TO BATTERY",
"B1313 BATTERY SAVER RELAY COIL CIRCUIT FAILURE",
"B1314 BATTERY SAVER RELAY COIL CIRCUIT OPEN",
"B1315 BATTERY SAVER RELAY COIL CIRCUIT SHORT TO BATTERY",
"B1316 BATTERY SAVER RELAY COIL CIRCUIT SHORT TO GROUND",
"B1317 BATTERY VOLTAGE HIGH",
"B1318 BATTERY VOLTAGE LOW",
"B1319 DRIVER DOOR AJAR CIRCUIT FAILURE",
"B1320 DRIVER DOOR AJAR CIRCUIT OPEN",
"B1321 DRIVER DOOR AJAR CIRCUIT SHORT TO BATTERY",
"B1322 DRIVER DOOR AJAR CIRCUIT SHORT TO GROUND",
"B1323 DOOR AJAR LAMP CIRCUIT FAILURE",
"B1324 DOOR AJAR LAMP CIRCUIT OPEN",
"B1325 DOOR AJAR LAMP CIRCUIT SHORT TO BATTERY",
"B1326 DOOR AJAR LAMP CIRCUIT SHORT TO GROUND",
"B1327 PASSENGER DOOR AJAR CIRCUIT FAILURE",
"B1328 PASSENGER DOOR AJAR CIRCUIT OPEN",
"B1329 PASSENGER DOOR AJAR CIRCUIT SHORT TO BATTERY",
"B1330 PASSENGER DOOR AJAR CIRCUIT SHORT TO GROUND",
"B1331 DECKLID AJAR REAR DOOR CIRCUIT FAILURE",
"B1332 DECKLID AJAR REAR DOOR CIRCUIT OPEN",
"B1333 DECKLID AJAR REAR DOOR CIRCUIT SHORT TO BATTERY",
"B1334 DECKLID AJAR REAR DOOR CIRCUIT SHORT TO GROUND",
"B1335 DOOR AJAR RR CIRCUIT FAILURE",
"B1336 DOOR AJAR RR CIRCUIT OPEN",
"B1337 DOOR AJAR RR CIRCUIT SHORT TO BATTERY",
"B1338 DOOR AJAR RR CIRCUIT SHORT TO GROUND",
"B1339 CHIME INPUT REQUEST CIRCUIT SHORT TO BATTERY",
"B1340 CHIME INPUT REQUEST CIRCUIT SHORT TO GROUND",
"B1341 POWER DOOR UNLOCK CIRCUIT SHORT TO GROUND",
"B1342 ECU IS FAULTED",
"B1343 HEATED BACKLITE INPUT CIRCUIT FAILURE",
"B1344 HEATED BACKLITE INPUT CIRCUIT OPEN",
"B1345 HEATED BACKLITE INPUT CIRCUIT SHORT TO GROUND",
"B1346 HEATED BACKLITE INPUT CIRCUIT SHORT TO BATTERY",
"B1347 HEATED BACKLITE RELAY CIRCUIT FAILURE",
"B1348 HEATED BACKLITE RELAY CIRCUIT OPEN",
"B1349 HEATED BACKLITE RELAY SHORT TO BATTERY",
"B1350 HEATED BACKLITE RELAY SHORT TO GROUND",
"B1351 IGNITION KEY-IN CIRCUIT SHORT TO BATTERY",
"B1352 IGNITION KEY-IN CIRCUIT FAILURE",
"B1353 IGNITION KEY-IN CIRCUIT OPEN",
"B1354 IGNITION KEY-IN CIRCUIT SHORT TO GROUND",
"B1355 IGNITION RUN CIRCUIT FAILURE",
"B1356 IGNITION RUN CIRCUIT OPEN",
"B1357 IGNITION RUN CIRCUIT SHORT TO BATTERY",
"B1358 IGNITION RUN CIRCUIT SHORT TO GROUND",
"B1359 IGNITION RUN/ACC CIRCUIT FAILURE",
"B1360 IGNITION RUN/ACC CIRCUIT OPEN",
"B1361 IGNITION RUN/ACC CIRCUIT SHORT TO BATTERY",
"B1362 IGNITION RUN/ACC CIRCUIT SHORT TO GROUND",
"B1363 IGNITION START CIRCUIT FAILURE",
"B1364 IGNITION START CIRCUIT OPEN",
"B1365 IGNITION START CIRCUIT SHORT TO BATTERY",
"B1366 IGNITION START CIRCUIT SHORT TO GROUND",
"B1367 IGNITION TACH CIRCUIT FAILURE",
"B1368 IGNITION TACH CIRCUIT OPEN",
"B1369 IGNITION TACH CIRCUIT SHORT TO BATTERY",
"B1370 IGNITION TACH CIRCUIT SHORT TO GROUND",
"B1371 ILLUMINATED ENTRY RELAY CIRCUIT FAILURE",
"B1372 ILLUMINATED ENTRY RELAY CIRCUIT OPEN",
"B1373 ILLUMINATED ENTRY RELAY SHORT TO BATTERY",
"B1374 ILLUMINATED ENTRY RELAY SHORT TO GROUND",
"B1375 OIL CHANGE LAMP CIRCUIT OPEN",
"B1376 OIL CHANGE LAMP CIRCUIT SHORT TO BATTERY",
"B1377 OIL CHANGE LAMP CIRCUIT FAILURE",
"B1378 OIL CHANGE LAMP CIRCUIT SHORT TO GROUND",
"B1379 OIL CHANGE RESET BUTTON CIRCUIT SHORT TO GROUND",
"B1380 OIL CHANGE RESET BUTTON CIRCUIT FAILURE",
"B1381 OIL CHANGE RESET BUTTON CIRCUIT OPEN",
"B1382 OIL CHANGE RESET BUTTON CIRCUIT SHORT TO BATTERY",
"B1383 OIL LEVEL LAMP CIRCUIT SHORT TO BATTERY",
"B1384 OIL LEVEL LAMP CIRCUIT FAILURE",
"B1385 OIL LEVEL LAMP CIRCUIT OPEN",
"B1386 OIL LEVEL LAMP CIRCUIT SHORT TO GROUND",
"B1387 OIL TEMPERATURE SENSOR CIRCUIT OPEN",
"B1388 OIL TEMPERATURE SENSOR CIRCUIT SHORT TO BATTERY",
"B1389 OIL TEMPERATURE SENSOR CIRCUIT FAILURE",
"B1390 OIL TEMPERATURE SENSOR CIRCUIT SHORT TO GROUND",
"B1391 OIL LEVEL SWITCH CIRCUIT FAILURE",
"B1392 POWER DOOR MEMORY LOCK RELAY CIRCUIT FAILURE",
"B1393 POWER DOOR MEMORY LOCK RELAY CIRCUIT OPEN",
"B1394 POWER DOOR MEMORY LOCK RELAY CIRCUIT SHORT TO BATTERY",
"B1395 POWER DOOR MEMORY LOCK RELAY CIRCUIT SHORT TO GROUND",
"B1396 POWER DOOR LOCK CIRCUIT SHORT TO BATTERY",
"B1397 POWER DOOR UNLOCK CIRCUIT SHORT TO BATTERY",
"B1398 DRIVER POWER WINDOW ONE TOUCH WINDOW RELAY CIRCUIT FAILURE",
"B1399 DRIVER POWER WINDOW ONE TOUCH WINDOW RELAY CIRCUIT OPEN",
"B1400 DRIVER POWER WINDOW ONE TOUCH WINDOW RELAY CIRCUIT SHORT TO BATTERY",
"B1401 DRIVER POWER WINDOW ONE TOUCH WINDOW RELAY CIRCUIT SHORT TO GROUND",
"B1402 DRIVER POWER WINDOW DOWN SWITCH CIRCUIT FAILURE",
"B1403 DRIVER POWER WINDOW UP SWITCH CIRCUIT FAILURE",
"B1404 DRIVER POWER WINDOW DOWN CIRCUIT OPEN",
"B1405 DRIVER POWER WINDOW DOWN CIRCUIT SHORT TO BATTERY",
"B1406 DRIVER POWER WINDOW DOWN CIRCUIT SHORT TO GROUND",
"B1407 DRIVER POWER WINDOW UP CIRCUIT OPEN",
"B1408 DRIVER POWER WINDOW UP CIRCUIT SHORT TO BATTERY",
"B1409 DRIVER POWER WINDOW UP CIRCUIT SHORT TO GROUND",
"B1410 DRIVER POWER WINDOW MOTOR CIRCUIT FAILURE",
"B1411 DRIVER POWER WINDOW MOTOR CIRCUIT OPEN",
"B1412 DRIVER POWER WINDOW MOTOR CIRCUIT SHORT TO BATTERY",
"B1413 DRIVER POWER WINDOW MOTOR CIRCUIT SHORT TO GROUND",
"B1414 POWER WINDOW LR MOTOR CIRCUIT FAILURE",
"B1415 POWER WINDOW LR MOTOR CIRCUIT OPEN",
"B1416 POWER WINDOW LR MOTOR CIRCUIT SHORT TO BATTERY",
"B1417 POWER WINDOW LR MOTOR CIRCUIT SHORT TO GROUND",
"B1418 PASSENGER POWER WINDOW MOTOR CIRCUIT FAILURE",
"B1419 PASSENGER POWER WINDOW MOTOR CIRCUIT OPEN",
"B1420 PASSENGER POWER WINDOW MOTOR CIRCUIT SHORT TO BATTERY",
"B1421 PASSENGER POWER WINDOW MOTOR CIRCUIT SHORT TO GROUND",
"B1422 POWER WINDOW RR MOTOR CIRCUIT FAILURE",
"B1423 POWER WINDOW RR MOTOR CIRCUIT OPEN",
"B1424 POWER WINDOW RR MOTOR CIRCUIT SHORT TO BATTERY",
"B1425 POWER WINDOW RR MOTOR CIRCUIT SHORT TO GROUND",
"B1426 LAMP SEAT BELT CIRCUIT SHORT TO BATTERY",
"B1427 LAMP SEAT BELT CIRCUIT OPEN",
"B1428 LAMP SEAT BELT CIRCUIT FAILURE",
"B1429 LAMP SEAT BELT CIRCUIT SHORT TO GROUND",
"B1430 SEAT BELT SWITCH CIRCUIT SHORT TO GROUND",
"B1431 WIPER BRAKE/RUN RELAY CIRCUIT FAILURE",
"B1432 WIPER BRAKE/RUN RELAY CIRCUIT SHORT TO BATTERY",
"B1433 WIPER BRAKE/RUN RELAY CIRCUIT SHORT TO GROUND",
"B1434 WIPER HI/LOW SPEED RELAY COIL CIRCUIT FAILURE",
"B1435 WIPER HI/LOW SPEED RELAY COIL CIRCUIT OPEN",
"B1436 WIPER HI/LOW SPEED RELAY COIL CIRCUIT SHORT TO BATTERY",
"B1437 WIPER HI/LOW SPEED RELAY COIL CIRCUIT SHORT TO GROUND",
"B1438 WIPER MODE SELECT SWITCH CIRCUIT FAILURE",
"B1439 WIPER MODE SELECT SWITCH CIRCUIT OPEN",
"B1440 WIPER MODE SELECT SWITCH CIRCUIT SHORT TO BATTERY",
"B1441 WIPER MODE SELECT SWITCH CIRCUIT SHORT TO GROUND",
"B1442 DOOR HANDLE SWITCH CIRCUIT FAILURE",
"B1443 DOOR HANDLE SWITCH CIRCUIT OPEN",
"B1444 DOOR HANDLE SWITCH CIRCUIT SHORT TO BATTERY",
"B1445 DOOR HANDLE SWITCH CIRCUIT SHORT TO GROUND",
"B1446 WIPER PARK SENSE CIRCUIT FAILURE",
"B1447 WIPER PARK SENSE CIRCUIT OPEN",
"B1448 WIPER PARK SENSE CIRCUIT SHORT TO BATTERY",
"B1449 WIPER PARK SENSE CIRCUIT SHORT TO GROUND",
"B1450 WIPER WASH/DELAY SWITCH CIRCUIT FAILURE",
"B1451 WIPER WASH/DELAY SWITCH CIRCUIT OPEN",
"B1452 WIPER WASH/DELAY SWITCH CIRCUIT SHORT TO BATTERY",
"B1453 WIPER WASH/DELAY SWITCH CIRCUIT SHORT TO GROUND",
"B1454 WIPER WASHER FLUID LAMP CIRCUIT FAILURE",
"B1455 WIPER WASHER FLUID LAMP CIRCUIT OPEN",
"B1456 WIPER WASHER FLUID LAMP CIRCUIT SHORT TO BATTERY",
"B1457 WIPER WASHER FLUID LAMP CIRCUIT SHORT TO GROUND",
"B1458 WIPER WASHER PUMP MOTOR RELAY CIRCUIT FAILURE",
"B1459 WIPER WASHER PUMP MOTOR RELAY COIL CIRCUIT OPEN",
"B1460 WIPER WASHER PUMP MOTOR RELAY COIL CIRCUIT SHORT TO BATTERY",
"B1461 WIPER WASHER PUMP MOTOR RELAY COIL CIRCUIT SHORT TO GROUND",
"B1462 SEAT BELT SWITCH CIRCUIT FAILURE",
"B1463 SEAT BELT SWITCH CIRCUIT OPEN",
"B1464 SEAT BELT SWITCH CIRCUIT SHORT TO BATTERY",
"B1465 WIPER BRAKE/RUN RELAY CIRCUIT OPEN",
"B1466 WIPER HI/LOW SPEED NOT SWITCHING",
"B1467 WIPER HI/LOW SPEED CIRCUIT MOTOR SHORT TO BATTERY",
"B1468 CHIME INPUT REQUEST CIRCUIT FAILURE",
"B1469 CHIME INPUT REQUEST CIRCUIT OPEN",
"B1470 LAMP HEADLAMP INPUT CIRCUIT FAILURE",
"B1471 LAMP HEADLAMP INPUT CIRCUIT OPEN",
"B1472 LAMP HEADLAMP INPUT CIRCUIT SHORT TO GROUND",
"B1473 WIPER LOW SPEED CIRCUIT MOTOR FAILURE",
"B1474 BATTERY SAVER POWER RELAY CIRCUIT SHORT TO BATTERY",
"B1475 ACCESSORY DELAY RELAY SHORT TO BATTERY",
"B1476 WIPER HIGH SPEED CIRCUIT MOTOR FAILURE",
"B1477 WIPER HI/LOW CIRCUIT MOTOR SHORT TO GROUND",
"B1478 POWER WINDOW ONE TOUCH UP/DOWN ACTIVATED SIMULTANEOUSLY",
"B1479 WIPER WASHER FLUID LEVEL SENSOR CIRCUIT FAILURE",
"B1480 WIPER WASHER FLUID LEVEL SENSOR CIRCUIT OPEN",
"B1481 WIPER WASHER FLUID LEVEL SENSOR CIRCUIT SHORT TO BATTERY",
"B1482 WIPER WASHER FLUID LEVEL SENSOR CIRCUIT SHORT TO GROUND",
"B1483 BRAKE PEDAL INPUT CIRCUIT FAILURE",
"B1484 BRAKE PEDAL INPUT OPEN CIRCUIT",
"B1485 BRAKE PEDAL INPUT SHORT TO BATTERY",
"B1486 BRAKE PEDAL INPUT CIRCUIT GROUND SHORT",
"B1487 DOOR HANDLE RIGHT FRONT CIRCUIT FAILURE",
"B1488 DOOR HANDLE RIGHT FRONT CIRCUIT OPEN",
"B1489 DOOR HANDLE RIGHT FRONT SHORT TO BATTERY",
"B1490 DOOR HANDLE RIGHT FRONT SHORT TO GROUND",
"B1491 IGNITION CYLINDER SENSOR CIRCUIT FAILURE",
"B1492 IGNITION CYLINDER SENSOR OPEN CIRCUIT",
"B1493 IGNITION CYLINDER SENSOR BATTERY SHORT",
"B1494 IGNITION CYLINDER SENSOR GROUND SHORT",
"B1495 DECKLID PUNCH-OUT SENSOR CIRCUIT FAILURE",
"B1496 DECKLID PUNCH-OUT SENSOR OPEN CIRCUIT",
"B1497 DECKLID PUNCH-OUT SENSOR BATTERY SHORT",
"B1498 DECKLID PUNCH-OUT SENSOR GROUND SHORT",
"B1499 LAMP TURN SIGNAL LEFT CIRCUIT FAILURE",
"B1500 LAMP TURN SIGNAL LEFT CIRCUIT OPEN",
"B1501 LAMP TURN SIGNAL LEFT CIRCUIT SHORT TO BATTERY",
"B1502 LAMP TURN SIGNAL LEFT CIRCUIT SHORT TO GROUND",
"B1503 LAMP TURN SIGNAL RIGHT CIRCUIT FAILURE",
"B1504 LAMP TURN SIGNAL RIGHT CIRCUIT OPEN",
"B1505 LAMP TURN SIGNAL RIGHT CIRCUIT SHORT TO BATTERY",
"B1506 LAMP TURN SIGNAL RIGHT CIRCUIT SHORT TO GROUND",
"B1507 FLASH TO PASS SWITCH CIRCUIT FAILURE",
"B1508 FLASH TO PASS SWITCH CIRCUIT OPEN",
"B1509 FLASH TO PASS SWITCH CIRCUIT SHORT TO BATTERY",
"B1510 FLASH TO PASS SWITCH CIRCUIT SHORT TO GROUND",
"B1511 DRIVER DOOR HANDLE  CIRCUIT FAILURE",
"B1512 DRIVER DOOR HANDLE  CIRCUIT OPEN",
"B1513 DRIVER DOOR HANDLE  CIRCUIT SHORT TO BATTERY",
"B1514 DRIVER DOOR HANDLE  CIRCUIT SHORT TO GROUND",
"B1515 SEAT DRIVER OCCUPIED SWITCH CIRCUIT FAILURE",
"B1516 SEAT DRIVER OCCUPIED SWITCH CIRCUIT OPEN",
"B1517 SEAT DRIVER OCCUPIED SWITCH CIRCUIT SHORT TO BATTERY",
"B1518 SEAT DRIVER OCCUPIED SWITCH CIRCUIT SHORT TO GROUND",
"B1519 HOOD SWITCH CIRCUIT FAILURE",
"B1520 HOOD SWITCH CIRCUIT OPEN",
"B1521 HOOD SWITCH CIRCUIT SHORT TO BATTERY",
"B1522 HOOD SWITCH CIRCUIT SHORT TO GROUND",
"B1523 KEYLESS ENTRY CIRCUIT FAILURE",
"B1524 KEYLESS ENTRY CIRCUIT OPEN",
"B1525 KEYLESS ENTRY CIRCUIT SHORT TO BATTERY",
"B1526 KEYLESS ENTRY CIRCUIT SHORT TO GROUND",
"B1527 MEMORY SET SWITCH CIRCUIT FAILURE",
"B1528 MEMORY SET SWITCH CIRCUIT OPEN",
"B1529 MEMORY SET SWITCH CIRCUIT SHORT TO BATTERY",
"B1530 MEMORY SET SWITCH CIRCUIT SHORT TO GROUND",
"B1531 MEMORY 1 SWITCH CIRCUIT FAILURE",
"B1532 MEMORY 1 SWITCH CIRCUIT OPEN",
"B1533 MEMORY 1 SWITCH CIRCUIT SHORT TO BATTERY",
"B1534 MEMORY 1 SWITCH CIRCUIT SHORT TO GROUND",
"B1535 MEMORY 2 SWITCH CIRCUIT FAILURE",
"B1536 MEMORY 2 SWITCH CIRCUIT OPEN",
"B1537 MEMORY 2 SWITCH CIRCUIT SHORT TO BATTERY",
"B1538 MEMORY 2 SWITCH CIRCUIT SHORT TO GROUND",
"B1539 MIRROR DRIVER SWITCH ASSEMBLY CIRCUIT FAILURE",
"B1540 MIRROR DRIVER SWITCH ASSEMBLY CIRCUIT OPEN",
"B1541 MIRROR DRIVER SWITCH ASSEMBLY CIRCUIT SHORT TO BATTERY",
"B1542 MIRROR DRIVER SWITCH ASSEMBLY CIRCUIT SHORT TO GROUND",
"B1543 SEAT DIRECTION SWITCH ASSEMBLY CIRCUIT FAILURE",
"B1544 SEAT DIRECTION SWITCH ASSEMBLY CIRCUIT OPEN",
"B1545 SEAT DIRECTION SWITCH ASSEMBLY CIRCUIT SHORT TO BATTERY",
"B1546 SEAT DIRECTION SWITCH ASSEMBLY CIRCUIT SHORT TO GROUND",
"B1547 POWER WINDOW MASTER CIRCUIT FAILURE",
"B1548 POWER WINDOW MASTER CIRCUIT OPEN",
"B1549 POWER WINDOW MASTER CIRCUIT SHORT TO BATTERY",
"B1550 POWER WINDOW MASTER CIRCUIT SHORT TO GROUND",
"B1551 LATCH/DECK LID RELEASE CIRCUIT FAILURE",
"B1552 DECKLID RELEASE CIRCUIT OPEN",
"B1553 DECKLID RELEASE CIRCUIT SHORT TO BATTERY",
"B1554 DECKLID RELEASE CIRCUIT SHORT TO GROUND",
"B1555 IGNITION RUN/START CIRCUIT FAILURE",
"B1556 IGNITION RUN/START CIRCUIT OPEN",
"B1557 IGNITION RUN/START CIRCUIT SHORT TO BATTERY",
"B1558 IGNITION RUN/START CIRCUIT SHORT TO GROUND",
"B1559 DOOR LOCK CYLINDER CIRCUIT FAILURE",
"B1560 DOOR LOCK CYLINDER CIRCUIT OPEN",
"B1561 DOOR LOCK CYLINDER CIRCUIT SHORT TO BATTERY",
"B1562 DOOR LOCK CYLINDER CIRCUIT SHORT TO GROUND",
"B1563 DOOR AJAR CIRCUIT FAILURE",
"B1564 DOOR AJAR CIRCUIT OPEN",
"B1565 DOOR AJAR CIRCUIT SHORT TO BATTERY",
"B1566 DOOR AJAR CIRCUIT SHORT TO GROUND",
"B1567 LAMP HEADLAMP HIGH-BEAM CIRCUIT FAILURE",
"B1568 LAMP HEADLAMP HIGH-BEAM CIRCUIT OPEN",
"B1569 LAMP HEADLAMP HIGH-BEAM CIRCUIT SHORT TO BATTERY",
"B1570 LAMP HEADLAMP HIGH-BEAM CIRCUIT SHORT TO GROUND",
"B1571 DOOR AJAR LR CIRCUIT FAILURE",
"B1572 DOOR AJAR LR CIRCUIT OPEN",
"B1573 DOOR AJAR LR CIRCUIT  SHORT TO BATTERY",
"B1574 DOOR AJAR LR CIRCUIT SHORT TO GROUND",
"B1575 LAMP PARK INPUT CIRCUIT FAILURE",
"B1576 LAMP PARK INPUT CIRCUIT OPEN",
"B1577 LAMP PARK INPUT CIRCUIT SHORT TO BATTERY",
"B1578 LAMP PARK INPUT CIRCUIT SHORT TO GROUND",
"B1579 DIM PANEL INCREASE INPUT CIRCUIT FAILURE",
"B1580 DIM PANEL INCREASE INPUT CIRCUIT OPEN",
"B1581 DIM PANEL INCREASE INPUT CIRCUIT SHORT TO BATTERY",
"B1582 DIM PANEL INCREASE INPUT CIRCUIT SHORT TO GROUND",
"B1583 DIM PANEL DECREASE INPUT CIRCUIT FAILURE",
"B1584 DIM PANEL DECREASE INPUT CIRCUIT OPEN",
"B1585 DIM PANEL DECREASE INPUT CIRCUIT SHORT TO BATTERY",
"B1586 DIM PANEL DECREASE INPUT CIRCUIT SHORT TO GROUND",
"B1587 AUTOLAMP DELAY INCREASE CIRCUIT FAILURE",
"B1588 AUTOLAMP DELAY INCREASE CIRCUIT OPEN",
"B1589 AUTOLAMP DELAY INCREASE CIRCUIT SHORT TO BATTERY",
"B1590 AUTOLAMP DELAY INCREASE CIRCUIT SHORT TO GROUND",
"B1591 AUTOLAMP DELAY DECREASE CIRCUIT FAILURE",
"B1592 AUTOLAMP DELAY DECREASE CIRCUIT OPEN",
"B1593 AUTOLAMP DELAY DECREASE CIRCUIT SHORT TO BATTERY",
"B1594 AUTOLAMP DELAY DECREASE CIRCUIT SHORT TO GROUND",
"B1595 IGNITION SWITCH ILLEGAL INPUT CODE",
"B1596 SERVICE CONTINUOUS CODES",
"B1597 DRIVER'S SEAT SEATBACK AUTOGLIDE FORWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1598 DRIVER'S SEAT SEATBACK AUTOGLIDE REARWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1599 PASSENGER'S SEATBACK AUTOGLIDE FORWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1600 PATS IGNITION KEY TRANSPONDER SIGNAL IS NOT RECEIVED",
"B1601 PATS RECEIVED INCORRECT KEY-CODE FROM IGNITION KEY TRANSPONDER",
"B1602 PATS RECEIVED INVALID FORMAT OF KEY-CODE FROM IGNITION KEY TRANSPONDER",
"B1603 LAMP ANTI-THEFT INDICATOR CIRCUIT FAILURE",
"B1604 LAMP ANTI-THEFT INDICATOR CIRCUIT OPEN",
"B1605 LAMP ANTI-THEFT INDICATOR CIRCUIT SHORT TO BATTERY",
"B1606 LAMP ANTI-THEFT INDICATOR CIRCUIT SHORT TO GROUND",
"B1607 ILLUMINATED ENTRY INPUT CIRCUIT FAILURE",
"B1608 ILLUMINATED ENTRY INPUT OPEN CIRCUIT",
"B1609 ILLUMINATED ENTRY INPUT SHORT CIRCUIT TO BATTERY",
"B1610 ILLUMINATED ENTRY INPUT SHORT CIRCUIT TO GROUND",
"B1611 WIPER REAR MODE SELECT SWITCH CIRCUIT FAILURE",
"B1612 WIPER REAR MODE SELECT SWITCH CIRCUIT OPEN",
"B1613 WIPER REAR MODE SELECT SWITCH CIRCUIT SHORT TO BATTERY",
"B1614 WIPER REAR MODE SELECT SWITCH CIRCUIT SHORT TO GROUND",
"B1615 WIPER REAR DISABLE SWITCH CIRCUIT FAILURE",
"B1616 WIPER REAR DISABLE SWITCH CIRCUIT OPEN",
"B1617 WIPER REAR DISABLE SWITCH CIRCUIT SHORT TO BATTERY",
"B1618 WIPER REAR DISABLE SWITCH CIRCUIT SHORT TO GROUND",
"B1619 WIPER REAR LOW LIMIT INPUT CIRCUIT FAILURE",
"B1620 WIPER REAR LOW LIMIT INPUT CIRCUIT OPEN",
"B1621 WIPER REAR LOW LIMIT INPUT CIRCUIT SHORT TO BATTERY",
"B1622 WIPER REAR LOW LIMIT INPUT CIRCUIT SHORT TO GROUND",
"B1623 LAMP KEYPAD OUTPUT CIRCUIT FAILURE",
"B1624 LAMP KEYPAD OUTPUT OPEN CIRCUIT",
"B1625 LAMP KEYPAD OUTPUT SHORT CIRCUIT TO BATTERY",
"B1626 LAMP KEYPAD OUTPUT SHORT CIRCUIT TO GROUND",
"B1627 PRNDL REVERSE INPUT CIRCUIT FAILURE",
"B1628 PRNDL REVERSE INPUT OPEN CIRCUIT",
"B1629 PRNDL REVERSE INPUT SHORT TO BATTERY",
"B1630 PRNDL REVERSE INPUT SHORT CIRCUIT TO GROUND",
"B1631 MIRROR DRIVER LEFT CIRCUIT FAILURE",
"B1632 MIRROR DRIVER LEFT CIRCUIT OPEN",
"B1633 MIRROR DRIVER LEFT CIRCUIT SHORT TO BATTERY",
"B1634 MIRROR DRIVER LEFT CIRCUIT SHORT TO GROUND",
"B1635 MIRROR DRIVER RIGHT CIRCUIT FAILURE",
"B1636 MIRROR DRIVER RIGHT CIRCUIT OPEN",
"B1637 MIRROR DRIVER RIGHT CIRCUIT SHORT TO BATTERY",
"B1638 MIRROR DRIVER RIGHT SHORT TO GROUND",
"B1639 MIRROR PASSENGER LEFT CIRCUIT FAILURE",
"B1640 MIRROR PASSENGER LEFT CIRCUIT OPEN",
"B1641 MIRROR PASSENGER LEFT CIRCUIT SHORT TO BATTERY",
"B1642 MIRROR PASSENGER LEFT CIRCUIT SHORT TO GROUND",
"B1643 MIRROR PASSENGER RIGHT CIRCUIT FAILURE",
"B1644 MIRROR PASSENGER RIGHT CIRCUIT OPEN",
"B1645 MIRROR PASSENGER RIGHT CIRCUIT SHORT TO BATTERY",
"B1646 MIRROR PASSENGER RIGHT CIRCUIT SHORT TO GROUND",
"B1647 SEAT DRIVER RECLINE FORWARD CIRCUIT FAILURE",
"B1648 SEAT DRIVER RECLINE FORWARD CIRCUIT OPEN",
"B1649 SEAT DRIVER RECLINE FORWARD CIRCUIT SHORT TO BATTERY",
"B1650 SEAT DRIVER RECLINE FORWARD CIRCUIT SHORT TO GROUND",
"B1651 SEAT DRIVER RECLINE BACKWARD CIRCUIT FAILURE",
"B1652 SEAT DRIVER RECLINE BACKWARD CIRCUIT OPEN",
"B1653 SEAT DRIVER RECLINE BACKWARD CIRCUIT SHORT TO BATTERY",
"B1654 SEAT DRIVER RECLINE BACKWARD CIRCUIT SHORT TO GROUND",
"B1655 SEAT DRIVER REAR UP  CIRCUIT FAILURE",
"B1656 SEAT DRIVER REAR UP CIRCUIT OPEN",
"B1657 SEAT DRIVER REAR UP CIRCUIT SHORT TO BATTERY",
"B1658 SEAT DRIVER REAR UP CIRCUIT SHORT TO GROUND",
"B1659 SEAT DRIVER FRONT UP CIRCUIT FAILURE",
"B1660 SEAT DRIVER FRONT UP CIRCUIT OPEN",
"B1661 SEAT DRIVER FRONT UP CIRCUIT SHORT TO BATTERY",
"B1662 SEAT DRIVER FRONT UP CIRCUIT SHORT TO GROUND",
"B1663 SEAT DRIVER FRONT UP/DOWN MOTOR STALLED",
"B1664 SEAT DRIVER REAR UP/DOWN MOTOR STALLED",
"B1665 SEAT DRIVER FORWARD/BACKWARD MOTOR STALLED",
"B1666 SEAT DRIVER RECLINE MOTOR STALLED",
"B1667 MIRROR DRIVER UP/DOWN MOTOR STALLED",
"B1668 MIRROR DRIVER RIGHT/LEFT MOTOR STALLED",
"B1669 MIRROR PASSENGER UP/DOWN MOTOR STALLED",
"B1670 MIRROR PASSENGER RIGHT/LEFT MOTOR STALLED",
"B1671 BATTERY MODULE VOLTAGE OUT OF RANGE",
"B1672 SEAT DRIVER OCCUPIED INPUT CIRCUIT FAILURE",
"B1673 SEAT DRIVER OCCUPIED INPUT CIRCUIT OPEN",
"B1674 SEAT DRIVER OCCUPIED INPUT CIRCUIT SHORT TO BATTERY",
"B1675 SEAT DRIVER OCCUPIED INPUT CIRCUIT SHORT TO GROUND",
"B1676 BATTERY PACK VOLTAGE OUT OF RANGE",
"B1677 ALARM PANIC INPUT CIRCUIT FAILURE",
"B1678 ALARM PANIC INPUT CIRCUIT OPEN",
"B1679 ALARM PANIC INPUT CIRCUIT SHORT TO BATTERY",
"B1680 ALARM PANIC INPUT CIRCUIT SHORT TO GROUND",
"B1681 PATS TRANSCEIVER MODULE SIGNAL IS NOT RECEIVED",
"B1682 PATS IS DISABLED (CHECK LINK BETWEEN PATS AND TRANSPONDER)",
"B1683 MIRROR DRIVER/PASSENGER SWITCH CIRCUIT FAILURE",
"B1684 MIRROR DRIVER/PASSENGER SWITCH CIRCUIT OPEN",
"B1685 LAMP DOME INPUT CIRCUIT FAILURE",
"B1686 LAMP DOME INPUT CIRCUIT OPEN",
"B1687 LAMP DOME INPUT CIRCUIT SHORT TO BATTERY",
"B1688 LAMP DOME INPUT CIRCUIT SHORT TO GROUND",
"B1689 AUTOLAMP DELAY CIRCUIT FAILURE",
"B1690 AUTOLAMP DELAY CIRCUIT OPEN",
"B1691 AUTOLAMP DELAY CIRCUIT SHORT TO BATTERY",
"B1692 AUTOLAMP DELAY CIRCUIT SHORT TO GROUND",
"B1693 AUTOLAMP ON CIRCUIT FAILURE",
"B1694 AUTOLAMP ON CIRCUIT OPEN",
"B1695 AUTOLAMP ON CIRCUIT SHORT TO BATTERY",
"B1696 AUTOLAMP ON CIRCUIT SHORT TO GROUND",
"B1697 MIRROR DRIVER/PASSENGER SWITCH CIRCUIT SHORT TO BATTERY",
"B1698 MIRROR DRIVER/PASSENGER SWITCH CIRCUIT SHORT TO GROUND",
"B1699 PASSENGER'S SEAT OCCUPIED SWITCH CIRCUIT SHORT TO GROUND",
"B1700 PASSENGER'S SEATBELT TENSION REDUCER CIRCUIT SHORT TO GROUND",
"B1701 SEAT DRIVER RECLINE FORWARD SWITCH CIRCUIT FAILURE",
"B1702 SEAT DRIVER RECLINE FORWARD SWITCH CIRCUIT OPEN",
"B1703 SEAT DRIVER RECLINE FORWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1704 SEAT DRIVER RECLINE FORWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1705 SEAT DRIVER RECLINE REARWARD SWITCH CIRCUIT FAILURE",
"B1706 SEAT DRIVER RECLINE REARWARD SWITCH CIRCUIT OPEN",
"B1707 SEAT DRIVER RECLINE REARWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1708 SEAT DRIVER RECLINE REARWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1709 SEAT DRIVER FRONT UP SWITCH CIRCUIT FAILURE",
"B1710 SEAT DRIVER FRONT UP SWITCH CIRCUIT OPEN",
"B1711 SEAT DRIVER FRONT UP SWITCH CIRCUIT SHORT TO BATTERY",
"B1712 SEAT DRIVER FRONT UP SWITCH CIRCUIT SHORT TO GROUND",
"B1713 SEAT DRIVER FRONT DOWN SWITCH CIRCUIT FAILURE",
"B1714 SEAT DRIVER FRONT DOWN SWITCH CIRCUIT OPEN",
"B1715 SEAT DRIVER FRONT DOWN SWITCH CIRCUIT SHORT TO BATTERY",
"B1716 SEAT DRIVER FRONT DOWN SWITCH CIRCUIT SHORT TO GROUND",
"B1717 SEAT DRIVER FORWARD SWITCH CIRCUIT FAILURE",
"B1718 SEAT DRIVER FORWARD SWITCH CIRCUIT OPEN",
"B1719 SEAT DRIVER FORWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1720 SEAT DRIVER FORWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1721 SEAT DRIVER REARWARD SWITCH CIRCUIT FAILURE",
"B1722 SEAT DRIVER REARWARD SWITCH CIRCUIT OPEN",
"B1723 SEAT DRIVER REARWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1724 SEAT DRIVER REARWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1725 SEAT DRIVER REAR UP SWITCH CIRCUIT FAILURE",
"B1726 SEAT DRIVER REAR UP SWITCH CIRCUIT OPEN",
"B1727 SEAT DRIVER REAR UP SWITCH CIRCUIT SHORT TO BATTERY",
"B1728 SEAT DRIVER REAR UP SWITCH CIRCUIT SHORT TO GROUND",
"B1729 SEAT DRIVER REAR DOWN SWITCH CIRCUIT FAILURE",
"B1730 SEAT DRIVER REAR DOWN SWITCH CIRCUIT OPEN",
"B1731 SEAT DRIVER REAR DOWN SWITCH CIRCUIT SHORT TO BATTERY",
"B1732 SEAT DRIVER REAR DOWN SWITCH CIRCUIT SHORT TO GROUND",
"B1733 MIRROR DRIVER VERTICAL SWITCH CIRCUIT FAILURE",
"B1734 MIRROR DRIVER VERTICAL SWITCH CIRCUIT OPEN",
"B1735 MIRROR DRIVER VERTICAL SWITCH CIRCUIT SHORT TO BATTERY",
"B1736 MIRROR DRIVER VERTICAL SWITCH CIRCUIT SHORT TO GROUND",
"B1737 MIRROR DRIVER HORIZONTAL SWITCH CIRCUIT FAILURE",
"B1738 MIRROR DRIVER HORIZONTAL SWITCH CIRCUIT OPEN",
"B1739 MIRROR DRIVER HORIZONTAL SWITCH CIRCUIT SHORT TO BATTERY",
"B1740 MIRROR DRIVER HORIZONTAL SWITCH CIRCUIT SHORT TO GROUND",
"B1741 MIRROR PASSENGER VERTICAL SWITCH CIRCUIT FAILURE",
"B1742 MIRROR PASSENGER VERTICAL SWITCH CIRCUIT OPEN",
"B1743 MIRROR PASSENGER VERTICAL SWITCH CIRCUIT SHORT TO BATTERY",
"B1744 MIRROR PASSENGER VERTICAL SWITCH CIRCUIT SHORT TO GROUND",
"B1745 MIRROR PASSENGER HORIZONTAL SWITCH CIRCUIT FAILURE",
"B1746 MIRROR PASSENGER HORIZONTAL SWITCH CIRCUIT OPEN",
"B1747 MIRROR PASSENGER HORIZONTAL SWITCH CIRCUIT SHORT TO BATTERY",
"B1748 MIRROR PASSENGER HORIZONTAL SWITCH CIRCUIT SHORT TO GROUND",
"B1749 PARK/NEUTRAL SWITCH CIRCUIT FAILURE",
"B1750 PARK/NEUTRAL SWITCH CIRCUIT OPEN",
"B1751 PARK/NEUTRAL SWITCH CIRCUIT SHORT TO BATTERY",
"B1752 PARK/NEUTRAL SWITCH CIRCUIT SHORT TO GROUND",
"B1753 HAZARD FLASH OUTPUT CIRCUIT FAILURE",
"B1754 HAZARD FLASH OUTPUT CIRCUIT OPEN",
"B1755 HAZARD FLASH OUTPUT CIRCUIT SHORT BATTERY",
"B1756 HAZARD FLASH OUTPUT CIRCUIT SHORT TO GROUND",
"B1757 SEAT DRIVER REAR DOWN  CIRCUIT FAILURE",
"B1758 SEAT DRIVER REAR DOWN CIRCUIT OPEN",
"B1759 SEAT DRIVER REAR DOWN CIRCUIT SHORT TO BATTERY",
"B1760 SEAT DRIVER REAR DOWN CIRCUIT SHORT TO GROUND",
"B1761 SEAT DRIVER FRONT DOWN  CIRCUIT FAILURE",
"B1762 SEAT DRIVER FRONT DOWN CIRCUIT OPEN",
"B1763 SEAT DRIVER FRONT DOWN CIRCUIT SHORT TO BATTERY",
"B1764 SEAT DRIVER FRONT DOWN CIRCUIT SHORT TO GROUND",
"B1765 SEAT DRIVER FORWARD CIRCUIT FAILURE",
"B1766 SEAT DRIVER FORWARD CIRCUIT OPEN",
"B1767 SEAT DRIVER FORWARD CIRCUIT SHORT TO BATTERY",
"B1768 SEAT DRIVER FORWARD CIRCUIT SHORT TO GROUND",
"B1769 SEAT DRIVER BACKWARD CIRCUIT FAILURE",
"B1770 SEAT DRIVER BACKWARD CIRCUIT OPEN",
"B1771 SEAT DRIVER BACKWARD CIRCUIT SHORT TO BATTERY",
"B1772 SEAT DRIVER BACKWARD CIRCUIT SHORT TO GROUND",
"B1773 MIRROR DRIVER UP CIRCUIT FAILURE",
"B1774 MIRROR DRIVER UP CIRCUIT OPEN",
"B1775 MIRROR DRIVER UP CIRCUIT SHORT TO BATTERY",
"B1776 MIRROR DRIVER UP CIRCUIT SHORT TO GROUND",
"B1777 DRIVER'S SEATBELT TENSION REDUCER CIRCUIT SHORT TO GROUND",
"B1778 MIRROR DRIVER DOWN CIRCUIT FAILURE",
"B1779 MIRROR DRIVER DOWN CIRCUIT OPEN",
"B1780 MIRROR DRIVER DOWN CIRCUIT SHORT TO BATTERY",
"B1781 MIRROR DRIVER DOWN SHORT TO GROUND",
"B1782 MIRROR PASSENGER UP CIRCUIT FAILURE",
"B1783 MIRROR PASSENGER UP CIRCUIT OPEN",
"B1784 MIRROR PASSENGER UP CIRCUIT SHORT TO BATTERY",
"B1785 MIRROR PASSENGER UP CIRCUIT SHORT TO GROUND",
"B1786 MIRROR PASSENGER DOWN CIRCUIT FAILURE",
"B1787 MIRROR PASSENGER DOWN CIRCUIT OPEN",
"B1788 MIRROR PASSENGER DOWN CIRCUIT SHORT TO BATTERY",
"B1789 MIRROR PASSENGER DOWN CIRCUIT SHORT TO GROUND",
"B1790 AUTOLAMP SENSOR INPUT CIRCUIT FAILURE",
"B1791 AUTOLAMP SENSOR INPUT CIRCUIT OPEN",
"B1792 AUTOLAMP SENSOR INPUT CIRCUIT SHORT TO BATTERY",
"B1793 AUTOLAMP SENSOR INPUT CIRCUIT SHORT TO GROUND",
"B1794 LAMP HEADLAMP LOW-BEAM CIRCUIT FAILURE",
"B1795 LAMP HEADLAMP LOW-BEAM CIRCUIT OPEN",
"B1796 LAMP HEADLAMP LOW-BEAM CIRCUIT SHORT TO BATTERY",
"B1797 LAMP HEADLAMP LOW-BEAM CIRCUIT SHORT TO GROUND",
"B1798 LAMP TURN SIGNAL FRONT OUTPUT CIRCUIT FAILURE",
"B1799 LAMP TURN SIGNAL FRONT OUTPUT CIRCUIT OPEN",
"B1800 LAMP TURN SIGNAL FRONT OUTPUT CIRCUIT SHORT TO BATTERY",
"B1801 LAMP TURN SIGNAL FRONT OUTPUT CIRCUIT SHORT TO GROUND",
"B1802 LAMP TURN SIGNAL REAR OUTPUT CIRCUIT FAILURE",
"B1803 LAMP TURN SIGNAL REAR OUTPUT CIRCUIT OPEN",
"B1804 LAMP TURN SIGNAL REAR OUTPUT CIRCUIT SHORT TO BATTERY",
"B1805 LAMP TURN SIGNAL REAR OUTPUT CIRCUIT SHORT TO GROUND",
"B1806 LAMP TAIL OUTPUT CIRCUIT FAILURE",
"B1807 LAMP TAIL OUTPUT CIRCUIT OPEN",
"B1808 LAMP TAIL OUTPUT CIRCUIT SHORT TO BATTERY",
"B1809 LAMP TAIL OUTPUT CIRCUIT SHORT TO GROUND",
"B1810 LAMP BACKUP SWITCH INPUT CIRCUIT FAILURE",
"B1811 LAMP BACKUP SWITCH INPUT CIRCUIT OPEN",
"B1812 LAMP BACKUP SWITCH INPUT CIRCUIT SHORT TO BATTERY",
"B1813 LAMP BACKUP SWITCH INPUT CIRCUIT SHORT TO GROUND",
"B1814 WIPER REAR MOTOR DOWN RELAY COIL CIRCUIT FAILURE",
"B1815 WIPER REAR MOTOR DOWN RELAY COIL CIRCUIT OPEN",
"B1816 WIPER REAR MOTOR DOWN RELAY COIL CIRCUIT SHORT TO BATTERY",
"B1817 WIPER REAR MOTOR DOWN RELAY COIL CIRCUIT SHORT TO GROUND",
"B1818 WIPER REAR MOTOR UP RELAY COIL CIRCUIT FAILURE",
"B1819 WIPER REAR MOTOR UP RELAY COIL CIRCUIT OPEN",
"B1820 WIPER REAR MOTOR UP RELAY COIL CIRCUIT SHORT TO BATTERY",
"B1821 WIPER REAR MOTOR UP RELAY COIL CIRCUIT SHORT TO GROUND",
"B1822 WIPER REAR PARK SENSE INPUT CIRCUIT FAILURE",
"B1823 WIPER REAR PARK SENSE INPUT CIRCUIT OPEN",
"B1824 WIPER REAR PARK SENSE INPUT CIRCUIT SHORT TO BATTERY",
"B1825 WIPER REAR PARK SENSE INPUT CIRCUIT SHORT TO GROUND",
"B1826 WIPER REAR HIGH LIMIT INPUT CIRCUIT FAILURE",
"B1827 WIPER REAR HIGH LIMIT INPUT CIRCUIT OPEN",
"B1828 WIPER REAR HIGH LIMIT INPUT CIRCUIT SHORT TO BATTERY",
"B1829 WIPER REAR HIGH LIMIT INPUT CIRCUIT SHORT TO GROUND",
"B1830 DOOR UNLOCK DISARM SWITCH CIRCUIT FAILURE",
"B1831 DOOR UNLOCK DISARM SWITCH CIRCUIT OPEN",
"B1832 DOOR UNLOCK DISARM SWITCH CIRCUIT SHORT TO BATTERY",
"B1833 DOOR UNLOCK DISARM SWITCH CIRCUIT SHORT TO GROUND",
"B1834 DOOR UNLOCK DISARM OUTPUT CIRCUIT FAILURE",
"B1835 DOOR UNLOCK DISARM OUTPUT CIRCUIT OPEN",
"B1836 DOOR UNLOCK DISARM OUTPUT CIRCUIT SHORT TO BATTERY",
"B1837 DOOR UNLOCK DISARM OUTPUT CIRCUIT SHORT TO GROUND",
"B1838 BATTERY SAVER POWER RELAY CIRCUIT FAILURE",
"B1839 WIPER REAR MOTOR CIRCUIT FAILURE",
"B1840 WIPER FRONT POWER CIRCUIT FAILURE",
"B1841 WIPER FRONT POWER CIRCUIT OPEN",
"B1842 WIPER FRONT POWER CIRCUIT SHORT TO BATTERY",
"B1843 WIPER FRONT POWER CIRCUIT SHORT TO GROUND",
"B1844 PHONE HANDSET CIRCUIT FAILURE",
"B1845 IGNITION TAMPER CIRCUIT FAILURE",
"B1846 IGNITION TAMPER CIRCUIT OPEN",
"B1847 IGNITION TAMPER CIRCUIT SHORT TO BATTERY",
"B1848 IGNITION TAMPER CIRCUIT SHORT TO GROUND",
"B1849 CLIMATE CONTROL TEMPERATURE DIFFERENTIAL CIRCUIT FAILURE",
"B1850 CLIMATE CONTROL TEMPERATURE DIFFERENTIAL CIRCUIT OPEN",
"B1851 CLIMATE CONTROL TEMPERATURE DIFFERENTIAL CIRCUIT SHORT TO BATTERY",
"B1852 CLIMATE CONTROL TEMPERATURE DIFFERENTIAL CIRCUIT SHORT TO GROUND",
"B1853 CLIMATE CONTROL AIR TEMPERATURE INTERNAL SENSOR MOTOR CIRCUIT FAILURE",
"B1854 CLIMATE CONTROL AIR TEMPERATURE INTERNAL SENSOR MOTOR CIRCUIT OPEN",
"B1855 CLIMATE CONTROL AIR TEMPERATURE INTERNAL SENSOR MOTOR CIRCUIT SHORT TO BATTERY",
"B1856 CLIMATE CONTROL AIR TEMPERATURE INTERNAL SENSOR MOTOR CIRCUIT SHORT TO GROUND",
"B1857 CLIMATE CONTROL ON/OFF SWITCH CIRCUIT FAILURE",
"B1858 CLIMATE CONTROL A/C PRESSURE SWITCH CIRCUIT FAILURE",
"B1859 CLIMATE CONTROL A/C PRESSURE SWITCH CIRCUIT OPEN",
"B1860 CLIMATE CONTROL A/C PRESSURE SWITCH CIRCUIT SHORT TO BATTERY",
"B1861 CLIMATE CONTROL A/C PRESSURE SWITCH CIRCUIT SHORT TO GROUND",
"B1862 CLIMATE CONTROL A/C LOCK SENSOR FAILURE",
"B1863 GROUND ECU CIRCUIT OPEN",
"B1864 BATTERY POWER SUPPLY ECU CIRCUIT FAILURE",
"B1865 BATTERY POWER SUPPLY ECU CIRCUIT OPEN",
"B1866 BATTERY POWER SUPPLY ECU CIRCUIT SHORT TO BATTERY",
"B1867 BATTERY POWER SUPPLY ECU CIRCUIT SHORT TO GROUND",
"B1868 LAMP AIR BAG WARNING INDICATOR CIRCUIT FAILURE",
"B1869 LAMP AIR BAG WARNING INDICATOR CIRCUIT OPEN",
"B1870 LAMP AIR BAG WARNING INDICATOR CIRCUIT SHORT TO BATTERY",
"B1871 PASSENGER AIR BAG DISABLE MODULE FAULT",
"B1872 TURN SIGNAL / HAZARD POWER FEED CIRCUIT SHORT TO BATTERY",
"B1873 TURN SIGNAL / HAZARD POWER FEED CIRCUIT SHORT TO GROUND",
"B1874 CELLULAR PHONE HANDSET NOT PRESENT",
"B1875 TURN SIGNAL / HAZARD SWITCH SIGNAL CIRCUIT FAILURE",
"B1876 SEATBELT DRIVER PRETENSIONER CIRCUIT FAILURE",
"B1877 SEATBELT DRIVER PRETENSIONER CIRCUIT OPEN",
"B1878 SEATBELT DRIVER PRETENSIONER CIRCUIT SHORT TO BATTERY",
"B1879 SEATBELT DRIVER PRETENSIONER CIRCUIT SHORT TO GROUND",
"B1880 SEATBELT PASSENGER PRETENSIONER CIRCUIT FAILURE",
"B1881 SEATBELT PASSENGER PRETENSIONER CIRCUIT OPEN",
"B1882 SEATBELT PASSENGER PRETENSIONER CIRCUIT SHORT TO BATTERY",
"B1883 SEATBELT PASSENGER PRETENSIONER CIRCUIT SHORT TO GROUND",
"B1884 PAD WARNING LAMP CIRCUIT FAILURE",
"B1885 SEATBELT DRIVER PRETENSIONER CIRCUIT RESISTANCE LOW ON SQUIB",
"B1886 SEATBELT PASSENGER PRETENSIONER CIRCUIT RESISTANCE LOW ON SQUIB",
"B1887 AIR BAG DRIVER CIRCUIT RESISTANCE LOW OR SHORTED TOGETHER",
"B1888 AIR BAG PASSENGER CIRCUIT RESISTANCE LOW OR SHORTED TOGETHER",
"B1889 PASSENGER AIRBAG DISABLE MODULE SENSOR OBSTRUCTED",
"B1890 PAD WARNING LAMP CIRCUIT SHORT TO BATTERY",
"B1891 AIR BAG TONE WARNING INDICATOR CIRCUIT SHORT TO BATTERY",
"B1892 AIR BAG TONE WARNING INDICATOR CIRCUIT FAILURE",
"B1893 GPS ANTENNA OPEN CIRCUIT",
"B1894 WIPER REAR MOTOR SPEED SENSE CIRCUIT FAILURE",
"B1895 DRIVER'S / PASSENGER'S DOOR AJAR OUTPUT CIRCUIT FAILURE",
"B1896 DRIVER'S / PASSENGER'S DOOR AJAR OUTPUT CIRCUIT SHORT TO BATTERY",
"B1897 HORN SWITCH CIRCUIT FAILURE",
"B1898 CHIME INPUT #2 CIRCUIT SHORT TO GROUND",
"B1899 MICROPHONE INPUT SIGNAL CIRCUIT OPEN",
"B1900 DRIVER SIDE AIRBAG FAULT",
"B1901 AIR BAG CRASH SENSOR #1 FEED/RETURN CIRCUIT SHORT TO GROUND",
"B1902 AIR BAG CRASH SENSOR #1 GROUND CIRCUIT FAILURE",
"B1903 AIR BAG CRASH SENSOR #1 GROUND CIRCUIT SHORT TO BATTERY",
"B1904 AIR BAG CRASH SENSOR #2 FEED/RETURN CIRCUIT FAILURE",
"B1905 AIR BAG CRASH SENSOR #2 FEED/RETURN CIRCUIT SHORT TO BATTERY",
"B1906 AIR BAG CRASH SENSOR #2 FEED/RETURN CIRCUIT SHORT TO GROUND",
"B1907 AIR BAG CRASH SENSOR #2 GROUND CIRCUIT FAILURE",
"B1908 AIR BAG CRASH SENSOR #2 GROUND CIRCUIT SHORT TO BATTERY",
"B1909 AIR BAG CRASH SENSOR #2 GROUND CIRCUIT SHORT TO GROUND",
"B1910 AIR BAG DIAGNOSTIC MONITOR GROUND CIRCUIT FAILURE",
"B1911 AIR BAG DIAGNOSTIC MONITOR GROUND CIRCUIT SHORT TO BATTERY",
"B1912 AIR BAG DIAGNOSTIC MONITOR GROUND CIRCUIT SHORT TO GROUND",
"B1913 AIR BAG DRIVER/PASSENGER CIRCUIT SHORT TO GROUND",
"B1914 AIR BAG CRASH SENSORS #1 / #2  CIRCUIT SHORT TO GROUND",
"B1915 AIR BAG DRIVER CIRCUIT FAILURE",
"B1916 AIR BAG DRIVER CIRCUIT SHORT TO BATTERY",
"B1917 AIR BAG MEMORY CLEAR CIRCUIT FAILURE",
"B1918 AIR BAG MEMORY CLEAR CIRCUIT OPEN",
"B1919 AIR BAG MEMORY CLEAR CIRCUIT SHORT TO BATTERY",
"B1920 AIR BAG PASSENGER CIRCUIT FAILURE",
"B1921 AIR BAG DIAGNOSTIC MONITOR GROUND CIRCUIT OPEN",
"B1922 AIR BAG SAFING SENSOR OUTPUT CIRCUIT SHORT TO BATTERY",
"B1923 AIR BAG MEMORY CLEAR CIRCUIT SHORT TO GROUND",
"B1924 AIR BAG INTERNAL DIAGNOSTIC MONITOR FAULT OR SYSTEM DISARM FAULT",
"B1925 AIR BAG PASSENGER CIRCUIT SHORT TO BATTERY",
"B1926 AIR BAG PASSENGER PRESSURE SWITCH CIRCUIT FAILURE",
"B1927 PASSENGER SIDE AIRBAG FAULT",
"B1928 AIR BAG SAFING SENSOR OUTPUT CIRCUIT FAILURE",
"B1929 AIR BAG SAFING SENSOR OUTPUT CIRCUIT OPEN",
"B1930 AIR BAG SAFING SENSOR OUTPUT CIRCUIT SHORT TO GROUND",
"B1931 AIR BAG CRASH SENSOR #1 FEED/RETURN CIRCUIT FAILURE",
"B1932 AIR BAG DRIVER CIRCUIT OPEN",
"B1933 AIR BAG PASSENGER CIRCUIT OPEN",
"B1934 AIR BAG DRIVER INFLATOR CIRCUIT RESISTANCE LOW ON SQUIB",
"B1935 AIR BAG PASSENGER INFLATOR CIRCUIT RESISTANCE LOW ON SQUIB",
"B1936 AIR BAG DRIVER CIRCUIT SHORT TO GROUND",
"B1937 AIR BAG PASSENGER PRESSURE SWITCH CIRCUIT OPEN",
"B1938 AIR BAG PASSENGER CIRCUIT SHORT TO GROUND",
"B1939 AIR BAG PASSENGER PRESSURE SWITCH CIRCUIT SHORT TO GROUND",
"B1940 SEAT MEMORY POSITION OUT OF RANGE.",
"B1941 AIR BAG CRASH SENSOR #1 FEED/RETURN CIRCUIT OPEN",
"B1942 AIR BAG CRASH SENSOR #2 FEED/RETURN CIRCUIT OPEN",
"B1943 AIR BAG CRASH SENSOR #1 GROUND CIRCUIT SHORT TO GROUND",
"B1944 AIR BAG CRASH SENSOR #1 GROUND CIRCUIT OPEN",
"B1945 AIR BAG CRASH SENSOR #2 GROUND CIRCUIT OPEN",
"B1946 CLIMATE CONTROL A/C POST EVAPORATOR SENSOR CIRCUIT FAILURE",
"B1947 CLIMATE CONTROL A/C POST EVAPORATOR SENSOR CIRCUIT SHORT TO GROUND",
"B1948 CLIMATE CONTROL WATER TEMPERATURE SENSOR CIRCUIT FAILURE",
"B1949 CLIMATE CONTROL WATER TEMPERATURE SENSOR CIRCUIT SHORT TO GROUND",
"B1950 SEAT REAR UP/DOWN POSITION FEEDBACK CIRCUIT FAILURE",
"B1951 SEAT REAR UP/DOWN POSITION FEEDBACK CIRCUIT OPEN",
"B1952 SEAT REAR UP/DOWN POSITION FEEDBACK CIRCUIT SHORT TO BATTERY",
"B1953 SEAT REAR UP/DOWN POSITION FEEDBACK CIRCUIT SHORT TO GROUND",
"B1954 SEAT FRONT UP/DOWN POSITION FEEDBACK CIRCUIT FAILURE",
"B1955 SEAT FRONT UP/DOWN POSITION FEEDBACK CIRCUIT OPEN",
"B1956 SEAT FRONT UP/DOWN POSITION FEEDBACK CIRCUIT SHORT TO BATTERY",
"B1957 SEAT FRONT UP/DOWN POSITION FEEDBACK CIRCUIT SHORT TO GROUND",
"B1958 SEAT RECLINE FORWARD/BACKWARD POSITION FEEDBACK CIRCUIT FAILURE",
"B1959 SEAT RECLINE FORWARD/BACKWARD POSITION FEEDBACK CIRCUIT OPEN",
"B1960 SEAT RECLINE FORWARD/BACKWARD POSITION FEEDBACK CIRCUIT SHORT TO BATTERY",
"B1961 SEAT RECLINE FORWARD/BACKWARD POSITION FEEDBACK CIRCUIT SHORT TO GROUND",
"B1962 SEAT HORIZONTAL FORWARD/REARWARD POSITION FEEDBACK CIRCUIT FAILURE",
"B1963 SEAT HORIZONTAL FORWARD/REARWARD POSITION FEEDBACK CIRCUIT OPEN",
"B1964 SEAT HORIZONTAL FORWARD/REARWARD POSITION FEEDBACK CIRCUIT SHORT TO BATTERY",
"B1965 SEAT HORIZONTAL FORWARD/REARWARD POSITION FEEDBACK CIRCUIT SHORT TO GROUND",
"B1966 A/C POST HEATER SENSOR CIRCUIT FAILURE",
"B1967 A/C POST HEATER SENSOR CIRCUIT SHORT TO GROUND",
"B1968 A/C WATER PUMP DETECTION CIRCUIT FAILURE",
"B1969 A/C CLUTCH MAGNETIC CONTROL CIRCUIT FAILURE",
"B1970 PASSENGER SEATBACK FORWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1971 PASSENGER SEATBACK REARWARD SWITCH CIRCUIT SHORT TO GROUND",
"B1972 PASSENGER REAR SEAT UP SWITCH CIRCUIT SHORT TO BATTERY",
"B1973 PASSENGER REAR SEAT DOWN SWITCH CIRCUIT SHORT TO BATTERY",
"B1974 PASSENGER'S SEAT RECLINE FORWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1975 PASSENGER'S SEAT RECLINE BACK SWITCH CIRCUIT SHORT TO BATTERY",
"B1976 PASSENGER'S SEAT FORWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1977 PASSENGER'S FRONT SEAT UP SWITCH CIRCUIT SHORT TO BATTERY",
"B1978 PASSENGER'S FRONT SEAT DOWN SWITCH CIRCUIT SHORT TO BATTERY",
"B1979 PASSENGER SEAT REARWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1980 BULB - OUTAGE CONDITION DETECTED",
"B1981 MEMORY OFF SWITCH CIRCUIT SHORT TO BATTERY",
"B1982 DRIVER'S DOOR UNLOCK RELAY CIRCUIT FAILURE",
"B1983 DRIVER'S DOOR UNLOCK RELAY CIRCUIT SHORT TO BATTERY",
"B1984 SEAT SWITCH LUMBAR INFLATE CIRCUIT FAILURE",
"B1985 SEAT SWITCH LUMBAR DEFLATE CIRCUIT FAILURE",
"B1986 DRIVER'S SEAT SEATBACK AUTOGLIDE REARWARD SWITCH CIRCUIT FAILURE",
"B1987 PEDAL FORWARD / REARWARD MOTOR STALLED",
"B1988 PEDAL POSITION FORWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1989 PEDAL POSITION REARWARD SWITCH CIRCUIT SHORT TO BATTERY",
"B1990 PEDAL FORWARD / REARWARD POTENTIOMETER FEEDBACK CIRCUIT FAILURE",
"B1991 PEDAL FORWARD / REARWARD POTENTIOMETER FEEDBACK CIRCUIT SHORT TO BATTERY",
"B1992 DRIVER SIDE, SIDE MOUNT AIRBAG CIRCUIT SHORT TO VBATT",
"B1993 DRIVER SIDE, SIDE MOUNT AIRBAG CIRCUIT SHORT TO GROUND",
"B1994 DRIVER SIDE, SIDE MOUNT AIRBAG CIRCUIT OPEN",
"B1995 DRIVER SIDE, SIDE MOUNT AIRBAG LOW RESISTANCE ON SQUIB",
"B1996 PASSENGER SIDE, SIDE MOUNT AIRBAG CIRCUIT SHORT TO VBATT",
"B1997 PASSENGER SIDE, SIDE MOUNT AIRBAG CIRCUIT SHORT TO GROUND",
"B1998 PASSENGER SIDE, SIDE MOUNT AIRBAG CIRCUIT OPEN",
"B1999 PASSENGER SIDE, SIDE MOUNT AIRBAG LOW RESISTANCE ON SQUIB",
"B2000 PEDAL POSITION FORWARD SWITCH CIRCUIT SHORT TO GROUND",
"B2001 PEDAL POSITION REARWARD SWITCH CIRCUIT SHORT TO GROUND",
"B2002 ECU BODY & ASSEMBLY TESTING INCOMPLETE",
"B2003 INCORRECT VEHICLE SECURITY IVIN",
"B2004 INTERNAL MEDIA OVER TEMPERATURE FAULT",
"B2005 CLIMATE CONTROL TEMPERATURE SWITCH OUT OF RANGE",
"B2006 BLOWER MOTOR SWITCH OUT OF RANGE",
"B2007 DRIVER SOLAR RADIATION SENSOR OUT OF RANGE",
"B2008 WIPERS ON SIGNAL CIRCUIT SHORT TO GROUND",
"B2009 SECURITY STATUS MISMATCH",
"B200A VSM INCLINATION FAILURE",
"B200B VSM ULTRASONIC FAILURE",
"B200C VSM MODULE FAILURE",
"B2010 SERVO MOTOR PANEL DOOR CIRCUIT FAILURE",
"B2011 PANEL DOOR ACTUATOR MOTOR OUT OF RANGE",
"B2012 DRIVER AIRINTAKE ACTUATOR MOTOR OUT OF RANGE",
"B2013 PASSENGER AIRINTAKE ACTUATOR MOTOR OUT OF RANGE",
"B2014 CLIMATE CONTROL A/C POST EVAPORATOR SENSOR OPEN CIRCUIT",
"B2015 POWER SLIDING DOOR LATCH SWITCH SHORT TO GROUND",
"B2016 POWER SLIDING DOOR LATCH SWITCH OPEN CIRCUIT",
"B2017 DAYTIME RUNNING LAMP LEFT OUTPUT CIRCUIT FAILURE",
"B2018 DAYTIME RUNNING LAMP RIGHT OUTPUT CIRCUIT FAILURE",
"B2019 LIFTAGE EXCEEDED TIME ALLOWED TO CINCH DOOR",
"B2020 COURTESY LAMP OUTPUT CKT SHORT TO GROUND",
"B2021 DOME LAMP OUTPUT RETURN CIRCUIT FAILURE",
"B2022 REAR COURTESY LAMP OUTPUT CIRCUIT FAILURE",
"B2023 REAR COURTESY LAMP OUTPUT CIRCUIT SHORT TO GROUND",
"B2024 REAR COURTESY LAMP OUTPUT RETURN CIRCUIT FAILURE",
"B2025 DEMAND LAMPS CIRCUIT FAILURE",
"B2026 INCANDESCENT BACKLIGHTING OUTPUT CIRCUIT FAILURE",
"B2027 LED BACKLIGHTING OUTPUT CIRCUIT FAILURE",
"B2028 POWER LIFTGATE OPEN/CLOSE OUTPUT CIRCUIT FAILURE",
"B2029 POWER LIFTGATE OPEN/CLOSE OUTPUT CIRCUIT SHORT TO BATTERY",
"B2030 FRONT FOG LAMP RELAY CKT FAILURE",
"B2031 LEFT CORNER LAMP OUTPUT CIRCUIT FAILURE",
"B2032 RIGHT CORNER LAMP OUTPUT CIRCUIT FAILURE",
"B2033 LEFT AUX PARK LAMP OUTPUT CIRCUIT FAILURE",
"B2034 RIGHT AUX PARK LAMP OUTPUT CIRCUIT FAILURE",
"B2035 LF SIDE REPEATER LAMP OUTPUT CKT FAILURE",
"B2036 LF SIDE REPEATER LAMP OUTPUT CKT SHORT TO GROUND",
"B2037 RF SIDE REPEATER LAMP OUTPUT CKT FAILURE",
"B2038 RF SIDE REPEATER LAMP OUTPUT CKT SHORT TO GROUND",
"B2039 LICENSE LAMP CIRCUIT SHORT TO GROUND",
"B2040 MIRROR LAMP OUTPUT CIRCUIT FAILURE",
"B2041 MIRROR LAMP OUTPUT CIRCUIT SHORT TO GROUND",
"B2042 LEFT MIRROR TURN SIGNAL OUTPUT CIRCUIT FAILURE",
"B2043 RIGHT MIRROR TURN SIGNAL OUTPUT CIRCUIT FAILURE",
"B2044 LEFT REAR STOP LAMP CIRCUIT SHORT TO GROUND",
"B2045 LEFT REAR STOP LAMP CIRCUIT OPEN",
"B2046 RIGHT REAR STOP LAMP CIRCUIT SHORT TO GROUND",
"B2047 RIGHT REAR STOP LAMP CIRCUIT OPEN",
"B2048 LEFT REAR TURN LAMP CIRCUIT SHORT TO GROUND",
"B2049 LEFT REAR TURN LAMP CIRCUIT OPEN",
"B2050 RIGHT REAR TURN LAMP CIRCUIT SHORT TO GROUND",
"B2051 RIGHT REAR TURN LAMP CIRCUIT OPEN",
"B2052 ACCESSORY DELAY RELAY OUTPUT FAILURE",
"B2053 ACCESSORY DELAY RELAY2 OUTPUT FAILURE",
"B2054 ACCESSORY DELAY RELAY2 SHORT TO BATTERY",
"B2055 LEFT POWER SLIDING DOOR OPEN/CLOSE OUTPUT CIRCUIT FAILURE",
"B2056 RIGHT POWER SLIDING DOOR OPEN/CLOSE OUTPUT CIRCUIT FAILURE",
"B2057 LEFT POWER SLIDING DOOR OPEN/CLOSE SWITCH CIRCUIT SHORT TO GROUND",
"B2058 RIGHT POWER SLIDING DOOR OPEN/CLOSE SWITCH CIRCUIT SHORT TO GROUND",
"B2059 A/C REQUEST INDICATOR SHORT TO GROUND",
"B2060 HEATED BACKLITE INDICATOR CIRCUIT FAILURE",
"B2061 HEATED BACKLITE INDICATOR CIRCUIT SHORTED TO GROUND",
"B2062 DRIVER WINDOW DATA OUTPUT CIRCUIT FAILURE",
"B2063 PASS WINDOW DATA OUTPUT CIRCUIT FAILURE",
"B2064 POWER PEDALS DISABLE RELAY CIRCUIT FAILURE",
"B2065 POWER PEDALS DISABLE RELAY CIRCUIT SHORT TO GROUND",
"B2066 PARK ENABLED STATUS OUTPUT CIRCUIT FAILURE",
"B2067 PARK ENABLED STATUS OUTPUT CIRCUIT SHORT TO GROUND",
"B2068 CONVERTIBLE TOP UP OUTPUT CIRCUIT FAILURE",
"B2069 CONVERTIBLE TOP DOWN OUTPUT CIRCUIT FAILURE",
"B2070 TRAILER TOW RELAY COIL(S) CIRCUIT FAILURE",
"B2071 HAZARD SWITCH SIGNAL SHORT TO GROUND",
"B2072 SEAT MEMORY MODULE DATA LINE SHORT TO BATTERY",
"B2073 SEAT MEMORY MODULE DATA LINE OPEN OR SHORT TO GROUND",
"B2074 SEAT MEMORY MODULE ENABLE LINE SHORT TO BATTERY",
"B2075 SEAT MEMORY MODULE ENABLE LINE OPEN OR SHORT TO GROUND",
"B2076 CELLULAR ANTENNA CONNECTION OPEN",
"B2077 LIFTGATE AJAR SW CIRCUIT FAILURE",
"B2078 DRIVER AIRBAG DEACTIVATION INDICATOR LAMP FAULT",
"B2079 DRIVER AIRBAG DEACTIVATION INDICATOR SHORT TO BATTERY",
"B2080 DRIVER AIRBAG DEACTIVATION INDICATOR SHORT TO GROUND",
"B2081 DRIVER AIRBAG DEACTIVATION INDICATOR OPEN CIRCUIT",
"B2082 MIRROR VERTICAL OUTPUT FAULT",
"B2083 MIRROR HORIZONTAL OUTPUT FAULT",
"B2084 MEMORY SET INDICATOR SHORT TO GROUND",
"B2085 REAR WINDOW LOCKOUT INDICATOR SHORT TO GROUND",
"B2086 REAR WINDOW LOCKOUT INDICATOR SHORT TO BATTERY",
"B2087 SECURITY LINE SHORT TO GROUND",
"B2088 CELLULAR ANTENNA SHORT TO GROUND",
"B2089 PUDDLE / APPROACH LAMP FAULT",
"B2090 REMOTE KEY ENTRY DATA LINE FAILURE",
"B2091 REMOTE KEY COMMUNICATION FAILURE",
"B2092 REMOTE KEY LOW BATTERY",
"B2093 HEATED WINDSHIELD CIRCUIT SHORT TO GROUND",
"B2094 HEATED WINDSHIELD CIRCUIT SHORT TO BATTERY",
"B2095 FRONT RESET SWITCH CIRCUIT FAILURE",
"B2096 FRONT SET SWITCH CIRCUIT FAILURE",
"B2097 COMPASS MODULE FAILURE",
"B2098 AUDIO NETWORK INITIALIZATION (ASYSON) CIRCUIT FAULT",
"B2100 DOOR DRIVER KEY CYLINDER SWITCH FAILURE",
"B2101 HEAD REST SWITCH CIRCUIT FAILURE",
"B2102 ANTENNA CIRCUIT SHORT TO GROUND",
"B2103 ANTENNA NOT CONNECTED",
"B2104 DOOR PASSENGER KEY CYLINDER SWITCH FAILURE",
"B2105 THROTTLE POSITION INPUT OUT OF RANGE LOW",
"B2106 THROTTLE POSITION INPUT OUT OF RANGE HIGH",
"B2107 FRONT WIPER MOTOR RELAY CIRCUIT SHORT TO VBATT",
"B2108 TRUNK KEY CYLINDER SWITCH FAILURE",
"B2109 HEATED WIND SHIELD RELAY SHORT TO VBATT (CHANGED FROM FAILURE 2/6/97)",
"B2110 FRONT WIPER MOTOR RELAY CIRCUIT OPEN (CHANGED FROM FAILURE 2/6/97)",
"B2111 ALL DOOR LOCK INPUT SHORT TO GROUND",
"B2112 DOOR DRIVER SET SWITCH STUCK FAILURE",
"B2113 HEATED WINDSHIELD INPUT SHORT TO GROUND",
"B2114 FRONT WASHER INPUT SHORT TO GROUND",
"B2115 REAR WASHER INPUT SHORT TO GROUND",
"B2116 DOOR DRIVER RESET SWITCH STUCK FAILURE",
"B2117 DRIVER SIDE, SIDE MOUNT AIRBAG LOW CAPACITANCE ON SQUIB",
"B2118 PASSENGER SIDE, SIDE MOUNT AIRBAG LOW CAPACITANCE ON SQUIB",
"B2119 COMPRESSOR FAILURE",
"B2120 DOOR PASSENGER SET SWITCH STUCK FAILURE",
"B2121 ILLUMINATION SWITCH SHORT TO BATTERY",
"B2122 DRIVER SIDE SATELLITE COMMUNICATION CIRCUIT SHORT TO GROUND",
"B2123 PASSENGER SIDE SATELLITE COMMUNICATION CIRCUIT SHORT TO GROUND",
"B2124 DOOR PASSENGER RESET SWITCH STUCK FAILURE",
"B2125 OPEN CIRCUIT ON DOUBLE LOCK RESET LINE",
"B2126 SHORT CIRCUIT TO BATTERY ON DOUBLE LOCK RESET LINE",
"B2127 SHORT CIRCUIT TO GROUND ON DOUBLE LOCK RESET LINE",
"B2128 CENTRAL LOCK MOTOR FAILURE",
"B2129 CENTRAL LOCK FEEDBACK FAILURE",
"B2130 DOUBLE LOCK TIMEOUT FAILURE",
"B2131 DOUBLE LOCK FEEDBACK FAILURE",
"B2132 DIMMER SWITCH CIRCUIT SHORT TO GND",
"B2133 BRAKE MOTOR WARNING LAMP CIRCUIT FAILURE",
"B2134 BRAKE MOTOR WARNING LAMP CIRCUIT SHORT TO VBATT",
"B2135 PARK BRAKE APPLIED WARNING LAMP CIRCUIT FAILURE",
"B2136 PARK BRAKE APPLIED WARNING LAMP CIRCUIT SHORT TO BATTERY",
"B2137 REAR EVAPORATOR TEMPERATURE SENSOR OUT OF RANGE",
"B2138 COOLANT OVERTEMP",
"B2139 DATA MISMATCH (RECEIVE DATA DOES NOT MATCH WHAT WAS EXPECTED)",
"B2140 INITIALIZATION FAILURE",
"B2141 NVM CONFIGURATION FAILURE",
"B2142 NVM TIC FAILURE",
"B2143 NVM MEMORY FAILURE",
"B2144 NVM ALARM DATA FAILURE",
"B2145 NVM RF HR FAILURE",
"B2146 SEAT RECLINE MOTOR POSITION OUT OF RANGE",
"B2147 DRIVER SEAT SWITCH FAULT",
"B2148 PWM INPUT CIRCUIT FAILURE",
"B2149 SEAT FRONT VERTICAL MOTOR POSITION OUT OF RANGE",
"B2150 POWER SUPPLY #1 CIRCUIT SHORT TO GROUND",
"B2151 POWER SUPPLY #2 CIRCUIT SHORT TO GROUND",
"B2152 SEAT REAR VERTICAL MOTOR POSITION OUT OF RANGE",
"B2153 REAR ECHO SENSOR CIRCUIT FAILURE",
"B2154 FRONT ECHO SENSOR CIRCUIT FAILURE",
"B2155 SEAT HORIZONTAL MOTOR POSITION OUT OF RANGE",
"B2156 REAR DOPPLER SENSOR CIRCUIT FAILURE",
"B2157 FRONT DOPPLER SENSOR CIRCUIT FAILURE",
"B2158 SEAT RECLINE MOTOR MEMORY POSITION OUT OF RANGE",
"B2159 MEMORY #1 OUTPUT SHORT TO GROUND",
"B2160 MEMORY #1 OUTPUT SHORT TO VBATT",
"B2161 SEAT FRONT VERTICAL MOTOR MEMORY POSITION OUT OF RANGE",
"B2162 DATA MISMATCH #2 (RECEIVE DATA DOES NOT MATCH WHAT WAS EXPECTED)",
"B2163 CLUTCH POSITION FAULT",
"B2164 SEAT REAR VERTICAL MOTOR MEMORY POSITION OUT OF RANGE",
"B2165 GEAR SHIFT POSITION FAULT",
"B2166 GEAR SELECT POSITION FAULT",
"B2167 SEAT HORIZONTAL MOTOR MEMORY POSITION OUT OF RANGE",
"B2168 UNABLE TO CONFIRM UNLOCK CONDITION",
"B2169 UNABLE TO CONFIRM LOCK CONDITION",
"B2170 STEERING COLUMN LOCK SWITCH CIRCUIT FAILURE",
"B2171 LH REAR SEAT SWITCH FAULT",
"B2172 INERTIA SWITCH INPUT CIRCUIT OPEN",
"B2173 RH REAR SEAT SWITCH FAULT",
"B2174 WINDOW DRIVER REAR REMOTE UP SWITCH SHORT TO BATTERY",
"B2175 A/C REQUEST SIGNAL CIRCUIT SHORT TO GROUND",
"B2176 OVERDRIVE SWITCH CIRCUIT SHORT TO VBATT",
"B2177 INTERIOR SCANNING SENSOR CIRCUIT FAILURE",
"B2178 WINDOW DRIVER REAR REMOTE DOWN SWITCH SHORT TO BATTERY",
"B2179 FRONT WIPER SELECT SWITCH "A" SHORT TO GROUND",
"B2180 FRONT WIPER SELECT SWITCH "B" SHORT TO GROUND",
"B2181 FRONT WIPER SELECT SWITCH "C" SHORT TO GROUND",
"B2182 WINDOW PASSENGER FRONT REMOTE UP SWITCH SHORT TO BATTERY",
"B2183 FRONT WIPER SELECT SWITCH "H" SHORT TO GROUND",
"B2184 FRONT WIPER SELECT SWITCH "W" SHORT TO GROUND",
"B2185 REAR WIPER SELECT SWITCH "D" SHORT TO GROUND",
"B2186 WINDOW PASSENGER FRONT REMOTE DOWN SWITCH SHORT TO BATTERY",
"B2187 REAR WIPER SELECT SWITCH "B" SHORT TO GROUND",
"B2188 REAR WIPER SELECT SWITCH "E" SHORT TO GROUND",
"B2189 DOUBLE LOCK OPEN CIRCUIT, FRONT DRV. AND REAR PSG. DOORS",
"B2190 WINDOW PASSENGER REAR REMOTE UP SWITCH SHORT TO BATTERY",
"B2191 DOUBLE LOCK SHORT TO GROUND, FRONT DRV. AND REAR PSG. DOORS",
"B2192 DOUBLE LOCK SHORT TO BATT, FRONT DRV. AND REAR PSG. DOORS",
"B2193 DOUBLE LOCK OPEN CIRCUIT, FRONT PSG. AND REAR DRV. DOORS",
"B2194 WINDOW PASSENGER REAR REMOTE DOWN SWITCH SHORT TO BATTERY",
"B2195 DRIVER WINDOW  UP / DOWN POWER CIRCUIT SHORT TO GROUND",
"B2196 PASSENGER WINDOW UP / DOWN POWER CIRCUIT SHORT TO GROUND",
"B2197 TV MODULE ERROR",
"B2198 TRAFFICMASTER MODULE ERROR",
"B2199 VICS MODULE ERROR",
"B2200 NO COMMUNICATION TO TV MODULE (NO FITTING OF TV)",
"B2201 NO COMMUNICATION WITH TRAFFIC MASTERMODULE",
"B2202 NO COMMUNICATION TO VICS MODULE (NO FITTING OF VICS)",
"B2203 CD-ROM ERROR",
"B2204 GPS ANTENNA CONNECTION OPEN OR SHORT",
"B2205 GPS RECEIVER ERROR",
"B2206 GYROSCOPE ERROR",
"B2207 ECU ROM CHECKSUM ERROR",
"B2208 NAVIGATION TO HEAD UNIT COMMUNICATION ERROR",
"B2209 INTERIOR LAMP OVERRIDE SWITCH OPEN CIRCUIT",
"B2210 INTERIOR LAMP OVERRIDE SWITCH SHORT TO GROUND",
"B2211 LOW COOLANT LAMP OUTPUT CIRCUIT SHORT TO BATTERY",
"B2212 PANEL DIM SWITCH OUT OF RANGE",
"B2213 DOUBLE LOCK SHORT TO GROUND, FRONT PSG. AND REAR DRV. DOORS",
"B2214 WINDOW PASSENGER FRONT UP SWITCH SHORT TO BATTERY",
"B2215 WINDOW PASSENGER FRONT DOWN SWITCH SHORT TO BATTERY",
"B2216 DOUBLE LOCK SET 2 SHORT TO BATT, FRONT PSG. AND REAR DRV. DOORS",
"B2217 CENTRAL LOCK OPEN CIRCUIT FAILURE",
"B2218 CENTRAL LOCK SHORT TO GROUND",
"B2219 WINDOW DRIVER FRONT CURRENT FEEDBACK EXCEEDED",
"B2220 WINDOW DRIVER REAR CURRENT FEEDBACK EXCEEDED",
"B2221 WINDOW PASSENGER FRONT CURRENT FEEDBACK EXCEEDED",
"B2222 WINDOW PASSENGER REAR CURRENT FEEDBACK EXCEEDED",
"B2223 MIRROR DRIVER DRIVE CIRCUIT FAILURE",
"B2224 MIRROR PASSENGER DRIVE CIRCUIT FAILURE",
"B2225 FRONT CRASH SENSOR MOUNT FAULT",
"B2226 FRONT CRASH SENSOR INTERNAL FAULT",
"B2227 FRONT CRASH SENSOR DRIVER COMMUNICATIONS FAULT",
"B2228 AIR BAG DRIVER CIRCUIT SHORT TO GROUND - LOOP #2",
"B2229 AIR BAG PASSENGER CIRCUIT SHORT TO GROUND - LOOP #2",
"B2230 AIR BAG DRIVER CIRCUIT SHORT TO BATTERY - LOOP #2",
"B2231 AIR BAG PASSENGER CIRCUIT SHORT TO BATTERY - LOOP #2",
"B2232 AIR BAG DRIVER CIRCUIT OPEN - LOOP #2",
"B2233 AIR BAG PASSENGER CIRCUIT OPEN - LOOP #2",
"B2234 AIR BAG DRIVER INFLATOR CIRCUIT RESISTANCE LOW ON SQUIB - LOOP #2",
"B2235 AIR BAG PASSENGER INFLATOR CIRCUIT",
"B2236 WEAK OR DEFECTED ELECTRIC VEHICLE BATTERY MODULE FAULT",
"B2237 VEHICLE SIGNAL INDICATING PARK WHILE VSS PRESENT",
"B2238 POWER CABLE FOR POWER SLIDING DOOR BROKEN",
"B2239 REAR CARGO DOOR SET SWITCH STUCK (SHORT TO GROUND)",
"B2240 REAR CARGO DOOR RESET SWITCH STUCK (SHORT TO GROUND)",
"B2241 REAR CARGO DOOR LOCK CIRCUIT SHORT TO GROUND",
"B2242 REAR CARGO DOOR UNLOCK CIRCUIT OPEN",
"B2243 DRIVER REAR DOOR AJAR CIRCUIT OPEN",
"B2244 DRIVER SLIDING DOOR AJAR CIRCUIT SHORT TO GND",
"B2245 PASSENGER REAR DOOR AJAR CIRCUIT OPEN",
"B2246 PASSENGER SLIDING DOOR AJAR CIRCUIT SHORT TO GND",
"B2247 EV BATTERY PACK TEMPERATURE FAULT",
"B2248 HEATED WINDSHIELD RELAY COIL CIRCUIT FAILURE",
"B2249 HEAD LAMP RELAY COIL SHORT TO BATTERY",
"B2250 ALL DOORS UNLOCK RELAY CIRCUIT FAILURE",
"B2251 PARKLAMP OUTPUT RELAY DRIVER CIRCUIT FAILURE",
"B2252 PARKLAMP OUTPUT RELAY DRIVER SHORT TO BATTERY",
"B2253 CENTRAL LOCK SHORT TO BATTERY",
"B2254 FRONT FOG LAMP SWITCH FAILURE",
"B2255 FRONT WASHER REQUEST TIMEOUT",
"B2256 FRONT WINDOW HEATER RELAY SHORT TO GROUND",
"B2257 FRONT WINDOW HEATER SWITCH SHORT TO GROUND",
"B2258 HEADLAMP WASHER RELAY CIRCUIT SHORT TO BATTERY",
"B2259 INTERMITTENT WIPER CIRCUIT SHORT TO BATTERY",
"B2260 DOOR MOTOR CIRCUIT SHORT TO BATTERY",
"B2261 PARK LAMP SWITCH FAILURE",
"B2262 WIPER PARK TO PARK TIMEOUT",
"B2263 RADIO INPUT CIRCUIT SHORT TO GROUND",

Коды ошибок CAN BUS(B2264-B2999)

"B2264 REAR FOG LAMP SWITCH SHORT TO GROUND",
"B2265 UNLOCK LINE CIRCUIT SHORT TO GROUND",
"B2266 LEFT SIDE BLEND DOOR CIRCUIT FAILURE",
"B2267 RIGHT SIDE BLEND DOOR CIRCUIT FAILURE",
"B2268 STEERING WHEEL CLIMATE CONTROL CIRCUIT OPEN",
"B2269 STEERING WHEEL CLIMATE CONTROL CIRCUIT SHORT TO GROUND",
"B2270 EXCESSIVE DOOR EFFORT DETECTED",
"B2271 OBSTACLE DETECTED DURING OPENING",
"B2272 MICROPHONE BIAS CIRCUIT FAILURE",
"B2273 RUN-DRY OUTPUT FEEDBACK  CIRCUIT FAULT",
"B2274 PHONE TRANSCEIVER ACTIVE CIRCUIT FAILURE",
"B2275 PEDAL FORWARD/REARWARD POT. FEEDBACK CKT. SHORT TO GND",
"B2276 LESS THAN 2 TRANSMITTERS PROGRAMMED",
"B2277 ELECTRONIC POWER STEERING MOTOR MALFUNCTION",
"B2278 STEERING SHAFT TORQUE SENSOR MALFUNCTION",
"B2279 ENGINE RUN SIGNAL SHORT TO BATTERY",
"B2280 CRASH UNLOCK SIGNAL NOT PRESENT",
"B2281 RIGHT TURN SWITCH SHORT TO GROUND",
"B2282 LEFT TURN SWITCH SHORT TO GROUND",
"B2283 TURN SIGNAL CHIME SHORT TO BATTERY",
"B2284 TURN SIGNAL CHIME SHORT TO GROUND",
"B2285 SIM CARD FAILURE",
"B2286 TRIP COMPUTER MODE SWITCH SHORT TO GROUND",
"B2287 INCLINATION SENSOR CIRCUIT FAILURE",
"B2288 VOICE MODULE ERROR",
"B2289 VOICE MODULE COMMUNICATION ERROR",
"B2290 OCCUPANT CLASSIFICATION SYSTEM FAULT",
"B2291 OCCUPANT POSITION SYSTEM FAULT",
"B2292 RESTRAINT SYSTEM - SEATBELT PRETENSIONER FAULT",
"B2293 RESTRAINT SYSTEM - AIRBAG FAULT",
"B2294 RESTRAINT SYSTEM - CURTAIN FAULT",
"B2295 RESTRAINT SYSTEM - SIDE AIRBAG FAULT",
"B2296 RESTRAINT SYSTEM - IMPACT SENSOR FAULT",
"B2297 AIR DISCHARGE TEMPERATURE SENSOR (PANEL) CIRCUIT OPEN",
"B2298 AIR DISCHARGE TEMPERATURE SENSOR (PANEL) SHORT TO GROUND",
"B2299 AIR DISCHARGE TEMPERATURE SENSOR (FLOOR) CIRCUIT OPEN",
"B2300 SEAT DRIVER MEMORY POSITION ERROR",
"B2301 SEAT PASSENGER MEMORY POSITION ERROR",
"B2302 SEAT HEADREST FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2303 SEAT HEADREST FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2304 SEAT HEADREST FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2305 SEAT HEADREST FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2306 SEAT HEADREST MOTOR STALLED",
"B2307 AIR DISCHARGE TEMPERATURE SENSOR (FLOOR) SHORT TO GROUND",
"B2308 INTERIOR AIR TEMPERATURE INLET MOTOR FAILURE",
"B2309 SEAT MOTOR OUT OF RANGE",
"B2310 MIRROR DRIVER MEMORY POSITION ERROR",
"B2311 MIRROR PASSENGER MEMORY POSITION ERROR",
"B2312 MIRROR PASSENGER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2313 MIRROR PASSENGER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2314 MIRROR PASSENGER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2315 MIRROR PASSENGER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2316 MIRROR PASSENGER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2317 MIRROR PASSENGER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2318 MIRROR PASSENGER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2319 MIRROR PASSENGER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2320 MIRROR DRIVER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2321 MIRROR DRIVER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2322 MIRROR DRIVER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2323 MIRROR DRIVER HORIZONTAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2324 MIRROR DRIVER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2325 MIRROR DRIVER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2326 MIRROR DRIVER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2327 MIRROR DRIVER VERTICAL FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2328 COLUMN REACH FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2329 COLUMN REACH FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2330 COLUMN REACH FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2331 COLUMN REACH FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2332 COLUMN TILT FEEDBACK POTENTIOMETER CIRCUIT FAILURE",
"B2333 COLUMN TILT FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2334 COLUMN TILT FEEDBACK POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"B2335 COLUMN TILT FEEDBACK POTENTIOMETER CIRCUIT SHORT TO GROUND",
"B2336 MIRROR SWITCH ASSEMBLY CIRCUIT FAILURE",
"B2337 MIRROR SWITCH ASSEMBLY CIRCUIT OPEN",
"B2338 MIRROR SWITCH ASSEMBLY CIRCUIT SHORT TO BATTERY",
"B2339 MIRROR SWITCH ASSEMBLY CIRCUIT SHORT TO GROUND",
"B2340 COLUMN REACH MOTOR STALLED",
"B2341 COLUMN TILT MOTOR STALLED",
"B2342 SEAT SWITCH REFERENCE VOLTAGE POSITIVE COMMON OPEN CIRCUIT",
"B2343 SEAT SWITCH REFERENCE VOLTAGE POSITIVE COMMON SUPPLY LOW VOLTAGE",
"B2344 SEAT SWITCH REFERENCE VOLTAGE POSITIVE COMMON SUPPLY VOLTAGE FAULT",
"B2345 SEAT SWITCH REFERENCE VOLTAGE NEGATIVE COMMON OPEN CIRCUIT",
"B2346 MIRROR SWITCH REFERENCE VOLTAGE POSITIVE COMMON OPEN CIRCUIT",
"B2347 MIRROR SWITCH REFERENCE VOLTAGE POSITIVE COMMON SUPPLY LOW VOLTAGE",
"B2348 MIRROR SWITCH REFERENCE VOLTAGE POSITIVE COMMON SUPPLY VOLTAGE FAULT",
"B2349 MIRROR SWITCH REFERENCE VOLTAGE NEGATIVE COMMON OPEN CIRCUIT",
"B2350 STEERING COLUMN SWITCH CIRCUIT SHORT TO BATTERY",
"B2351 STEERING COLUMN SWITCH CIRCUIT FAILURE",
"B2352 DRIVER MEMORY POWER SWITCH INDICATOR CIRCUIT SHORT TO BATTERY",
"B2353 DRIVER MIRROR POWER DRIVER CIRCUIT SHORT GROUND",
"B2354 DRIVER MIRROR HORIZONTAL / VERTICAL FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2355 PASSENGER MIRROR HORIZONTAL / VERTICAL FEEDBACK POTENTIOMETER CIRCUIT OPEN",
"B2356 DRIVER SEAT HEATER OUTPUT FAULT",
"B2357 DRIVER WINDOW DOWN CURRENT SENSE LOW CIRCUIT FAILURE",
"B2358 ADJUSTABLE PEDAL SWITCH FAILURE",
"B2359 ACCESSORY DELAY OUTPUT CIRCUIT FAILURE",
"B2360 WINDOW MOTOR CONTROL OUTPUT CIRCUIT FAILURE",
"B2361 PASSENGER SEAT HEATER OUTPUT FAULT",
"B2362 REMOTE OPEN/CLOSE SIGNAL CIRCUIT SHORT TO GROUND",
"B2363 OPTICAL SENSOR SYSTEM FAILURE",
"B2364 FUEL FILLER DOOR CIRCUIT OPEN",
"B2365 B-PILLAR POWER SLIDING DOOR OPEN/CLOSE SWITCH INPUT CKT. SHORT TO GND.",
"B2366 IP POWER SLIDING DOOR OPEN/CLOSE SWITCH CKT. SHORT TO GND.",
"B2367 POWER SLIDING DOOR OVERRIDE SWITCH INPUT CKT. SHORT TO GND.",
"B2368 STEERING COLUMN SWITCH CIRCUIT OUT OF RANGE",
"B2369 CHIME OUTPUT REQUEST CKT. SHORT TO GROUND",
"B236A CHIME OUTPUT CIRCUIT OPEN",
"B2370 SEAT HEATER POWER SHUTDOWN",
"B2371 INVALID DRIVER SEAT TEMPERATURE SET POINT",
"B2372 INVALID  PASSENGER SEAT TEMPERATURE SET POINT",
"B2373 LED #1 CIRCUIT SHORT TO BATTERY",
"B2374 POWER SLIDING DETENT (LATCH) CIRCUIT  FAILURE",
"B2375 SCLM INVALID UNLOCK ACTION",
"B2376 SCLM LOCK STATUS NOT CONFIRMED.",
"B2377 SCLM UNLOCK STATUS NOT CONFIRMED.",
"B2378 SCLM INVALID LOCK ACTION",
"B2379 SCL NOT CONFIGURED - ID NOT STORED",
"B2380 HEATER COOLANT TEMP. SENSOR CIRCUIT SHORT TO GND",
"B2381 HEATER COOLANT TEMP. SENSOR CIRCUIT OPEN",
"B2382 BACKUP LIGHT RELAY CIRCUIT- OPEN",
"B2383 BACKUP LIGHT RELAY CIRUCIT- LOW",
"B2384 AUDIO REVERSE AID MUTE INPUT CKT. FAILURE",
"B2385 AUDIO NAVIGATION MUTE INPUT CKT. FAILURE",
"B2386 GAS DISCHARGE LAMP INGITION FAILED",
"B2387 GAS DISCHARGE LAMP IGNITOR MODULE CIRCUIT FAILURE",
"B2388 GAS DISCHARGE LAMP OPERATING VOLTAGE OUT OF RANGE DURING STATIC OPERATION",
"B2389 IGNITION COUNTER OR TIMEOUT EXPIRED",
"B2390 MASTER / SLAVE COMMUNICATION FAILURE",
"B2391 RESISTANCE AT LOW BEAM HEADLIGHT SWITCH INPUT TOO HIGH",
"B2392 VOLTAGE AT LOW BEAM HEADLIGHT SWITCH INPUT TOO HIGH",
"B2393 ECU OUTPUT TO IGNITOR CIRCUIT FAILURE",
"B2394 HEADREST UP SWITCH TIMEOUT",
"B2395 HEADREST DOWN SWITCH TIMEOUT",
"B2396 HEADREST IDENT-INPUT CIRCUIT FAILURE",
"B2397 HEADREST POTENTIOMETER REFERENCE CIRCUIT FAILURE",
"B2398 HEADREST POTENTIOMETER REFERENCE CIRCUIT SHORT TO GROUND",
"B2399 HEADREST POTENTIOMETER GROUND CIRCUIT FAILURE",
"B2400 HEADREST POTENTIOMETER GROUND CIRCUIT SHORT TO BATTERY",
"B2401 AUDIO TAPE DECK MECHANISM FAULT",
"B2402 AUDIO CD/DJ THERMAL SHUTDOWN FAULT",
"B2403 AUDIO CD/DJ INTERNAL FAULT",
"B2404 AUDIO STEERING WHEEL SWITCH CIRCUIT FAULT",
"B2405 AUDIO SINGLE-DISC CD PLAYER THERMAL SHUTDOWN FAULT",
"B2406 AUDIO SINGLE-DISC CD PLAYER INTERNAL FAULT",
"B2407 BACKUP LIGHT RELAY CIRCUIT - HIGH",
"B2408 SPEAKER LINE SHORT CIRCUIT",
"B2409 AM RECEIVING SIGNAL ERROR",
"B2410 FM RECEIVING SIGNAL ERROR",
"B2411 HUMIDITY SENSOR OPEN",
"B2412 HUMIDITY SENSOR SHORT",
"B2413 HUMIDITY SENSOR FAILURE",
"B2414 HEADLAMP WASHER RELAY CIRCUIT SHORT CIRCUIT GND",
"B2415 PINCH STRIP OPEN OR SHORT TO BATTERY",
"B2416 CLIMATE CONTROL RECIRCULATION ACTUATOR OUT OF LIMITS",
"B2417 PINCH STRIP STUCK ACTIVE",
"B2418 SENSOR POWER SHORT TO GROUND",
"B2419 SENSOR 1 INVALID",
"B2420 SENSOR 2 INVALID",
"B2421 VSS STUCK HIGH",
"B2422 OPENSW INPUT STUCK ACTIVE",
"B2423 CLOSESW INPUT STUCK ACTIVE",
"B2424 LATCH "ENGAGED" MISMATCH",
"B2425 REMOTE KEYLESS ENTRY OUT OF SYNCHRONIZATION",
"B2426 PASSENGER SOLAR RADIATION SENSOR  CIRCUIT OPEN",
"B2427 PASSENGER SOLAR RADIATION SENSOR  CIRCUIT SHORT TO GROUND",
"B2428 A/C POST HEATER SENSOR #2 CIRCUIT FAILURE",
"B2429 A/C POST HEATER SENSOR #2 CIRCUIT SHORT TO GROUND",
"B2430 LATCH "UP" MISMATCH",
"B2431 TRANSPONDER PROGRAMMING FAILED",
"B2432 DRIVERS SEAT BELT BUCKLE SWITCH CIRCUIT OPEN",
"B2433 DRIVERS SEAT BELT BUCKLE SWITCH CIRCUIT SHORT TO BATTERY",
"B2434 DRIVERS SEAT BELT BUCKLE SWITCH CIRCUIT SHORT TO GROUND",
"B2435 DRIVERS SEAT BELT BUCKLE SWITCH RESISTANCE OUT OF RANGE",
"B2436 PASSENGERS SEAT BELT BUCKLE SWITCH CIRCUIT OPEN",
"B2437 PASSENGERS SEAT BELT BUCKLE SWITCH CIRCUIT SHORT TO BATTERY",
"B2438 PASSENGERS SEAT BELT BUCKLE SWITCH CIRCUIT SHORT TO GROUND",
"B2439 PASSENGERS SEAT BELT BUCKLE SWITCH RESISTANCE OUT OF RANGE",
"B2440 PASSENGER SIDE IMPACT SENSOR MOUNTING FAULT",
"B2441 DRIVER SIDE IMPACT SENSOR MOUNTING FAULT",
"B2442 INTRUSION SENSOR FAULT",
"B2443 POWERTRAIN PERFORMANCE MODE SWITCH CIRCUIT FAILURE",
"B2444 DRIVER SIDE IMPACT SENSOR IS FAULTED",
"B2445 PASSENGER SIDE IMPACT SENSOR IS FAULTED",
"B2446 RESCU/VEMS INPUT CIRCUIT OPEN",
"B2447 RESCU/VEMS INPUT CIRCUIT SHORT TO BATTERY",
"B2448 RESCU/VEMS INPUT CIRCUIT SHORT TO GROUND",
"B2449 AUX. HEATER GLOW PLUG CIRCUIT SHORT TO GROUND",
"B2450 AUX. HEATER GLOW PLUG CIRCUIT OPEN",
"B2451 AUX. HEATER FUEL PUMP CIRCUIT SHORT TO GROUND",
"B2452 AUX. HEATER FUEL PUMP CIRCUIT OPEN",
"B2453 AUX. HEATER BLOWER FAN CIRCUIT SHORT TO GROUND",
"B2454 AUX. HEATER BLOWER FAN CIRCUIT OPEN",
"B2455 AUX. HEATER BLOWER FAULTED",
"B2456 AUX. HEATER COOLANT SENSOR CIRCUIT SHORT TO GROUND",
"B2457 AUX. HEATER COOLANT SENSOR CIRCUIT OPEN",
"B2458 AUX. HEATER OVERHEAT SENSOR CIRCUIT SHORT TO GROUND",
"B2459 AUX. HEATER OVERHEAT SENSOR CIRCUIT OPEN",
"B2460 AUX. HEATER FLAME SENSOR CIRCUIT SHORT TO GROUND",
"B2461 AUX. HEATER FLAME SENSOR CIRCUIT OPEN",
"B2462 AUX. HEATER FLAME OUT FAULT",
"B2463 AUX. HEATER OVERHEAT FAULT",
"B2464 AUX. HEATER START TIME EXCEEDED",
"B2465 AUX. HEATER START COUNTER OVERRUN/SYSTEM LOCKED (SAME AS BELOW ")",
"B2466 AUX. HEATER OVERHEAT COUNTER OVERRUN/SYSTEM LOCKED",
"B2467 AUX. HEATER COOL DOWN TIME EXCEEDED (MAY BE CON. TO A453-5 )",
"B2468 AUX. HEATER COOLANT PUMP CIRCUIT SHORT TO GROUND",
"B2469 AUX. HEATER COOLANT PUMP CIRCUIT OPEN",
"B2470 INTERIOR FAN CONTROL CIRCUIT SHORT TO GROUND",
"B2471 INTERIOR FAN CONTROL CIRCUIT OPEN",
"B2472 FOG LAMP SWITCH  FAILURE",
"B2473 PASSENGER DOOR DISARM SWITCH CKT SHORT TO GND",
"B2474 PASSENGER DOOR LOCK SWITCH CKT. SHORT TO GROUND",
"B2475 PASSENGER DOOR UNLOCK SWITCH CKT. SHORT TO GROUND",
"B2476 RADIO PRESENT SWITCH CKT FAILURE",
"B2477 MODULE CONFIGURATION FAILURE",
"B2478 ANTI THEFT INPUT SIGNAL SHORT TO GROUND",
"B2479 BRAKE PARK SWITCH CIRCUIT SHORT TO GROUND",
"B2480 LF CORNER LAMP OUTPUT CKT SHORT TO BATTERY",
"B2481 CONVERTIBLE TOP UP/DOWN SWITCH FAULT",
"B2482 RF CORNER LAMP OUTPUT CKT SHORT TO BATTERY",
"B2483 ENABLE SIGNAL OPEN CIRCUIT",
"B2484 DISABLE SIGNAL SHORT TO GROUND",
"B2485 LF SIDE REPEATER LAMP OUTPUT CKT SHORT TO BATTERY",
"B2486 CLIMATE CONTROL SEAT MODULE VOLTAGE OUT OF RANGE",
"B2487 RF SIDE REPEATER LAMP OUTPUT CKT SHORT TO BATTERY",
"B2488 THUMB-WHEEL SWITCH VOLTAGE OUT OF RANGE HIGH",
"B2489 UNDERHOOD LAMP OUTPUT CIRCUIT FAILURE",
"B2490 UNDERHOOD LAMP OUTPUT CIRCUIT SHORT TO BATTERY",
"B2491 RF PARK LAMP OUTPUT CIRCUIT SHORT TO BATTERY",
"B2492 ALREADY PROGRAMMED (TEST MODE DTC ONLY !!!)",
"B2493 LF PARK LAMP OUTPUT CIRCUIT SHORT TO BATTERY",
"B2494 ANTI THEFT HORN OUTPUT CIRCUIT SHORT TO BATT",
"B2495 ANTI THEFT HORN OUTPUT CIRCUIT FAILURE",
"B2496 ANTI THEFT HORN OUTPUT CIRCUIT SHORT TO GND",
"B2497 BLOWER RPM OUT OF RANGE",
"B2498 HEADLAMP SWITCH MULTIPLE SIGNALS INPUT ACTIVE",
"B2499 COURTESY LAMP OUTPUT FAILURE",
"B2500 COURTESY LAMP OUTPUT CKT SHORT TO BATTERY",
"B2501 LF LAMP LOW BEAM CIRCUIT FAILURE",
"B2502 LF LAMP LOW BEAM CIRCUIT SHORT TO BATTERY",
"B2503 RF LAMP LOW BEAM CIRCUIT FAILURE",
"B2504 RF LAMP LOW BEAM CIRCUIT SHORT TO BATTERY",
"B2505 LF LAMP HIGH BEAM CIRCUIT FAILURE",
"B2506 LF LAMP HIGH BEAM CIRCUIT SHORT TO BATTERY",
"B2507 RF LAMP HIGH BEAM CIRCUIT FAILURE",
"B2508 RF LAMP HIGH BEAM CIRCUIT SHORT TO BATTERY",
"B2509 REAR FOG LAMP SWITCH CIRCUIT FAILURE",
"B2510 MAIN BLOWER MOTOR RELAY CIRCUIT SHORT TO BATTERY",
"B2511 HORN OUTPUT RELAY CIRCUIT SHORT TO BATTERY",
"B2512 FRONT FOG LAMP RELAY CKT SHORT TO BATTERY",
"B2513 BLOWER (FAN) CIRCUIT FAILURE",
"B2514 BLOWER (FAN) CIRCUIT SHORT TO VBATT",
"B2515 HEATER BLOWER RELAY CIRCUIT FAILURE",
"B2516 BLOWER CONTROL CIRCUIT FAILURE",
"B2517 EMERGENCY POWER OFF SYSTEM FAULTED",
"B2518 COMPRESSOR OVERTEMP FAULT",
"B2519 HIGH MOUNT STOP LAMP CIRCUIT FAILURE",
"B251A PASSENGER TACH CIRCUIT FAILURE",
"B2520 HIGH MOUNT STOP LAMP CIRCUIT SHORT TO BATTERY",
"B2521 TACH CIRCUIT FAILURE",
"B2522 VBATT 1 CIRCUIT FAILURE",
"B2523 LICENSE LAMP CIRCUIT FAILURE",
"B2524 LICENSE LAMP CIRCUIT SHORT TO BATTERY",
"B2525 LEFT REAR BACKUP LAMP CIRCUIT FAILURE",
"B2526 LEFT REAR BACKUP LAMP CIRCUIT SHORT TO BATTERY",
"B2527 LEFT REAR STOP LAMP CIRCUIT FAILURE",
"B2528 LEFT REAR STOP LAMP CIRCUIT SHORT TO BATTERY",
"B2529 LEFT REAR  TURN LAMP CIRCUIT FAILURE",
"B2530 LEFT REAR  TURN LAMP CIRCUIT SHORT TO BATTERY",
"B2531 RIGHT REAR BACKUP LAMP CIRCUIT FAILURE",
"B2532 RIGHT REAR BACKUP LAMP CIRCUIT SHORT TO BATTERY",
"B2533 RIGHT REAR STOP LAMP CIRCUIT FAILURE",
"B2534 RIGHT REAR STOP LAMP CIRCUIT SHORT TO BATTERY",
"B2535 RIGHT REAR  TURN LAMP CIRCUIT FAILURE",
"B2536 RIGHT REAR  TURN LAMP CIRCUIT SHORT TO BATTERY",
"B2537 AUX. HEATER NO START FAULT",
"B2538 AUX. HEATER UNSTABLE FLAME FAULT",
"B2539 AUX A/C MODE POSITION REFERENCE CIRCUIT SHORT TO GROUND",
"B2540 AUX A/C MODE POSITION REFERENCE CIRCUIT SHORT TO BATTERY",
"B2541 LATCH "DOWN" MISMATCH",
"B2542 LCLUTCH OPEN CIRCUIT",
"B2543 AUX A/C CONTROL SWITCH REFERENCE CIRCUIT SHORT TO GROUND",
"B2544 AUX A/C CONTROL SWITCH REFERENCE CIRCUIT SHORT TO BATTERY",
"B2545 SYSTEM POWER RELAY CIRCUIT SHORT TO BATTERY",
"B2546 SYSTEM POWER RELAY CIRCUIT FAILURE",
"B2547 AUX. HEATER FLAME PRIOR TO OPERATION FAULT",
"B2548 AUX. HEATER LOCK OUT MODE FAULT",
"B2549 VEHICLE AIR FAN ACTUATION CIRCUIT SHORT TO GROUND",
"B2550 DOME LAMP OUTPUT CIRCUIT SHORT TO GROUND",

"B2551 RCLUTCH OPEN CIRCUIT",
"B2552 VBATT 2 CIRCUIT OPEN",
"B2553 DISABLE SIGNAL OUTPUT CIRCUIT SHORT TO BATTERY",
"B2554 DOME LAMP OUTPUT CIRCUIT FAILURE",
"B2555 DOME LAMP OUTPUT CIRCUIT SHORT TO BATTERY",
"B2556 ENABLE SIGNAL  CIRCUIT SHORT TO BATTERY",
"B2557 LEFT POWER SLIDING DOOR OPEN/CLOSE OUTPUT CIRCUIT SHORT TO BATTERY",
"B2558 RIGHT POWER SLIDING DOOR OPEN/CLOSE OUTPUT CIRCUIT SHORT TO BATTERY",
"B2559 AUX A/C BLOWER MOTOR RELAY CIRCUIT SHORT TO BATTERY",
"B2560 AUX A/C BLOWER MOTOR RELAY CIRCUIT SHORT TO GROUND",
"B2561 AUX A/C BLOWER SPEED 1 CIRCUIT FAILURE",
"B2562 AUX A/C BLOWER SPEED 1 CIRCUIT SHORT TO GROUND",
"B2563 AUX A/C BLOWER SPEED 2 CIRCUIT FAILURE",
"B2564 AUX A/C BLOWER SPEED 2 CIRCUIT SHORT TO GROUND",
"B2565 RIGHT TAIL LAMP CIRCUIT FAILURE",
"B2566 RIGHT TAIL LAMP CIRCUIT SHORT TO GROUND",
"B2567 REVERSE MIRROR OUTPUT CIRCUIT FAILURE",
"B2568 REVERSE MIRROR OUTPUT CIRCUIT SHORT TO GROUND",
"B2569 LIFTGATE DISARM SWITCH CIRCUIT SHORT TO GROUND",
"B2570 RIGHT LAMP OUTAGE SIGNAL CIRCUIT SHORT TO GROUND",
"B2571 LEFT LAMP OUTAGE SIGNAL CIRCUIT SHORT TO GROUND",
"B2572 BRAKE SHIFT INTERLOCK OUTPUT CIRCUIT FAILURE",
"B2573 BRAKE SHIFT INTERLOCK OUTPUT CIRCUIT SHORT TO GROUND",
"B2574 DRIVERS DOOR LOCK SWITCH SHORT TO GROUND",
"B2575 DRIVERS DOOR UNLOCK SWITCH SHORT TO GROUND",
"B2576 HARDTOP SENSE INPUT SHORT TO GROUND",
"B2577 LEFT TAIL LAMP CIRCUIT FAILURE",
"B2578 PASSENGER POWER WINDOW DOWN SWITCH CIRCUIT FAILURE",
"B2579 PASSENGER POWER WINDOW UP SWITCH CIRCUIT FAILURE",
"B2580 AUX BLOWER SENSE SWITCH CIRCUIT FAILURE",
"B2581 PASSENGER SEAT OCCUPANT DETECTION CIRCUIT SHORT TO GROUND",
"B2582 PASSENGER SEAT OCCUPANT DETECTION CIRCUIT OPEN",
"B2583 CHILD SEAT DETECTION CIRCUIT SHORT TO GROUND",
"B2584 CHILD SEAT DETECTION CIRCUIT OPEN",
"B2585 ANTI THEFT INPUT SIGNAL CIRCUIT SHORT TO BATTERY",
"B2586 HEADLAMP MODE SELECT CIRCUIT FAILURE",
"B2587 PASSENGER SEAT OCCUPANT DETECTION CIRCUIT SHORT TO BATTERY",
"B2588 CHILD SEAT DETECTION CIRCUIT SHORT TO BATTERY",
"B2589 UNEXPECTED DOOR REVERSAL DURING CLOSE",
"B2590 VEHICLE PARK/SPEED SIGNAL CIRCUIT FAILURE",
"B2591 DETENT SIGNAL MISSING DURING UNLATCH",
"B2592 PSD NOT FULLY CLOSED (MODULE COMMANDED SUCCESSFULLY)",
"B2593 POWER SLIDING DOOR OPENED DURING MODULE CLOSE COMMAND",
"B2594 NO MOVEMENT DETECTED AFTER AN UNLATCH DURING POWER OPEN",
"B2595 ANTI THEFT INPUT SIGNAL CIRCUIT FAILURE",
"B2596 HEADLAMP AIM OUTPUT RELAY CIRCUIT SHORT TO BATTERY",
"B2597 HEADLAMP AIM OUTPUT RELAY CIRCUIT FAILURE",
"B2598 HEADLAMP RELAY CIRCUIT FAILURE",
"B2599 TAILGATE RELEASE OPEN CIRCUIT",
"B2600 DOUBLE LOCKING DOOR MOTOR FROZEN",
"B2601 NO LATCH SIGNAL SENSED ON CLOSING AND DOOR REVERSED",
"B2602 MISSING LATCH SIGNAL DURING POWER SLIDING DOOR UNLATCH",
"B2603 PSD NOT FULLY CLOSED DURING SELF-TEST",
"B2604 POWER SLIDING DOOR ON/OFF SWITCH OPEN CIRCUIT",
"B2605 DISABLE SIGNAL OPEN CIRCUIT",
"B2606 A/C TEMPERATURE SENSOR OUT OF RANGE",
"B2607 HARNESS/CONFIGURATION MISMATCH",
"B2608 ECU OUTPUT TO LEFT HEADLAMP STEPPER MOTOR SHORT TO GROUND",
"B2609 ECU OUTPUT TO LEFT HEADLAMP STEPPER MOTOR CIRCUIT FAILURE",
"B2610 ECU OUTPUT DRIVER TO LEFT HEADLAMP STEPPER MOTOR OVERTEMPERATURE",
"B2611 ECU OUTPUT TO RIGHT HEADLAMP STEPPER MOTOR SHORT TO GROUND",
"B2612 ECU OUTPUT TO RIGHT HEADLAMP STEPPER MOTOR CIRCUIT FAILURE",
"B2613 ECU OUTPUT DRIVER TO RIGHT HEADLAMP STEPPER MOTOR OVERTEMPERATURE",
"B2614 FRONT OR REAR AXLE VEHICLE LEVEL SENSOR SUPPLY SHORT TO GROUND.",
"B2615 FRONT OR REAR AXLE VEHICLE LEVEL SENSOR SUPPLY CIRCUIT FAILURE",
"B2616 FRONT AXLE VEHICLE LEVEL SENSOR SIGNAL CIRCUIT FAILURE",
"B2617 FRONT AXLE VEHICLE LEVEL SENSOR SIGNAL SHORT TO GROUND.",
"B2618 FRONT AXLE VEHICLE LEVEL SENSOR SIGNAL NOT PLAUSIBLE.",
"B2619 REAR AXLE VEHICLE LEVEL SENSOR SIGNAL CIRCUIT FAILURE",
"B2620 REAR AXLE VEHICLE LEVEL SENSOR SIGNAL SHORT TO GROUND.",
"B2621 REAR AXLE VEHICLE LEVEL SENSOR SIGNAL NOT PLAUSIBLE.",
"B2622 AUTO LEVELLING ECU SPEED MESSAGE INVALID / NOT AVAILABLE",
"B2623 AUTO LEVELLING ECU LOW BEAM MESSAGE INVALID / NOT AVAILABLE",
"B2624 AUTO LEVELLING ECU SPEED SIGNAL NOT AVAILABLE",
"B2625 AUTO LEVELLING ECU LOW BEAM SIGNAL INPUT OPEN CIRCUIT.",
"B2626 AUTOLEVELLING ECU NOT CALIBRATED",
"B2627 FUEL SENDER CIRCUIT OPEN #2",
"B2628 FUEL SENDER CIRCUIT SHORT TO GROUND #2",
"B2629 OFFBOARD CHARGING CONTINUED AFTER STOP COMMAND ISSUED",
"B2630 OVER CURRENT FAULT DURING OFFBOARD CHARGING",
"B2631 UNDER CURRENT FAULT DURING OFFBOARD CHARGING",
"B2632 OVER VOLTAGE FAULT DURING OFFBOARD CHARGING",
"B2633 DRIVER-FRONT MICROPHONE CIRCUIT FAILURE",
"B2634 LEFT-REAR MICROPHONE CIRCUIT FAILURE",
"B2635 RIGHT-REAR MICROPHONE CIRCUIT FAILURE",
"B2636 EMERGENCY (SOS) SWITCH INPUT SHORT TO GROUND",
"B2637 INFORMATION SWITCH INPUT SHORT TO GROUND",
"B2638 PHONE RECHARGEABLE BATTERY FAULT",
"B2639 DEPLOYMENT INDICATION INPUT OPEN",
"B2640 DEPLOYMENT INDICATION INPUT SHORT TO GROUND",
"B2641 DEPLOYMENT INDICATION INPUT SHORT TO BATTERY",
"B2642 LOW POWER DETECTED",
"B2643 HIGH POWER DETECTED",
"B2644 PHONE MUTE SIGNAL OPEN CIRCUIT",
"B2645 UNDER TEMPERATURE FAULT",
"B2646 ANTENNA CIRCUIT OPEN CIRCUIT #1",
"B2647 ANTENNA CIRCUIT OPEN CIRCUIT #2",
"B2648 ANTENNA CIRCUIT OPEN CIRCUIT #3",
"B2649 ANTENNA CIRCUIT OPEN CIRCUIT #4",
"B2650 ANTENNA CIRCUIT SHORT CIRCUIT #1",
"B2651 ANTENNA CIRCUIT SHORT CIRCUIT #2",
"B2652 ANTENNA CIRCUIT SHORT CIRCUIT #3",
"B2653 ANTENNA CIRCUIT SHORT CIRCUIT #4",
"B2654 HARD/SOFT KEY FAULT",
"B2655 SWITCH AND DISPLAY ECU IS DEFECTIVE",
"B2656 DVD (DIGITAL VERSATILE DISK) ERROR",
"B2657 ELECTRIC VEHICLE DEGRADED BATTERY CAPACITY FAULT",
"B2658 WAIT TO START WARNING INDICATOR CIRCUIT OPEN",
"B2659 COURTESY SWITCH FAULT",
"B2660 CYCLING FAULT DURING OFFBOARD CHARGING",
"B2661 PARKLAMP RELAY OUTPUT SHORT TO VBATT",
"B2662 PARKLAMP RELAY OUTPUT OPEN CIRCUIT",
"B2663 HEADLAMP RELAY OUTPUT SHORT TO VBATT",
"B2664 HEADLAMP RELAY OUTPUT OPEN CIRCUIT",
"B2665 BATTERY BACK SOUNDER CIRCUIT FAILURE",
"B2666 LIFTGATE RELEASE SWITCH CIRCUIT FAILURE",
"B2667 LIFTGLASS RELEASE SWITCH CIRCUIT FAILURE",
"B2668 LIFTGATE RELEASE RELAY COIL SHORT TO VBATT",
"B2669 LIFTGATE RELEASE RELAY COIL FAILURE",
"B2670 LIFTGLASS RELEASE RELAY COIL SHORT TO VBATT",
"B2671 LIFTGLASS RELEASE RELAY COIL CIRCUIT FAILURE",
"B2672 DISCHARGE AIR TEMPERATURE SENSOR CIRCUIT OPEN",
"B2673 DISCHARGE AIR TEMPERATURE SENSOR CIRCUIT SHORT TO GROUND",
"B2674 DOUBLE LOCK OUTPUT SHORT TO VBATT",
"B2675 TRIP RESET BUTTON STUCK",
"B2676 LPG SENDER FAILURE",
"B2677 LOW OIL PRESSURE WARNING ACTIVATED",
"B2678 LOW COOLANT SENDER FAILURE",
"B2679 AIRBAG WARNING ACTIVATED",
"B2680 ODOMETER CHANGED",
"B2681 PRNDL SENDER FAILURE",
"B2682 EEC (PCM) COMMUNICATION FAULT",
"B2683 OVERSPEED "-" BUTTON STUCK",
"B2684 OVERSPEED "+" BUTTON STUCK",
"B2685 OVERSPEED "SEEK" BUTTON STUCK",
"B2686 RIGHT TAIL LAMP CIRCUIT SHORT TO BATTERY",
"B2687 LEFT TAIL LAMP CIRCUIT SHORT TO BATTERY",
"B2688 AUX A/C BLOWER MOTOR RELAY CIRCUIT FAILURE",
"B2689 AUX A/C BLOWER SPEED 1 CIRCUIT SHORT TO VBATT",
"B2690 AUX A/C BLOWER SPEED 2 CIRCUIT SHORT TO VBATT",
"B2691 SEAT BELT BUCKLE SWITCH CIRCUIT FAULT, FRONT DRIVER'S SIDE",
"B2692 FRONT PASSENGER'S SEAT BELT BUCKLE SWITCH CIRCUIT FAULT",
"B2693 INTRUSION POWER SHORT TO VBATT",
"B2694 INTRUSION POWER OUTPUT FAILURE",
"B2695 KEYPAD_A SWITCH CIRCUIT FAILURE",
"B2696 KEYPAD_B SWITCH CIRCUIT FAILURE",
"B2697 KEYPAD_C SWITCH CIRCUIT FAILURE",
"B2698 VBATT 2 CIRCUIT FAILURE",
"B2699 LEFT PINCH STRIP OPEN OR SHORT TO BATTERY",
"B2700 RIGHT PINCH STRIP OPEN OR SHORT TO BATTERY",

"B2701 LEFT PINCH STRIP STUCK ACTIVE",
"B2702 RIGHT PINCH STRIP STUCK ACTIVE",
"B2703 OPEN/CLOSE SWITCH STUCK ACTIVE",
"B2704 OPTICAL SENSOR POWER SHORT TO GROUND",
"B2705 OPTICAL SENSOR 1 INPUT NOT ACTIVE DURING POWERED GATE MOVEMENT",
"B2706 OPTICAL SENSOR 2 INPUT NOT ACTIVE DURING POWERED GATE MOVEMENT",
"B2707 DECK LID/GATE OPEN OUTPUT OVER CURRENT",
"B2708 DECKLID/GATE CLOSE OUTPUT OVER CURRENT",
"B2709 GATE OPEN SHORT TO BATTERY",
"B2710 GATE CLOSE SHORT TO BATTERY",
"B2711 GATE OPEN OUTPUT SHORT TO GROUND OR OPEN",
"B2712 GATE CLOSE OUTPUT SHORT TO GROUND OR OPEN",
"B2713 UNLATCH OUTPUT SHORT TO GROUND",
"B2714 UNCINCH OUTPUT SHORT TO GROUND",
"B2715 CINCH OUTPUT SHORT TO GROUND",
"B2716 LEFT POWER RUNNING BOARD OUTPUT SHORT TO BATTERY",
"B2717 RIGHT POWER RUNNING BOARD OUTPUT SHORT TO BATTERY",
"B2718 LIFTGATE/DECKLID AJAR OUTPUT SHORT TO BATTERY",
"B2719 LEFT POWER RUNNING BOARD OUTPUT SHORT TO GROUND OR OPEN",
"B2720 RIGHT POWER RUNNING BOARD OUTPUT SHORT TO GROUND OR OPEN",
"B2721 LIFTGATE/DECKLID AJAR OUTPUT SHORT TO GROUND OR OPEN",
"B2722 OPEN/CLOSE SWITCH ACTIVE DURING SELFTEST",
"B2723 GLASS POSITION SWITCH ACTIVE DURING SELFTEST",
"B2724 FORKBOLT SWITCH INVALID DURING SELFTEST",
"B2725 DETENT SWITCH INVALID DURING SELFTEST",
"B2726 HOME SWITCH INVALID DURING SELFTEST",
"B2727 HEADREST TILT SWITCH TIMEOUT",
"B2728 CUSHION TEMP 20 DEG.C LESS THAN BACK TEMP",
"B2729 CUSHION OVER-TEMP DETECTED",
"B272A PASSENGER CUSHION OVER-TEMP DETECTED",
"B272B PASSENGER BACK-OVER TEMP DETECTED",
"B272C DRIVER DIFFERENTIAL TEMPERATURE FAULT",
"B272D PASSENGER DIFFERENTIAL TEMPERATURE FAULT",
"B272E DRIVER IGNITION RUN/BLOWE CIRCUIT SHORT TO GROUND",
"B272F PASSENGER IGNITION RUN/BLOWE CIRCUIT SHORT TO GROUND",
"B2730 BACK-OVER TEMP DETECTED",
"B2731 CUSHION TEMP 20 DEG. C HIGHER THAN BACK TEMP",
"B2732 PEDAL TRAVEL SENSOR SHORT TO GROUND",
"B2733 PEDAL TRAVEL SENSOR SHORT TO IGNITION",
"B2734 PEDAL TRAVEL SENSOR SUPPLY ERROR",
"B2735 ECU OUTPUT TO HEADLAMP STEPPER MOTOR CIRCUIT FAILURE",
"B2736 PEDAL TRAVEL SENSOR CIRCUIT FAULT",
"B2737 PEDAL TRAVEL SENSOR JAMMED ERROR",
"B2738 PEDAL TRAVEL SENSOR VELOCITY ERROR",
"B2739 PEDAL TRAVEL SENOSR SIGNAL FAULT",
"B2740 PEDAL TRAVEL SENSOR SPIKE ERROR",
"B2741 SENSOR CLUSTER DEFECTIVE",
"B2742 SENSOR CLUSTER OVERVOLTAGE",
"B2743 SENSOR CLUSTER UNDERVOLTAGE",
"B2744 LEFT COVER OPEN OUTPUT CIRCUIT OVER CURRENT",
"B2745 LEFT COVER OPEN OUTPUT OVER CURRENT",
"B2746 LEFT COVER CLOSE OUTPUT OVER CURRENT",
"B2747 LEFT CINCHER MOTOR SHORT TO BATTERY",
"B2748 LEFT DRIVE MOTOR OPEN CIRCUIT",
"B2749 RIGHT COVER OPEN OUTPUT OVER CURRENT",
"B2750 RIGHT COVER CLOSE OUTPUT OVER CURRENT",
"B2751 RIGHT CINCHER MOTOR SHORT TO BATTERY",
"B2752 RIGHT DRIVE MOTOR OPEN CIRCUIT",
"B2753 LEFT CINCH OUTPUT OVER CURRENT",
"B2754 LEFT UNCINCH OUTPUT OVER CURRENT",
"B2755 LEFT DRIVE SHORT TO BATTERY",
"B2756 LEFT CINCHER MOTOR OPEN",
"B2757 LEFT DRIVE OUTPUT SHORT TO GROUND",
"B2758 RIGHT CINCH OUTPUT OVER CURRENT",
"B2759 RIGHT UNCINCH OUTPUT OVER CURRENT",
"B2760 RIGHT DRIVE SHORT TO BATTERY",
"B2761 RIGHT CINCHER MOTOR OPEN",
"B2762 RIGHT DRIVE OUTPUT SHORT TO GROUND",
"B2763 SENSOR CALIBRATION SHORT TO GROUND",
"B2764 SESNOR CALIBRATION SUPPLY ERROR",
"B2765 SENSOR CALIBRATION SHORT TO IGNITION",
"B2766 SENSOR CALIBRATION CIRCUIT FAULT",
"B2767 SENSOR CALIBRATION JAMMED ERROR",
"B2768 SENSOR CALIBRATION VELOCITY ERROR",
"B2769 SENSOR CALIBRATION SPIKE ERROR",
"B2770 SENSOR CALIBRATION SIGNAL FAULT",

"B2771 LEFT FRONT DOOR AJAR CKT. SHORT TO GROUND",
"B2772 RIGHT FRONT DOOR AJAR CKT SHORT TO GROUND",
"B2773 DRIVERS SIDE AIR BAG CURTAIN RESISTANCE TOO LOW",
"B2774 DRIVERS SIDE AIR BAG CURTAIN OPEN CIRCUIT",
"B2775 DRIVERS SIDE AIR BAG CURTAIN SHORT TO GROUND",
"B2776 DRIVERS SIDE AIR BAG CURTAIN SHORT TO BATTERY",
"B2777 PASSENGER'S SIDE AIR BAG CURTAIN RESISTANCE TO LOW",
"B2778 PASSENGER'S SIDE AIR BAG CURTAIN OPEN CIRCUIT",
"B2779 PASSENGER'S SIDE AIR BAG CURTAIN SHORT TO GROUND",
"B2780 PASSENGER'S SIDE AIR BAG CURTAIN SHORT TO BATTERY",
"B2781 INTERIOR AIR QUALITY SENSOR TO DATC OPEN CIRCUIT",
"B2782 INTERIOR AIR QUALITY SENSOR TO DATC SHORT CIRCUIT",
"B2783 INTERIOR HUMIDITY SENSOR TO DATC SHORT CIRCUIT",
"B2784 INTERIOR HUMIDITY SENSOR TO DATC OPEN CIRCUIT",
"B2785 TIM DIGITAL OUTPUTS CIRCUIT FAILURE",
"B2786 LATCH SWITCHES MISMATCH",
"B2787 RIGHT LATCH SWITCH INVALID",
"B2788 LEFT LATCH SWITCH INVALID",
"B2789 LEFT OR RIGHT LATCH RELEASE CIRCUIT FAILURE",
"B2790 LCLUTCH OR RCLUTCH CIRCUIT FAILURE",
"B2791 AIRBAG CUTOFF SWITCH (ACS) OUT OF RANGE",
"B2792 CROSS LINK BETWEEN FIRING LOOPS",
"B2793 COOL SWITCH SHORT TO GROUND",
"B2794 3RD ROW POWER FOLD CIRCUIT FAILURE",
"B2795 DRIVER SOLAR RADIATION SENSOR CIRCUIT SHORT TO GROUND",
"B2796 DRIVER SOLAR RADIATION SENSOR CIRCUIT OPEN",
"B2797 DRIVER WATER VALVE CIRCUIT OPEN",
"B2798 DRIVER WATER VALVE CIRCUIT SHORT",
"B2799 PASSENGER WATER VALVE CIRCUIT OPEN",
"B2800 PASSENGER WATER VALVE CIRCUIT SHORT",
"B2801 HEAD LAMP OPEN CIRCUIT",
"B2802 HEAD LAMP SHORT TO BATTERY",
"B2803 HEAD LAMP SHORT TO GROUND",
"B2804 RESERVOIR SOLENOID SIGNAL SHORT TO BATTERY",
"B2805 RESERVOIR SOLENOID SENSOR SUPPLY SHORT TO BATTERY",
"B2806 RESERVOIR SOLENOID SENSOR SUPPLY SHORT TO GROUND",
"B2807 PRESSURE SENSOR SIGNAL SHORT TO BATTERY",
"B2808 PRESSURE SENSOR SUPPLY SHORT TO BATTERY",
"B2809 PRESSURE SENSOR SUPPLY SHORT TO GROUND",
"B2810 AIR SUSPENSION VENT SOLENOID CIRCUIT FAILURE",
"B2811 ECU IS IN ASSEMBLY STATE",
"B2812 LH POWER RUNNING BOARD CONNECTION FAIL",
"B2813 LH POWER RUNNING BOARD STOW TIME FAIL",
"B2814 LH POWER RUNNING BOARD DEPLOY TIME FAIL",
"B2815 RH POWER RUNNING BOARD CONNECTION FAIL",
"B2816 RH POWER RUNNING BOARD STOW TIME FAIL",
"B2817 RH POWER RUNNING BOARD DEPLOY TIME FAIL",
"B2818 A/C REQUEST SIGNAL CIRCUIT SHORT TO BATTERY",
"B2819 GATE MOTOR CIRCUIT SHORT TO BATTERY",
"B2820 GATE MOTOR CIRCUIT SHORT TO GROUND OR OPEN",
"B2821 CINCHER MOTOR / UNLATCH ACTUATOR SHORT TO GROUND OR OPEN",
"B2822 CINCHER MOTOR / UNLATCH ACTUATOR SHORT TO BATTERY",
"B2823 LEFT TAILGATE DOOR AJAR CIRCUIT SHORT TO GROUND",
"B2824 RIGHT TAILGATE DOOR AJAR CIRCUIT SHORT TO GROUND",
"B2825 MOVEMENT CEASED DUE TO EXCESSIVE SPEED DEVIATION",
"B2826 FRONT EVAPORATOR TEMP SENSOR CIRCUIT FAILURE",
"B2827 FRONT EVAPORATOR TEMP SENSOR SHORT TO GROUND",
"B2828 REAR EVAPORATOR TEMP SENSOR CIRCUIT FAILURE",
"B2829 REAR EVAPORATOR TEMP SENSOR SHORT TO GROUND",
"B2830 RAW ATTITUDE SIGNAL NOT PLAUSABLE",
"B2831 RAW ATTITUDE CIRCUIT FAILURE",
"B2832 FAULT DTC (CM): MODE SERVO FAILURE",
"B2833 FAULT DTC (CM): SENSOR SUPPLY FAULT",
"B2834 FAULT DTC (CM): AIR MIX SERVO FAILURE",
"B2835 FAULT DTC (CM): OUTLET AIR TEMPERATURE THERMISTOR CIRCUIT FAILURE",
"B2836 FRONT THERMISTOR CIRCUIT FAILURE",
"B2837 FRONT THERMISTOR SHORT TO GROUND",
"B2838 REAR THERMISTOR CIRCUIT FAILURE",
"B2839 REAR THERMISTOR SHORT TO GROUND",
"B2840 AMBIENT AIR THERMISTOR CIRCUIT FAILURE",
"B2841 AMBIENT AIR THERMISTOR SHORT TO GROUND",
"B2842 FATULT DTC (CM): COOL AIR BYPASS FAILURE",
"B2843 FAULT DTC (CM): AIR INTAKE FAILURE",
"B2844 IGNITION FAULT",
"B2845 SMOG SENSOR CIRCUIT FAILURE",
"B2846 SOLAR SENSOR CIRCUIT FAILURE",
"B2847 INTRUSION SENSOR POWER SHORT TO GROUND",
"B2848 HORN OUTPUT RELAY CIRCUIT SHORT TO GROUND",
"B2849 HORN OUTPUT RELAY CIRCUIT OPEN",
"B2850 DRIVER'S SIDE AIR BAG CURTAIN LOW CAPACITANCE ON SQUIB",
"B2851 PASSENGER'S SIDE AIR BAG CURTAIN LOW CAPACITANCE ON SQUIB",
"B2852 RIGHT SIDE SATELLITE SENSOR CIRCUIT SHORT TO GROUND/VBATT",
"B2853 LEFT SIDE SATELLITE SENSOR CIRCUIT SHORT TO GROUND/VBATT",
"B2854 LEFT SIDE CRASH SENSOR ID FAULT",
"B2855 FRONT CRASH SENSOR SHORT TO GROUND/VBATT",
"B2856 FRONT CRASH SENSOR ID FAULT",
"B2857 AUDIO INTERNAL MULTI-DISC FAULT",
"B2858 SDARS MODULE IS DEFECTIVE",
"B2859 POWER SLIDING DOOR POSITION SENSOR OUT OF RANGE",
"B2860 AIRBAG CUTOFF SWITCH (ACS) ECU FAILURE",
"B2861 AIRBAG CUTOFF SWITCH (ACS) COMMUNICATION FAILURE",
"B2862 AIRBAG CUTOFF SWITCH (ACS) INDICATOR FAILURE",
"B2863 AUX. CABIN HEATER #1 RELAY CIRCUIT OPEN",
"B2864 AUX. CABIN HEATER #1 RELAY CIRCUIT SHORT TO BATTERY",
"B2865 AUX. CABIN HEATER #2 RELAY CIRCUIT OPEN",
"B2866 AUX. CABIN HEATER #2 RELAY CIRCUIT SHORT TO BATTERY",
"B2867 CONNECTOR HALF INSERTION DETECTED",
"B2868 LEFT FRONT TIRE PRESSURE SENSOR FAULT",
"B2869 RIGHT FRONT TIRE PRESSURE SENSOR FAULT",
"B2870 RIGHT REAR TIRE PRESSURE SENSOR FAULT",

"B2871 LEFT REAR TIRE PRESSURE SENSOR FAULT",
"B2872 TIRE PRESSURE SENSOR FAULT",
"B2873 LEFT SIDE CRASH SENSOR INTERNAL FAULT",
"B2874 RIGHT SIDE CRASH SENSOR INTERNAL FAULT",
"B2875 RIGHT SIDE CRASH SENSOR ID FAULT",
"B2876 STRIKER DRIVE MOTOR SHORT TO BATTERY",
"B2877 STRIKER DRIVE OUTPUT SHORT TO GROUND",
"B2878 TELEMATICS/OHC BUTTON STUCK FAILURE",
"B2879 FUEL TANK JET PUMP FAULT",
"B2880 SDARS TERRESTRIAL ANTENNA OPEN/SHORT",
"B2881 COLUMN REACH MOVEMENT FAULT - PRIMARY AXIS",
"B2882 COLUMN REACH MOVEMENT FAULT - SECONDARY AXIS",
"B2883 COLUMN TILT MOVEMENT FAULT - PRIMARY AXIS",
"B2884 COLUMN TILT MOVEMENT FAULT - SECONDARY AXIS",
"B2885 SPARE TIRE PRESSURE SENSOR FAULT",
"B2886 PASSENGER SIDE CRASH SENSOR ID FAULT",
"B2887 DRIVER SIDE CRASH SENSOR ID FAULT",
"B2888 AUDIO HEAD UNIT MEDIA FAULT",
"B2889 PASSENGER SOLAR RADIATION SENSOR CIRCUIT SHORT TO BATTERY",
"B2890 PASSENGER SOLAR RADIATION SENSOR OUT OF RANGE",
"B2891 FRONT WIPER SWITCH POTENTIOMETER CIRCUIT FAILURE",
"B2892 FRONT WIPER SWITCH POTENTIOMETER OUT OF RANGE",
"B2893 FRONT WIPER MOTOR CIRCUIT FAILURE",
"B2894 LIFTGATE/DECKLID RELEASE CIRCUIT FAILURE",
"B2895 TRIP COMPUTER MODE SWITCH CIRCUIT FAILURE",
"B2896 ODOMETER DATA FAILURE",
"B2897 AUTOLAMP RELAY CIRCUIT FAILURE",
"B2898 RIGHT TURN SIGNAL INDICATOR OUTPUT FAILURE",
"B2899 LEFT TURN SIGNAL INDICATOR OUTPUT FAILURE",
"B2900 VIN MISMATCH",

"B2901 PARK BRAKE SWITCH INPUT CIRCUIT FAILURE",
"B2902 REAR WINDOW AJAR SWITCH INPUT FAILURE",
"B2903 CHIME OUTPUT CIRCUIT SHORT TO BATTERY",
"B2904 PARTIAL MUTE CIRCUIT FAILURE",
"B2905 STRIKER DRIVE MOTOR OPEN CIRCUIT",
"B2906 STRIKER UP SWITCH INPUT INVALID",
"B2907 STRIKER DOWN SWITCH INPUT INVALID",
"B2908 LATCH SWITCH INVALID",
"B2909 BELT TENSION SENSOR FAULT",
"B2910 STRIKER UP / STRIKER DOWN SWITCH MISMATCH",
"B2911 TRIP COMPUTER DATA UNAVAILABLE",
"B2912 REVERSE GEAR SWITCH PLAUSIBILITY FAILURE",
"B2913 AUDIO SUBWOOFER NOT CONNECTED",
"B2914 CENTER SUBWOOFER / SPEAKER NOT CONNECTED",
"B2915 FUEL SENDER CIRCUIT FAILURE #2",
"B2916 REAR BLEND DOOR CIRCUIT FAILURE",
"B2917 REAR MODE DOOR CIRCUIT FAILURE",
"B2918 AUX TEMP BLEND INPUT CIRCUIT FAILURE",
"B2919 AUX BLOWER MOTOR SPEED INPUT CIRCUIT FAILURE",
"B2920 AUX (REAR) MODE DOOR POSITION FAILURE",
"B2921 AUX (REAR) TEMP BLEND DOOR CIRCUIT FAILURE",
"B2922 AUXLIARY BUTTON STUCK",
"B2923 CLIMATE CONTROL BUTTON STUCK",
"B2924 AUDIO BUTTON STUCK",
"B2925 SUBWOOFER SPEAKER SHORT CIRCUIT",
"B2926 DEFROST ACTUATOR MOTOR OUT OF RANGE",
"B2927 MIRROR SWITCH ASSEMBLY CIRCUIT - OVER VOLTAGE",
"B2928 RF RECEIVER NOT CONNECTED",
"B2929 TRANSMIT DATA LINE SHORT TO BATTERY",
"B2930 TRANSMIT DATA LINE OPEN CIRCUIT OR SHORT TO GROUND",

"B2931 OPTICAL SENSOR 1 SHORT TO BATTERY OR OPEN",
"B2932 OPTICAL SENSOR 1 SHORT TO GROUND",
"B2933 OPTICAL SENSOR 2 SHORT TO BATTERY OR OPEN",
"B2934 OPTICAL SENSOR 2 SHORT TO GROUND",
"B2935 DRIVE UNIT FAILURE",
"B2936 GATE MOTOR OPEN",
"B2937 GATE MOTOR SHORT TO GROUND",
"B2938 GATE CLUTCH SHORT TO BATTERY",
"B2939 GATE CLUTCH SHORT TO GROUND OR OPEN",
"B2940 CHIME OUTPUT CIRCUIT SHORT TO GROUND",
"B2941 CINCH MOTOR OPEN",
"B2942 CINCH OUTPUT SHORT TO BATTERY",
"B2943 UNCINCH OUTPUT SHORT TO BATTERY",
"B2944 UNLATCH OUTPUT SHORT TO BATTERY",
"B2945 RF RECEIVER ENABLE SHORT TO GROUND",
"B2946 RF RECEIVER POWER SHORT TO GROUND",
"B2947 GLOBAL OPENING/CLOSING CIRCUIT OPEN",
"B2948 GLOBAL OPENING/CLOSING CIRCUIT SHORT TO GROUND",
"B2949 GLOBAL OPENING/CLOSING CIRCUIT SHORT TO BATTERY",
"B2950 AIR CONDITIONING SYSTEM FAULT",
"B2951 THREE-WAY VALVE RELAY CIRCUIT FAILURE",
"B2952 WAKEUP CIRCUIT FAILURE",
"B2953 ELECTRICAL HAZARD LAMP CITCUIT FAILURE",
"B2954 CHARGE LAMP CIRCUIT FAILURE",
"B2955 CLUSTER POWER CIRCUIT FAILURE",
"B2956 SERVO MOTOR LEFT BLEND DOOR CLOSE LINE CIRCUIT FAILURE",
"B2957 SERVO MOTOR LEFT BLEND DOOR OPEN LINE CIRCUIT FAILURE",
"B2958 SERVO MOTOR VENT OPEN LINE CIRCUIT FAILURE",
"B2959 SERVO MOTOR VENT CLOSE LINE CIRCUIT FAILURE",
"B2960 AIR FLOW RECIRCULATION DOOR OPEN LINE DRIVER CIRCUIT FAILURE",

"B2961 AIR FLOW RECIRCULATION DOOR CLOSE LINE DRIVER CIRCUIT FAILURE",
"B2962 PASSENGER SEAT HEATER OUTPUT FAULT",
"B2963 DRIVER SEAT HEATER FEEDBACK CIRCUIT FAULT",
"B2964 PASSENGER SEAT HEATER FEEDBACK CIRCUIT FAULT",
"B2965 AUDIO SYSTEM SPEAKER CIRCUIT FAULT",
"B2966 FRONT WASHER SWITCH STUCK",
"B2967 REAR WASHER SWITCH STUCK",
"B2968 BATTERY BACK SOUNDER CIRCUIT SHORT TO GROUND",
"B2969 FUEL PUMP STATUS INPUT CIRCUIT FAILURE",
"B2970 TAILGATE RELEASE SWITCH CIRCUIT FAILURE",
"B2971 PEDAL POSITION INPUT SHORT TO GROUND",
"B2972 PEDAL POSITION INPUT SHORT TO BATTERY",
"B2973 DAYTIME RUNNING LAMP OUTPUT SHORTED TO GROUND",
"B2974 LIGHTING MODE SWITCH INPUT CIRCUIT FAILURE",
"B2975 AUX. HEATER LINE OVERLOAD",
"B2976 AUX. HEATER LINE FAILURE",
"B2977 PEDAL MEMORY POSITION OUT OF RANGE",
"B2978 PEDAL MOTOR OUT OF RANGE",
"B2979 HIGH PRESSURE A/C COMPRESSOR CUT OUT",
"B2980 SERVO MOTOR RIGHT BLEND DOOR CLOSE LINE CIRCUIT FAILURE",
"B2981 SERVO MOTOR RIGHT BLEND DOOR OPEN LINE CIRCUIT FAILURE",
"B2982 PARK BRAKE SWITCH INPUT CIRCUIT OPEN",
"B2983 DRIVER DOOR SWITCH OUT OF SELF TEST RANGE",
"B2984 DEPLOYABLE STEERING COLUMN CIRCUIT OPEN",
"B2985 DEPLOYABLE STEERING COLUMN CIRCUIT SHORT TO BATTERY",
"B2986 DEPLOYABLE STEERING COLUMN CIRCUIT SHORT TO GROUND",
"B2987 DEPLOYABLE STEERING COLUMN CIRCUIT RESISTANCE LOW ON SQUIB",
"B2988 KNEE BOLSTER COLUMN CIRCUIT OPEN",
"B2989 KNEE BOLSTER CIRCUIT SHORT TO BATTERY",
"B2990 KNEE BOLSTER CIRCUIT SHORT TO GROUND",
"B2991 KNEE BOLSTER CIRCUIT RESISTANCE LOW ON SQUIB",
"B2992 ELECTRIC PARK BRAKE OVERLOAD",
"B2993 ELECTRIC PARK BRAKE TEMPERATURE MODEL TOO HIGH",
"B2994 ELECTRIC PARK BRAKE TEMPERATURE SENSOR TOO HIGH",
"B2995 VIDEO FEED MISSING",
"B2996 SERVO MOTOR FLOOR CLOSE LINE CIRCUIT FAILURE",
"B2997 SERVO MOTOR FLOOR OPEN LINE CIRCUIT FAILURE",
"B2998 INFLATABLE KNEE BOLSTER CIRCUIT FAILURE",
"B2999 RESTRAINT EVENT NOTIFICATION SIGNAL FAULT",

Коды ошибок CAN BUS(C0869-C2808)

"C0869 AIR SUSPENSION AUXILIARY INFLATOR INDICATOR LAMP CIRCUIT FAILURE",
"C1011 RF ABS VLV-OPEN CKT",
"C1012 RF ABS VLV-B+ SHRT",
"C1013 RF ABS VLV-GND SHRT",
"C1026 LF ABS VLV-OPEN CKT",
"C1027 LF ABS VLV-B+ SHRT",
"C1028 LF ABS VLV-GND SHRT",
"C1056 RR ABS VLV-OPEN CKT",
"C1057 RR ABS VLV-B+ SHRT",
"C1058 RR ABS VLV-GND SHRT",
"C1071 LR ABS VLV-OPEN CKT",
"C1072 LR ABS VLV-B+ SHRT",
"C1073 LR ABS VLV-GND SHRT",
"C1081 SAFETY RELAY-OPEN CKT",
"C1082 SAFETY RELAY-B+ SHRT",
"C1083 SAFETY RELAY-GND SHRT",
"C1084 SAFETY RELAY CONTACT-B+ SHRT",
"C1085 SAFETY RELAY CONTACT-GND SHRT",
"C1090 BLOCKING FAIL-RR & LR AXLE",
"C1091 SPEED WHEEL SENSOR ALL COHERENCY FAILURE",
"C1092 UNABLE TO CALCULATE ENGINE TORQUE DATA",
"C1093 TRACTION CONTROL DISABLE SWITCH CIRCUIT FAILURE",
"C1094 PARK BRAKE APPLY SWITCH CIRCUIT FAILURE",
"C1095 ABS HYDRAULIC PUMP MOTOR CIRCUIT FAILURE",
"C1096 ABS HYDRAULIC PUMP MOTOR CIRCUIT OPEN",
"C1097 ABS HYDRAULIC PUMP MOTOR CIRCUIT SHORT TO GROUND",
"C1098 ABS HYDRAULIC PUMP MOTOR CIRCUIT SHORT TO BATTERY",
"C1099 ELECTRONIC POWER STEERING MOTOR MALFUNCTION",
"C1100 ABS PUMP SWITCH CIRCUIT FAILURE",
"C1101 ABS HYDRAULIC VALVE CIRCUIT FAILURE",
"C1102 ABS ACCELERATION SWITCH CIRCUIT FAILURE",
"C1103 ABS HYDRAULIC BRAKE SWITCH CIRCUIT FAILURE",
"C1104 TRACTION CONTROL ACTIVE LAMP - CIRCUIT SHORT TO BATTERY",
"C1105 TRACTION CONTROL DISABLE LAMP - CIRCUIT SHORT TO BATTERY",
"C1106 TRACTION CONTROL DISABLE SWITCH CIRCUIT SHORT TO BATTERY",
"C1107 ABS FUNCTION ENABLED INPUT CIRCUIT FAILURE",
"C1108 AIR IN HYDRAULIC SYSTEM",
"C1109 SPEED CONTROL ACTUATOR ASSEMBLY CABLE RELEASE  FAILURE",
"C1110 ABS POWER RELAY COIL CIRCUIT FAILURE",
"C1111 ABS POWER RELAY COIL OPEN CIRCUIT",
"C1112 ABS POWER RELAY COIL SHORT CIRCUIT TO GROUND",
"C1113 ABS POWER RELAY COIL SHORT CIRCUIT TO BATTERY",
"C1114 ABS POWER RELAY OUTPUT SHORT CIRCUIT TO GROUND",
"C1115 ABS POWER RELAY OUTPUT SHORT CIRCUIT TO BATTERY",
"C1116 STARTER MOTOR CIRCUIT FAILURE",
"C1117 RPM INPUT CIRCUIT FAILURE",
"C1118 TRACTION CONTROL INDICATED TROQUE REDUCTION CIRCUIT FAILURE",
"C1119 TRACTION CONTROL ACTUAL TORQUE REDUCTION CIRCUIT FAILURE",
"C1120 LEFT FRONT VERTICAL ACCELEROMETER OFFSET OUT OF RANGE",
"C1121 RIGHT FRONT VERTICAL ACCELEROMETER OFFSET OUT OF RANGE",
"C1122 REAR VERTICAL ACCELEROMETER OFFSET OUT OF RANGE",
"C1123 VEHICLE SPEED SENSOR INPUT SHORT TO BATTERY",
"C1124 INPUT SHAFT SPEED SIGNAL MISSING/FAULTED",
"C1125 BRAKE FLUID LEVEL SENSOR INPUT CIRCUIT FAILURE",
"C1126 CRUISE CONTROL COMMAND SWITCH ASSEMBLY CIRCUIT FAILURE",
"C1127 CRUISE CONTROL DEACTIVATOR BRAKE SWITCH CIRCUIT FAILURE",
"C1128 LATERAL ACCELEROMETER OFFSET OUT OF RANGE",
"C1129 RR HEIGHT SENSOR CIRCUIT FAILURE",
"C1130 RR HEIGHT SENSOR CIRCUIT 'OUT OF RANGE'",
"C1131 CLUTCH CIRCUIT FAILURE",
"C1132 CLUTCH POSITION CKT SHORT TO GROUND",
"C1133 CLUTCH POSITION CKT SHORT TO BATTERY",
"C1134 GEAR SHIFT POSITION SHORT TO GROUND",
"C1135 GEAR SHIFT POSITION SHORT TO BATTERY",
"C1136 GEAR SELECT POSITION SHORT TO GROUND",
"C1137 ECU IS DEFECTIVE - DON'T USE; USE 9342",
"C1138 GEAR SELECT POSITION SHORT TO BATTERY",
"C1139 WHEEL SPEED SENSOR CENTER TONE RING MISSING TOOTH FAULT",
"C1140 HYDRAULIC BASE BRAKE FAILURE",
"C1141 WHEEL SPEED SENSOR LF TONE RING TOOTH MISSING FAULT",
"C1142 WHEEL SPEED SENSOR RF TONE RING TOOTH MISSING FAULT",
"C1143 WHEEL SPEED SENSOR LR TONE RING TOOTH MISSING FAULT",
"C1144 WHEEL SPEED SENSOR RR TONE RING TOOTH MISSING FAULT",
"C1145 SPEED WHEEL SENSOR RF INPUT CIRCUIT FAILURE",
"C1146 SPEED WHEEL SENSOR RF CIRCUIT OPEN",
"C1147 VEHICLE SPEED SENSOR SIGNAL SHORT TO GROUND",
"C1148 SPEED WHEEL SENSOR RF COHERENCY FAULT",
"C1149 HYDRAULIC FLUID PRESSURE/ FLOW CIRCUIT FAILURE",
"C1150 TWO SPEED REAR AXLE INPUT SWITCH CIRCUIT SHORT TO VBATT",
"C1151 USED FOR 1995 CONTOUR",
"C1152 USED FOR 1995 CONTOUR",
"C1153 HEIGHT SENSOR POWER CIRCUIT FAILURE",
"C1154 HEIGHT SENSOR POWER CIRCUIT SHORT TO BATTERY",
"C1155 SPEED WHEEL SENSOR LF INPUT CIRCUIT FAILURE",
"C1156 SPEED WHEEL SENSOR LF CIRCUIT OPEN",
"C1157 PARK BRAKE ACTUATOR ASSEMBLY SWITCH APPLIED CIRCUIT FAILURE",
"C1158 SPEED WHEEL SENSOR LF COHERENCY FAULT",
"C1159 HYDRAULIC FLUID PRESSURE/ FLOW CIRCUIT SHORT TO GND",
"C1160 CENTER AXLE DISCONNECT (CAD)  SYSTEM GENERAL FAILURE",
"C1161 AIR PRESSURE LOW CIRCUIT SHORT TO GND",
"C1162 PARK BRAKE SWITCH # 2 RELEASED CIRCUIT FAILURE",
"C1163 PARK BRAKE SWITCH # 2 APPLIED CIRCUIT SHORT TO GND",
"C1164 PARK BRAKE ACTUATOR ASSEMBLY SWITCH CIRCUIT FAILURE",
"C1165 SPEED WHEEL SENSOR RR INPUT CIRCUIT FAILURE",
"C1166 SPEED WHEEL SENSOR RR INPUT OPEN CIRCUIT",
"C1167 PARK BRAKE ACTUATOR ASSEMBLY SWITCH RELEASED CIRCUIT SHORT TO GND",
"C1168 SPEED WHEEL SENSOR RR COHERENCY FAULT",
"C1169 ABS FLUID DUMPING EXCEEDS MAXIMUM TIMING",
"C1170 PRNDL  SWITCH CIRCUIT FAILURE",
"C1171 RR SPD SENS-BLOCKING FAIL",
"C1172 PARK BRAKE SWITCH # 1 APPLIED CIRCUIT FAILURE",
"C1173 PARK BRAKE SWITCH # 1 RELEASED CIRCUIT SHORT TO GND",
"C1174 PARK BRAKE SWITCH # 2 APPLIED CIRCUIT FAILURE",
"C1175 SPEED WHEEL SENSOR LR INPUT CIRCUIT FAILURE",
"C1176 SPEED WHEEL SENSOR LR CIRCUIT OPEN",
"C1177 PARK BRAKE ACTUATOR ASSEMBLY SWITCH RELEASED CIRCUIT FAILURE",
"C1178 SPEED WHEEL SENSOR LR COHERENCY FAULT",
"C1179 SPEED CONTROL ACTUATOR ASSEMBLY CABLE SLACK FAILURE",
"C1180 PARK BRAKE VALVE SOLENOID #1 SENSE INPUT CIRCUIT FAILURE",
"C1181 PARK BRAKE VALVE SOLENOID #1 SENSE INPUT CIRCUIT SHORT TO GOUND",
"C1182 PARK LAMP FLASH RELAY CIRCUIT FAILURE",
"C1183 PARK LAMP FLASH RELAY CIRCUIT SHORT TO BATTERY",
"C1184 ABS SYSTEM IS NOT OPERATIONAL",
"C1185 ABS POWER RELAY OUTPUT CIRCUIT FAILURE",
"C1186 ABS POWER RELAY OUTPUT OPEN CIRCUIT",
"C1187 BRAKE FLUID LEVEL SENSOR INPUT OPEN CIRCUIT",
"C1188 BRAKE FLUID LEVEL SENSOR INPUT SHORT CIRCUIT TO BATTERY",
"C1189 BRAKE FLUID LEVEL SENSOR INPUT SHORT CIRCUIT TO GROUND",
"C1190 SPEED WHEEL SENSOR LF INPUT SHORT CIRCUIT TO BATTERY",
"C1191 SPEED WHEEL SENSOR LF INPUT SHORT CIRCUIT TO GROUND",
"C1192 SPEED WHEEL SENSOR RF INPUT SHORT CIRCUIT TO BATTERY",
"C1193 SPEED WHEEL SENSOR RF INPUT SHORT CIRCUIT TO GROUND",
"C1194 ABS OUTLET VALVE COIL LF CIRCUIT FAILURE",
"C1195 ABS OUTLET VALVE COIL LF CIRCUIT OPEN",
"C1196 ABS OUTLET VALVE COIL LF CIRCUIT SHORT TO BATTERY",
"C1197 ABS OUTLET VALVE COIL LF CIRCUIT SHORT TO GROUND",
"C1198 ABS INLET VALVE COIL LF CIRCUIT FAILURE",
"C1199 ABS INLET VALVE COIL LF CIRCUIT OPEN",
"C1200 ABS INLET VALVE COIL LF CIRCUIT SHORT TO BATTERY",
"C1201 ABS INLET VALVE COIL LF CIRCUIT SHORT TO GROUND",
"C1202 ABS OUTLET VALVE COIL REAR CIRCUIT FAILURE",
"C1203 ABS OUTLET VALVE COIL REAR CIRCUIT OPEN",
"C1204 ABS OUTLET VALVE COIL REAR CIRCUIT SHORT TO BATTERY",
"C1205 ABS OUTLET VALVE COIL REAR CIRCUIT SHORT TO GROUND",
"C1206 ABS INLET VALVE COIL REAR CIRCUIT FAILURE",
"C1207 ABS INLET VALVE COIL REAR CIRCUIT OPEN",
"C1208 ABS INLET VALVE COIL REAR CIRCUIT SHORT TO BATTERY",
"C1209 ABS INLET VALVE COIL REAR CIRCUIT SHORT TO GROUND",
"C1210 ABS OUTLET VALVE COIL RF CIRCUIT FAILURE",
"C1211 ABS OUTLET VALVE COIL RF CIRCUIT OPEN",
"C1212 ABS OUTLET VALVE COIL RF CIRCUIT SHORT TO BATTERY",
"C1213 ABS OUTLET VALVE COIL RF CIRCUIT SHORT TO GROUND",
"C1214 ABS INLET VALVE COIL RF CIRCUIT FAILURE",
"C1215 ABS INLET VALVE COIL RF CIRCUIT OPEN",
"C1216 ABS INLET VALVE COIL RF CIRCUIT SHORT TO BATTERY",
"C1217 ABS INLET VALVE COIL RF CIRCUIT SHORT TO GROUND",
"C1218 LAMP ABS WARNING OUTPUT CIRCUIT FAILURE",
"C1219 LAMP ABS WARNING OUTPUT CIRCUIT OPEN",
"C1220 LAMP ABS WARNING OUTPUT CIRCUIT SHORT TO BATTERY",
"C1221 LAMP ABS WARNING OUTPUT CIRCUIT SHORT TO GROUND",
"C1222 SPEED WHEEL MISMATCH",
"C1223 LAMP BRAKE WARNING OUTPUT CIRCUIT FAILURE",
"C1224 LAMP BRAKE WARNING OUTPUT CIRCUIT OPEN",
"C1225 LAMP BRAKE WARNING OUTPUT CIRCUIT SHORT TO BATTERY",
"C1226 LAMP BRAKE WARNING OUTPUT CIRCUIT SHORT TO GROUND",
"C1227 SPEED WHEEL SENSOR LR INPUT SHORT CIRCUIT TO BATTERY",
"C1228 SPEED WHEEL SENSOR LR INPUT SHORT CIRCUIT TO GROUND",
"C1229 SPEED WHEEL SENSOR REAR CENTER COHERENCY FAULT",
"C1230 SPEED WHEEL SENSOR REAR CENTER INPUT CIRCUIT FAILURE",
"C1231 SPEED WHEEL SENSOR REAR CENTER CIRCUIT OPEN",
"C1232 SPEED WHEEL SENSOR REAR CENTER INPUT SHORT CIRCUIT TO BATTERY",
"C1233 SPEED WHEEL LF INPUT SIGNAL MISSING",
"C1234 SPEED WHEEL RF INPUT SIGNAL MISSING",
"C1235 SPEED WHEEL RR INPUT SIGNAL MISSING",
"C1236 SPEED WHEEL LR INPUT SIGNAL MISSING",
"C1237 SPEED WHEEL REAR INPUT SIGNAL MISSING",
"C1238 ABS HYDRAULIC PRESSURE DIFFERENTIAL SWITCH INPUT CIRCUIT FAILURE",
"C1239 ABS HYDRAULIC PRESSURE DIFFERENTIAL SWITCH INPUT  OPEN CIRCUIT",
"C1240 ABS HYDRAULIC PRESSURE DIFFERENTIAL SWITCH INPUT SHORT CIRCUIT TO BATTERY",
"C1241 ABS HYDRAULIC PRESSURE DIFFERENTIAL SWITCH INPUT SHORT CIRCUIT TO GROUND",
"C1242 ABS OUTLET VALVE COIL LR CIRCUIT FAILURE",
"C1243 ABS OUTLET VALVE COIL LR CIRCUIT OPEN",
"C1244 ABS OUTLET VALVE COIL LR CIRCUIT SHORT TO BATTERY",
"C1245 ABS OUTLET VALVE COIL LR CIRCUIT SHORT TO GROUND",
"C1246 ABS OUTLET VALVE COIL RR CIRCUIT FAILURE",
"C1247 ABS OUTLET VALVE COIL RR CIRCUIT OPEN",
"C1248 ABS OUTLET VALVE COIL RR CIRCUIT SHORT TO BATTERY",
"C1249 ABS OUTLET VALVE COIL RR CIRCUIT SHORT TO GROUND",
"C1250 ABS INLET VALVE COIL LR CIRCUIT FAILURE",
"C1251 ABS INLET VALVE COIL LR CIRCUIT OPEN",
"C1252 ABS INLET VALVE COIL LR CIRCUIT SHORT TO BATTERY",
"C1253 ABS INLET VALVE COIL LR CIRCUIT SHORT TO GROUND",
"C1254 ABS INLET VALVE COIL RR CIRCUIT FAILURE",
"C1255 ABS INLET VALVE COIL RR CIRCUIT OPEN",
"C1256 ABS INLET VALVE COIL RR CIRCUIT SHORT TO BATTERY",
"C1257 ABS INLET VALVE COIL RR CIRCUIT SHORT TO GROUND",
"C1258 SPEED WHEEL LF COMPARISON FAILURE",
"C1259 SPEED WHEEL RF COMPARISON FAILURE",
"C1260 SPEED WHEEL RR COMPARISON FAILURE",
"C1261 SPEED WHEEL LR COMPARISON FAILURE",
"C1262 LAMP WARNING RELAY CIRCUIT FAILURE",
"C1263 LAMP WARNING RELAY CIRCUIT OPEN",
"C1264 LAMP WARNING RELAY CIRCUIT SHORT TO BATTERY",
"C1265 LAMP WARNING RELAY CIRCUIT SHORT TO GROUND",
"C1266 ABS VALVE POWER RELAY CIRCUIT FAILURE",
"C1267 ABS FUNCTIONS TEMPORARILY DISABLED",
"C1268 MOTOR RELAY # 1 CIRCUIT FAILURE",
"C1269 MOTOR RELAY # 1 CIRCUIT SHORT TO BATTERY",
"C1270 MOTOR # 1 INPUT CIRCUIT FAILURE",
"C1271 MOTOR # 1 INPUT CIRCUIT SHORT TO GND",
"C1272 MOTOR # 2 INPUT CIRCUIT FAILURE",
"C1273 MOTOR # 2 INPUT CIRCUIT SHORT TO VBAT",
"C1274 SOLENOID RELAY # 1 CIRCUIT FAILURE",
"C1275 SOLENOID RELAY # 1 CIRCUIT SHORT TO VBATT",
"C1276 PARK BRAKE ACTUATOR ASSEMBLY SWITCH APPLIED CIRCUIT SHORT TO GND",
"C1277 STEERING WHEEL ANGLE 1AND 2 CIRCUIT FAILURE",
"C1278 STEERING WHEEL ANGLE 1AND 2 SIGNAL FAULTED",
"C1279 YAW RATE SENSOR CIRCUIT FAILURE",
"C1280 YAW RATE SENSOR SIGNAL FAULT",
"C1281 LATERAL ACCELEROMETER CIRCUIT FAILURE",
"C1282 LATERAL ACCELEROMETER SIGNAL FAULT",
"C1283 SWITCH TEST SIGNAL FAILURE",
"C1284 OIL PRESSURE SWITCH FAILURE",
"C1285 BOOSTER SOLENOID CIRCUIT FAILURE",
"C1286 BOOSTER MECHANICAL FAILURE",
"C1287 BOOSTER PEDAL FORCE SWITCH CIRCUIT FAILURE",
"C1288 PRESSURE TRANSDUCER MAIN / PRIMARY INPUT CIRCUIT FAILURE",
"C1289 PRESSURE TRANSDUCER REDUNDANT / SECONDARY INPUT CIRCUIT FAILURE",
"C1290 PRESSURE TRANSDUCER CIRCUIT FAILURE",
"C1291 ACC MODULE OVERHEATED",
"C1292 ACC BLOCKAGE DETECTION",
"C1293 ACC ALIGNMENT OFFSET ANGLE OUT OF RANGE",
"C1294 ACC ACTIVE SPEED OUT OF RANGE",
"C1295 STEERING WHEEL ANGLE SENSOR INTERNAL FAULT",
"C1296 WHEEL SPEED LF SIGNAL FAULT",
"C1297 WHEEL SPEED RF SIGNAL FAULT",
"C1298 WHEEL SPEED RR SIGNAL FAULT",
"C1299 WHEEL SPEED LR SIGNAL FAULT",
"C1300 ABS PUMP MOTOR CKT FAILURE",
"C1301 ABS OPERATION TIMED OUT",
"C1302 LEFT FRONT ISOLATION CLAMPING CIRCUIT FAILURE",
"C1303 RIGHT FRONT ISOLATION CLAMPING CIRCUIT FAILURE",
"C1304 CRUISE CONTROL COMMAND SWITCH RESISTANCE OUT OF RANGE",
"C1305 LONGITUDINAL ACCELEROMETER SIGNAL FAULT",
"C1306 STEERING WHEEL ANGLE - NO CENTER FOUND DURING INITIALIZATION",
"C1307 STEERING WHEEL ANGLE SENSOR ENCODER RING DEFECTIVE",
"C1308 WHEEL SPEED SENSOR WIRE(S) SHORTED TO GROUND",
"C1309 WHEEL SPEED SENSOR WIRES SHORTED TOGETHER",
"C1310 BRAKE HYDRAULIC PRESSURE TRANSDUCER FRONT LEFT WHEEL CIRCUIT FAILURE",
"C1311 BRAKE HYDRAULIC PRESSURE TRANSDUCER FRONT LEFT WHEEL SIGNAL FAULT",
"C1312 BRAKE HYDRAULIC PRESSURE TRANSDUCER FRONT RIGHT WHEEL CIRCUIT FAILURE",
"C1313 BRAKE HYDRAULIC PRESSURE TRANSDUCER FRONT RIGHT WHEEL SIGNAL FAULT",
"C1314 BRAKE HYDRAULIC PRESSURE TRANSDUCER REAR LEFT WHEEL CIRCUIT FAILURE",
"C1315 BRAKE HYDRAULIC PRESSURE TRANSDUCER REAR LEFT WHEEL SIGNAL FAULT",
"C1316 BRAKE HYDRAULIC PRESSURE TRANSDUCER REAR RIGHT WHEEL CIRCUIT FAILURE",
"C1317 BRAKE HYDRAULIC PRESSURE TRANSDUCER REAR RIGHT WHEEL SIGNAL FAULT",
"C1318 BRAKE HYDRAULIC PRESSURE TRANSDUCER ACCUMULATOR CIRCUIT FAULT",
"C1319 BRAKE HYDRAULIC PRESSURE TRANSDUCER ACCUMULATOR SIGNAL FAULT",
"C1320 BRAKE HYDRAULIC ACCUMULATOR TRAVEL SENSOR CIRCUIT FAILURE",
"C1321 BRAKE HYDRAULIC ACCUMULATOR TRAVEL SENSOR SIGNAL FAULT",
"C1322 BRAKE HYDRAULIC MASTER CYLINDER PISTON-TRAVEL SENSOR 1 CIRCUIT FAILURE",
"C1323 BRAKE HYDRAULIC MASTER CYLINDER PISTON-TRAVEL SENSOR 1 SIGNAL FAULT",
"C1324 BRAKE HYDRAULIC MASTER CYLINDER PISTON-TRAVEL SENSOR 2 CIRCUIT FAILURE",
"C1325 BRAKE HYDRAULIC MASTER CYLINDER PISTON-TRAVEL SENSOR 2 SIGNAL FAULT",
"C1326 HYDRAULIC CONTROL UNIT IS FAULTED",
"C1327 BRAKE FLUID LEVEL LOW",
"C1328 ELECTRO-HYDRAULIC GENERAL PRESSURE SENSOR FAILURE",
"C1400 TRACTION CONTROL VALVE RF CIRCUIT FAILURE",
"C1401 TRACTION CONTROL VALVE RF CIRCUIT OPEN",
"C1402 TRACTION CONTROL VALVE RF CIRCUIT SHORT TO GROUND",
"C1403 TRACTION CONTROL VALVE RF CIRCUIT SHORT TO BATTERY",
"C1404 TRACTION CONTROL VALVE REAR CIRCUIT FAILURE",
"C1405 TRACTION CONTROL VALVE REAR CIRCUIT OPEN",
"C1406 TRACTION CONTROL VALVE REAR CIRCUIT SHORT TO GROUND",
"C1407 TRACTION CONTROL VALVE REAR CIRCUIT SHORT TO BATTERY",
"C1408 PARK BRAKE RELEASE SWITCH CIRCUIT OUT OF RANGE",
"C1409 PARK BRAKE APPLY SWITCH CIRCUIT OUT OF RANGE",
"C1410 TRACTION CONTROL VALVE LF CIRCUIT FAILURE",
"C1411 TRACTION CONTROL VALVE LF CIRCUIT OPEN",
"C1412 TRACTION CONTROL VALVE LF CIRCUIT SHORT TO GROUND",
"C1413 TRACTION CONTROL VALVE LF CIRCUIT SHORT TO BATTERY",
"C1414 INCORRECT MODULE DESIGN LEVEL",
"C1415 INCORRECT MODULE CONFIGURATION",
"C1416 DAMPER RF CIRCUIT SHORT TO BATTERY",
"C1417 DAMPER RF CIRCUIT SHORT TO GROUND",
"C1418 DAMPER RF CIRCUIT FAILURE",
"C1419 DAMPER RF CIRCUIT OPEN",
"C1420 HYDRAULIC FLUID PRESSURE/ FLOW CIRCUIT SHORT TO VBATT",
"C1421 DAMPER LF CIRCUIT SHORT TO BATTERY",
"C1422 DAMPER LF CIRCUIT SHORT TO GROUND",
"C1423 DAMPER LF CIRCUIT FAILURE",
"C1424 DAMPER LF CIRCUIT OPEN",
"C1425 DAMPER RR CIRCUIT SHORT TO GROUND",
"C1426 DAMPER RR CIRCUIT SHORT TO BATTERY",
"C1427 DAMPER RR CIRCUIT OPEN",
"C1428 DAMPER RR CIRCUIT FAILURE",
"C1429 INPUT-SHAFT-SPEED INPUT CIRCUIT FAILURE",
"C1430 DAMPER LR CIRCUIT OPEN",
"C1431 DAMPER LR CIRCUIT SHORT TO BATTERY",
"C1432 DAMPER LR CIRCUIT SHORT TO GROUND",
"C1433 DAMPER LR CIRCUIT FAILURE",
"C1435 ACCELEROMETER REAR CIRCUIT FAILURE",
"C1436 ACCELEROMETER REAR CIRCUIT SIGNAL IS NOT SENSED",
"C1437 ACCELEROMETER REAR CIRCUIT SHORT TO GROUND",
"C1438 ACCELEROMETER REAR CIRCUIT SHORT TO BATTERY",
"C1439 VEHICLE ACCELERATION EEC-IV CIRCUIT FAILURE",
"C1440 PRESSURE TRANSDUCER MAIN / PRIMARY SIGNAL FAULTED",
"C1441 STEERING PHASE A CIRCUIT SIGNAL IS NOT SENSED",
"C1442 STEERING PHASE B CIRCUIT SIGNAL IS NOT SENSED",
"C1443 STEERING PHASE A CIRCUIT SHORT TO GROUND",
"C1444 STEERING PHASE B CIRCUIT SHORT TO GROUND",
"C1445 SPEED VEHICLE SIGNAL CIRCUIT FAILURE",
"C1446 BRAKE SWITCH CIRCUIT FAILURE",
"C1447 TRACTION CONTROL MODULE REQUEST CIRCUIT FAILURE",
"C1448 LAMP ADAPTIVE DAMPING WARNING CIRCUIT FAILURE",
"C1449 TRACTION CONTROL MOTOR COHERENCY FAULT",
"C1450 TRACTION CONTROL MOTOR CIRCUIT FAILURE",
"C1451 TRACTION CONTROL MOTOR CIRCUIT OPEN",
"C1452 TRACTION CONTROL MOTOR CIRCUIT SHORT TO BATTERY",
"C1453 TRACTION CONTROL MOTOR CIRCUIT SHORT TO GROUND",
"C1454 FRONT LATERAL ACCELEROMETER CIRCUIT FAILURE",
"C1455 ACCELEROMETER FRONT CIRCUIT FAILURE",
"C1456 ACCELEROMETER FRONT CIRCUIT IS NOT SENSED",
"C1457 ACCELEROMETER FRONT CIRCUIT SHORT TO GROUND",
"C1458 ACCELEROMETER FRONT CIRCUIT SHORT TO BATTERY",
"C1459 ADAPTIVE MODE SWITCH CIRCUIT FAILURE",
"C1460 VEHICLE ACCELEROMETER POWER CIRCUIT FAILURE",
"C1461 VEHICLE ACCELEROMETER POWER CIRCUIT SHORT TO BATTERY",
"C1462 LEFT FRONT VERTICAL ACCELEROMETER CIRCUIT FAILURE",
"C1463 RIGHT FRONT VERTICAL ACCELEROMETER CIRCUIT FAILURE",
"C1464 PRESSURE TRANSDUCER REDUNDANT / SECONDARY SIGNAL FAULTED",
"C1465 DAMPER HIGH SIDE FRONT CIRCUIT SHORT TO BATTERY",
"C1466 DAMPER CIRCUIT FAILURE",
"C1467 DAMPER HIGH SIDE REAR CIRCUIT SHORT TO BATTERY",
"C1468 DAMPER LOW SIDE FRONT CIRCUIT FAILURE",
"C1469 DAMPER LOW SIDE REAR CIRCUIT FAILURE",
"C1470 TCS FUNCTIONS TEMPORARILY DISABLED (THERMAL BRAKE PROTECTION)",
"C1471 HIGH PRESSURE ACCUMULATOR (HPA) VOLUME CONSUMPTION PLAUSIBILITY FAILURE",
"C1472 MASTER CYLINDER VOLUME/TRAVEL PLAUSIBILITY FAILURE",
"C1473 BRAKE SYSTEM VALVE CALIBRATION DATA FAILURE",
"C1474 HIGH PRESSURE ACCUMULATOR (HPA) SENSOR CALIBRATION DATA FAILURE",
"C1475 HIGH PRESSURE ACCUMULATOR (HPA) PRESSURE/VOLUME/TEMPERATURE PLAUSIBILITY FAILURE",
"C1476 BRAKE SYSTEM PUMP VOLUME FEED TOO LOW PLAUSIBILITY FAILURE",
"C1477 HIGH PRESSURE HYDRAULIC CIRCUIT LEAKAGE PLAUSIBILITY FAILURE",
"C1478 LEFT FRONT WHEEL BRAKE PRESSURE CONTROL PLAUSIBILITY FAILURE",
"C1479 LEFT REAR WHEEL BRAKE PRESSURE CONTROL PLAUSIBILITY FAILURE",
"C1480 RIGHT FRONT WHEEL BRAKE PRESSURE CONTROL PLAUSIBILITY FAILURE",
"C1481 RIGHT REAR WHEEL BRAKE PRESSURE CONTROL PLAUSIBILITY FAILURE",
"C1482 AIR BLEED CHECK INCOMPLETE",
"C1483 VALVE CALIBRATION INCOMPLETE",
"C1491 TC MTR-OPEN CKT",
"C1492 TC MTR-B+ SHRT",
"C1493 TC MTR-GND SHRT",
"C1495 TRACTION CONTROL MOTOR POTENTIOMETER CIRCUIT FAILURE",
"C1496 TRACTION CONTROL MOTOR POTENTIOMETER CIRCUIT OPEN",
"C1497 TRACTION CONTROL MOTOR POTENTIOMETER CIRCUIT SHORT TO BATTERY",
"C1498 TRACTION CONTROL MOTOR POTENTIOMETER CIRCUIT SHORT TO GROUND",
"C1499 TRANSFER CASE CONTACT PLATE "A" ENCODER CIRCUIT FAILURE",
"C1500 TRANSFER CASE CONTACT PLATE "B" ENCODER CIRCUIT FAILURE",
"C1501 TRANSFER CASE CONTACT PLATE "C" ENCODER CIRCUIT FAILURE",
"C1502 TRANSFER CASE CONTACT PLATE "D" ENCODER CIRCUIT FAILURE",
"C1503 DYNAMIC STABILITY CONTROL LEFT FRONT VALVE MALFUNCTION",
"C1504 DYNAMIC STABILITY CONTROL RIGHT FRONT VALVE MALFUNCTION",
"C1505 DYNAMIC STABILITY CONTROL LEFT REAR VALVE MALFUNCTION",
"C1506 DYNAMIC STABILITY CONTROL RIGHT REAR VALVE MALFUNCTION",
"C1507 TRACTION CONTROL OF BRAKE EXCEEDS TIME-OUT",
"C1508 TRACTION CONTROL OF ENGINE EXCEEDS TIME-OUT",
"C1510 RIGHT FRONT WHEEL PRESSURE REDUCTION PERFORMANCE PROBLEM",
"C1511 LEFT FRONT WHEEL PRESSURE REDUCTION PERFORMANCE PROBLEM",
"C1512 RIGHT REAR WHEEL PRESSURE REDUCTION PERFORMANCE PROBLEM",
"C1513 LEFT REAR WHEEL PRESSURE REDUCTION PERFORMANCE PROBLEM",
"C1515 LATERAL ACCELEROMETER OPEN/SHORT OR DISORIENTATION",
"C1516 ROLL RATE SENSOR SIGNAL FAULT",
"C1517 ROLL RATE SENSOR CIRCUIT FAILURE",
"C1518 RED FAULT WARNING LAMP INDICATOR SHORT TO BATTERY",
"C1519 RED FAULT WARNING LAMP INDICATOR CIRCUIT FAILURE",
"C1520 DELTA-S PLAUSIBILITY FAILURE",
"C1521 DELTA-S CIRCUIT FAILURE",
"C1522 BRAKE PEDAL TRAVEL SENSOR INTERNAL POWER SUPPLY FAILURE",
"C1523 BRAKE FLUID LEVEL SENSOR OUT OF RANGE",
"C1524 BRAKE PEDAL TRAVEL SENSOR CALIBRATION INCOMPLETE",
"C1525 BRAKE SYSTEM INITIALIZATION INCOMPLETE",
"C1526 BRAKE PEDAL TRAVEL SENSOR FAULT",
"C1530 IGN RUN CKT FAIL",
"C1600 REGENERATIVE BRAKE SYSTEM FAULT",
"C1699 LEFT REAR SENSOR CIRCUIT SHORT TO VBAT",
"C1700 LEFT REAR SENSOR CIRCUIT FAILURE OR BLOCKAGE",
"C1701 LEFT REAR SENSOR CIRCUIT FAULT",
"C1702 RIGHTREAR SENSOR CIRCUIT SHORT TO VBAT",
"C1703 RIGHT REAR SENSOR CIRCUIT FAILURE OR BLOCKAGE",
"C1704 RIGHT REAR SENSOR CIRCUIT FAULT",
"C1705 LEFT REAR CENTER SENSOR CIRCUIT SHORT TO VBAT",
"C1706 LEFT REAR CENTER SENSOR CIRCUIT FAILURE",
"C1707 LEFT REAR CENTER SENSOR CIRCUIT FAULT",
"C1708 RIGHT REAR CENTER SENSOR CIRCUIT SHORT TO VBAT",
"C1709 RIGHT REAR CENTER SENSOR CIRCUIT FAILURE",
"C1710 RIGHT REAR CENTER SENSOR CIRCUIT FAULT",
"C1711 LEFT FRONT SENSOR CIRCUIT SHORT TO VBAT",
"C1712 LEFT FRONT SENSOR CIRCUIT FAILURE",
"C1713 LEFT FRONT SENSOR CIRCUIT FAULT",
"C1714 RIGHT FRONT SENSOR CIRCUIT SHORT TO VBAT",
"C1715 RIGHT FRONT SENSOR CIRCUIT FAILURE",
"C1716 RIGHT FRONT SENSOR CIRCUIT FAULT",
"C1717 LEFT FRONT CENTER SENSOR CIRCUIT SHORT TO VBAT",
"C1718 LEFT FRONT CENTER SENSOR CIRCUIT FAILURE",
"C1719 LEFT FRONT CENTER SENSOR CIRCUIT FAULT",
"C1721 AIR SUSPENSION HEIGHT SENSOR POWER CIRCUIT OPEN",
"C1722 AIR SUSPENSION HEIGHT SENSOR POWER CIRCUIT SHORT TO BATTERY",
"C1723 AIR SUSPENSION HEIGHT SENSOR POWER CIRCUIT SHORT TO GROUND",
"C1724 FAULT DTC: AIR SUSPENSION HEIGHT SENSOR POWER CIRCUIT FAILURE",
"C1725 AIR SUSPENSION FRONT PNEUMATIC FAILURE",
"C1726 AIR SUSPENSION REAR PNEUMATIC FAILURE",
"C1727 AIR SUSPENSION RESERVOIR PNEUMATIC FAILURE",
"C1728 TRANSFER CASE UNABLE TO TRANSITION BETWEEN 2H AND 4H",
"C1729 TRANSFER CASE UNABLE TO TRANSITION BETWEEN 4H AND 4L",
"C1730 REFERENCE VOLTAGE OUT OF RANGE (+5 V)",
"C1731 AIR SUSPENSION LF CORNER UP TIMEOUT",
"C1732 AIR SUSPENSION LF CORNER DOWN TIMEOUT",
"C1733 AIR SUSPENSION RF CORNER UP TIMEOUT",
"C1734 AIR SUSPENSION RF CORNER DOWN TIMEOUT",
"C1735 AIR SUSPENSION LR CORNER UP TIMEOUT",
"C1736 AIR SUSPENSION LR CORNER DOWN TIMEOUT",
"C1737 AIR SUSPENSION RR CORNER UP TIMEOUT",
"C1738 AIR SUSPENSION RR CORNER DOWN TIMEOUT",
"C1739 RIGHT FRONT CENTER SENSOR CIRCUIT SHORT TO VBAT",
"C1740 RIGHT FRONT CENTER SENSOR CIRCUIT FAILURE",
"C1741 RIGHT FRONT CENTER SENSOR CIRCUIT FAULT",
"C1742 REAR SOUNDER CIRCUIT FAILURE",
"C1743 REAR SOUNDER CIRCUIT SHORT TO VBATT",
"C1744 FRONT SOUNDER CIRCUIT FAILURE",
"C1745 FRONT SOUNDER CIRCUIT SHORT TO VBATT",
"C1748 SWITCH INPUT CIRCUIT SHORT TO GND",
"C1749 TRAILER INPUT CIRCUIT FAILURE",
"C1750 ACCELERATOR POSITION SENSOR OUT OF RANGE",
"C1751 VEHICLE SPEED SENSOR # 1 OUTPUT CIRCUIT SHORT TO VBATT",
"C1752 VEHICLE SPEED SENSOR # 1 OUTPUT CIRCUIT SHORT TO GND",
"C1753 HYDRAULIC CLUTCH ACTUATOR VALVE SIGNAL FAULT",
"C1754 HYDRAULIC CLUTCH ACTUATOR VALVE CIRCUIT FAILURE",
"C1755 POWER LIMIT SHUTDOWN FAULT",
"C1756 AIR SUSPENSION FRONT HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT FAILURE",
"C1757 AIR SUSPENSION FRONT HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT OPEN",
"C1758 AIR SUSPENSION FRONT HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT SHORT TO BATTERY",
"C1759 AIR SUSPENSION FRONT HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT SHORT TO GROUND",
"C1760 AIR SUSPENSION REAR HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT FAILURE",
"C1761 AIR SUSPENSION REAR HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT OPEN",
"C1762 AIR SUSPENSION REAR HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT SHORT TO BATTERY",
"C1763 AIR SUSPENSION REAR HEIGHT SENSOR HIGH (SE) SIGNAL CIRCUIT SHORT TO GROUND",
"C1765 AIR SUSPENSION REAR HEIGHT SENSOR LOW SIGNAL CIRCUIT FAILURE",
"C1766 AIR SUSPENSION REAR HEIGHT SENSOR LOW SIGNAL CIRCUIT OPEN",
"C1767 AIR SUSPENSION REAR HEIGHT SENSOR LOW SIGNAL CIRCUIT SHORT TO BATTERY",
"C1768 AIR SUSPENSION REAR HEIGHT SENSOR LOW SIGNAL CIRCUIT SHORT TO GROUND",
"C1769 PARK BRAKE APPLY SWITCH CIRCUIT SHORT TO GROUND",
"C1770 AIR SUSPENSION VENT SOLENOID OUTPUT CIRCUIT FAILURE",
"C1771 AIR SUSPENSION VENT SOLENOID OUTPUT CIRCUIT OPEN",
"C1772 AIR SUSPENSION VENT SOLENOID OUTPUT CIRCUIT SHORT TO BATTERY",
"C1773 AIR SUSPENSION VENT SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1774 COOLANT TEMP. OUT OF RANGE",
"C1775 DC-DC CONVERTER FAILURE",
"C1776 HEATER SYSTEM FAILURE",
"C1777 VACUUM PRESSURE CIRCUIT FAILURE",
"C1778 POWER STEERING FAILURE",
"C1779 BLOWER SWITCH FAILURE",
"C1780 TEMPERATURE SELECT FAILURE",
"C1781 ENGINE COOLANT TEMPERATURE SIGNAL MISSING/FAULT",
"C1782 PARK BRAKE RELEASE SWITCH CIRCUIT FAILURE",
"C1783 PARK BRAKE RELEASE SWITCH SHORT TO GROUND",
"C1784 ELECTRIC PARK BRAKE MOTOR OUTPUT SHORT TO GROUND",
"C1785 ELECTRIC PARK BRAKE MOTOR OUTPUT OPEN CIRCUIT",
"C1786 ELECTRIC PARK BRAKE MOTOR OUTPUT BATTERY SHORT TO GROUND",
"C1787 STOPLAMP RELAY OUTPUT CIRCUIT SHORT TO BATTERY",
"C1788 STOPLAMP RELAY OUTPUT CIRCUIT SHORT TO GROUND",
"C1789 STOPLAMP RELAY OUTPUT CIRCUIT OPEN",
"C1790 AIR SUSPENSION LR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT FAILURE",
"C1791 AIR SUSPENSION LR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT OPEN",
"C1792 AIR SUSPENSION LR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT SHORT TO BATTERY",
"C1793 AIR SUSPENSION LR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1794 AIR SUSPENSION VEHICLE OVER GROSS VEHICLE WEIGHT",
"C1795 AIR SUSPENSION RR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT FAILURE",
"C1796 AIR SUSPENSION RR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT OPEN",
"C1797 AIR SUSPENSION RR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT SHORT TO BATTERY",
"C1798 AIR SUSPENSION RR AIR SPRING/SHOCK SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1799 HALL EFFECT CIRCUIT FAILURE",
"C1800 AIR SUSPENSION RESERVOIR SOLENOID CIRCUIT FAILURE",
"C1801 MOTOR ENGAGE CURRENT REACHED  BEFORE FULL APPLY TRAVEL DISTANCE",
"C1802 MOTOR ENGAGE CURRENT NOT REACHED OR TRAVELED TOO FAR APPLY",
"C1803 MOTOR DISENGAGE FULL TRAVEL DISTANCE NOT REACHED UPON RELEASE",
"C1804 PARK BRAKE APPLY SWITCH STUCK ON",
"C1805 MISMATCHED PCM AND/OR ABS-TC MODULE",
"C1806 PARK BRAKE RELEASE SWITCH STUCK ON",
"C1807 VENT SOLENOID SUPPLY SHORT TO BATTERY",
"C1808 VENT SOLENOID SUPPLY SHORT TO GROUND",
"C1809 AIR SUSPENSION VENT TIMEOUT",
"C1810 AIR SUSPENSION HEIGHT SENSOR OUT OF RANGE",
""C1811 AIR SUSPENSION RETURN TO TRIM TIMEOUT
MANY VALVE FAILURE DTCS.","
"C1812 AIR SUSPENSION HEIGHT SENSOR FAILURE",
"C1813 AIR SUSPENSION LR VENT REQUEST EXCEEDED MAX. TIMING",
"C1814 AIR SUSPENSION RR VENT REQUEST EXCEEDED MAX. TIMING",
"C1815 ELECTRIC PARK BRAKE MOTOR OUTPUT SHORT TO BATTERY",
"C1818 AIR SUSPENSION LR AIR COMPRESS REQUEST EXCEEDED MAX. TIMING",
"C1819 AIR SUSPENSION RR AIR COMPRESS REQUEST EXCEEDED MAX. TIMING",
"C1820 AIR SUSPENSION RF AIR COMPRESS REQUEST EXCEEDED MAX. TIMING",
"C1821 ELECTRIC PARK BRAKE MOTOR FAILURE",
"C1822 ELECTRIC PARK BRAKE SENSOR ELECTRICAL FAILURE",
"C1823 ELECTRIC PARK BRAKE SENSOR SIGNAL FAILURE",
"C1824 ELECTRIC PARK BRAKE MOTOR H-BRIDGE FAILURE",
"C1825 MISSING CRANKING SIGNAL",
"C1826 ELECTRIC PARK BRAKE ELECTRICAL FAILURE",
"C1827 ELECTRIC PARK BRAKE SWITCH DEFECTIVE",
"C1828 ELECTRIC PARK BRAKE FORCE SENSOR NOT CALIBRATED",
"C1829 ELECTRIC PARK BRAKE SWITCH NOT CONNECTED",
"C1830 AIR SUSPENSION COMPRESSOR RELAY CIRCUIT FAILURE",
"C1831 AIR SUSPENSION COMPRESSOR RELAY CIRCUIT OPEN",
"C1832 AIR SUSPENSION COMPRESSOR RELAY CIRCUIT SHORT TO BATTERY",
"C1833 AIR SUSPENSION COMPRESSOR  RELAY CIRCUIT SHORT TO GROUND",
"C1834 GAUGE DRIVE CURRENT FAULT",
"C1835 CURRENT SENSE CIRCUIT FAILURE",
"C1836 BATTERY TEMP. OUT OF RANGE",
"C1837 BATTERY HEATER CIRCUIT FAILURE",
"C1838 CHARGING SYSTEM FAULT",
"C1839 LEAKAGE FAULT",
"C1840 AIR SUSPENSION DISABLE SWITCH CIRCUIT FAILURE",
"C1841 AIR SUSPENSION DISABLE SWITCH CIRCUIT OPEN",
"C1842 AIR SUSPENSION DISABLE SWITCH CIRCUIT SHORT TO BATTERY",
"C1843 AIR SUSPENSION DISABLE SWITCH CIRCUIT SHORT TO GROUND",
"C1844 AIR SUSPENSION SECONDARY FRONT INFLATOR SOLENOID OUTPUT CIRCUIT FAILURE",
"C1845 AIR SUSPENSION FRONT INFLATOR SOLENOID OUTPUT CIRCUIT FAILURE",
"C1846 AIR SUSPENSION FRONT INFLATOR SOLENOID OUTPUT CIRCUIT OPEN",
"C1847 AIR SUSPENSION FRONT INFLATOR SOLENOID OUTPUT CIRCUIT SHORT TO  BATTERY",
"C1848 AIR SUSPENSION FRONT INFLATOR SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1849 MASTER CYLINDER PRESSURE OUT OF RANGE",
"C1850 AIR SUSPENSION WARNING LAMP CIRCUIT FAILURE",
"C1851 AIR SUSPENSION WARNING LAMP CIRCUIT OPEN",
"C1852 AIR SUSPENSION WARNING LAMP CIRCUIT SHORT TO BATTERY",
"C1853 AIR SUSPENSION WARNING LAMP CIRCUIT SHORT TO GROUND",
"C1854 MOTOR TEMPERATURE OUT OF RANGE",
"C1855 ACCELERATION POSITION SENSOR CONFLICT",
"C1856 TRACTION MOTOR ENCODER  CIRCUIT FAILURE",
"C1859 PRNDL INPUT #2 CIRCUIT FAILURE",
"C1860 PRNDL INPUT #3 CIRCUIT FAILURE",
"C1861 PRNDL INPUT #4 CIRCUIT FAILURE",
"C1862 CONTACTOR CIRCUIT FAILURE",
"C1863 EXTERNAL CHARGING FAULT",
"C1864 BATTERY MODULE FAULT",
"C1865 AIR SUSPENSION REAR INFLATOR SOLENOID OUTPUT CIRCUIT FAILURE",
"C1866 AIR SUSPENSION REAR INFLATOR SOLENOID OUTPUT CIRCUIT OPEN",
"C1867 AIR SUSPENSION REAR INFLATOR SOLENOID OUTPUT CIRCUIT SHORT TO  BATTERY",
"C1868 AIR SUSPENSION REAR INFLATOR SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1869 AIR SUSPENSION GATE SOLENOID OUTPUT CIRCUIT FAILURE",
"C1870 AIR SUSPENSION GATE SOLENOID OUTPUT CIRCUIT OPEN",
"C1871 AIR SUSPENSION GATE SOLENOID OUTPUT CIRCUIT SHORT TO  BATTERY",
"C1872 AIR SUSPENSION GATE SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1873 AIR SUSPENSION RF AIR SPRING SOLENOID OUTPUT CIRCUIT FAILURE",
"C1874 AIR SUSPENSION RF AIR SPRING SOLENOID OUTPUT CIRCUIT OPEN",
"C1875 AIR SUSPENSION RF AIR SPRING SOLENOID OUTPUT CIRCUIT SHORT TO BATTERY",
"C1876 AIR SUSPENSION RF AIR SPRING SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1877 AIR SUSPENSION LF AIR SPRING SOLENOID OUTPUT CIRCUIT FAILURE",
"C1878 AIR SUSPENSION LF AIR SPRING SOLENOID OUTPUT CIRCUIT OPEN",
"C1879 AIR SUSPENSION LF AIR SPRING SOLENOID OUTPUT CIRCUIT SHORT TO BATTERY",
"C1880 AIR SUSPENSION LF AIR SPRING SOLENOID OUTPUT CIRCUIT SHORT TO GROUND",
"C1881 AIR SUSPENSION RF HEIGHT SENSOR CIRCUIT FAILURE",
"C1882 AIR SUSPENSION RF HEIGHT SENSOR CIRCUIT OPEN",
"C1883 AIR SUSPENSION RF HEIGHT SENSOR CIRCUIT SHORT TO BATTERY",
"C1884 AIR SUSPENSION RF HEIGHT SENSOR CIRCUIT SHORT TO GROUND",
"C1885 AIR SUSPENSION RR HEIGHT SENSOR CIRCUIT FAILURE",
"C1886 AIR SUSPENSION RR HEIGHT SENSOR CIRCUIT OPEN",
"C1887 AIR SUSPENSION RR HEIGHT SENSOR CIRCUIT SHORT TO BATTERY",
"C1888 AIR SUSPENSION RR HEIGHT SENSOR CIRCUIT SHORT TO GROUND",
"C1889 AIR SUSPENSION LF HEIGHT SENSOR CIRCUIT FAILURE",
"C1890 AIR SUSPENSION LF HEIGHT SENSOR CIRCUIT OPEN",
"C1891 AIR SUSPENSION LF HEIGHT SENSOR CIRCUIT SHORT TO BATTERY",
"C1892 AIR SUSPENSION LF HEIGHT SENSOR CIRCUIT SHORT TO GROUND",
"C1893 AIR SUSPENSION LR HEIGHT SENSOR CIRCUIT FAILURE",
"C1894 AIR SUSPENSION LR HEIGHT SENSOR CIRCUIT OPEN",
"C1895 AIR SUSPENSION LR HEIGHT SENSOR CIRCUIT SHORT TO BATTERY",
"C1896 AIR SUSPENSION LR HEIGHT SENSOR CIRCUIT SHORT TO GROUND",
"C1897 STEERING VAPS II CIRCUIT LOOP FAILURE",
"C1898 STEERING VAPS II CIRCUIT LOOP OPEN",
"C1899 STEERING VAPS II CIRCUIT LOOP SHORT TO BATTERY",
"C1900 STEERING VAPS II CIRCUIT LOOP SHORT TO GROUND",
"C1901 RIDE CONTROL RR SHOCK ACTUATOR CIRCUIT FAILURE",
"C1902 RIDE CONTROL RR SHOCK ACTUATOR CIRCUIT OPEN",
"C1903 RIDE CONTROL RR SHOCK ACTUATOR CIRCUIT SHORT TO BATTERY",
"C1904 RIDE CONTROL RR SHOCK ACTUATOR CIRCUIT SHORT TO GROUND",
"C1905 RIDE CONTROL LR SHOCK ACTUATOR CIRCUIT FAILURE",
"C1906 RIDE CONTROL LR SHOCK ACTUATOR CIRCUIT OPEN",
"C1907 RIDE CONTROL LR SHOCK ACTUATOR CIRCUIT SHORT TO BATTERY",
"C1908 RIDE CONTROL LR SHOCK ACTUATOR CIRCUIT SHORT TO GROUND",
"C1909 RIDE CONTROL RF SHOCK ACTUATOR CIRCUIT FAILURE",
"C1910 RIDE CONTROL RF SHOCK ACTUATOR CIRCUIT OPEN",
"C1911 RIDE CONTROL RF SHOCK ACTUATOR CIRCUIT SHORT TO BATTERY",
"C1912 RIDE CONTROL RF SHOCK ACTUATOR CIRCUIT SHORT TO GROUND",
"C1913 RIDE CONTROL LF SHOCK ACTUATOR CIRCUIT FAILURE",
"C1914 RIDE CONTROL LF SHOCK ACTUATOR CIRCUIT OPEN",
"C1915 RIDE CONTROL LF SHOCK ACTUATOR CIRCUIT SHORT TO BATTERY",
"C1916 RIDE CONTROL LF SHOCK ACTUATOR CIRCUIT SHORT TO GROUND",
"C1917 STEERING EVO OUT-OF-RANGE FAULT",
"C1918 AIR SUSPENSION RIDE HEIGHT SELECT SWITCH CIRCUIT FAILURE",
"C1920 LED #1 CIRCUIT FAILURE",
"C1921 VAPS SOLENOID ACTUATOR OUTPUT CIRCUIT FAILURE",
"C1922 VAPS SOLENOID ACTUATOR OUTPUT CIRCUIT OPEN",
"C1923 VAPS SOLENOID ACTUATOR OUTPUT CIRCUIT SHORT TO BATTERY",
"C1924 VAPS SOLENOID ACTUATOR OUTPUT CIRCUIT SHORT TO GROUND",
"C1925 VAPS SOLENOID ACTUATOR RETURN CIRCUIT FAILURE",
"C1926 VAPS SOLENOID ACTUATOR RETURN CIRCUIT OPEN",
"C1927 VAPS SOLENOID ACTUATOR RETURN CIRCUIT SHORT TO BATTERY",
"C1928 VAPS SOLENOID ACTUATOR RETURN CIRCUIT SHORT TO GROUND",
"C1929 AIR SUSPENSION FRONT COMPRESSOR RELAY CIRCUIT FAILURE",
"C1930 AIR SUSPENSION FRONT COMPRESSOR RELAY CIRCUIT OPEN",
"C1931 AIR SUSPENSION FRONT COMPRESSOR RELAY CIRCUIT SHORT TO BATTERY",
"C1932 AIR SUSPENSION FRONT COMPRESSOR RELAY CIRCUIT SHORT TO GROUND",
"C1933 SOLENOID CURRENT OUT OF RANGE",
"C1934 HPU (HYDRAULIC PUMP UNIT) PRESSURISATION FAILURE",
"C1935 CHIME CIRCUIT FAILURE",
"C1936 HYDRAULIC PUMP RELAY CIRCUIT FAILURE",
"C1937 STEERING WHEEL ANGLE SENSOR OFFSET FAILURE",
"C1938 INVALID STEERING WHEEL ANGLE SENSOR ID",
"C1939 BRAKE PRESSURE SWITCH INPUT CIRCUIT FAILURE",
"C1940 BRAKE PRESSURE SWITCH MECHANICAL FAILURE",
"C1942 UNRECOGNIZED POWERTRAIN CONFIGURATION",
"C1943 AIRBAG DEPLOYMENT INDICATION INPUT FAULT",
"C1944 GAUGE DRIVER CIRCUIT FAULT",
"C1945 PARK SWITCH INDICATES PARK WITH VEHICLE MOVING",
"C1946 FRONT DRIVER'S SEAT TRACK POSITION SWITCH CIRCUIT OPEN",
"C1947 FRONT DRIVER'S SEAT TRACK POSITION SWITCH CIRCUIT SHORT TO GROUND",
"C1948 FRONT DRIVER'S SEAT TRACK POSITION SWITCH CIRCUIT RESISTANCE OUT OF RANGE",
"C1949 ACCELEROMETER SENSOR CIRCUIT OPEN",
"C1950 ACCELEROMETER SENSOR CIRCUIT FAILURE",
"C1951 LATERAL ACCELEROMETER SENSOR CIRCUIT OPEN",
"C1952 YAW RATE SENSOR CIRCUIT OPEN",
"C1953 MASTER CYLINDER PRESSURE SENSOR CIRCUIT OPEN",
"C1954 MASTER CYLINDER PRESSURE SENSOR CIRCUIT FAILURE",
"C1955 STEERING ANGLE SENSOR CIRCUIT OPEN",
"C1956 STEERING ANGLE SENSOR CIRCUIT FAILURE",
"C1957 DYNAMIC STABILITY CONTROL VALVE RF CIRCUIT FAILURE",
"C1958 DYNAMIC STABILITY CONTROL VALVE LF CIRCUIT FAILURE",
"C1959 LATERAL ACCELEROMETER SENSOR CIRCUIT FAILURE",
"C1960 DRIVER BRAKE APPLY CIRCUIT FAULT",
"C1961 PARK LAMP RELAY COIL CIRCUIT FAILURE",
"C1962 PARK LAMP RELAY COIL SHORT TO BATTERY",
"C1963 STABILITY CONTROL INHIBIT WARNING",
"C1964 AIR SUSP'N AIR COMPRESSOR REQUEST EXCEEDED MAX TIMING",
"C1965 FUEL LEVEL CIRCUIT FAILURE",
"C1966 LOW FUEL INDICATOR CIRCUIT SHORT TO BATTERY",
"C1967 LOW FUEL INDICATOR CIRCUIT FAILURE",
"C1968 ELECTRONIC PANIC BRAKE ASSIST FAILURE",
"C1969 TC/YC SWITCH LAMP CIRCUIT FAULT.",
"C1970 4X4 LOW MODE SWITCH LED SHORT TO BATTERY",
"C1971 4X4 LOW MODE SWITCH LED CIRCUIT FAILURE",
"C1972 AIR SUSPENSION KNEEL SWITCH CIRCUIT FAILURE",
"C1973 AIR SUSPENSION INCHING SWITCH CIRCUIT FAILURE",
"C1974 AIR RESERVOIR NOT FILLING",
"C1975 IVD PLAUSIBILTY FAILURE",
"C1976 AUDIO STEERING WHEEL SWITCH CIRCUIT - OPEN CIRCUIT",
"C1977 AUDIO STEERING WHEEL SWITCH CIRCUIT SHORT TO GND",
"C1978 AUDIO STEERING WHEEL SWITCH CIRCUIT SHORT TO BATTERY",
"C1979 IWE SOLENOID CIRCUIT FAILURE",
"C1980 IWE SOLENOID SHORT TO BATTERY",
"C1981 FRONT DRIVER'S SEAT TRACK POSITION SWITCH CIRCUIT FAULT",
"C1982 FRONT DRIVER'S SEAT TRACK POSITION SWITCH CIRCUIT SHORT TO BATTERY",
"C1983 RADAR SENSOR FAULT",
"C1984 RADAR SENSOR CIRCUIT FAILURE",
"C1985 BACK UP AID DISABLE SWITCH STUCK LOW",
"C1986 VAPS INITIAL SPEED ABOVE THRESHOLD",
"C1987 YELLOW FAULT WARNING LAMP INDICATOR SHORT TO BATTERY",
"C1988 YELLOW FAULT WARNING LAMP INDICATOR CIRCUIT FAILURE",
"C1989 PARK BRAKE APPLY AND RELEASE SWITCH CONTACTS ENERGIZED SIMULTANEOUSLY",
"C1990 INCOMPLETE ONLINE TESTS",
"C1991 MODULE CALIBRATION FAILURE",
"C1992 VEHICLE SPEED CIRCUIT FAILURE",
"C1993 AIR SUSPENSION PRESSURE SENSOR CIRCUIT FAILURE",
"C1994 ESP CONTINUOUS OPERATION FAULT",
"C1995 AIR SUSPENSION MOISTURE EJECTOR VALVE CIRCUIT FAILURE",
"C1996 ACTIVE YAW AND/OR ROLL CONTROL DISABLED",
"C1997 PRESSURE CONTROLLER PLAUSIBILITY FAULT",
"C1998 MODULE CALIBRATION NOT COMPLETE",
"C1999 VEHICLE SPEED SIGNAL CIRCUIT SHORT TO GROUND",
"C2200 FRONT PASSENGER'S SEAT TRACK POSITION SWITCH CIRCUIT FAULT",
"C2201 FRONT PASSENGER'S SEAT TRACK POSITION SWITCH CIRCUIT OPEN",
"C2202 FRONT PASSENGER'S SEAT TRACK POSITION SWITCH CIRCUIT SHORT TO GROUND",
"C2203 FRONT PASSENGER'S SEAT TRACK POSITION SWITCH CIRCUIT SHORT TO BATTERY",
"C2204 FRONT PASSENGER'S SEAT TRACK POSITION SWITCH CIRCUIT RESISTANCE OUT OF RANGE",
"C2250 VEHICLE SPEED SIGNAL CIRCUIT SHORT TO BATTERY",
"C2300 VALVE SUPPLY CIRCUIT FAILURE",
"C2301 DAMPER SUPPLY CIRCUIT FAILURE",
"C2302 LEVELLING PLAUSIBILITY FAILURE",
"C2303 RESERVOIR PLAUSIBILITY FAILURE",
"C2304 DAMPER SUPPLY CIRCUIT SHORT TO GROUND",
"C2305 DAMPER SUPPLY CIRCUIT SHORT TO BATTERY",
"C2767 RESERVED - TBD",
"C2768 SENSOR SELF TEST SIGNAL FAULTED",
"C2769 LONGITUDINAL ACCELERATION SENSOR ELECTRICAL FAILURE",
"C2770 LONGITUDINAL ACCELERATION SENSOR PLAUSIBILITY FAILURE",
"C2774 PEDAL TRAVEL SENSOR PLAUSIBILITY FAILURE",
"C2775 TC/AYC ON/OFF SWITCH STUCK FAILURE",
"C2777 SENSOR CLUSTER BUS FAILURE",
"C2778 SENSOR POWER SUPPLY FAILURE",
"C2779 FAULT DTC (CM): AIR SUSPENSION AIR SPRING/SHOCK SOLENOID CIRCUIT FAILURE",
"C2780 ECU IN MANUFACTURER SUB-STATE",
"C2781 COMPRESSOR SOLENOID CIRCUIT FAULT",
"C2782 TEMPERATURE SENSOR FAULT",
"C2783 SENSOR CLUSTER INCORRECT",
"C2784 RAM CHECKSUM FAILURE",
"C2785 SENSOR(S) OUT OF CALIBRATION",
"C2786 LEFT REAR SENSOR OPEN CIRCUIT",
"C2787 RIGHT REAR SENSOR OPEN CIRCUIT",
"C2788 LEFT REAR CENTER SENSOR OPEN CIRCUIT",
"C2789 RIGHT REAR CENTER SENSOR OPEN CIRCUIT",
"C2790 LED ARRAY CIRCUIT FAILURE",
"C2791 POWER STEERING MOTOR CIRCUIT OPEN",
"C2792 POWER STEERING MOTOR CIRCUIT SHORT TO BATTERY",
"C2793 POWER STEERING MOTOR CIRCUIT SHORT TO GROUND",
"C2794 POWER STEERING MOTOR OVERHEAT PROTECTION",
"C2795 BRAKE ASSIST UNABLE TO INITIALIZE",
"C2796 BRAKE PRESSURE TRANSDUCER SUPPLY CIRCUIT FAILURE",
"C2797 BRAKE PRESSURE TRANSDUCER SUPPLY SHORT TO BATTERY",
"C2798 BRAKE PRESSURE TRANSDUCER SUPPLY SHORT TO GROUND",
"C2799 BRAKE PRESSURE TRANSDUCER SUPPLY CIRCUIT OPEN",
"C2800 BRAKE PRESSURE TRANSDUCER SENSE CIRCUIT OPEN",
"C2801 BRAKE PRESSURE TRANSDUCER SENSE  SHORT TO GROUND",
"C2802 BRAKE PRESSURE TRANSDUCER SENSE  SHORT TO BATTERY",
"C2803 BRAKE PRESSURE TRANSDUCER SENSE CIRCUIT FAILURE",
"C2804 BRAKE PRESSURE TRANSDUCER GROUND CIRCUIT OPEN",
"C2805 BRAKE PRESSURE TRANSDUCER GROUND CIRCUIT SHORT TO BATTERY",
"C2806 TRAILER BRAKE OUTPUT CIRCUIT SHORT TO VBATT",
"C2807 TRAILER BRAKE OUTPUT CIRCUIT SHORT TO GROUND",
"C2808 TRAILER BRAKE OUTPUT CIRCUIT OPEN",

Коды ошибок CAN BUS(U0248-U3011)

"U0248 LOST COMMUNICATION WITH REMOTE ACCESSORY MODULE",
"U0249 LOST COMMUNICATION WITH ENTERTAINMENT CONTROL MODULE - REAR B",
"U02796 BRAKE PRESSURE TRANSDUCER SUPPLY CIRCUIT FAILURE",
"U02797 BRAKE PRESSURE TRANSDUCER SUPPLY SHORT TO BATTERY",
"U0332 SOFTWARE INCOMPATIBILITY WITH MULTI-AXIS ACCELERATION SENSOR MODULE",
"U1000 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $00",
"U1001 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $01",
"U1002 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $02",
"U1003 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $03",
"U1004 SCP (J1850) INVALID OR MISSING DATA FOR EEC PROGRAMMING",
"U1005 SCP (J1850) INVALID OR MISSING DATA FOR EEC PROGRAMMING",
"U1006 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $06",
"U1007 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $07",
"U1008 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE TORQUE",
"U1009 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE TORQUE",
"U1010 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE AIR INTAKE",
"U1011 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE AIR INTAKE",
"U1012 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $0C",
"U1013 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $0D",
"U1014 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $0E",
"U1015 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $0F",
"U1016 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $10",
"U1017 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $11",
"U1018 SCP (J1850) INVALID OR MISSING DATA FOR THROTTLE",
"U1019 SCP (J1850) INVALID OR MISSING DATA FOR THROTTLE",
"U1020 SCP (J1850) INVALID OR MISSING DATA FOR AIR CONDITIONING CLUTCH",
"U1021 SCP (J1850) INVALID OR MISSING DATA FOR AIR CONDITIONING CLUTCH",
"U1022 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $16",
"U1023 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $17",
"U1024 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $18",
"U1025 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $19",
"U1026 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE RPM",
"U1027 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE RPM",
"U1028 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $1C",
"U1029 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $1D",
"U1030 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #1",
"U1031 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #1",
"U1032 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $20",
"U1033 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $21",
"U1034 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $22",
"U1035 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $23",
"U1036 SCP (J1850) INVALID OR MISSING DATA FOR WHEELS",
"U1037 SCP (J1850) INVALID OR MISSING DATA FOR WHEELS",
"U1038 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $26",
"U1039 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $27",
"U1040 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE SPEED",
"U1041 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE SPEED",
"U1042 SCP (J1850) INVALID OR MISSING DATA FOR TRACTION CONTROL",
"U1043 SCP (J1850) INVALID OR MISSING DATA FOR TRACTION CONTROL",
"U1044 SCP (J1850) INVALID OR MISSING DATA FOR TRACTION MOTOR",
"U1045 SCP (J1850) INVALID OR MISSING DATA FOR TRACTION MOTOR",
"U1046 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $2E",
"U1047 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $2F",
"U1048 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $30",
"U1049 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $31",
"U1050 SCP (J1850) INVALID OR MISSING DATA FOR BRAKES",
"U1051 SCP (J1850) INVALID OR MISSING DATA FOR BRAKES",
"U1052 SCP (J1850) INVALID OR MISSING DATA FOR STEERING / STEERING WHEEL",
"U1053 SCP (J1850) INVALID OR MISSING DATA FOR STEERING / STEERING WHEEL",
"U1054 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $36",
"U1055 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $37",
"U1056 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE CONFIGURATION",
"U1057 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE CONFIGURATION",
"U1058 SCP (J1850) INVALID OR MISSING DATA FOR TRANSMISSION / TRANSAXLE / PRNDL",
"U1059 SCP (J1850) INVALID OR MISSING DATA FOR TRANSMISSION / TRANSAXLE / PRNDL",
"U1060 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $3C",
"U1061 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $3D",
"U1062 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $3E",
"U1063 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $3F",
"U1064 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $40",
"U1065 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $41",
"U1066 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $42",
"U1067 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $43",
"U1068 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $44",
"U1069 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $45",
"U1070 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE SENSORS",
"U1071 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE SENSORS",
"U1072 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE COOLANT",
"U1073 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE COOLANT",
"U1074 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE OIL",
"U1075 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE OIL",
"U1076 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $4C",
"U1077 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $4D",
"U1078 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $4E",
"U1079 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $4F",
"U1080 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $50",
"U1081 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $51",
"U1082 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE SYSTEMS OTHER",
"U1083 SCP (J1850) INVALID OR MISSING DATA FOR ENGINE SYSTEMS OTHER",
"U1084 SCP (J1850) INVALID OR MISSING DATA FOR POWERTRAIN STATUS REQUEST",
"U1085 SCP (J1850) INVALID OR MISSING DATA FOR POWERTRAIN STATUS REQUEST",
"U1086 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $56",
"U1087 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $57",
"U1088 SCP (J1850) INVALID OR MISSING DATA FOR SUSPENSION",
"U1089 SCP (J1850) INVALID OR MISSING DATA FOR SUSPENSION",
"U1090 SCP (J1850) INVALID OR MISSING DATA FOR NON-LEGISLATED DIAGNOSTICS",
"U1091 SCP (J1850) INVALID OR MISSING DATA FOR NON-LEGISLATED DIAGNOSTICS",
"U1092 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $5C",
"U1093 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $5D",
"U1094 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #2",
"U1095 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #2",
"U1096 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $60",
"U1097 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $61",
"U1098 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE SPEED CONTROL",
"U1099 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE SPEED CONTROL",
"U1100 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $64",
"U1101 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $65",
"U1102 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $66",
"U1103 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $67",
"U1104 SCP (J1850) INVALID OR MISSING DATA FOR CHASSIS STATUS REQUEST",
"U1105 SCP (J1850) INVALID OR MISSING DATA FOR CHASSIS STATUS REQUEST",
"U1106 SCP (J1850) INVALID OR MISSING DATA FOR LEGISLATED DIAGNOSTICS",
"U1107 SCP (J1850) INVALID OR MISSING DATA FOR LEGISLATED DIAGNOSTICS",
"U1108 SCP (J1850) INVALID OR MISSING DATA FOR ELECTRIC TRACTION DRIVE (INVERTER)",
"U1109 SCP (J1850) INVALID OR MISSING DATA FOR ELECTRIC TRACTION DRIVE (INVERTER)",
"U1110 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $6E",
"U1111 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $6F",
"U1112 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $70",
"U1113 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $71",
"U1114 SCP (J1850) INVALID OR MISSING DATA FOR CHARGING SYSTEM",
"U1115 SCP (J1850) INVALID OR MISSING DATA FOR CHARGING SYSTEM",
"U1116 SCP (J1850) INVALID OR MISSING DATA FOR ELECTRICAL ENERGY MANAGEMENT",
"U1117 SCP (J1850) INVALID OR MISSING DATA FOR ELECTRICAL ENERGY MANAGEMENT",
"U1118 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $76",
"U1119 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $77",
"U1120 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $78",
"U1121 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $79",
"U1122 SCP (J1850) INVALID OR MISSING DATA FOR ODOMETER",
"U1123 SCP (J1850) INVALID OR MISSING DATA FOR ODOMETER",
"U1124 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $7C",
"U1125 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $7D",
"U1126 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $7E",
"U1127 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $7F",
"U1128 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $80",
"U1129 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $81",
"U1130 SCP (J1850) INVALID OR MISSING DATA FOR FUEL SYSTEM",
"U1131 SCP (J1850) INVALID OR MISSING DATA FOR FUEL SYSTEM",
"U1132 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE MOTION",
"U1133 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE MOTION",
"U1134 SCP (J1850) INVALID OR MISSING DATA FOR IGNITION SWITCH / STARTER",
"U1135 SCP (J1850) INVALID OR MISSING DATA FOR IGNITION SWITCH / STARTER",
"U1136 SCP (J1850) INVALID OR MISSING DATA FOR TELLTALES",
"U1137 SCP (J1850) INVALID OR MISSING DATA FOR TELLTALES",
"U1138 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $8A",
"U1139 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $8B",
"U1140 SCP (J1850) INVALID OR MISSING DATA FOR GATEWAY",
"U1141 SCP (J1850) INVALID OR MISSING DATA FOR GATEWAY",
"U1142 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $8E",
"U1143 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $8F",
"U1144 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $90",
"U1145 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $91",
"U1146 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE SECURITY",
"U1147 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE SECURITY",
"U1148 SCP (J1850) INVALID OR MISSING DATA FOR AUDIO CONTROL",
"U1149 SCP (J1850) INVALID OR MISSING DATA FOR AUDIO CONTROL",
"U1150 SCP (J1850) INVALID OR MISSING DATA FOR AUDIBLE WARNINGS",
"U1151 SCP (J1850) INVALID OR MISSING DATA FOR AUDIBLE WARNINGS",
"U1152 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #3",
"U1153 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #3",
"U1154 SCP (J1850) INVALID OR MISSING DATA FOR COMPACT DISC",
"U1155 SCP (J1850) INVALID OR MISSING DATA FOR COMPACT DISC",
"U1156 SCP (J1850) INVALID OR MISSING DATA FOR DIGITAL SIGNAL PROCESSING",
"U1157 SCP (J1850) INVALID OR MISSING DATA FOR DIGITAL SIGNAL PROCESSING",
"U1158 SCP (J1850) INVALID OR MISSING DATA FOR ANTENNA",
"U1159 SCP (J1850) INVALID OR MISSING DATA FOR ANTENNA",
"U1160 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $A0",
"U1161 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $A1",
"U1162 SCP (J1850) INVALID OR MISSING DATA FOR DIGITAL AUDIO TAPE",
"U1163 SCP (J1850) INVALID OR MISSING DATA FOR DIGITAL AUDIO TAPE",
"U1164 SCP (J1850) INVALID OR MISSING DATA FOR TUNER / RECEIVER",
"U1165 SCP (J1850) INVALID OR MISSING DATA FOR TUNER / RECEIVER",
"U1166 SCP (J1850) INVALID OR MISSING DATA FOR CASSETTE TAPE",
"U1167 SCP (J1850) INVALID OR MISSING DATA FOR CASSETTE TAPE",
"U1168 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $A8",
"U1169 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $A9",
"U1170 SCP (J1850) INVALID OR MISSING DATA FOR CELLULAR PHONE / PAGING SYSTEM",
"U1171 SCP (J1850) INVALID OR MISSING DATA FOR CELLULAR PHONE / PAGING SYSTEM",
"U1172 SCP (J1850) INVALID OR MISSING DATA FOR REMOTE BUTTON CONTROL",
"U1173 SCP (J1850) INVALID OR MISSING DATA FOR REMOTE BUTTON CONTROL",
"U1174 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $AE",
"U1175 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $AF",
"U1176 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $B0",
"U1177 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $B1",
"U1178 SCP (J1850) INVALID OR MISSING DATA FOR CLIMATE CONTROL (HVAC)",
"U1179 SCP (J1850) INVALID OR MISSING DATA FOR CLIMATE CONTROL (HVAC)",
"U1180 SCP (J1850) INVALID OR MISSING DATA FOR PERSONALIZATION (MEMORY) FEATURES",
"U1181 SCP (J1850) INVALID OR MISSING DATA FOR PERSONALIZATION (MEMORY) FEATURES",
"U1182 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $B6",
"U1183 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $B7",
"U1184 SCP (J1850) INVALID OR MISSING DATA FOR WINDOW WIPER / WASHER",
"U1185 SCP (J1850) INVALID OR MISSING DATA FOR WINDOW WIPER / WASHER",
"U1186 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $BA",
"U1187 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $BB",
"U1188 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $BC",
"U1189 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $BD",
"U1190 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $BE",
"U1191 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $BF",
"U1192 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $C0",
"U1193 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $C1",
"U1194 SCP (J1850) INVALID OR MISSING DATA FOR MIRRORS",
"U1195 SCP (J1850) INVALID OR MISSING DATA FOR MIRRORS",
"U1196 SCP (J1850) INVALID OR MISSING DATA FOR DOOR LOCKS",
"U1197 SCP (J1850) INVALID OR MISSING DATA FOR DOOR LOCKS",
"U1198 SCP (J1850) INVALID OR MISSING DATA FOR EXTERNAL ACCESS (DOORS)",
"U1199 SCP (J1850) INVALID OR MISSING DATA FOR EXTERNAL ACCESS (DOORS)",
"U1200 SCP (J1850) INVALID OR MISSING DATA FOR SEAT MOTION / CONTROL",
"U1201 SCP (J1850) INVALID OR MISSING DATA FOR SEAT MOTION / CONTROL",
"U1202 SCP (J1850) INVALID OR MISSING DATA FOR WINDOWS",
"U1203 SCP (J1850) INVALID OR MISSING DATA FOR WINDOWS",
"U1204 SCP (J1850) INVALID OR MISSING DATA FOR STEERING COLUMN",
"U1205 SCP (J1850) INVALID OR MISSING DATA FOR STEERING COLUMN",
"U1206 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $CE",
"U1207 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $CF",
"U1208 SCP (J1850) INVALID OR MISSING DATA FOR SEAT SWITCHES",
"U1209 SCP (J1850) INVALID OR MISSING DATA FOR SEAT SWITCHES",
"U1210 SCP (J1850) INVALID OR MISSING DATA FOR RESTRAINTS",
"U1211 SCP (J1850) INVALID OR MISSING DATA FOR RESTRAINTS",
"U1212 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $D4",
"U1213 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $D5",
"U1214 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $D6",
"U1215 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $D7",
"U1216 SCP (J1850) INVALID OR MISSING DATA FOR EXTERNAL LAMP OUTAGE",
"U1217 SCP (J1850) INVALID OR MISSING DATA FOR EXTERNAL LAMP OUTAGE",
"U1218 SCP (J1850) INVALID OR MISSING DATA FOR EXTERNAL LAMPS",
"U1219 SCP (J1850) INVALID OR MISSING DATA FOR EXTERNAL LAMPS",
"U1220 SCP (J1850) INVALID OR MISSING DATA FOR INTERIOR LAMP OUTAGE",
"U1221 SCP (J1850) INVALID OR MISSING DATA FOR INTERIOR LAMP OUTAGE",
"U1222 SCP (J1850) INVALID OR MISSING DATA FOR INTERIOR LAMPS",
"U1223 SCP (J1850) INVALID OR MISSING DATA FOR INTERIOR LAMPS",
"U1224 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $E0",
"U1225 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $E1",
"U1226 SCP (J1850) INVALID OR MISSING DATA FOR BODY STATUS REQUEST",
"U1227 SCP (J1850) INVALID OR MISSING DATA FOR BODY STATUS REQUEST",
"U1228 SCP (J1850) INVALID OR MISSING DATA FOR TIRES",
"U1229 SCP (J1850) INVALID OR MISSING DATA FOR TIRES",
"U1230 SCP (J1850) INVALID OR MISSING DATA FOR ELECTRIC DEFROST",
"U1231 SCP (J1850) INVALID OR MISSING DATA FOR ELECTRIC DEFROST",
"U1232 SCP (J1850) INVALID OR MISSING DATA FOR NAVIGATION",
"U1233 SCP (J1850) INVALID OR MISSING DATA FOR NAVIGATION",
"U1234 SCP (J1850) INVALID OR MISSING DATA FOR DISPLAYS",
"U1235 SCP (J1850) INVALID OR MISSING DATA FOR DISPLAYS",
"U1236 SCP (J1850) INVALID OR MISSING DATA FOR MEMORY STORAGE",
"U1237 SCP (J1850) INVALID OR MISSING DATA FOR MEMORY STORAGE",
"U1238 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #4",
"U1239 SCP (J1850) INVALID OR MISSING DATA FOR EXPERIMENTAL #4",
"U1240 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $F0",
"U1241 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $F1",
"U1242 SCP (J1850) INVALID OR MISSING DATA FOR EXTERIOR ENVIRONMENT",
"U1243 SCP (J1850) INVALID OR MISSING DATA FOR EXTERIOR ENVIRONMENT",
"U1244 SCP (J1850) INVALID OR MISSING DATA FOR INTERIOR ENVIRONMENT",
"U1245 SCP (J1850) INVALID OR MISSING DATA FOR INTERIOR ENVIRONMENT",
"U1246 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $F6",
"U1247 SCP (J1850) INVALID OR MISSING DATA FOR PRIMARY ID $F7",
"U1248 SCP (J1850) INVALID OR MISSING DATA FOR TIME / DATE",
"U1249 SCP (J1850) INVALID OR MISSING DATA FOR TIME / DATE",
"U1250 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE ID (VIN)",
"U1251 SCP (J1850) INVALID OR MISSING DATA FOR VEHICLE ID (VIN)",
"U1252 SCP (J1850) INVALID OR MISSING DATA FOR CLASS A FUNCTIONS",
"U1253 SCP (J1850) INVALID OR MISSING DATA FOR CLASS A FUNCTIONS",
"U1254 SCP (J1850) INVALID OR MISSING DATA FOR NETWORK CONTROL",
"U1255 SCP (J1850) INVALID OR MISSING DATA FOR NETWORK CONTROL",
"U1256 SCP(J1850) INVALID OR MISSING DATA FOR PRIMARY ID $FF",
"U1260 SCP (J1850) SINGLE ENDED (+) CIRCUIT FAILURE",
"U1261 SCP (J1850) SINGLE ENDED (-) CIRCUIT FAILURE",
"U1262 SCP (J1850) COMMUNICATION BUS FAULT",
"U1263 INVALID OR MISSING DATA FROM SECOND SCP LINK",
"U1308 SCP (J1850) INVALID OR MISSING DATA FOR FUNCTION READ  ENGINE TORQUE",
"U1341 SCP (J1850) INVALID OR MISSING DATA FOR FUNCTION READ VEHICLE SPEED",
"U1430 SCP (J1850) INVALID OR MISSING DATA FOR FUNCTION READ FUEL SYSTEM",
"U1451 SCP (J1850) INVALID OR MISSING DATA FOR FUNCTION READ AUDIBLE WARNINGS",
"U1612 SCP (J1850) LACK OF ACKNOWLEDGMENT FOR PRIMARY ID $0C",
"U1736 SCP (J1850) LACK OF ACKNOWLEDGMENT FOR  TELLTALES",
"U1738 SCP NO ACK FOR TELLTALES",
"U1750 SCP (J1850) LACK OF ACKNOWLEDGMENT FOR  AUDIBLE WARNINGS",
"U1751 SCP (J1850) SCLM SYSTEM STATUS MISSING FROM REM",
"U1752 SCP (J1850) SCLM SYSTEM STATUS MISSING FROM FEM",
"U1794 SCP (J1850) LACK OF ACKNOWLEDGMENT FOR MIRRORS",
"U1797 SCP (J1850) LACK OF ACKNOWLEDGMENT FOR  DOOR LOCKS",
"U1798 SCP (J1850) LACK OF ACKNOWLEDGMENT FOR  EXTERNAL ACCESS (DOORS)",
"U1806 SCP (J1850) LACK OF ACKNOWLEDGEMENT FOR PRIMARY ID $CE",
"U1812 SEAT MOTION SW SIG-NO ACK.",
"U1834 SCP NO ACK FOR DISPLAYS",
"U1900 CAN COMMUNICATION BUS FAULT - RECEIVE ERROR",
"U1901 CAN NETWORK #2 COMMUNICATION BUS FAULT - RECEIVE ERROR",
"U1950 UBP COMMUNICATION BUS FAULT",
"U2000 AUDIO REAR CONTROL UNIT IS NOT RESPONDING",
"U2001 AUDIO TAPE DECK UNIT IS NOT RESPONDING",
"U2002 AUDIO BEZEL IS NOT RESPONDING",
"U2003 AUDIO COMPACT DISK / DISK JOCKEY UNIT IS NOT RESPONDING",
"U2004 AUDIO STEERING WHEEL CONTROL UNIT IS NOT RESPONDING",
"U2005 AUDIO REAR INTEGRATED CONTROL PANEL UNIT / RDM IS NOT RESPONDING",
"U2006 AUDIO REMOTE CLIMATE CONTROL UNIT IS NOT RESPONDING",
"U2007 AUDIO NAVIGATION UNIT IS NOT RESPONDING",
"U2008 AUDIO PHONE IS NOT RESPONDING",
"U2009 AUDIO FRONT CONTROL MODULE (ACM) IS NOT RESPONDING",
"U2010 MODULE IS NOT RESPONDING (NON SCP)",
"U2011 MODULE TRANSMITTED INVALID DATA (NON SCP)",
"U2012 COMMUNICATION BUS ERROR (NON SCP)",
"U2013 COMPASS MODULE IS NOT RESPONDING",
"U2014 AUDIO SUBWOOFER UNIT IS NOT RESPONDING",
"U2015 SIGNAL LINK FAULT (NON SCP)",
"U2016 SIGNAL LINK SHORT TO GROUND (NON SCP)",
"U2017 DRIVER SIDE CRASH SENSOR COMMUNICATION FAULT (NON SCP)",
"U2018 PASSENGER SIDE CRASH SENSOR COMMUNICATION FAULT (NON SCP)",
"U2019 AUDIO VOICE MODULE NOT RESPONDING",
"U2020 AUDIO CENTER AMP IS NOT RESPONDING",
"U2021 INVALID /FAULT DATA RECEIVED (NON SCP)",
"U2022 COMMUNICATION FAULT ON DEDICATED PROTOCOL",
"U2023 FAULT RECEIVED FROM EXTERNAL NODE",
"U2024 AUDIO REDUNDANT STEERING WHEEL CONTROL NOT RESPONDING",
"U2025 SDARS MODULE IS NOT RESPONDING",
"U2026 FAMILY ENTERTAINMENT SYSTEM IS NOT RESPONDING",
"U2027 LEFT SIDE CRASH SENSOR COMMUNICATION FAULT (NON SCP)",
"U2028 RIGHT SIDE CRASH SENSOR COMMUNICATION FAULT (NON SCP)",
"U2029 DVD UNIT IS NOT RESPONDING",
"U2030 RAIN SENSOR COMMUNICATION FAULT",
"U2031 INNER LEFT REAR (ILR) TIRE PRESSURE SENSOR IS NOT RESPONDING",
"U2032 INNER RIGHT REAR (IRR) TIRE PRESSURE SENSOR IS NOT RESPONDING",
"U2050 NO APPLICATION PRESENT",
"U2051 ONE OR MORE CALIBRATION FILES MISSING / CORRUPT",
"U2060 ECU REDUNDANT POWER CIRCUIT OPEN",
"U2061 ECU REDUNDANT POWER CIRCUIT SHORT TO GROUND",
"U2062 ECU REDUNDANT GROUND CIRCUIT OPEN",
"U2063 ECU REDUNDANT GROUND CIRCUIT SHORT TO BATTERY",
"U2064 WARNING INDICATOR REQUESTED BY ANOTHER CONTROL MODULE",
"U2150 SCP (J1850) INVALID DATA FROM REM",
"U2152 SCP (J1850) INVALID DATA FROM GEM",
"U2160 SCP (J1850) INVALID DATA FROM IC",
"U2195 SCP (J1850) INVALID DATA FROM SCLM",
"U2196 INVALID 'ENGINE RPM' DATA",
"U2197 INVALID 'VEHICLE SPEED' DATA",
"U2198 INVALID 'FUEL PULSE' DATA",
"U2199 INVALID 'ENGINE COOLANT TEMPERATURE' DATA",
"U2200 INVALID 'ODO COUNT' DATA",
"U2201 INVALID 'AMBIENT TEMPERATURE' DATA",
"U2202 INVALID CONFIGURATION DATA RECEIVED",
"U2226 UBP INVALID DATA FROM NODE ID $10",
"U2235 UBP INVALID DATA FROM NODE ID $19",
"U2306 UBP INVALID DATA FROM NODE ID $60",
"U2338 UBP INVALID DATA FROM NODE ID $80",
"U2355 UBP INVALID DATA FROM NODE ID $91",
"U2362 UBP INVALID DATA FROM NODE ID $98",
"U2366 UBP INVALID DATA FROM NODE ID $9C",
"U2367 UBP INVALID DATA FROM NODE ID $9D",
"U2385 UBP INVALID DATA FROM NODE ID $AF",
"U2403 UBP INVALID DATA FROM NODE ID $C1",
"U2428 UBP INVALID DATA FROM NODE ID $DA",
"U2469 POWER LIFTGATE DISABLED BY CUSTOMER INTERFACE",
"U2470 UNEXPECTED KEYFOB / KEYPAD BUTTON PRESS",
"U2471 UNEXPECTED PRNDL STATE",
"U2472 UNEXPECTED IGNITION STATE",
"U2473 UNEXPECTED VEHICLE SPEED (VSS)",
"U2499 ECU OVERHEAT PROTECTION",
"U2500 (CAN) LACK OF ACKNOWLEDGEMENT FROM ENGINE MANAGEMENT",
"U2501 MISSING TOKEN FROM ENGINE MANAGEMENT SYSTEM FOR ACC",
"U2502 MISSING TOKEN FROM TRANSMISSION CONTROL MODULE FOR ACC",
"U2503 MISSING TOKEN FROM INSTRUMENT CLUSTER FOR ACC",
"U2504 MISSING TOKEN FROM ABS FOR ACC",
"U2505 MISSING MESSAGE FROM SMART BOOSTER CONTROLLER FOR ACC",
"U2506 MISSING TOKEN FROM ADAPTIVE CRUISE CONTROL FOR SMART BOOSTER",
"U2507 MISSING TOKEN FROM ENGINE MANAGEMENT SYSTEM FOR SMART BOOSTER",
"U2508 MISSING TOKEN FROM ABS FOR SMART BOOSTER",
"U2509 TORQUE REDUCTION REQUEST CANNOT BE FULLFILLED BY EMS",
"U2510 CAN - INVALID DATA FOR VEHICLE SECURITY.",
"U2511 CAN - DATA MIS-MATCH (RECEIVE DATA DOES NOT MATCH EXPECTED)",
"U2512 MISSING MESSAGE FOR ENGINE SPEED",
"U2513 MISSING MESSAGE FOR TRANSMISSION GEAR SELECTED",
"U2514 MISSING MESSAGE FOR VEHICLE SPEED",
"U2515 MISSING MESSAGE FOR ADAPTIVE CRUISE CONTROL",
"U2516 CAN BUS OFF - TRANSMIT ERROR (USE DTC $C073 INSTEAD)",
"U2517 RESERVED FOR JAGUAR CAN FAULTS",
"U2518 RESERVED FOR JAGUAR CAN FAULTS",
"U2519 RESERVED FOR JAGUAR CAN FAULTS",
"U2520 RESERVED FOR JAGUAR CAN FAULTS",
"U2521 RESERVED FOR JAGUAR CAN FAULTS",
"U2522 RESERVED FOR JAGUAR CAN FAULTS",
"U2523 RESERVED FOR JAGUAR CAN FAULTS",
"U2524 RESERVED FOR JAGUAR CAN FAULTS",
"U2525 RESERVED FOR JAGUAR CAN FAULTS",
"U2526 RESERVED FOR JAGUAR CAN FAULTS",
"U2527 CAN NETWORK #2 BUS OFF - TRANSMIT ERROR",
"U2528 PRNDL DATA MISMATCH",
"U2600 (D2B) WAKE-UP LINE SHORT TO BATT",
"U2601 (D2B) WAKE-UP LINE SHORT TO GROUND",
"U2602 FAULT DTC (CM): INCOMPLETE RING-FAULT REPORT RECEIVED",
"U2603 INCOMPLETE RING- NO FAULT REPORT RECEIVED",
"U2604 INCOMPLETE RING- CORRUPTED FAULT REPORT RECEIVED",
"U2605 MASTER ECU UNABLE TO INITIALIZE IT'S ADDRESS",
"U2606 FAULT DTC (CM): SLAVE ECU UNABLE TO INITIALIZE IT'S ADDRESS",
"U2607 FAULT DTC (CM): SLAVE SWITCHED INTO BYPASS MODE",
"U2609 D2B WAKEUP PULSE WIDTH OUT OF SPEC",
"U2610 D2B SLAVE ECU FAILED TO RECEIVE A REPORT POSITION",
"U2611 D2B SLAVE ECU FAILED TO RECEIVE AN ALARM CLEAR COMMAND",
"U2613 NAV MODULE NOT RESPONDING ON D2B",
"U2614 AMP MODULE NOT RESPONDING ON D2B",
"U2615 REAR ENT MODULE NOT RESPONDING ON D2B",
"U2616 LEFT FRONT TIRE PRESSURE SENSOR IS NOT RESPONDING",
"U2617 RIGHT FRONT TIRE PRESSURE SENSOR IS NOT RESPONDING",
"U2618 LEFT REAR TIRE PRESSURE SENSOR IS NOT RESPONDING",
"U2619 RIGHT REAR TIRE PRESSURE SENSOR IS NOT RESPONDING",
"U3000 CONTROL MODULE",
"U3001 CONTROL MODULE IMPROPER SHUTDOWN",
"U3002 VEHICLE IDENTIFICATION NUMBER",
"U3003 BATTERY VOLTAGE",
"U3004 ACCESSORY POWER RELAY",
"U3005 RETAINED ACCESSORY POWER",
"U3006 CONTROL MODULE INPUT POWER A",
"U3007 CONTROL MODULE INPUT POWER B",
"U3008 CONTROL MODULE GROUND A",
"U3009 CONTROL MODULE GROUND B",
"U300A IGNITION SWITCH",
"U300B IGNITION INPUT ACCESSORY/ON/START",
"U300C IGNITION INPUT OFF/ON/START",
"U300D IGNITION INPUT ON/START",
"U300E IGNITION INPUT ON",
"U300F IGNITION INPUT ACCESSORY",
"U3010 IGNITION INPUT START",
"U3011 IGNITION INPUT OFF",