U0001 High Speed CAN Communication Bus
U0002 High Speed CAN Communication Bus Performance
U0003 High Speed CAN Communication Bus (+) Open
U0004 High Speed CAN Communication Bus (+) Low
U0005 High Speed CAN Communication Bus (+) High
U0006 High Speed CAN Communication Bus (-) Open
U0007 High Speed CAN Communication Bus (-) Low
U0008 High Speed CAN Communication Bus (-) High
U0009 High Speed CAN Communication Bus (-) shorted to Bus (+)
U0010 Medium Speed CAN Communication Bus
U0011 Medium Speed CAN Communication Bus Performance
U0012 Medium Speed CAN Communication Bus (+) Open
U0013 Medium Speed CAN Communication Bus (+) Low
U0014 Medium Speed CAN Communication Bus (+) High
U0015 Medium Speed CAN Communication Bus (-) Open
U0016 Medium Speed CAN Communication Bus (-) Low
U0017 Medium Speed CAN Communication Bus (-) High
U0018 Medium Speed CAN Communication Bus (-) shorted to Bus (+)
U0019 Low Speed CAN Communication Bus
U0020 Low Speed CAN Communication Bus Performance
U0021 Low Speed CAN Communication Bus (+) Open
U0022 Low Speed CAN Communication Bus (+) Low
U0023 Low Speed CAN Communication Bus (+) High
U0024 Low Speed CAN Communication Bus (-) Open
U0025 Low Speed CAN Communication Bus (-) Low
U0026 Low Speed CAN Communication Bus (-) High
U0027 Low Speed CAN Communication Bus (-) shorted to Bus (+)
U0028 Vehicle Communication Bus A
U0029 Vehicle Communication Bus A Performance
U0030 Vehicle Communication Bus A (+) Open
U0031 Vehicle Communication Bus A (+) Low
U0032 Vehicle Communication Bus A (+) High
U0033 Vehicle Communication Bus A (-) Open
U0034 Vehicle Communication Bus A (-) Low
U0035 Vehicle Communication Bus A (-) High
U0036 Vehicle Communication Bus A (-) shorted to Bus A (+)
U0037 Vehicle Communication Bus B
U0038 Vehicle Communication Bus B Performance
U0039 Vehicle Communication Bus B (+) Open
U0040 Vehicle Communication Bus B (+) Low
U0041 Vehicle Communication Bus B (+) High
U0042 Vehicle Communication Bus B (-) Open
U0043 Vehicle Communication Bus B (-) Low
U0044 Vehicle Communication Bus B (-) High
U0045 Vehicle Communication Bus B (-) shorted to Bus B (+)
U0046 Vehicle Communication Bus C
U0047 Vehicle Communication Bus C Performance
U0048 Vehicle Communication Bus C (+) Open
U0049 Vehicle Communication Bus C (+) Low
U0050 Vehicle Communication Bus C (+) High
U0051 Vehicle Communication Bus C (-) Open
U0052 Vehicle Communication Bus C (-) Low
U0053 Vehicle Communication Bus C (-) High
U0054 Vehicle Communication Bus C (-) shorted to Bus C (+)
U0055 Vehicle Communication Bus D
U0056 Vehicle Communication Bus D Performance
U0057 Vehicle Communication Bus D (+) Open
U0058 Vehicle Communication Bus D (+) Low
U0059 Vehicle Communication Bus D (+) High
U0060 Vehicle Communication Bus D (-) Open
U0061 Vehicle Communication Bus D (-) Low
U0062 Vehicle Communication Bus D (-) High
U0063 Vehicle Communication Bus D (-) shorted to Bus D (+)
U0064 Vehicle Communication Bus E
U0065 Vehicle Communication Bus E Performance
U0066 Vehicle Communication Bus E (+) Open
U0067 Vehicle Communication Bus E (+) Low
U0068 Vehicle Communication Bus E (+) High
U0069 Vehicle Communication Bus E (-) Open
U0070 Vehicle Communication Bus E (-) Low
U0071 Vehicle Communication Bus E (-) High
U0072 Vehicle Communication Bus E (-) shorted to Bus E (+)
U0073 Control Module Communication Bus Off
U0100 Lost Communication With ECM/PCM "A"
U0101 Lost Communication with TCM
U0102 Lost Communication with Transfer Case Control Module
U0103 Lost Communication With Gear Shift Module
U0104 Lost Communication With Cruise Control Module
U0105 Lost Communication With Fuel Injector Control Module
U0106 Lost Communication With Glow Plug Control Module
U0107 Lost Communication With Throttle Actuator Control Module
U0108 Lost Communication With Alternative Fuel Control Module
U0109 Lost Communication With Fuel Pump Control Module
U0110 Lost Communication With Drive Motor Control Module
U0111 Lost Communication With Battery Energy Control Module A
U0112 Lost Communication With Battery Energy Control Module B
U0113 Lost Communication With Emissions Critical Control Information
U0114 Lost Communication With Four-Wheel Drive Clutch Control Module
U0115 Lost Communication With ECM/PCM B
U0121 Lost Communication With Anti-Lock Brake System (ABS) Control Module
U0122 Lost Communication With Vehicle Dynamics Control Module
U0123 Lost Communication With Yaw Rate Sensor Module
U0124 Lost Communication With Lateral Acceleration Sensor Module
U0125 Lost Communication With Multi-axis Acceleration Sensor Module
U0126 Lost Communication With Steering Angle Sensor Module
U0127 Lost Communication With Tire Pressure Monitor Module
U0128 Lost Communication With Park Brake Control Module
U0129 Lost Communication With Brake System Control Module
U0130 Lost Communication With Steering Effort Control Module
U0131 Lost Communication With Power Steering Control Module
U0132 Lost Communication With Ride Level Control Module
U0140 Lost Communication With Body Control Module
U0141 Lost Communication With Body Control Module A
U0142 Lost Communication With Body Control Module B
U0143 Lost Communication With Body Control Module C
U0144 Lost Communication With Body Control Module D
U0145 Lost Communication With Body Control Module E
U0146 Lost Communication With Gateway A
U0147 Lost Communication With Gateway B
U0148 Lost Communication With Gateway C
U0149 Lost Communication With Gateway D
U0150 Lost Communication With Gateway E
U0151 Lost Communication With Restraints Control Module
U0152 Lost Communication With Side Restraints Control Module (Left)
U0153 Lost Communication With Side Restraints Control Module (Right)
U0154 Lost Communication With Restraints Occupant Sensing Control Module
U0155 Lost Communication With Instrument Panel Cluster (IPC) Control Module
U0156 Lost Communication With Information Center A
U0157 Lost Communication With Information Center B
U0158 Lost Communication With Head Up Display
U0159 Lost Communication With Parking Assist Control Module
U0160 Lost Communication With Audible Alert Control Module
U0161 Lost Communication With Compass Module
U0162 Lost Communication With Navigation Display Module
U0163 Lost Communication With Navigation Control Module
U0164 Lost Communication With HVAC Control Module
U0165 Lost Communication With HVAC Control Module (Rear)
U0166 Lost Communication With Auxiliary Heater Control Module
U0167 Lost Communication With Vehicle Immobilizer Control Module
U0168 Lost Communication With Vehicle Security Control Module
U0169 Lost Communication With Sunroof Control Module
U0170 Lost Communication With "Restraints System Sensor A"
U0171 Lost Communication With "Restraints System Sensor B"
U0172 Lost Communication With "Restraints System Sensor C"
U0173 Lost Communication With "Restraints System Sensor D"
U0174 Lost Communication With "Restraints System Sensor E"
U0175 Lost Communication With "Restraints System Sensor F"
U0176 Lost Communication With "Restraints System Sensor G"
U0177 Lost Communication With "Restraints System Sensor H"
U0178 Lost Communication With "Restraints System Sensor I"
U0179 Lost Communication With "Restraints System Sensor J"
U0180 Lost Communication With Automatic Lighting Control Module
U0181 Lost Communication With Headlamp Leveling Control Module
U0182 Lost Communication With Lighting Control Module (Front)
U0183 Lost Communication With Lighting Control Module (Rear)
U0184 Lost Communication With Radio
U0185 Lost Communication With Antenna Control Module
U0186 Lost Communication With Audio Amplifier
U0187 Lost Communication With Digital Disc Player/Changer Module A
U0188 Lost Communication With Digital Disc Player/Changer Module B
U0189 Lost Communication With Digital Disc Player/Changer Module C
U0190 Lost Communication With Digital Disc Player/Changer Module D
U0191 Lost Communication With Television
U0192 Lost Communication With Personal Computer
U0193 Lost Communication With "Digital Audio Control Module A"
U0194 Lost Communication With "Digital Audio Control Module B"
U0195 Lost Communication With Subscription Entertainment Receiver Module
U0196 Lost Communication With Rear Seat Entertainment Control Module
U0197 Lost Communication With Telephone Control Module
U0198 Lost Communication With Telematic Control Module
U0199 Lost Communication With "Door Control Module A"
U0200 Lost Communication With "Door Control Module B"
U0201 Lost Communication With "Door Control Module C"
U0202 Lost Communication With "Door Control Module D"
U0203 Lost Communication With "Door Control Module E"
U0204 Lost Communication With "Door Control Module F"
U0205 Lost Communication With "Door Control Module G"
U0206 Lost Communication With Folding Top Control Module
U0207 Lost Communication With Movable Roof Control Module
U0208 Lost Communication With "Seat Control Module A"
U0209 Lost Communication With "Seat Control Module B"
U0210 Lost Communication With "Seat Control Module C"
U0211 Lost Communication With "Seat Control Module D"
U0212 Lost Communication With Steering Column Control Module
U0213 Lost Communication With Mirror Control Module
U0214 Lost Communication With Remote Function Actuation
U0215 Lost Communication With "Door Switch A"
U0216 Lost Communication With "Door Switch B"
U0217 Lost Communication With "Door Switch C"
U0218 Lost Communication With "Door Switch D"
U0219 Lost Communication With "Door Switch E"
U0220 Lost Communication With "Door Switch F"
U0221 Lost Communication With "Door Switch G"
U0222 Lost Communication With "Door Window Motor A"
U0223 Lost Communication With "Door Window Motor B"
U0224 Lost Communication With "Door Window Motor C"
U0225 Lost Communication With "Door Window Motor D"
U0226 Lost Communication With "Door Window Motor E"
U0227 Lost Communication With "Door Window Motor F"
U0228 Lost Communication With "Door Window Motor G"
U0229 Lost Communication With Heated Steering Wheel Module
U0230 Lost Communication With Rear Gate Module
U0231 Lost Communication With Rain Sensing Module
U0232 Lost Communication With Side Obstacle Detection Control Module (Left)
U0233 Lost Communication With Side Obstacle Detection Control Module (Right)
U0234 Lost Communication With Convenience Recall Module
U0235 Lost Communication With Cruise Control Front Distance Range Sensor
U0300 Internal Control Module Software Incompatibility
U0301 Software Incompatibility with ECM/PCM
U0302 Software Incompatibility with Transmission Control Module
U0303 Software Incompatibility with Transfer Case Control Module
U0304 Software Incompatibility with Gear Shift Control Module
U0305 Software Incompatibility with Cruise Control Module
U0306 Software Incompatibility with Fuel Injector Control Module
U0307 Software Incompatibility with Glow Plug Control Module
U0308 Software Incompatibility with Throttle Actuator Control Module
U0309 Software Incompatibility with Alternative Fuel Control Module
U0310 Software Incompatibility with Fuel Pump Control Module
U0311 Software Incompatibility with Drive Motor Control Module
U0312 Software Incompatibility with Battery Energy Control Module A
U0313 Software Incompatibility with Battery Energy Control Module B
U0314 Software Incompatibility with Four-Wheel Drive Clutch Control Module
U0315 Software Incompatibility with Anti-Lock Brake System Control Module
U0316 Software Incompatibility with Vehicle Dynamics Control Module
U0317 Software Incompatibility with Park Brake Control Module
U0318 Software Incompatibility with Brake System Control Module
U0319 Software Incompatibility with Steering Effort Control Module
U0320 Software Incompatibility with Power Steering Control Module
U0321 Software Incompatibility with Ride Level Control Module
U0322 Software Incompatibility with Body Control Module
U0323 Software Incompatibility with Instrument Panel Control Module
U0324 Software Incompatibility with HVAC Control Module
U0325 Software Incompatibility with Auxiliary Heater Control Module
U0326 Software Incompatibility with Vehicle Immobilizer Control Module
U0327 Software Incompatibility with Vehicle Security Control Module
U0328 Software Incompatibility with Steering Angle Sensor Module
U0329 Software Incompatibility with Steering Column Control Module
U0330 Software Incompatibility with Tire Pressure Monitor Module
U0331 Software Incompatibility with Body Control Module A
U0400 Invalid Data Received
U0401 Invalid Data Received From ECM/PCM
U0402 Invalid Data Received From Transmission Control Module
U0403 Invalid Data Received From Transfer Case Control Module
U0404 Invalid Data Received From Gear Shift Control Module
U0405 Invalid Data Received From Cruise Control Module
U0406 Invalid Data Received From Fuel Injector Control Module
U0407 Invalid Data Received From Glow Plug Control Module
U0408 Invalid Data Received From Throttle Actuator Control Module
U0409 Invalid Data Received From Alternative Fuel Control Module
U0410 Invalid Data Received From Fuel Pump Control Module
U0411 Invalid Data Received From Drive Motor Control Module
U0412 Invalid Data Received From Battery Energy Control Module A
U0413 Invalid Data Received From Battery Energy Control Module B
U0414 Invalid Data Received From Four-Wheel Drive Clutch Control Module
U0415 Invalid Data Received From Anti-Lock Brake System Control Module
U0416 Invalid Data Received From Vehicle Dynamics Control Module
U0417 Invalid Data Received From Park Brake Control Module
U0418 Invalid Data Received From Brake System Control Module
U0419 Invalid Data Received From Steering Effort Control Module
U0420 Invalid Data Received From Power Steering Control Module
U0421 Invalid Data Received From Ride Level Control Module
U0422 Invalid Data Received From Body Control Module
U0423 Invalid Data Received From Instrument Panel Control Module
U0424 Invalid Data Received From HVAC Control Module
U0425 Invalid Data Received From Auxiliary Heater Control Module
U0426 Invalid Data Received From Vehicle Immobilizer Control Module
U0427 Invalid Data Received From Vehicle Security Control Module
U0428 Invalid Data Received From Steering Angle Sensor Module
U0429 Invalid Data Received From Steering Column Control Module
U0430 Invalid Data Received From Tire Pressure Monitor Module
U0431 Invalid Data Received From Body Control Module A

U1000 Invalid or Missing Data for Primary Id 
U1001 Invalid or Missing Data for Primary Id 
U1002 Invalid or Missing Data for Primary Id 
U1003 Invalid or Missing Data for Primary Id 
U1004 Invalid or Missing Data for EEC Programming 
U1005 Invalid or Missing Data for EEC Programming 
U1006 Invalid or Missing Data for Primary Id 
U1007 Invalid or Missing Data for Primary Id 
U1008 Invalid or Missing Data for Engine Torque 
U1009 Invalid or Missing Data for Engine Torque 
U1010 Invalid or Missing Data for Engine Air Intake 
U1011 Invalid or Missing Data for Engine Air Intake 
U1012 Invalid or Missing Data for Primary Id
U1013 Invalid or Missing Data for Primary Id 
U1014 Invalid or Missing Data for Primary Id
U1015 Invalid or Missing Data for Primary Id 
U1016 Invalid or Missing Data for Primary Id 
U1017 Invalid or Missing Data for Primary Id 
U1018 Invalid or Missing Data for Throttle 
U1019 Invalid or Missing Data for Throttle 
U1020 Invalid or Missing Data for Air Conditioning Clutch 
U1021 Invalid or Missing Data for Air Conditioning Clutch 
U1022 Invalid or Missing Data for Primary Id
U1023 Invalid or Missing Data for Primary Id 
U1024 Invalid or Missing Data for Primary Id 
U1025 Invalid or Missing Data for Primary Id 
U1026 Invalid or Missing Data for Engine RPM 
U1027 Invalid or Missing Data for Engine RPM 
U1028 Invalid or Missing Data for Primary Id 
U1029 Invalid or Missing Data for Primary Id 
U1030 Invalid or Missing Data for Experimental #1 
U1031 Invalid or Missing Data for Experimental #1 
U1032 Invalid or Missing Data for Primary Id 
U1033 Invalid or Missing Data for Primary Id 
U1034 Invalid or Missing Data for Primary Id 
U1035 Invalid or Missing Data for Primary Id 
U1036 Invalid or Missing Data for Wheels 
U1037 Invalid or Missing Data for Wheels 
U1038 Invalid or Missing Data for Primary Id 
U1039 Invalid or Missing Data for Primary Id / Vehicle Speed
U1040 Invalid or Missing Data for Vehicle Speed 
U1041 Invalid or Missing Data for Vehicle Speed 
U1042 Invalid or Missing Data for Traction Control 
U1043 Invalid or Missing Data for Traction Control 
U1044 Invalid or Missing Data for Traction Motor
U1045 Invalid or Missing Data for Traction Motor 
U1046 Invalid or Missing Data for Primary Id 
U1047 Invalid or Missing Data for Primary Id 
U1048 Invalid or Missing Data for Primary Id 
U1049 Invalid or Missing Data for Primary Id 
U1050 Invalid or Missing Data for Brakes 
U1051 Invalid or Missing Data for Brakes 
U1052 Invalid or Missing Data for Steering / Steering Wheel 
U1053 Invalid or Missing Data for Steering / Steering Wheel 
U1054 Invalid or Missing Data for Primary Id 
U1055 Invalid or Missing Data for Primary Id 
U1056 Invalid or Missing Data for Vehicle Configuration 
U1057 Invalid or Missing Data for Vehicle Configuration 
U1058 Invalid or Missing Data for Transmission / Transaxle / PRNDL 
U1059 Invalid or Missing Data for Transmission / Transaxle / PRNDL 
U1060 Invalid or Missing Data for Primary Id 
U1061 Invalid or Missing Data for Primary Id 
U1062 Invalid or Missing Data for Primary Id 
U1063 Invalid or Missing Data for Primary Id 
U1064 Invalid or Missing Data for Primary Id 
U1065 Invalid or Missing Data for Primary Id 
U1066 Invalid or Missing Data for Primary Id 
U1067 Invalid or Missing Data for Primary Id 
U1068 Invalid or Missing Data for Primary Id
U1069 Invalid or Missing Data for Primary Id 
U1070 Invalid or Missing Data for Engine Sensors 
U1071 Invalid or Missing Data for Engine Sensors 
U1072 Invalid or Missing Data for Engine Coolant 
U1073 Invalid or Missing Data for Engine Coolant 
U1074 Invalid or Missing Data for Engine Oil 
U1075 Invalid or Missing Data for Engine Oil Temp
U1076 Invalid or Missing Data for Primary Id 
U1077 Invalid or Missing Data for Primary Id
U1078 Invalid or Missing Data for Primary Id 
U1079 Invalid or Missing Data for Primary Id 
U1080 Invalid or Missing Data for Primary Id 
U1081 Invalid or Missing Data for Primary Id 
U1082 Invalid or Missing Data for Engine Systems Other 
U1083 Invalid or Missing Data for Engine Systems Other 
U1084 Invalid or Missing Data for Powertrain Status Request 
U1085 Invalid or Missing Data for Powertrain Status Request 
U1086 Invalid or Missing Data for Primary Id
U1087 Invalid or Missing Data for Primary Id 
U1088 Invalid or Missing Data for Suspension 
U1089 Invalid or Missing Data for Suspension 
U1090 Invalid or Missing Data for Non-Legislated Diagnostics 
U1091 Invalid or Missing Data for Non-Legislated Diagnostics 
U1092 Invalid or Missing Data for Primary Id 
U1093 Invalid or Missing Data for Primary Id 
U1094 Invalid or Missing Data for Experimental #2 
U1095 Invalid or Missing Data for Experimental #2 
U1096 Invalid or Missing Data for Primary Id
U1097 Invalid or Missing Data for Primary Id 
U1098 Invalid or Missing Data for Vehicle Speed Control 
U1099 Invalid or Missing Data for Vehicle Speed Control 
U1100 Invalid or Missing Data for Primary Id 
U1101 Invalid or Missing Data for Primary Id 
U1102 Invalid or Missing Data for Primary Id 
U1103 Invalid or Missing Data for Primary Id
U1104 Invalid or Missing Data for Chassis Status Request 
U1105 Invalid or Missing Data for Chassis Status Request 
U1106 Invalid or Missing Data for Legislated Diagnostics 
U1107 Invalid or Missing Data for Legislated Diagnostics 
U1108 Invalid or Missing Data for Electric Traction Drive (Inverter) 
U1109 Invalid or Missing Data for Electric Traction Drive (Inverter) 
U1110 Invalid or Missing Data for Primary Id
U1111 Invalid or Missing Data for Primary Id 
U1112 Invalid or Missing Data for Primary Id 
U1113 Invalid or Missing Data for Primary Id 
U1114 Invalid or Missing Data for Charging System 
U1115 Invalid or Missing Data for Charging System 
U1116 Invalid or Missing Data for Electrical Energy Management 
U1117 Invalid or Missing Data for Electrical Energy Management 
U1118 Invalid or Missing Data for Primary Id 
U1119 Invalid or Missing Data for Primary Id 
U1120 Invalid or Missing Data for Primary Id 
U1121 Invalid or Missing Data for Primary Id 
U1122 Invalid or Missing Data for Odometer 
U1123 Invalid or Missing Data for Odometer 
U1124 Invalid or Missing Data for Primary Id 
U1125 Invalid or Missing Data for Primary Id 
U1126 Invalid or Missing Data for Primary Id 
U1127 Invalid or Missing Data for Primary Id 
U1128 Invalid or Missing Data for Primary Id 
U1129 Invalid or Missing Data for Primary Id 
U1130 Invalid or Missing Data for Fuel System 
U1131 Invalid or Missing Data for Fuel System 
U1132 Invalid or Missing Data for Vehicle Motion 
U1133 Invalid or Missing Data for Vehicle Motion 
U1134 Invalid or Missing Data for Ignition Switch / Starter 
U1135 Invalid or Missing Data for Ignition Switch / Starter 
U1136 Invalid or Missing Data for Telltales 
U1137 Invalid or Missing Data for Telltales 
U1138 Invalid or Missing Data for Primary Id 
U1139 Invalid or Missing Data for Primary Id 
U1140 Invalid or Missing Data for Gateway 
U1141 Invalid or Missing Data for Gateway 
U1142 Invalid or Missing Data for Primary Id 
U1143 Invalid or Missing Data for Primary Id 
U1144 Invalid or Missing Data for Primary Id 
U1145 Invalid or Missing Data for Primary Id 
U1146 Invalid or Missing Data for Vehicle Security 
U1147 Invalid or Missing Data for Vehicle Security 
U1148 Invalid or Missing Data for Audio Control 
U1149 Invalid or Missing Data for Audio Control 
U1150 Invalid or Missing Data for Audible Warnings 
U1151 Invalid or Missing Data for Audible Warnings 
U1152 Invalid or Missing Data for Experimental #3 
U1153 Invalid or Missing Data for Experimental #3 
U1154 Invalid or Missing Data for Compact Disc 
U1155 Invalid or Missing Data for Compact Disc 
U1156 Invalid or Missing Data for Digital Signal Processing 
U1157 Invalid or Missing Data for Digital Signal Processing 
U1158 Invalid or Missing Data for Antenna 
U1159 Invalid or Missing Data for Antenna 
U1160 Invalid or Missing Data for Primary Id 
U1161 Invalid or Missing Data for Primary Id 
U1162 Invalid or Missing Data for Digital Audio Tape 
U1163 Invalid or Missing Data for Digital Audio Tape 
U1164 Invalid or Missing Data for Tuner / Receiver 
U1165 Invalid or Missing Data for Tuner / Receiver 
U1166 Invalid or Missing Data for Cassette Tape 
U1167 Invalid or Missing Data for Cassette Tape 
U1168 Invalid or Missing Data for Primary Id 
U1169 Invalid or Missing Data for Primary Id 
U1170 Invalid or Missing Data for Cellular Phone / Paging System 
U1171 Invalid or Missing Data for Cellular Phone / Paging System 
U1172 Invalid or Missing Data for Remote Button Control 
U1173 Invalid or Missing Data for Remote Button Control 
U1174 Invalid or Missing Data for Primary Id 
U1175 Invalid or Missing Data for Primary Id 
U1176 Invalid or Missing Data for Primary Id 
U1177 Invalid or Missing Data for Primary Id 
U1178 Invalid or Missing Data for Climate Control (HVAC) 
U1179 Invalid or Missing Data for Climate Control (HVAC) 
U1180 Invalid or Missing Data for Personalization (Memory) Features 
U1181 Invalid or Missing Data for Personalization (Memory) Features 
U1182 Invalid or Missing Data for Primary Id 
U1183 Invalid or Missing Data for Primary Id 
U1184 Invalid or Missing Data for Window Wiper / Washer 
U1185 Invalid or Missing Data for Window Wiper / Washer 
U1186 Invalid or Missing Data for Primary Id 
U1187 Invalid or Missing Data for Primary Id 
U1188 Invalid or Missing Data for Primary Id 
U1189 Invalid or Missing Data for Primary Id 
U1190 Invalid or Missing Data for Primary Id 
U1191 Invalid or Missing Data for Primary Id 
U1192 Invalid or Missing Data for Primary Id 
U1193 Invalid or Missing Data for Primary Id 
U1194 Invalid or Missing Data for Mirrors 
U1195 Invalid or Missing Data for Mirrors 
U1196 Invalid or Missing Data for Door Locks 
U1197 Invalid or Missing Data for Door Locks 
U1198 Invalid or Missing Data for External Access (Doors) 
U1199 Invalid or Missing Data for External Access (Doors) 
U1200 Invalid or Missing Data for Seat Motion / Control 
U1201 Invalid or Missing Data for Seat Motion / Control 
U1202 Invalid or Missing Data for Windows 
U1203 Invalid or Missing Data for Windows 
U1204 Invalid or Missing Data for Steering Column 
U1205 Invalid or Missing Data for Steering Column 
U1206 Invalid or Missing Data for Primary Id 
U1207 Invalid or Missing Data for Primary Id 
U1208 Invalid or Missing Data for Seat Switches 
U1209 Invalid or Missing Data for Seat Switches 
U1210 Invalid or Missing Data for Restraints 
U1211 Invalid or Missing Data for Restraints 
U1212 Invalid or Missing Data for Primary Id 
U1213 Invalid or Missing Data for Primary Id 
U1214 Invalid or Missing Data for Primary Id 
U1215 Invalid or Missing Data for Primary Id 
U1216 Invalid or Missing Data for External Lamp Outage 
U1217 Invalid or Missing Data for External Lamp Outage 
U1218 Invalid or Missing Data for External Lamps 
U1219 Invalid or Missing Data for External Lamps 
U1220 Invalid or Missing Data for Interior Lamp Outage 
U1221 Invalid or Missing Data for Interior Lamp Outage 
U1222 Invalid or Missing Data for Interior Lamps 
U1223 Invalid or Missing Data for Interior Lamps 
U1224 Invalid or Missing Data for Primary Id 
U1225 Invalid or Missing Data for Primary Id 
U1226 Invalid or Missing Data for Body Status Request 
U1227 Invalid or Missing Data for Body Status Request 
U1228 Invalid or Missing Data for Tires 
U1229 Invalid or Missing Data for Tires 
U1230 Invalid or Missing Data for Electric Defrost 
U1231 Invalid or Missing Data for Electric Defrost 
U1232 Invalid or Missing Data for Navigation 
U1233 Invalid or Missing Data for Navigation 
U1234 Invalid or Missing Data for Displays 
U1235 Invalid or Missing Data for Displays 
U1236 Invalid or Missing Data for Memory Storage 
U1237 Invalid or Missing Data for Memory Storage 
U1238 Invalid or Missing Data for Experimental #4 
U1239 Invalid or Missing Data for Experimental #4 
U1240 Invalid or Missing Data for Primary Id 
U1241 Invalid or Missing Data for Primary Id 
U1242 Invalid or Missing Data for Exterior Environment 
U1243 Invalid or Missing Data for Exterior Environment 
U1244 Invalid or Missing Data for Interior Environment 
U1245 Invalid or Missing Data for Interior Environment 
U1246 Invalid or Missing Data for Primary Id 
U1247 Invalid or Missing Data for Primary Id 
U1248 Invalid or Missing Data for Time / Date 
U1249 Invalid or Missing Data for Time / Date 
U1250 Invalid or Missing Data for Vehicle Id (VIN) 
U1251 Invalid or Missing Data for Vehicle Id (VIN) 
U1252 Invalid or Missing Data for Class A Functions 
U1253 Invalid or Missing Data for Class A Functions 
U1254 Invalid or Missing Data for Network Control 
U1255 Invalid or Missing Data for Network Control 
U1260 Single Ended (+) Circuit Failure 
U1261 Single Ended (-) Circuit Failure 
U1262 Communication Bus Fault 
U1308 Invalid or Missing Data for Function Read Engine Torque 
U1341 Invalid or Missing Data for Function Read Vehicle Speed 
U1430 Invalid or Missing Data for Function Read Fuel System 
U1451 Invalid or Missing Data for Function Read Audible Warnings /Anti-Theft Module, Vehicle Immobilized 
U1612 Lack of Acknowledgment for Primary Id 
U1736 Lack of Acknowledgment for Telltales 
U1750 Lack of Acknowledgment for Audible Warnings 
U1794 Lack of Acknowledgment for Mirrors 
U1797 Lack of Acknowledgment for Door Locks 
U1798 Lack of Acknowledgment for External Access (Doors) 
U1806 Lack of Acknowledgment for Primary Id 
U1900 CAN Communication Bus Fault 
U1950 UPB Communication Bus Fault 
U2000 Audio Rear Control Unit is Not Responding 
U2001 Audio Tape Deck Unit is Not Responding 
U2002 Audio Bezel is Not Responding 
U2003 Audio Compact Disk / Disk Jockey Unit is Not Responding 
U2004 Audio Steering Wheel Control Unit is Not Responding 
U2005 Audio Rear Integrated Control Panel Unit is Not Responding 
U2006 Audio Remote Climate Control Unit is Not Responding 
U2007 Audio Navigation Unit is Not Responding 
U2008 Audio Phone is Not Responding 
U2009 Audio Front Control Module (ACM) is Not Responding 
U2010 Module is Not Responding (Non SCP) 
U2011 Module Transmitted Invalid Data (Non SCP) 
U2012 Communication Bus Error (Non SCP) 
U2013 Compass Module is not Responding 
U2014 Audio Subwoofer Unit is Not Responding 
U2015 Signal Link Fault (Non SCP) 
U2016 Signal Link Short to Ground (Non SCP) / From NGV Module 
U2017 Driver Side Crash Sensor Communication Fault (Non SCP) 
U2018 Passenger Side Crash Sensor Communication Fault (Non SCP) 
U2019 Audio Voice Module Not Responding 
U2020 Audio Center Amp is not responding 
U2021 Invalid /fault data received (Non SCP) 
U2150 Invalid Data from REM 
U2152 Invalid Data from GEM 
U2160 Invalid Data from IC 
U2195 Invalid Data from SCLM 
U2500 (CAN) Lack of Acknowledgement From Engine Management