MERCEDES BENZ W124 200E 16V - 220E 16V

Air conditioning installation instructions

PRESCRIPTIONS FOR MOUNTING THE DIAVIA A/C SYSTEM TO BE FOLLOWED BY THE TECHNICIAN INSTALLING THE SYSTEM. SHOULD THEY NOT BE OBSERVED THE TECHNICIAN WILL BE DIRECTLY AND EXCLUSIVELY RESPONSIBLE TO THE CLIENT.

- check the propper tightening of the supplied nuts and bolts and removal, and otherwise, of all parts involved in assembly of the A/C system;

- check that there are no water, oil or air leaks on the engine, brackes, power steering, power brakes, etc;

- check the level of all liquids. Should the radiator water be removed, reload the same discharged water in the circuit ana, if it is necessary to fill to the brim add the prescribed liquid anti-freeze. Furthermore, make sure that the air cleaning is carried out as prescribed by the builder;

- check the proper tension of all the belts and check the state of wear on those which have not been replaced;

- check that there is no1 critical interference under any function condition. In particular check that the safety distances between all parts subject to relative movement are guaranteed;

- ensure that there is no rubbing between parts with consequent wear by means of proper tightening and positioning of the parts themselves;

- check that electric insulation, fuse installation and all parts of the electrical system are correct;

- after having charged the coolant make a careful search for any leaks of gas;

- carry out all operations according to the rules of good technology; 10   should any holes or cuts be made during installation of the system, it is absolutely necessary to protect such parts with the rust-proof product supplied with the system.

UPDATING

MERCEDES BENZ W124 (all Models)

- It is necessary to remove and discard the O-R seal (GREEN) situated on the supplied water pipe coupling, pos. 98 of the Fitting Instructions (DIAVIA Part. No. 069428/2), because it is not suitable.

- Replace it with the original O-R seal taken from the original discarded water pipe.

Radiator kit (supplied upon request)

MERCEDES BENZ W124 200E16V-220E16V

1 MB 243 98E/1

System and cooling fluid circulation diagram

SUPPLIED MATERIAL

View of the compressor, condenser, receiver drier and accessories assembly components.

View of the updated radiator assembly kit (Kit A03533/1 supplied on request).

| LIST OF SUPPLIED MATERIALS |
| --- |
| Pos | Description | Code | Qty |
| 1 | Compressor support plate | 001856MB | 1 |
| 2 | Bracket | 002974MB/1 | 1 |
| 3 | Plain washer D10 UNI 6592 | — | 1 |
| 4 | Left side air conveyor | 083107 | 1 |
| 5 | Corrugated washer D10 DIN 137B | — | 4 |
| 6 | Receiver drier | 017041 | 1 |
| 7 | Receiver drier support bracket | 036574 | 1 |
| 8 | Poly-V belt compressor Poly-V 6Kx2145 | 013506 | 1 |
| 9 | Pressure switch | 043118 | 1 |
| 10 | Bag of screws and clamps | 039001 | 1 |
| 11 | Relay screen | 0361067/1 | 1 |
| 12 | Compressor | 084014218 | 1 |
| 14 | Self-locking nut M6 UNI 7474 | — | — |
| 15 | Hexagonal head screw M10x30 UNI 5739 | — | — |
| 16 | Bracket | 008350 | 1 |
| * 17 | Radiator | 031660 | 1 |
| * 18 | Radiator air conveyor | 031661 | 1 |
| 19 | Condenser securing spring | 007247 |  |
| 20 | Rubber condenser protection | 007245 | 2 |
| * 21 | Radiator water couple | 031664 | 1 |
| * 22 | Radiator water couple | 031665 | 1 |
| 23 | Self-locking nut MS UNI 7474 | — | — |
| * 25 | Rivet 4,8x14 | 062023 | 18 |
| 27 | Hexagonal head screw M8x20 UNI 5739 | — | — |
| 26 | "PACKARD" wiring for compressor | 028839 | 1 |
| 29 | Self-tapping screw socket head 4,2x22 DIN 7983 | _ | _ |
| * 30 | Spring 13x13 pin 4 | 062001 | 6 |
| 31 | Electrically cooled condenser | 025240/2 | 1 |
| * 32 | Radiator support | 036281/1 | 1 |
| * 33 | Air intake grill | 036282 | 1 |
| * 34 | Lower condenser bracket | 081035 | 1 |
| 35 | Plain washer 06x18 UNI 6593 | — | — |
| 36 | Hexagonal head screw M8x16 UNI 5739 | - | — |
| 41 | Self-locking nut M10 UNI 7474 | — | — |
| 42 | Cheese-headed screw with inner hexagon M10x60 UNI 5931 | — | — |
| * 44 | Lower condenser bracket | 081836 | 1 |
| 45 | Evaporator | 030565 | 1 |
| 46 | Self-tapping screw 4,8x13 | 061030 | _ |
| 47 | Gas pipe fitting flange | 043061/1 | 1 |
| * 53 | Right radiator band | 031662 | 1 |
| 54 | Condensate drain pipe 012 (m. 0,250) | 069007 | 2 |
| 55 | Hexagonal head screw M6x16 UNI 5739 | — | — |
| 56 | Motor horn support bracket | 036887 | 1 |
| * 57 | Universal rubber pipe lead | 069031 | 2 |
| 58 | Sealant 10x3 (mt. 2,5) | 070054 | 1 |
| 59 | Allen head screw M4x18 UNI 5931 | _ | _ |
| 60 | Self-locking nut M4 UNI 7474 | — | 4 |
| 61 | Oil pipe coupling | 007449 | 1 |
| 61.1 | External air temperature probe | ECA068680.2 | 1 |
| 62 | Oil pipe coupling | 007450 | 1 . |
| 62.1 | Cylindrical terminals | — | 2 |
| 63 | Washer 012x016x1,5 | 007026 | 2 |
| 63.1 | Valve unit | — | 1 |
| 64 | Oil pipe | 007456 | 1 |
| 65 | Plain washer 04 UNI 6592 |  | — |
| 72 | Shelf under the dashboard | 032912 | 1 |
| 74 | Control panel cutting face plate | 032484 | 1 |
| 76 | Electrical system and controls | 0281355 | 1 |
| 77 | Electrical system for electric fan control | 0281356 | 1 |
| 79 | Corrugated washer 06 DIN 137B | — | — |
| 80 | Corrugated washer 08 DIN 137B | — | — |
| 96 | Electronic control box | 132061 | 1 |
| 97 | Switch | 0681549 | 1 |
| 98 | Water pipe | 069428/2 | 1 |
| 99 | Plain washer 05x015 UNI 6593C | — | 2 |
| 100 | Adhesive Tampocrill 2 mm. thick | 070012 | 1 |
| 104 | Self-tapping screw cheese-headed 3,9x16 DIN 7981B | 061010 | — |
| 105 | Upper air conveyor | 031182 | 1 |
| 106 | No-frost probe | ECA068724 | 1 |
| 107 | Fixing part tor water pipes | 031173 | 1 |
| 108 | Adhesive tape mt. 2,000 | 070052 | 1 |
| 109 | BEHR heater right cap | 031179 | 1 |
| 110 | BEHR heater left cap | 031178 | 1 |
| 111 | VALEO heater cap | 031175 | 1 |
| 112 | VALEO heater cap | 031176 | 1 |
| 113 | VALEO heater cap | 031177 | 1 |
| 114 | Left stiffening tie-rod | 031180 | 1 |
| 115 | Right stiffening tie-rod | 031181 | 1 |
| 116 | Fixing part for water pipes | 031174 | 1 |
| 117 | Self-tapping screw cheese-headed cross-slotted 3,5x9,5 | 061009 | _ |
| 118 | Plug | 036438 | 1 |
| 119 | Cheese-headed screw with inner hexagon M6x16 UNI 5931 | — | _ |
| 120 | Rubber grommet | 0691D8 | 1 |
| 121 | Gas pipe support bracket | 008219 | 1 |
| 122 | Plain washer D6x15 UNI 6592 | — | 1 |
| 123 | Minimum idle device (complete) | 0281268 | 1 |
| • 124 | Refrigerant overflow pipe | 031681 | 1 |
| 125 | 5/16" CF (condenser-receiver drier) gas pipe | 820AA710 | 1 |
|  | 5/16" FE (receiver drier-evaporator) gas pipe | 806GA429 | 1 |
|  | 13/32" CC (condenser-compressor) gas pipe | 808GA430 | 1 |
|  | 1/2" EC (evaporator-compressor) gas pipe | 810GA358 | 1 |
| ■ | Note: Included in the bag of findings pos. 10. |
| * | Note: Supplied upon request. |

NOTE:

This instruction manual illustrates the A.C. system and ai times, includes accessories (eg. idle-speed device, radiator, fan, etc.), These parts, however, must be ordered separately from the basic kit, consult our parts list.

All references to RIGHT and LEFT hand are related to driving direction: LEFT = driver's side. RIGHT = passengers side.

All numbers quoted in the next and under the photos refer to ihe components supplied of the air conditioning unit. One must therefore reier to the kits shown in fig. 1, 2 and 3/4/5.

All screws and gas pipes fittings must be locked without exceeding the maximum value of the driving torques indicated in the following table, if not otherwise. To ensure functioning and reliability of installed belts, carry out the following procedures:

a) Start motor with A.C. system switched on and after about 15 minutes adjust belt tension.

b) The same adjustment procedure should be repeated after 1500 Km from the in-staliation of the system.

In those vehicles with AIR BAGS or PROCON-TEN® safety devices, these components must be removed carefully following the instructions given by the manufacturer. The quantity of gas R134a necessary for charging the system is Kg. 0.350 (±0.020).

| MAXIMUM VALUES OF THE DRIVING TOURQUES FOR SCREWS (in N.m.} |
| --- |
| Thread | Screw steel class | Wrench opening (mm) |
|  | 6.8 | 8.8 | 10.9 |  |
| M 4(!lO,7) | 1.8 | 2.9 | 4.2 | 7 |
| M 5(xO.8) | 3 4 | 5.5 | 7.5 | 8 |
| M 6(x1) | 6.00 | 10 | 13 | 10 |
| M 7(x1) | 11 | 16 | 21 | 11 |
| M 8(x1.25) | 14 | 22 | 3D | 13 |
| M 8x1 | 15 | 23 | 32 | 13 |
| M10(x1.5) | 27 | 45 | 61 | 17 |
| M10 x1.25 | 31 | 50 | 67 | 17 |
| M10 x1 | 33 | 53 | 71 | 17 |
| M12 x1.5 | 51 | 78 | 105 | 19 |
| M12 x1.25 | 60 | 94 | 125 | 19 |
| M12 x1.75 | 84,8 | 119 | 143 | 19 |
| M14 x1.5 | 80 | 120 | 165 | 22 |
| M16 x1.5 | 120 | 185 | 255 | 24 |
| M18 x1.5 | 165 | 265 | 350 | 27 |
| M20 x1.5 | 225 | 360 | 490 | 30 |
| M22 x1.5 | 295 | 480 | 640 | 32 |
| M24 x2 |  | 610 | 305 | 36 |

| FITTINGS | MAXIMUM VALUES OF THE DRIVING TORQUES (in N.m.) |
| --- | --- |
| 5/8" | 15 4 - 17 |
| 3/4" | 15.4 - 17 |
| 7/8' | 24.4 - 27 |
| 1" | 24.4 - 27 |